## Slide 1: Pushing the LHC peak luminosity in 2011: Beam instabilities
Giovanni Rumolo
in the Mini-Chamonix Workshop
Friday 15.07.2011, Jiva Hill Park Hotel
With the invaluable contributions of: W. Hoefle, K. Li, E. Métral, N. Mounet, F. Roncarolo, B. Salvant, E. Shaposhnikova, M. Taborelli, C. Yin-Vallgren
BE-ABP-ICE

## Slide 2: Goal & outline
Based on observations, theory and simulations, review possible instability mechanisms and extrapolate stability criteria for
  50ns beams with Nb up to 1.7e11 ppb and ex,y<2mm
  Nominal 25ns
Instabilities driven by the machine impedance:
  Single bunch: Head-tail instabilities and TMCI
  Excitation of coupled bunch modes
Electron cloud effects on the beam
  Build up conditions
  Coherent instabilities & tune footprint
    Thresholds
    Parameter dependence
Longitudinal instabilities

## Slide 3: Impedance driven instabilities: possible effects
Single bunch instabilities
  Headtail modes
    Modes |m|≥1 unstable when Q’>0
    At all intensities, however with growth rate proportional to bunch intensity
    Can be damped with tune spread with amplitude (octupoles)
  Transverse Mode Coupling Instability
    Only above an intensity threshold (Nb > Nth)
    The threshold is usually increased by positive chromaticity and octupoles
    Possibly cured by a high bandwidth feedback system
W(z-z‘)l(z‘)<x>(z‘)dz‘
z

## Slide 4: Impedance driven instabilities: possible effects
Single bunch instabilities
  Headtail modes
  Transverse Mode Coupling Instability (TMCI)
Coupled bunch instabilities
  Rigid bunch oscillations
    At all intensities, however with growth rate proportional to bunch intensity
    Can be damped with transverse feedback
  Higher order modes
    Are characterized by both intra-bunch and bunch-to-bunch oscillation
    Can be Landau damped with octupoles
W(kd)N(kd)<x>(kd)
d

## Slide 5: Overview on possible instabilities (transverse plane)
Single bunch instabilities
  Headtail modes
  Transverse Mode Coupling Instability (TMCI)
Coupled bunch instabilities
  Rigid bunch oscillations
  Higher order modes
Electron cloud effect
  In general, multi-bunch effect, because bunch trains are needed to build up an electron cloud
  Can be source of Electron Cloud Instability (ECI)
    By coupling the motion of subsequent bunches through a bunch-to-bunch wake (rigid or headtail modes). E.g. horizontal coupled bunch ECI is observed in the SPS and suppressed with the damper
    By coupling the motion of head and tail of the same bunch and exciting a headtail mode. E.g. vertical single bunch ECI is observed in the SPS and suppressed with high chromaticity
Protons per bunch, Nb
Bunch spacing, number of bunches, number of batches
Transverse emittances, ex,y
Transverse emittances, ex,y

## Slide 6: Overview on possible instabilities (transverse plane)
Single bunch instabilities
  Headtail modes
  Transverse Mode Coupling Instability (TMCI)
Coupled bunch instabilities
  Rigid bunch oscillations
  Higher order modes
Electron cloud effect
  In general, multi-bunch effect, because bunch trains are needed to build up an electron cloud
  Can be source of Electron Cloud Instability (ECI)
    By coupling the motion of subsequent bunches through a bunch-to-bunch wake (rigid or headtail modes). E.g. horizontal coupled bunch ECI is observed in the SPS and suppressed with the damper
    By coupling the motion of head and tail of the same bunch and exciting a headtail mode. E.g. vertical single bunch ECI is observed in the SPS and suppressed with high chromaticity

## Slide 7: Single bunch instabilities Headtail modes
First observed in the LHC on acceleration of the nominal bunch
  Excited on the ramp (around 2 TeV) with ~6 Q’ units
  Measured rise time of ~10s
  Clearly a mode m=-1, as seen from the spectrum
  Suppressed with Landau damping through octupoles
Courtesy E. Métral
Beginning of instability
Advanced phase of instability

## Slide 8: Single bunch instabilities Headtail modes
Explained and reproduced with simulations and theory (nominal intensity)
  Growth rate proportional to bunch intensity
  Efficiency of octupole stabilization depends on transverse emittance
Depending on chromaticity control or requirements, larger bunch intensity and smaller transverse emittances might take stronger octupole currents for the suppression of this instability
Courtesy E. Métral, B. Salvant
HEADTAIL simulation
HEADTAIL simulation

## Slide 9: Single bunch instabilities TMCI
Not observed experimentally with intensities presently injected into the LHC
  Up to 2.8 x 1011 p at 450 GeV
  Up to 1.7 x 1011 p at 3.5 TeV
Indeed simulated thresholds with our impedance model are higher with the nominal collimator settings at both injection and top energy
Courtesy B. Salvant
HEADTAIL simulation @450 GeV
HEADTAIL simulation @3.5 TeV
Nth = 8 x 1011 p
Nth = 8 x 1011 p

## Slide 10: Single bunch instabilities TMCI
However, tight collimator settings (presently considered , at least at flat top) lower the TMCI threshold by more than a factor 2
Even with these settings, single bunch intensities up to 3 x 1011 should not suffer from TMCI
Courtesy N. Mounet
HEADTAIL simulation @3.5 TeV
Nth ≈3 x 1011 p
This threshold can be actually lower if:
A significant contribution to the global short range wake is still missing from the LHC impedance database
The multi-bunch effect plays an important role

## Slide 11: Overview on possible instabilities (transverse plane)
Single bunch instabilities
  Headtail modes
  Transverse Mode Coupling Instability (TMCI)
Coupled bunch instabilities
  Rigid bunch oscillations
  Higher order modes
Electron cloud effect
  In general, multi-bunch effect, because bunch trains are needed to build up an electron cloud
  Can be source of Electron Cloud Instability (ECI)
    By coupling the motion of subsequent bunches through a bunch-to-bunch wake (rigid or headtail modes). E.g. horizontal coupled bunch ECI is observed in the SPS and suppressed with the damper
    By coupling the motion of head and tail of the same bunch and exciting a headtail mode. E.g. vertical single bunch ECI is observed in the SPS and suppressed with high chromaticity

## Slide 12: Coupled bunch instabilities Rigid bunch mode (m=0)
Courtesy N. Mounet
Damped by the transverse feedback system in routinely operation
LHC MD 8th May 2011
  Inject two batches of 12 and 36 bunches (50ns spacing)
  Switch off the feedback system with ~0 chromaticity (it was tried both at injection and top energy)
  Coupled bunch instability (mode 0) excited
@450 GeV
@3.5 TeV

## Slide 13: Coupled bunch instabilities Rigid bunch mode (m=0)
Courtesy N. Mounet
HEADTAIL simulation @450 GeV
HEADTAIL simulations (multi-bunch mode) could reproduce the measured rise times within a factor 1.4 at injection and 2 at top energy
Higher charge per bunch, higher number of bunches, closer spacing (25ns), tighter collimator settings could all contribute to decrease the rise times measured during the MD, but should be still in a range in which the damper can suppress this unstable mode. Simulations could be used to check this
HEADTAIL simulation @3.5 TeV

## Slide 14: Coupled bunch instabilities Headtail modes (m≥1)
Courtesy N. Mounet
The growth rates of the coupled bunch headtail modes m=1 are evaluated analytically with Sacherer’s formula
Worst case considered  tight collimator setting at 3.5 TeV
Two cases have been checked
  25ns with 1.2 x 1011 ppb and 2.5mm transverse emittance, Q’ from 0 to 8 units
  50ns with 1.7 x 1011 ppb and 1.9mm transverse emittance, Q’ from 0 to 8 units
Stability boundary for Ioct=-150A
50ns, 1.7 x 1011 ppb, ex,y=1.9mm
Stability boundary for Ioct=-300A
Stability boundary for Ioct=-150A
25ns, 1.2 x 1011 ppb, ex,y=2.5mm
Stability boundary for Ioct=-300A

## Slide 15: Overview on possible instabilities (transverse plane)
Single bunch instabilities
  Headtail modes
  Transverse Mode Coupling Instability (TMCI)
Coupled bunch instabilities
  Rigid bunch oscillations
  Higher order modes
Electron cloud effect
  In general, multi-bunch effect, because bunch trains are needed to build up an electron cloud
  Can be source of Electron Cloud Instability (ECI)
    By coupling the motion of subsequent bunches through a bunch-to-bunch wake (rigid or headtail modes). E.g. horizontal coupled bunch ECI is observed in the SPS and suppressed with the damper
    By coupling the motion of head and tail of the same bunch and exciting a headtail mode. E.g. vertical single bunch ECI is observed in the SPS and suppressed with high chromaticity

## Slide 16: Electron cloud effects Considerations on the build up
StSt
DLC
DLC cond. and StSt cond.
a-C
50 ns threshold (simul.)
Courtesy M. Taborelli
1380 bunches per ring
e growth < 2% /h
Courtesy F. Roncarolo
Build up is stronger with closer bunch spacing (in the LHC range)
  SPS experience
    Threshold SEYmax is about 1.7 with 50ns beams and 1.3 with 25ns beams (nominal intensity)
    Surface scrubbing leads to SEYmax=1.5-1.6 on StSt (measured) and saturates at this value
  LHC
    Presently, nominal 50ns beams do not suffer from obvious electron cloud limitations (after 10 days dedicated scrubbing + few months of “free scrubbing” with physics)  SEYmax ≤ 1.7
    First injections of 25ns beams in batches of 24 bunches  difficult to conclude on electron cloud effects on the beam

## Slide 17: Electron cloud effects Considerations on the build up
Build up is stronger with closer bunch spacing (in the LHC range)
  SPS experience
    Threshold SEYmax is about 1.7 with 50ns beams and 1.3 with 25ns beams (nominal intensity)
    Surface scrubbing leads to SEYmax=1.5-1.6 on StSt (measured) and saturates at this value
  LHC
    Presently, nominal 50ns beams do not suffer from obvious electron cloud limitations (after 10 days dedicated scrubbing + few months of “free scrubbing” with physics)
    First injections of 25ns beams in batches of 24 bunches  difficult to conclude on electron cloud effects on the beam
Effect of bunch intensity
  Simulations suggest a decrease of the electron cloud activity when increasing the intensity per bunch of 50ns beams to values higher than nominal
  Lack of clear experimental verification in the SPS
Effect of transverse emittances
  Little influence expected when the SEY is far above the threshold value for build up
  Smaller emittances can significantly enhance the electron cloud when SEY is close to the threshold value for build up

## Slide 18: Electron cloud effects Considerations on the build up
SPS MD on 11th May 2011
4 batches 50ns, 1.4 x 1011 ppb ex,y=1.6mm
4 batches 50ns, 1.6 x 1011 ppb ex,y=1.9mm
4 batches 50ns, 1.4 x 1011 ppb ex,y=2.5mm
Courtesy C. Yin Vallgren
Increasing the intensity:
1, 2, 3 batches 50ns, 1.4 x 1011 ppb ex,y=1.6mm

## Slide 19: Electron cloud effects Single bunch ECI
During the scrubbing run and first physics runs, some bunches at the tails of batches were observed to suffer from emittance growth (BSRT) and larger losses (FBCT), probably a signature of coherent instability
ECI can be enhanced by:
  More electron cloud
    50ns with higher charge per bunch (?) and smaller transverse emittances
    25ns (at least one order of magnitude more)
  Smaller transverse emittances
    Due to stronger pinching effect
    Experimental verification at the SPS in 2008
Beam 1 (flat top screen shots), Fill 1728

## Slide 20: Electron cloud effects Single bunch ECI
HEADTAIL simulations of ECI @ 450 GeV and ex,y=1.5 to 3.5mm , electron cloud density threshold value for the onset of the ECI
  Field-free region (total length ~30% of the ring)  1 – 1.4 x 1012 m-3
  Arc dipoles (total length ~60% of the ring)  0.85 – 1.1 x 1012 m-3
Threshold values are probably about a factor 2 lower if the electron cloud is present both in the dipoles and in field-free regions. These densities are compatible with central densities from 25ns beams
Q’=15 is sufficient to recover stability
Courtesy K. Li

## Slide 21: Electron cloud effects Tune footprint
HEADTAIL simulations @ 450 GeV with electron cloud density values below threshold for the onset of the ECI are used to quantify possible tune spreads from electron cloud
DQy=0.02
DQy=6 x 10-3
Courtesy K. Li

## Slide 22: Longitudinal plane Dipole and quadrupole instabilities
Loss of Landau damping is observed at injection in the LHC
  For intensities above 1.5 x 1011 ppb and longitudinal emittances below 0.75 eVs without phase loop
  The phase loop works well for single bunch injection but is less efficient for multi-bunch injections
  Oscillation growth is very slow and stops when the longitudinal emittance has grown above the threshold value
Dipole oscillations can also become unstable along the ramp for intense bunches
Quadrupole oscillations are excited at flat top for small longitudinal emittances
There is no observation of longitudinal coupled bunch instabilities
Courtesy E. Shaposhnikova
Both can be stabilized by longitudinal emittance blow up along the ramp

## Slide 23: Summary
 | 50ns with higher Nb and lower ex,y | 25ns nominal
Single bunch headtail instabilities | More Landau damping required | Present Landau damping settings sufficient
TMCI | Both safely below threshold, multi-bunch effect? | 
Coupled bunch instabilities (m=0) | Transverse feedback | 
Coupled bunch instabilities (headtail modes) | More Landau damping required | Present Landau damping settings marginally sufficient
Electron cloud build up | Larger than now, maybe more scrubbing needed | Significantly larger than now, efficiency of scrubbing?
Single bunch ECI | Higher chromaticity setting to suppress it during scrubbing | Higher chromaticity setting to suppress it, if e-cloud level tolerable