## Slide 1: Session 1 Review 2011, efficiency, turn-around
G. Papotti,J. Wenninger
M. Pojer, M. Albert, A. MacPherson,
W. Venturini

## Slide 2: Efficiency
Effective efficiency: ~34%  1 h SB – 2 hours ‘off’
  MD, TS removed.
Massi by JW
Mean = 6.1 hours

## Slide 3: Turn-around mystery…
About the definition of turn-around and histogram limits..
  “I only believe the stats that I distorted myself”
Massi by JW
Mean = 11.1 hours
Mean = 5.4 hours
Efficiency SB =

## Slide 4: LEP
Efficiency of stable beams: 35% to 59%
More or less equivalent definition
34%

## Slide 5: Faults accounting
Tedious job – will never be 100% ‘fair’ (fault shadowing).
  But can be improved… for example injection phases.
Need consistent handling on time scales >> single shift.
Need a person to follow fault tracking on time scale of a week.
  Obvious candidates.

## Slide 6: Turn-around 2011 - 2010
Turnaround still largely dominated by machine availability.
When there are no faults, injection is the dominating factor.
Improvements in spread due to automation / sequencing.
  Ramp, squeeze, adjust.
  Also safer - fewer human errors !!!

## Slide 7: Turn-around improvements (1)
Combined Ramp & Squeeze – gain ~ 6 mins
  All IRs to ~3 m (also ALICE for sat-main).
  More complicated ramp, but no optics correction needed before 3m (in 2011). Smaller ups&downs of LSS quad currents.
  VdMs : should be OK – tbc.
  OFB and QFB reference – OK.
  Injection with collision tunes.
  Need another ramp for 90m, but ramp commissioning is no problem (see ATS).
IP1/5/8 = 1.0/1.0/3.0 m → 554 s
= 0.7/0.7/3.0 m → 697 s
= 0.6/0.6/3.0 m → 784 s
4 TeV squeeze

## Slide 8: Turn-around improvements (2)
B3 & Q decay on FT – gain 6 mins
  Trim MCS using FIDEL like correction scheme (no squeeze functions for MCS).
  Could glue squeeze to ramp into one function.
    Watch out for extra-complication for QFB/OFB – requires significant changes and commissioning. OFB limited presently by linear changes, places strong constraints on Xing and separation bump fcts.
Ramp-down – gain 11 mins
  Pretty transparent if no HW issue.
  Test during HWC – easy to fall back !
General consideration:
  Faster cycle can also help significantly for MDs.
  Combined R&S experience for 7 TeV operation – could of course test only in MD…
  Watch out for MKI heating effect during HI p operation.

## Slide 9: Turn-around improvements (3)
From adjust to stable beams before performing lumi scans.
  Ensure LHCb and ALICE luminosities will not go through the roof !
  No issue from MP side.
  Need experiments consensus.
A ‘charming’ idea:
LHCb proposal to collide as soon as IR8 squeeze finished – while other IPs still squeeze (and later collide).
  Challenge to keep the beams colliding stably, squeeze with FBs in parallel to lumi leveling – flair of ‘combined lumi leveling by offset and beta*’.
  Risk of lumi hitting values well above max of 4E32 cm-2s-1.
  Keep this for ‘later’…

## Slide 10: Injection
Injection is the phase where the LHC ‘encounters’ the rest of the complex.
  There are colleagues working on the other machines – cannot always ask them to immediately stop all current activities in order to fill LHC. Must accept occasional overhead.
Steering:
  As long as lines drift, some overhead for steering – must streamline with clean references (and if necessary new TCDI setups).

## Slide 11: Line steering during ramp down?
Use 12b beam.
Need ‘perfect’ reference, use only upstream steerers.
Line must be stable over ~2 hours !
LHCb and ALICE need to give injection permit !
Could (should) be tried !