## Slide 1
R2E – Experience and Outlook for LS1
G. Spiezia for the R2E Project
!!! Many Thanks To Everybody !!!

## Slide 2: Overview
Radiation levels and source terms
Failures observed during 2012
What’s to be expected for LS1

## Slide 3: R2E Mitigation Strategy
1st Safety Critical
2nd Shielding
3rd Most Sensitive
4th Remaining
Immediate Relocation
“Fast” & Global Improvement
Highest Impact on Operation:
Relocation
Shielding
Relocation
Shielding
New Design

## Slide 4
Radiation levels and scaling

## Slide 5
Critical areas well within predictions for radiation levels
Operational parameters can have important impact
Other areas not to be forgotten:
  e.g, UX45
    2011: 2.6x106
    2012: almost 2x107cm-2
Radiation Levels
Predictions versus Observations (scaled to exp. lumi)
1.1x108
1.8x107
1.2x108
1.8x107
5.5x107
3.0x107
2.6x108
6.5x107
…and Today
Decrease: TCL closed
Increase: Tight Collimators
Notes: Quick explanation: monitors (various) + operation (Lumi + Losses)
Good agreement with predictions + P4 behaviour
Showing also doses in the DS/ARC?

## Slide 6
Leakage into DS
  Cells 7-10: ~10Gy
  <Cell17: ~1Gy
  >Cell17: ~0.1Gy
Currently relatively low vacuum activity
?How will this possibly change with 25ns?
Effect of Operation

## Slide 7
Failures analysis

## Slide 8: Information collection
R2E weekly shift to collect information
Analysis
  Radiation levels at the failure location
  Failure mode and comparison with the rad-test
  Rate of the failures
  Iteration with the equipment owners
What we store:
  Location
  Date-Time failure
  Equipment/Component
  Consequence of the failure
  Beam fill

## Slide 9: Information collection
Post Mortem Database
Rad WG web site-Detail
Details on radiation failure
Link with the fill number

## Slide 10: Mitigation Measures XMas 2011
Shielding thanks to EN/MEF
  P1 (UJ 14/16) – various equipments Gain factor ~2. Take into account shielding efficiency and radiation level increases.
Relocation
  Cryogenic equipment from Point 4/6/8
  B/P/WIC equipment from UJ56 US85
  EN/EL UPS from UJ56
  No events anymore
Equipment actions
  QPS: Fw, Hw updates
  EPC: Fw updates
  CRYO: Hw updates (Temperature sens)

## Slide 11
Failure Overview
Dump Confirmed | Dump TBC | No Dump | No Dump TBC
58 | 10 | 36 | 7
Destructive failures |  |  | 
Dump Confirmed | Dump TBC | No Dump | No Dump TBC
17 | 1 | 4 | 0
Status November 2012
Notes: PM-DB Extraction -> slope for this year
Area/Equipment (both for confirmed/possible) -> Ruben help!

## Slide 12: QPS
Locations: UJ14/16, UJ56, RRs P1/P7, DS
Failure types:
  Digital detection system for nQPS (very few)
  600A protection (DSP based system)
  uFIP communication
  DAQ&uFip: no dump but required access
Mitigations:
  New DAQ system under design (FPGA)
  Firmware upgrades
  BricoFip (mid-term)/NanoFip (long-term)
Main Impact: caused most of the R2E dumps
Dump | Dump/TBC | No Dump | No Dump/ TBC
32 | 2 | 22 | 1

## Slide 13
QPS – Detail
Chart: 
| unclear | DSP based | DQQBS old fw | DQQDC old fw
 | 1 | 22 | 1 | 3
R2E consolidation
Chart: 
| mitigated | unclear
 | 26 | 1
2012: 27 R2E trips during stable beam
>LS1: with all foreseen measures in place: 1
© R. Denz, J. Steckert
2011: 3.5 dumps per fb-1
2012: 1.4 dumps per fb-1
1/3 of errors in UJ14/16/56
Notes: Observed failures & Analysis

## Slide 14
Locations: UJs, RRs, ARC
Failure types (only confirmed ones kept in follow-up):
  600A: Aux Power Supply [14 events]
  FGC [10 events]
  120A failure [1 event]
Mitigations:
  AC/DC power supply problem understood, corrected during LS1
  New FGClite design (on-going)
  Radiation tolerant power converters (started)
Main Impact:
  Many destructive failures
Power Converter
Dump | Dump/TBC | No Dump | No Dump/ TBC
14 | 0 | 11 | 0
Status November 2012
Notes: Observed failures & Analysis

## Slide 15: Cryo
Locations: UJ56, UJ76, UX45, US85
Failure types
  Mecos AMB
  Profibus communications
Mitigations
  AMB case (UX45, UX65, US85): Relocation under study [Mecos, S2M]
  Profibus: Relocation from UJs during LS1
  31 events mitigated due to autoreset
Main Impact
  Important contribution to R2E downtime
Dump | Dump/TBC | No Dump | No Dump/ TBC
4 | 2 | 1 | 0

## Slide 16: Vacuum
Locations: UJ76, UX45
Failure types
  Loss of the PLC control (soft)
  Power supply (destructive failures)
Mitigations
  Relocation from UJ76
Dump | Dump/TBC | No Dump | No Dump/ TBC
4 | 3 | 0 | 0

## Slide 17: EN/EL
Locations: US85
Failure types
  IGBT failure
Mitigations
  Relocation from US85 to UA83
  Remain REs
  Recently tested at H4
Dump | Dump/TBC | No Dump | No Dump/ TBC
1 | 0 | 0 | 0

## Slide 18: Collimation control
Locations: UJ16, UJ56
Failure types
  Loss of communication
Mitigations:
  Relocation
Dump | Dump/TBC | No Dump | No Dump/ TBC
1 | 0 | 2 | 0

## Slide 19: RF Equipment
Locations: UX45
Failure types
  Power supply
  Vacuum gauge
Mitigations
  Cases are still under investigations
  Radiation effects to confirm
Dump | Dump/TBC | No Dump | No Dump/ TBC
1 | 2 | 0 | 0

## Slide 20: Access system
Locations: P1, P5
Failure types
  Functionality loss of the MAD/PAD system
  Difficult to relate to Radiation
  Higher failure rate in exposed areas
Mitigations
  Relocation
Main Impact
  Downtime during access
Dump | Dump/TBC | No Dump | No Dump/ TBC
0 | 0 | 5 | 0

## Slide 21: Downtime due to Failures
A preliminary analysis was done taking into account
  RadWG list PM database and e-logbook entries
  Time interval between beam fills
  Manual iteration  avoid downtime due to other failures

## Slide 22
Total R2E related downtime ~250h-300h
Mainly based on dump cases (others difficult to track)
Downtime Analysis
Status November 2012
Notes: Update of table -> Petra

## Slide 23
Summary and outlook for >LS1

## Slide 24
What Changes After LS1
Main impacted systems – observed failure signatures:
  Equipment Upgrades
  New developments
  Relocation (UJs, US85, UX45 partly)
  Shielding (RRs)
Remaining (future) commercial systems:
  Full relocation (except REs)
  No new installation in critical areas without radiation tests & developments
  Equipment inventory for P4 (UX45)
Enormous Effort during LS1
Notes: Power-Converters (Tunnel + RRs)
P4 remaining (25ns?)
QPS and other tunnel equipment (incl. future requirements)

## Slide 25
Tunnel Equipment:
  DS/ARC will be more and more loaded
  Long-term damage to be considered in cells 8-13
  Impact of 25ns operation to be evaluated
  Future upgrades/changes/new installations
RRs & Power Converters
  FGClite prototype available, available in time and to be deployed
  Power-part R&D started & component tests on-going
Areas to be watched
  UX45, UX65, UX25, UJ/UA23, UJ/UA87 (+REs)
What Remains After LS1
Notes: Observed failures & Analysis

## Slide 26: What do we expect for LS1
Equipment | Dump 2012 | >LS1 Expectations
QPS | 31 | 5
Power Converter | 14 | 3
Cryo | 4 | 1
EN/EL | 1 | 0
Vacuum | 4 | 2
Collimation | 1 | 0
Other |  | 5
10-20 Expected Dumps

## Slide 27: R2E: Past/Present/Future
~3 dumps per fb-1
2012
~12 dumps per fb-1
2011
2011/12 xMasBreak ‘Early’ Relocation + Additional Shielding + Equipment Upgrades
Several shielding campaigns prior 2011 + Relocations ‘on the fly’ + Equipment Upgrades
< 0.5 dump per fb-1
R2E-Project aiming for … >LS1 (nominal -> ultimate)
2012 SEE Failure Analysis
Equipment relocations @ 4 LHC Points (>100 Racks, >60 weeks of work)
Additional shielding
Critical system upgrades (QPS, FGC)
Status November 2012
Notes: Extract latest PM-DB plot

## Slide 28
2011, xMasBreak and previous actions very efficient
2012 Failures
  Within Chamonix predictions
  … and the winner is: QPS + EPC (+Cryo)
LS1: ~10-20 dump events
  Mitigations
    Enormous relocation campaign (4+ Points)
    Remaining shielding
    Numerous system upgrades (QPS, EPC)
  To be taken into account
    Long-Term Damage & 25ns Operation
Conclusions
Notes: Long-Term damage -> rad levels TID in DS

## Slide 29
THANK YOU

## Slide 30: Back-up

## Slide 31
Predictions based on the integrated luminosity for many critical areas
Radiation Levels
Cum lumi (fb-1) | 2011 | 2012
ATLAS | 5.3 | 23.1
CMS | 5.4 | 23.1
ALICE | 4.8 (pb-1) | 9.7 (pb-1)
LHCb | 1.2 | 2.2
Cumulated lumi ~1.5x larger than initially foreseen for 2012
Notes: Quick explanation: monitors (various) + operation (Lumi + Losses)
Good agreement with predictions + P4 behaviour
Showing also doses in the DS/ARC?

## Slide 32: UJ: Effect of Operation
High Energy Hadron Fluence [F/cm-2] |  |  |  |  | 
Area | 2011 | 2012 | 2011/fb-1 | 2012/fb-1 | Comments
UJ14 | 2.8*108 | 1.4*108 | 5.1x107 | 7.9x106 | Physics deb.
UJ16 | 2.2*108 | 1.1*108 | 4.2x107 | 6.2x106 | Physics deb.
UJ23 | 1.5*106 | 2.6*106 | 2.8x105 (*) | 1.5x105 (*) | Injection
UJ56 | 3.9*107 | 1.3*108 | 7.2x106 | 7.3x106 | Physics deb.
UJ76 | 6.4*106 | 6.0*107 | 1.2x106 (*) | 3.4x106 (*) | Collimation
UJ87 | 3.0*106 | 2.6*106 | 5.7x105 (*) | 1.5x105 (*) | Injection
P1: decrease by factor of 6x, thanks to additional shielding
P7: increase due to tight collimator settings
P2/8: reduction because of cleaner injections in the LHC
(*) = ATLAS/CMS luminosity

## Slide 33: RR: Effect of Operation
P1/5: decrease up to a factor of 2x (1.5-2x) due to TCL.4 closure
P7: asymmetry L/R (also observed in operation)
High Energy Hadron Fluence [F/cm-2] |  |  |  |  | 
Area | 2011 | 2012 | 2011/fb-1 | 2012/fb-1 | Comments
RR13 | 7.2*106 | 1.4x107 | 1.4x106 | 7.9x105 | Physics deb.
RR17 | 8.4*106 | 2.0x107 | 1.6x106 | 1.1x106 | Physics deb.
RR53 | 1.2*107 | 2.0x107 | 2.3x106 | 1.1x106 | Physics deb.
RR57 | 1.0*107 | 2.0x107 | 1.9x106 | 1.1x106 | Physics deb.
RR73 | 7.7*106 | 4.2x107 | 1.5x106 (*) | 2.4x106 (*) | Collimation
RR77 | 1.1*107 | 2.1x107 | 2.1x106 (*) | 1.2x106 (*) | Collimation
(*) = ATLAS/CMS luminosity

## Slide 34: UX: Effect of Operation
P4: increase, beam-gas coupled with higher cumulative current in the machine
  How much can/will it go up in view of 25ns operation?
High Energy Hadron Fluence [F/cm-2] |  |  |  |  | 
Area | 2011 | 2012 | 2011/fb-1 | 2012/fb-1 | Comments
UX45 | 2.6*106 | 1.4x107 | 4.3x105 (*) | 8.2x105 (*) | Beam-gas
UX65 | N/A | ~1.x106 | N/A | N/A | Beam-gas
UX85 | 2.1*108 | 2.8x108 | 1.7x108 (**) | 1.6x108 (**) | Physics deb.
US85 | 4.4*107 | 7.0x107 | 3.7x107 (**) | 4.1x107 (**) | Physics deb.
(*) = ATLAS/CMS luminosity
(**) = LHCb luminosity

## Slide 35: Predictions for >LS1
© M. Calviani & MCWG
Areas | HEH Fluence |  | 
 | 2012 | Nominal | 
 |  | Lumi =50fb-1 | Lumi=100fb-1
UJ14/16 | 1.60E+08 | 3.95E+08 | 7.90E+08
RR13/17 | 2.50E+07 | 5.00E+07 | 1.00E+08
UJ56 | 1.50E+08 | 3.65E+08 | 7.30E+08
RR53/57 | 2.50E+07 | 5.00E+07 | 1.00E+08
UJ76 | 6.00E+07 | 1.70E+08 | 3.40E+08
RR73/77 | 5.00E+07 | 1.20E+08 | 2.40E+08
UX85b | 3.50E+08 | 3.52E+08 | 3.52E+08
US85 | 8.80E+08 | 9.02E+07 | 9.02E+07
 | TID |  | 
DS | 25 | 50 | 100
ARC | 1 | 1 | 2

## Slide 36
xMasBreak Actions very efficient
Mecos AMB Events (P4/8)
© A. Suraci et al. TE-CRG-OA
Better cleaning/control of the beam
CV891/fb-1
2.3
1.9
0.7
4.3
4.3
3.2
-
1.5
?
Cryogenics
TS2/3 Period interesting
2011
2012
Notes: Observed failures & Analysis

## Slide 37: Downtime analysis
Example
Beam Stop |  | (Next Beam Ramp) |  | Delay [h:m] | Accounted [h:m] | shadow | Manual Change | Access (yes/no) | Dump (yes/no) | Group | Point | Area | Failure Type | Comment
Date (2012) | TimeStamp | Next Date (2012) | Next TimeStamp |  |  |  |  |  |  |  |  |  |  | 
10-Apr | 06:48:55 | 10-Apr | 15:54:00 | 09:05:05 | 04:50:00 |  |  | yes | yes | QPS | 5 | UJ56 | Protection 600A | 
16-Apr | 14:21:54 | 16-Apr | 17:57:00 | 03:35:06 | 00:40:00 |  |  | no | no | EPC | 7 | ARCs | FGC COD | 
19-Apr | 10:10:00 | 19-Apr | 17:39:00 | 07:29:00 | 02:00:00 |  |  | yes | no | QPS | 5 | DS | DAQ system | during access to RF

## Slide 38: Mitigation Measures LS1-details
Equipment actions
  Cryo.
    Relocation of the AMB from UX45
    Better distribution of the charge for 24V DC
  QPS.
    Relocation from UJs
    Firmware update (RR)
    DSP replaced by FPGA
    Auto reset of MicroFip  Then, NanoFip