## Slide 2: Potential improvements of the PS 10 MHz cavities driving amplifier
G. Favia
Acknowledgments: V. Desquiens, F. Di Lorenzo S. Energico, M. Morvillo, C. Rossi
LIU-PS Student Day 21 April 2015

## Slide 3: Overview
The PS 10 MHz RF system
Beam loading instability and cures
The PS 10 MHz cavities driving amplifier
Improvements of the 10 MHz wideband feedback
Concluding remarks

## Slide 4
The PS 10 MHz RF System

## Slide 5
The PS machine contains cavities operating at different frequencies. The 10 MHz cavities are the most important because they accelerate the bunches to the desired energy and perform beam gymnastic.
The 10 MHz cavities (10+1 double gap cavities tuneable from 2.8 to 10 MHz) are driven by amplifiers based on electron tubes (power up to 60 kW), for reasons of radiation hardness and power dissipation.
2
The PS RF system
New LHC beam planned for the LIU project -> Increased intensity:
ppb at extraction
The 10 MHz cavities also constitute the major source of instabilities in the PS, that limit the increase of the beam intensity in the framework of the LIU project

## Slide 6
Ferrite loaded cavity
Gap voltage 0.5 - 10kVp
Frequency range 2.8 – 10 MHz
Tuning via bias current
that saturates the ferrite
Ferrite loss resistance:
22kΩ/gap @3MHz
10kΩ/gap @10MHz
RF amplifier adopting:
3xYL1056 tubes for predriver and driver
1xRS1084 in the final stage
Housed in the cavity base
Built in 1975, upgraded in 1988
Courtesy of C. Rossi
Courtesy of C. Rossi
The PS 10 MHz system

## Slide 7
Beam loading instability and cures

## Slide 8
Beam loading represents the effect induced by the beam passage in an RF cavity.
RF in a cavity
A short bunch arrives and generates a wakefield
The field in the cavity has a phase and an amplitude distortion
The beam loading instability
Beam = beam current IB inducing a beam loading voltage VB
Cavity = resonant impedance ZRF
The total voltage seen by the beam is the vector sum of the voltage due to the generator and the beam loading :
In stationary conditions, VRF must compensate VB , to keep Vt at the desired value.
In transient situations the voltage Vt will vary (Transient Beam Loading).

## Slide 9
R = final resistance of the amplifier and cavity losses
= current provided by the power RF amplifier
= beam current producing a voltage in the cavity called beam loading voltage
V = total voltage in the cavity ()
minimize the effect of -> minimize
Reduce the impedance seen by the beam
BEAM LOADING VOLTAGE
Enclose the cavity in a feedback loop
The impedance of the 10 MHz cavity as observed by the beam would be several kΩ per gap due to the ferrite losses and the final tube anode resistance. This high impedance would lead to strong beam loading.
The wideband negative feedback

## Slide 10
Phase shift introduced
by
cables and electronics
INSTABILITY ->
Minimize
increase the loop gain GL=A∙β
    maximize A (limited by the amplifier maximum rating)
    maximize β (limited by the maximum input power)
gain margin (mg)
and
phase margin (mϕ)
LIMITS:
= feedback factor
= A0 R = forward gain
Increase the margins, by limiting the phase shift
How to decrease Z?

## Slide 11
The PS 10 MHz system driving amplifier

## Slide 12
LOAD IMPEDANCE TRANSFORMATION FROM 50Ω TO 200Ω(1:4)
FREQUENCY TUNING VIA A DC CURRENT
180° PHASE SHIFT FOR THE LOCAL FEEDBACK
BW= 1.25 MHz
BW= 3.5 MHz
Frequency
BW = 1.2 MHz
BW = 65 kHz
LG=21 dB
The PS 10 MHz cavities driving amplifier

## Slide 13
Improvements of the 10 MHz wideband feedback

## Slide 14
STAGE | GAIN Old configuration | GAIN New configuration
Predriver | 11.1 dB | 12.76 dB
Driver | 26.7 dB @3MHz 24 dB @3MHz | 28.5 dB @3MHz 26 dB @10MHz
Final | 42.9 dB @3MHz 39.5 dB @10MHz | 44.9 dB @3MHz 43.2 dB @10MHz
TOTAL INCREASE OF GAIN:
~4dB IN THE FIRST TWO STAGES
~2dB IN THE FINAL STAGE
In order to get higher tubes transconductance and hence higher open loop gain, the working point of the tube has been modified.
Increase of A

## Slide 15
3 MHz
β has been increased by 3 dB → GL= 24 dB
that means more input power needed (but still achievable);
2. A has been increased by 6 dB → GL=30 dB
that means keeping the same input power.
The additional 6 dB will be distributed in this way:
Starting from GL =24 dB
3 dB will be used for decreasing the cavity impedance;
3 dB will be used for reducing the total group delay by acting on the local feedback or implementing hardware modifications;
GL=27 dB + stability
10 MHz
10 kvp/gap
NOT ACHIEVABLE!
Increase of β

## Slide 16
Increase of margins
In order to increase the stability margins hardware modification have been implemented
Improvement of the internal connections and damping of resonances
Old resonator: stray capacitance and leakage inductance, high losses at 10 MHz.
OLD | 3 MHz | 10 MHz
DRIVER LOAD | 194 Ω | 120 Ω
new connection
old connection
Replacement of the old resonator
New resonator: simpler device, less capacitance and leakage inductance, losses reduced at 10 MHz.
3 separated devices
tuneable resonator coil;
200Ω load transformer;
inverter.
NEW | 3 MHz | 10 MHz
DRIVER LOAD | 196 Ω | 177 Ω

## Slide 17
Results

## Slide 18
TOTAL LOOP 10 MHz
OL=64.3 dB
CL=42.1 dB
LG= 22.2 dB
64.3 dB
42.1 dB
INPUT POWER REQUIRED FOR 10 kVP
120 W
TOTAL LOOP 3 MHz
OL=69.5 dB
CL=42.8 dB
LG= 26.7 dB
69.5 dB
42.8 dB
INPUT POWER REQUIRED FOR 10 kVP
80 W
Results

## Slide 19
PSPICE model of the 10 MHz amplifier

## Slide 20
Higher amplifier gain is achievable without complete re-designing;
Up to 9 dB of additional loop gain have been demonstrated;
A stable operation with additional 6 dB of loop gain at 3 MHz can be achieved with an achievable input power by implementing few changes to the amplifier
    New modifications will be implemented in order to get higher loop gain with less input power at 10 MHz;
The overall feedback pickup will be moved from the anode of the final tube to the cavity, since the cavity acts as a good bandpass filter;
Asymmetries in the distribution of the beam induced voltage in the two cavity gaps will be analyzed;
The possibility to replace the first two stages with solid state amplifiers, or to clearly change technology for the cavity-amplifier system (wideband Finemet© cavity) will be investigated, if necessary.
Next steps
Summary

## Slide 21
THANK YOU
FOR YOUR ATTENTION

## Slide 22
Spare Slides

## Slide 24
PS ring cavities

## Slide 25
The LHC 25ns Cycle In The PS (pre-LS1)
h = 7
Eject 72 bunches
Inject 4+2 bunches
gtr
h = 84
h = 21
Instability
In the PS different multi-bunch beams are generated: 25, 50, 75 ns LHC physics beams. The 25 ns LHC physics beam is referred to as ‘nominal’ LHC beam.
Split in four at flat top energy
Courtesy of H. Damerau & L. Ventura
Triple splitting after 2nd injection

## Slide 26
STATIONARY BEAM LOADING
TRANSIENT BEAM LOADING
In stationary conditions, Vg must compensate Vb , to keep Vt at the desired value, providing an extra driving power or detuning the cavity.
In transient situations the voltage Vt will vary. It happens in many circumstances, such as at the injection or when the ring is not filled uniformly. The transient beam loading experienced by the bunch is the result of different spectral components besides the ones at the RF frequency.
Beam Loading