## Slide 1
PyECLOUD for PyHEADTAIL: development work
G. Iadarola, A. Axford, H. Bartosik, K. Li, G. Rumolo
Electron cloud meeting – 14 May 2015
Many thanks to:
A. Oeftiger, M. Schenk

## Slide 2
PyHEADTAIL
v
The PyECLOUD-PyHEADTAIL simulation setup
  We dropped the traditional approach of having separate tools for ecloud buildup and instability
  Use PyECLOUD also simulate the interaction beam/ecloud within PyHEADTAIL
     Possible thanks to the highly modular structure of the two codes (object oriented)
PyHEADTAIL bunch
PyHEADTAIL slicer
For each slice
PyHEADTAIL bunch
PyECLOUD
(PyEC4PyHT object)
Evaluate beam slice electric field (Particle in Cell)
Generate seed e-
Compute e- motion (t->t+Δt)
(possibly with substeps)
Detect impacts and generate secondaries
Evaluate the e- electric field
(Particle in Cell)
Apply kick on the beam particles
Legend: From PyHEADTAIL From PyECLOUD Developed ad hoc
Initial e- distribution
(from PyECLOUD buildup sim.)
PyHEADTAIL
Transverse tracking
   with Q’, octupoles etc.
Longitudinal tracking
Transverse feedback
Impedances
Space charge
…
Transverse tracking
   with Q’, octupoles etc.
Longitudinal tracking
Transverse feedback
Impedances
Space charge
…

## Slide 3
The PyECLOUD-PyHEADTAIL simulation setup
  We dropped the traditional approach of having separate tools for ecloud buildup and instability
  Use PyECLOUD also simulate the interaction beam/ecloud within PyHEADTAIL
     Possible thanks to the highly modular structure of the two codes (object oriented)
  Advantages of this approach:
    Profits from years of optimization and testing work on PyECLOUD and PyHEADTAIL
    All advanced e-cloud modeling features implemented in PyECLOUD become naturally available for beam dynamics simulations (arbitrary chamber shape, secondary electron emission, arbitrary magnetic field map, Boris electron tracker, accurate modeling for curved boundary)
    From now on the two tools can share most of the work of development and maintenance
This enables several new simulation scenarios:
  Scenarios where the electron wall interaction cannot be neglected, e.g. long bunches (PS), doublet beams
  Quadrupoles (including triplets, for example we could keep one beam rigid…)
  Combined function magnets
    … but simulations can become very heavy (>1 Week)  performance optimization is crucial!

## Slide 4
The computational core: PyPIC
  A key component of the e-cloud simulator is the Particle In Cell (PIC) Poisson solver (takes >50% of the computational time)
  Born as a buildup code, PyECLOUD did not allow to simulate the e-cloud dynamics in free space, extensively used in the past for HEADTAIL simulations  impossible to start the development from a well known model
  We decided to reorganize our Particle In Cell (PIC) Poisson solvers
  We wrote a Python library (PyPIC) including different PIC solvers having the same interface which can be used as plug-in modules for PyECLOUD but also for other applications (e.g. space charge, beam-beam)
  PyPIC is now available on the PyCOMPLETE git repository: https://github.com/PyCOMPLETE/PyPIC/

## Slide 5
The computational core: PyPIC
  A key component of the e-cloud simulator is the Particle In Cell (PIC) Poisson solver (takes >50% of the computational time)
  Born as a buildup code, PyECLOUD did not allow to simulate the e-cloud dynamics in free space, extensively used in the past for HEADTAIL simulations  impossible to start the development from a well known model
  We decided to reorganize our Particle In Cell (PIC) Poisson solvers
  We wrote a Python library (PyPIC) including different PIC solvers having the same interface which can be used as plug-in modules for PyECLOUD but also for other applications (e.g. space charge, beam-beam)
  PyPIC is now available on the PyCOMPLETE git repository: https://github.com/PyCOMPLETE/PyPIC/

## Slide 6
The computational core: PyPIC
  PyPIC includes the following solvers:
    Open boundary FFT
    PEC rectangular boundary FFT
    PEC arbitrarily shaped boundary – Finite Differences – staircase approx. of curved boundaries
    PEC arbitrarily shaped boundary – Finite Differences – Shortley-Weller method for curved bound.
    Bassetti-Erskine (not really a solver, for testing purposes)
  + test scripts: crosscheck the different modules against each other (for special cases in which this is possible)
  Uniformly charged cylinder
  inside circular boundary
  Uniformly charged cylinder
  inside square boundary

## Slide 7
The computational core: PyPIC
  In PyECLOUD-PyHEADTAIL simulations the PIC solver is called twice per slice at each e-cloud interaction
  e.g. 512 turns x 35 kicks x 64 slices: 2.3 x 106 recalculations!!!  speed is crucial
  Performance optimization carried out for all the modules:
    FFTW routines used for the FFT based solvers
    LU factorization precomputed and stored the FD solvers
    Special properties of the relevant matrices have been exploited
      FFT is performed block-wise skipping blocks filled with zeros
      Trivial equations for points outside the chamber are removed
Open boundary is heavier (2x larger matrix)
For PEC: FFT and FD have similar performances
3.2 x 106 nodes

## Slide 8
The computational core: PyPIC
Situation different for smaller matrices but still FD has the best performance
3.2 x 105 nodes
  In PyECLOUD-PyHEADTAIL simulations the PIC solver is called twice per slice at each e-cloud interaction
  e.g. 512 turns x 35 kicks x 64 slices: 2.3 x 106 recalculations!!!  speed is crucial
  Performance optimization carried out for all the modules:
    FFTW routines used for the FFT based solvers
    LU factorization precomputed and stored the FD solvers
    Special properties of the relevant matrices have been exploited
      FFT is performed block-wise skipping blocks filled with zeros
      Trivial equations for points outside the chamber are removed

## Slide 9
An extra boost to the Finite Difference solver
  Even after these optimizations simulation for the LHC at 7 TeV would still take ~8 days
  PIC still completely dominant in the profiling  tried to optimize even further:
  Iterative method turned out to be slower 
  Cython wrapped C-implemented SuperLU gave performances similar to scipy 
    …but we learnt how to use C libraries in Python 
  Found in literature that a simpler algorithm (KLU) outperforms SuperLU for very sparse matrices
    Implemented using Cython to wrap the available C implementation  PyKLU
      Available on the PyCOMPLETE git repository
It worked! 

## Slide 10
Optimization on other modules of PyECLOUD
  Performance optimization through Cython and small C parts applied also in other parts of the code:
    Polygonal chamber routines
      Gives more flexibility  made much easier the implementation of the non-convex case
    Boris tracker
      Ready for the implementation of the generic multipole
  This routines offered also the occasion for first parallelization tests in Cython
      Promising (x2 speedup with 4 cores) but for now not in the production version...
  Side effect of optimization work: also PyECLOUD buildup simulations became faster
     x2 gain on HL-LHC triplet simulations between Nov. 2013 and Nov. 2014

## Slide 11
Validation procedure
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
Turn 1

## Slide 12
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
Turn 10
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 13
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
  Check with multiple e-cloud kicks (on the integer)
    Phase advance correctly applied
Turn 1, 3 kicks
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 14
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
  Check with multiple e-cloud kicks (on the integer)
    Phase advance correctly applied
  Check with betatron motion enabled
Turn 1
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 15
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
  Check with multiple e-cloud kicks (on the integer)
    Phase advance correctly applied
  Check with betatron motion enabled
  Check on many turns in stable conditions (bunch by bunch tunes)
    simulation is reasonably noise free
Dipole
Quadrupole
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 16
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
  Check with multiple e-cloud kicks (on the integer)
    Phase advance correctly applied
  Check with betatron motion enabled
  Check on many turns in stable conditions (bunch by bunch tunes)
    simulation is reasonably noise free
  Check on many turns in unstable conditions
    coherent bunch motion is correct
HEADTAIL
PyHEADTAIL
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 17
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
  Check with multiple e-cloud kicks (on the integer)
    Phase advance correctly applied
  Check with betatron motion enabled
  Check on many turns in stable conditions (bunch by bunch tunes)
    simulation is reasonably noise free
  Check on many turns in unstable conditions
    coherent bunch motion is correct
HEADTAIL
PyHEADTAIL
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 18
Validation procedure
  Check on the single e-cloud kick (no betatron motion) change in angle)
    e-cloud dynamics is correct
    forces are correctly applied on the beam
    crosscheck on synchrotron motion
  Check with multiple e-cloud kicks (on the integer)
    Phase advance correctly applied
  Check with betatron motion enabled
  Check on many turns in stable conditions (bunch by bunch tunes)
    simulation is reasonably noise free
  Check on many turns in unstable conditions
    coherent bunch motion is correct
HEADTAIL
PyHEADTAIL
  Very difficult to benchmark directly on instability simulations
    Started from more basic but deterministic checks comparing against HEADTAIL for dipole and drift
    5000 probe particles start from the same initial conditions in HEADTAIL and PyHEADTAIL

## Slide 19
First pilot study
  Started with simple model and complicated it in steps:
  Smooth approximation of the optics, Dx,y = 0, no boundary, linear longitudinal motion, uniform initial e- distribution
  Nonlinear longitundinal motion
  (implemented longitudinal losses)
  Realistic chamber shape (see Kevin’s talk)
  (implemented transverse losses)
  Instability thresholds as a function of the intensity for the SPS at 26 GeV – Q26 vs Q20 – dipoles and drifts
    Reasonably “lightweight”, corresponding HEADTAIL simulations already available

## Slide 20
First pilot study
  Instability thresholds as a function of the intensity for the SPS at 26 GeV – Q26 vs Q20 – dipoles and drifts
    Reasonably “lightweight”, corresponding HEADTAIL simulations already available
  Each simulation (512 turns) is divided in few jobs (4x128 turns) launched subsequently (automatic)
    Easier to recover crashed simulations
    Single Job size can be optimized for lxplus queues
    Simulation can be “extended” a posteriori
  For the same simulations settings we repeat the simulation 5 times with different seeds and take the average emittance evolution

## Slide 21
PyECLOUD-PyHEADTAIL at work
  Already used for studies for the SPS and for the LHC, profiting already of features that were no available in HEADTAIL:
    Quadrupolar field
    Realistic chamber shape
    Correct tracking of the electrons in the H plane for dipoles
    Simulations with recorded pinch field map for tune footprint estimation

## Slide 22
Summary and future work
  PyECLOUD and PyHEADTAIL can be used together to simulate effects of e-cloud on beam dynamics
  Fields from the electrons and from the beam are calculated using PyPIC, a newly developed library including several different Poisson solvers
  Important work on performance optimization was necessary to make computational time affordable
  Simulation results validated against HEADTAIL New tool already used for SPS and LHC simulations (see following talks)
  What next:
  We know for quadrupoles we need the distribution from buildup  robust way to get good resolution for buildup still to be developed, some work on job management “infrastructure” also to be done
  Investigate effect of non uniform beta function
  Other important players (Q’, octupoles, damper), should be included in the simulations
  And then to simulate the triplets:
  Double de-synchronized pinch
  Beta variation along the device
  Position variation along the device

## Slide 23
Thanks for your attention!