## Slide 1: What do the experiments want?
prepared by N. Hessey, J. Nash, M.Nessi, W.Rieger, W. Witzeling
LHC Performance Workshop, Session 9 - Chamonix 2010

## Slide 2: sLHC as a luminosity upgrade
x1p
x2p
(sx1x2) = (sx)
proton beams
proton
proton
[ “Hard scattering partons” ]
The physics potential will be better tuned once the LHC reaches its discovery phase
Today’s forecast is that the requirements on the detectors will remain the same or will even increase. The detector environment will become more complex

## Slide 3: 3000 fb-1 on tape
/ experiment (ATLAS, CMS)
100 fb-1 on tape
/ LHCb
a programme which lasts out to 2030 !
10 nb-1 PbPb (+pA, light ions)
/ Alice

## Slide 4: Luminosity evolution ?
L= 1 * 1034
L= 2 * 1034 ?
L= 4-5 * 1034 ?
Years ~20
~ 3000 fb-1
~ 600 fb-1
~ 100 fb-1
Phase 2
Phase 1
LINAC 4

## Slide 5: Detector limitations
Some detectors will age at a given integrated Luminosity (different case by case)
      ATLAS b-layer PIXEL ~ Lint = 200-300 fb-1
      ATLAS Silicon Tracker (SCT + PIXEL) ~ Lint = 600-700 fb-1
      ATLAS LAr Hadron Calorimeter FE Electronics ~ Lint = 1000 fb-1
      CMS PIXEL ~ Lint = 300 fb-1
      CMS Silicon Tracker ~ Lint = 600-700 fb-1
      ….
Some detectors will become inefficient or problematic at a given peak Luminosity
      ATLAS TRT (transition radiation tracker) ~ L = 2-3 1034
      ATLAS FCAL (forward calorimeters) ~ L = 2-3 1034
      ATLAS SS external beam pipes (activation) ~ L = 1 1034
      ATLAS&CMS Silicon trackers ~ L = 2-3 1034
      ……

## Slide 6: ATLAS and CMS strategy
Use efficiently the next 4-5 years shutdowns to fix problems, consolidate infrastructure, anticipate issues related to rate effects at nominal Luminosity and restore the original full detector layout (un-staging)
Make efficient use of the long shutdown (9 months? foreseen in 2015) for the LINAC 4 installation. ATLAS, for example, is making plans to insert a 4th Pixel layer around the beam pipe
Anticipate all possible upgrade activities towards sLHC that can be factorized out of the main sLHC detector upgrade plans. Make use of all shutdowns before 2020 for installation …. If not we will need later a very long shutdown!
Request a long shutdown (>18 months), just after ~600-700 fb-1 of good data have been collected, to install the new Inner Detectors of ATLAS and CMS (plan today for end 2020 ?)

## Slide 7: CMS upgrade overview
System
Phase 1
Phase 2
Tracker
FEDs?
New Tracking System (incl Pixel)
HCAL
Electronics + PD replacement
HF/HE (hadronic calorimeters)?
Pixel
ECAL
Muons
Trigger
New Pixel Detector
(1 or 2 iterations?)
TP (Off Detector Electronics) ?
EE (endcap EM calorimeter)?
HCAL/RCT/GCT to mTCA
Complete replacement
ME4/2, ME1/1 ,RPC endcap, Minicrate spares, some CSC Electronics
Electronics replacement
Similar picture for ATLAS !

## Slide 8: A few examples
ATLAS LAr forward calorimeters
ATLAS innermost Pixel layer
CMS low-mass Pixel detector
CMS and ATLAS inner detectors
First level trigger considerations

## Slide 9: ATLAS LAr forward calorimeters
Currently FCal1 will work properly up to peak luminosities of 1*1034cm-2s-1
• The FCal1 will however not work efficiently above 2-3*1034cm-2s-1
- positive Ar ions build-up leads to field distortion and to signal loss
- high HV currents lead to voltage drop
- heating of Ar and boiling (only at very high luminosities)

## Slide 10: ATLAS LAr forward calorimeters
Two options:
• new cold FCal1 with smaller gaps: 250 μm → 100 μm : this will require a major shutdown of ~ 15 months (2020 ?)
• new warm Mini-Fcal in front of current FCAL : this can be ready in phase I and will need a 8-9 months shutdown for installation
LAr read out rod
LAr end cap calorimeter

## Slide 11: ATLAS innermost PIXEL layer (b-layer)
Present Pixel detector, in particular the innermost layer (out of 3) will become inefficient (100-300 fb-1, L ~2-3 1034 cm-2 s-1)
ATLAS has officially approved this project. TDR & MOU expected soon
Ready for 2014
Existing b-layer
New b-layer
Add a new b-layer around a smaller beam pipe (in radius), stave structure, 160 MHz readout, CO2 cooling
ATLAS

## Slide 12: CMS low-mass PIXEL detector
Radiation damage due to integrated luminosity
  Today sensors designed to survive 61014neq/cm2 ( 300 fb-1 )
  n-on-n sensors degrade gradually at large fluences
New design adds a fourth pixel layer, is capable of higher rate running, and total material is substantially reduced from current 3 layer Pixel detector. In addition inner layer modules can be replaced during shutdown
Aim to be ready by 2014

## Slide 13: CMS Inner Detector (1)
  Studying several potential layouts for a new outer tracker
  Want to increase granularity as well as minimize material in future tracker
  Need to understand how many triggering layers (in red at left), and where they need to be located in order to provide adequate triggering capability
  No final decision on layout of tracker until final requirements determined

## Slide 14: ATLAS Inner Detector (1)
4 layers of pixels
3 double-layers of short strips
2 double-layers of long strips
Approx. 400 Million pixels (cf 80 Million now)‏
Approx. 45 Million strips (cf 6.3 Million now)‏
Prototype strip sensors (ATLAS07), read-out chips (ABCNext) and hybrids built into modules with excellent performance

## Slide 15: ATLAS Inner Detector (2)
Very high track density
Picture shows hits in inner tracker from one bunch crossing with 400 pile up events; only tracks in forward half of detector were generated.
The inner tracker gets about 15,000 tracks per bunch crossing (and a similar number of photons which can produce e+e- pairs)‏
The challenge is to find all the tracks, without also finding many fake tracks from random combinations of hits.
Work in progress; we can cope with 400 events, but it requires a tight cut of at least 11 hits on a track (yellow line) to control the fake rate. Then the number of tracks found follows the black dotted line of actual number generated, but with some inefficiency.

## Slide 16: LVL1 trigger considerations
We need to keep the stored event rate roughly the same as now : ~200 events per bunch crossing. The events are much bigger at high luminosity, so this is quite a challenge.
It means rejecting 10 to 20 times as many events as now, each of which is about 10 times as big.
To meet this challenge, we can increase the latency at level-1 and move some of what is done in software at high level, such as combining trigger objects, into LVL1.
We consider introducing new elements at LVL1, including a track-trigger.
Full granularity of the calorimeters at trigger level will allow better particle id.
The muon trigger needs better resolution to allow higher momentum thresholds to reduce the muon trigger rate. Adding some new chambers can achieve this.
It is not known how the very important forward calorimeter trigger will perform at these sLHC high rates.

## Slide 17: Detectors limitations
In general some detector components will need to be replaced, upgraded or just consolidated. A large fraction of the front-end electronics and trigger electronics will need to be upgraded before going to sLHC Luminosity
In the early half of the last decade, some detector components necessary to run at nominal Luminosity have been staged and need now to be restored
we do not yet know how the various detector components will react once we stress them by operation nearer to design rates. Special corrective interventions and consolidation programmes may prove to be necessary
The experiments feel now it is very important to have a basic scenario for all what concerns beam periods and shutdown periods over the next 5-6 years, at least until the LINAC 4 is installed and is operational. Actions on the detectors need to be anticipated with enough time for preparation.

## Slide 18: Detector Activities
L= 1 * 1034
L= 2 * 1034
L= 4-5 * 1034
~ 600 fb-1
~ 100 fb-1
Phase 2
Phase 1
New forward beam pipes
Consolidate infrastructure
Solve single points of failure
Fix detectors problems
Restore nominal design
ATLAS installs 4th Pixel layer
CMS new low mass Pixel ?
Modification of the TAS regions?
Install new shielding elements
ATLAS new warm FCAl
ATLAS new muon forward det.
……..
new Inner Detectors
ATLAS open endcap LAr?
Upgrade front end electronics
and upgrade triggers

## Slide 19: LHCb upgrade strategy
Strategy
  First collect ~10 fb-1
  Upgrade LHCb to 40MHz read-out (requires ~8-10 month shutdown)
  Then collect ~100 fb-1
This requires running LHC at a Luminosity of 5*1033 at Point 8
LHC and sLHC operation schemes must be designed to allow
running of LHCb after 2020 with L=5*1033
  Need to ensure full compatibility with LHCb requirements in IP8, in particular:
  Compatibility of triplets in IP8 with higher luminosity (at present no TAS in P8)
  Optics and crossing scheme (displaced collision point, de-focussed beams)
  R2E of electronics in UX85, US85…
  Coordination of the Phase-1 shutdown/upgrade activities such to include LHCb upgrade
This needs to be clarified a.s.a.p.

## Slide 20: ALICE upgrade strategy (>2017)
For the ‘Phase II’ operation one assumes the typical scheme of a yearly Ion run together with a (short) period of p+p running (data comparison+detector startup) .
For pp, the luminosity has to stay below few 1031 (displaced beams and/or short dedicated low Lum runs).
Detector upgrades:
- 2nd generation vertex detector (using a smaller beam pipe)
- Detectors for forward physics (in particular, forward calorimetry)
- Particle ID for pT 5 – 20 GeV
- Increased rate capability of TPC (faster gas, increased R/O speed)
- Upgraded DAQ & HLT
LHC upgrade:
- increase PbPb by factor five to 5*1027 (still compatible with TPC operation)
LHC and sLHC operation schemes must be designed to allow heavy ion operation and short periods (few weeks/year) of pp with L<5*1031 in IP2

## Slide 21: Summary (1)
The experiments urgently need a plan for shutdowns over the next 5-6 years (LINAC 4) to organize the first stage of upgrade work
We need a credible programme of long-term LHC operation in order to be able to justify planning and resources for the phase II upgrades
Preparing new trackers is a 10 year programme. They are very challenging, and we have to push ahead with the R&D now in order to be able to consider building these devices. Signals that this is not going to happen will be deadly.
  We should not be planning that the LHC will reach its end of life (~ 2030) with a few 100 fb-1/year

## Slide 22: Summary (2)
Today the experiments have not yet demonstrated to be able to run efficiently, with an upgraded detector, at a peak Luminosity of 1035 cm-2 s-1. Occupancy and Track density are still major concerns. Any solution which will allow to minimize pileup while reaching the goal of 3000 fb-1 is strongly preferred (see luminosity leveling)
The compatibility between running CMS and ATLAS at sLHC and at the same time colliding at point 2 and 8 should be urgently clarified
  All plans to modify, upgrade the interface regions between experiment and machine (TAS, triplets, …) need a new and a proper level of organization and visibility