## Slide 1: Illumination of test stand BGC camera due to cathode radiation & Synchrotron radiation on BGC in current LHC setup
Noah Jens – 03.02.2021

## Slide 2
Cathode in e-gun
Camera
HEL test stand model in MolFlow

## Slide 3: Correction of interaction chamber coating
Interaction chamber is NOT AC coated
about 10875 are expected at camera facet (instead of 1783 )

## Slide 4: Measures to reduce photon rate at camera
30/40/50mm ID
Steel
25mm ID
AC coated
25mm ID
Mask in front of gun
Mask in camera arm
Narrower bellows

## Slide 5: Repositioning of front mask
Front mask moved behind the 8-way intersection to ensure best pumping performance of the gun

## Slide 6: Simulation results in photons per second
Mask in front of gun
Mask in camera arm
Narrower bellows
None | 10875 1/s
50mm ID | 4052 1/s
40mm ID | 3011 1/s
30mm ID | 1966 1/s
No front mask | 6186 1/s
50mm ID front mask | 2325 1/s
40mm ID front mask | 1723 1/s
30mm ID front mask | 1088 1/s
No front mask | 4078 1/s
50mm ID front mask | 1597 1/s
40mm ID front mask | 1189 1/s
30mm ID front mask | 737 1/s

## Slide 7: Simulation results in counts per second
Mask in front of gun
Mask in camera arm
Narrower bellows
Due to the maximum transmission of the filter (80%) and the quantum efficiency of the photocathode (10%), the counts per second can be estimated by multiplying the hits by 8%:
None | 871 cps
50mm ID | 324 cps
40mm ID | 241 cps
30mm ID | 158 cps
No front mask | 495 cps
50mm ID front mask | 186 cps
40mm ID front mask | 138 cps
30mm ID front mask | 88 cps
No front mask | 327 cps
50mm ID front mask | 128 cps
40mm ID front mask | 96 cps
30mm ID front mask | 59 cps

## Slide 8: Blackout material in camera arm port in photons per second (top) & counts per second (bottom)
50mm ID front mask | 3549 1/s
40mm ID front mask | 2717 1/s
30mm ID front mask | 1707 1/s
50mm ID front mask | 284 cps
40mm ID front mask | 218 cps
30mm ID front mask | 137 cps
Black port (sticking factor of 0.9)
Mask in front of gun
None | 10875 1/s
50mm ID | 4052 1/s
40mm ID | 3011 1/s
30mm ID | 1966 1/s
None | 871 cps
50mm ID | 324 cps
40mm ID | 241 cps
30mm ID | 158 cps

## Slide 9: Distribution at the camera facet (normalized and in percent, no lens system)
Mask front
Mask front & mask in camera arm
Mask front & narrow bellows

## Slide 10: Synchrotron radiation on BGC
Geometry based on the information in the layout database
D3 and D4 bending magnets implemented
D4
D3

## Slide 11: SynRad
Software to simulate synchrotron radiation
Based on the information about beam and magnetic regions

## Slide 12: Simplifications
No outer shell assumption that photons, which hit the holes in the RF fingers won’t come back
No adjustments for holes in other regions of the geometry (for example beam screens)
Adjusted sticking factor of RF finger regions, according to the area ratio of holes to metal

## Slide 13: Need for iterative simulation
Due to difference in photon flux of about 11 orders of magnitude, not enough test photons hit the camera facet
Low flux mode could not deliver enough statistics either
No direct recording of angle map in SynRad possible
The particle logger can record information about incident angle of each photon

## Slide 14: Transferring simulation to MolFlow
Angle map out of the incident angle
New simulation in MolFlow including the angle map and the scaled desorption

## Slide 15: Simulation results
According to the MolFlow simulation the camera facet receives 58004 photons per second
Reduced to 39787 with mask in camera arm (68.6%)
Reduced to 31076 with narrow bellows (53.6%)