Beam-Induced Depolarization: HERA vs. LHC*
Giuseppe Ciullo (Ferrara) and Erhard Steffens (Erlangen)
Introduction
Comparison of PGT for LHC with HERA-e
Beam-induced depolarization
Conclusions
 *) See PBC Notes 2018 001 https://cds.cern.ch/record/2632904?ln=de
BID: Comp. HERA and LHC
LHC PGT: kick-off 19.02.2021

---
Beam-induced depolarization (BID)
After its 1st observation at VEPP-3, this effect has been studied at HERMES, see first measurement with Blong publ. in PRL 82 (1999) 1164, and analyzed together with Btransv in Diss. Ph. Tait, Erlangen (2006): http://www.hermes.desy.de/notes/pub/06LIB/pntait.06-060.thesis.ps.gz .
BID is based on resonant transitions caused by the beam field acting on the polarized H-atoms in an external guide field B0 ≈ 300 mT. There are different classes of transitions, depending on the relative orientation of the guide field B0 and B1, the rapidly varying beam field component.
p resonances for B1 ┴ B0 DF = 0, ±1 DmF = ± 1, and
s resonances for B1 ═ B0 DF = ±1 DmF = 0.
Some of these resonances change nuclear polarization. For longitudinal guide field, only the p resonances are present. For transverse field, like at LHCspin, both types of resonances are present. The s resonances, interchanging states 2 and 4, are densely spaced, i.e. its prevention requires a very high homogeneity of the guide field.
1 - 2
Hydrogen hfs diagram
Bcrit = 50.7 mT
2 - 4
3 - 4

---
Transverse guide field magnet (HERMES)
In order to resolve the s24 resonances, a field homogeneity in the order of their spacing is required (0.37 mT in the high-field limit).
A special magnet with large gap height and high field quality had been built. With the help of shims and correction coils a high homogeneity could be achieved.

---
Observation of the p resonances
A practical method to detect the p resonances was the wide range Flip-in method: States |1> and |4> are injected by the ABS, and states |2> and |3> are mea-sured by the BRP. With e beam, the population of the cell gas is changed and detected by the BRP.
As an example, the BRP rate is shown as function of the current I in the transverse magnet. The p reso-nances 3-4 and 1-2 are clearly visible. At high field the spacing is wide, and individual resonances can be easily selected.
This is different for the s24 resonances with narrow spacing. In order to suppress them, the B-field must be set to the minimum in-between.

---
HERMES transverse Running (2002-2005)
During transverse running (2002 – 2005), careful studies to optimize the target polari-zation have been performed - see a final result of Diss. Ph. Tait on the s24 resonance taken by the target polarimeter (BRP) where the nuclear polarization Pz± is shown as function of B0.
Two polarization minima caused by the s24 resonances are clearly visible at a distance in field of about 0.36 mT as expected, demonstrating the high field quality of this rather open magnet.
The Polarization P in between the sigma resonances is 2% higher, only.

---
Comparison of BID for HERA and LHC
Key parameters of both machines:
Machine	NBunch	fBunch / MHz	Ibeam / A	sz / cm	st / ps	a = 1/st2 / ps2	1/e width of Fourier spectrum	I0 Peak current (A)
HERA-e	210	10.41	0.04	0.93	31	5.203 10-4	5.1 GHz	57.3
LHC	2600	40.08	1.0	7.55	253	7.81 10-6	0.63 GHz	41.2
Assumptions:
The trajectories of the MolFlow simulation are equivalent (see Tait Fig. 4.7 on the right: trajectories are shown in red, blue dots at cell wall are wall bounces, blue dots within the cell: crossings of a resonance).
Inhomogeneity equivalent, i.e. the shape of the resonant surfaces are similar (see Tait Fig. 4.6) → duration of resonance crossings have the same statistical distribution.
Beam size very small compared to cell radius
The main differences come from the bunch frequency, and the longitudinal width in z or in t (sz/t) (see Table).

---
Comparison of BID for HERA and LHC
Spin-flip Probability for crossing a s2-4 resonance, with q = mixing angle, t = crossing time and n index of passage (Tait Equ. 4.11):
With our assumptions, we estimate the relative strength of BID by the ratio of the square of B|| for both beams. For the k-th harmonic of the Fourier spectrum (Tait 2.59) we obtain at the s2-4 transition frequency of 8.54 GHz with the parameters of the table
LHC: F213 = 2 ∙ 1.0 A ∙ 1.53 10-20
HERA: F820 = 2 ∙ 0.04 A ∙ 7.53 10-2
We conclude that resonant depolarization at the LHC via the s2-4 transition is negligible compared to HERA (where it was small, already!), despite the 25 times higher beam current!
B|| is the RF field parallel to B0 , the guide field. B0 = x ∙ Bc, the critical field of the H-atom. Strong field: x >> 1.
tan2q ≈ 1/x, i.e. q small in strong field, and spin-flip probability low.

---
Conclusions
In summary, the main differences between HERA-e and LHC are:
Bunch frequency fB: 10.41 MHz vs. 40.08 MHz. This results for the LHC in a 4x larger spacing of the ‘resonant B-values’, i.e. it reduces requirements on field quality.
Width of the Fourier spectrum: 5.1 GHz vs. 0.63 GHz. This leads to a rapid fall-off of the relevant Fourier amplitudes of the s2-4 resonance (8.54 GHz) at the LHC.
We conclude that depolarization of the H target at the LHC via the s2-4 resonances is neglible. In strong field B0 ≈ 6∙Bc the p-transitions are about 30 mT apart.
B/mT →
Thank you !

---
Back-up slides

---
Estimate of the areal density of the PGT
Assumed:
IH (100 % HERMES ABS flow) = 6.5∙1016/s, may be limited by LHC vacuum constraints or space limitations for the PGT;
Cell 20 cm long, 1.0 cm i.d., at 100K, with standard feed tube 10 cm long, 1.0 cm i.d.
The resulting 100% density of the polarized gas target is q = 0.64 ∙ 1014/cm2, about 50% lower than HERMES.
For the future HL-LHC-25ns, the Luminosity achievable with the PGT would be up to 4.4 ∙ 1032/ cm2 s. To which extent such densities can be realized and exploited in a real experiment, depends on many factors and has to be investigated in more detail.

---
Coating of the cell surface?
Cell surface with a-C coating: may need a thin water/ice layer to suppress recombination (and thus depolarization)
see HERMES measurement with water on Drifilm, indicating close-to-zero recombination!
A water layer can be produced in dynamical equi-librium by injecting a low water fraction together with the polarized H atoms, set by the O2 admix-ture in the dissociator gas H2.
A lower Tcell has two effects: (i) target density increases, and (ii) the ice layer can be produced at a lower O2 admixture in the dissociator.
note: a = 1 indicates no molecules detected by TGA!
HERMES-target: Degree of dissociation a as function of the cell temperature T. The cell was in use for an extended period (not a new cell).
The SEY of this surface is not known to us and needs to be studied.