## Slide 1
Conceptual Design Review of R2D2
3
- Mechanical Design -
CEA: E. Rochepault, V. Calvelli, M. Durante, H. Felice, P. Mallon, P. Manil, G. Minier, G. Maitre, B. Prevet, S. Perraud, F. Rondeaux
CERN: S. Izquierdo Bermudez, J.C. Perez, D. Tommasini, J. Fleiter, H. Felice
08/03/2021
https://indico.cern.ch/event/1003865/

## Slide 2: Mechanical Material Properties
Material | Stress limit (MPa, Von Mises) |  | E (GPa) |  | ν | α
 | 293 K | 4.2 K | 293 K | 4.2 K | 293 K / 4.2 K | 293  4.2 K
Coil X: Axial direction Y: Azimuthal direction | 150 | 200 | EX = 30 EY = 25 GXY = 21 | EX = 33 EY = 27.5 GXY = 21 | 0.3 | X = 3.1E-3 Y = 3.4E-3
Austenitic steel 316LN | 350 | 1050 | 193 | 210 | 0.28 | 2.8E-3
Al 7075 | 480 | 690 | 70 | 79 | 0.3 | 4.2E-3
Ferromagnetic iron | 180 | 720 | 213 | 224 | 0.28 | 2.0E-3
Pole (Ti6Al4V) | 800 | 1650 | 130 | 130 | 0.3 | 1.7E-3
G11* | 260 |  | 30 | 30 | 0.3 | 
Coil shim material same as coil
  Behavior as a single impregnated pack
  Avoid stress concentrations during cool-down
Plane53 (magnetic), Plane82 (mechanical) elements
Plane stress condition: more conservative

## Slide 3: Contacts and Couplings: Coil
Unprescribed interfaces
Standard contact between all interfaces surrounding coil assembly, friction coefficient = 0.2
Coupling between coils and their proximal shims
Coupling used to:
  Force coil pack to behave as a unit
  Avoid stress concentrations during cool-down
IRFU/DACM/LEAS
Standard contact (Separation and Sliding permitted)
No initial penetration or gap
Friction coefficient = 0.2

## Slide 4: R2D2 coils in F2D2 structure
Too much pre-load because of the thick shell
High peak stress
Need to redesign the structure
Different fillers and pads
 Marginal cost saving
0.10 mm Xinterf
0.05 mm Yinterf
+cool-down
208 MPa
Nominal:
13.38 kA, 11T
201 MPa
Short sample:
16.88 kA, 11T
205 MPa
v6.9.16
HF
LF

## Slide 5: Structure parametric study
Parameter |  | Criterion | I | II | III | IV | V | VI
Shell Thick. (mm) |  | >15 mm | 26 | 22 | 20 | 22 | 22 | 22
Yoke Ext. Rad. (mm) |  | >190 mm | 190 | 190 | 190 | 195 | 210 | 220
Overall Rad. (mm) |  | >205 mm | 216 | 212 | 210 | 217 | 232 | 242
Max. Von Mises stress in coil [MPa] | Nominal SS 1.9K | <150 MPa No limit | 129 217 | 123 247 | 120 201 | 126 211 | 134 218 | 128 222
Coil-Pole Contact [MPa] | Nominal SS 1.9K | >10 MPa >10 MPa | 12 16 | 7 8 | 5 2 | 9 10 | 12 12 | 13 12
Max. Von Mises stress in Iron at max preload [MPa] |  | <180 MPa | 257 | 247 | 240 | 223 | 186 | 174
Step 1: shell thickness/radius reduced to decrease coil stress below 150 MPa at nominal
Step 2: pre-load tuned to guarantee 10 MPa contact from nominal to SS
Step 3: Yoke radius varied to keep peak stress at warm below 180 MPa
IRFU/DACM/LEAS
v6.14.R1

## Slide 6: A wide range of pre-load
Chart: I [kA]
| 0 | 13.2 | 13.772 | 16.5 | 18.100000000000001
0.2 mm - 2D | 107.4 | 10.7 | 4 | 0 | 0
0.4 mm - 2D | 135.8 | 30.1 | 27 | 10 | 0 | 0 | 0
0.6 mm - 2D | 161.8 | 55 | 48.7 | 32.1 | 12.7 | 11 | 7.4 | 0 | 0
0.8 mm - 2D | 184.4 | 84.1 | 76.4 | 59.4 | 38.1 | 37.5 | 26.8 | 14.2 | 11.1
0.2 mm - 3D | 110 | 0 | 0
0.4 mm - 3D | 137.2 | 25.3 | 0
0.6 mm - 3D | 159.8 | 52.8 | 15.1
0.8 mm - 3D | 180.9 | 81.7 | 43
Criterion | 10 | 10
NOM 4.2 K | 0 | 160
UWP | 0 | 160
SS 1.9 K | 0 | 160
Parameter | Unit | NOM 4.2 K | NOM 1.9 K | UWP 4.2K | UWP 1.9K | SS 4.2 K | SS 1.9 K
Current | A | 13772 | 15055 | 16500 | 16500 | 17215 | 18819
Margin HF | % | 20.0 | 20.9 | 4.5 | 12.9 | 0.0 | 0.9
Margin LF | % | 20.5 | 20.0 | 4.0 | 11.3 | 0.7 | 0.0
B (0,0) | T | 10.42 | 11.15 | 11.98 | 11.98 | 12.46 | 13.29
Max. Von Mises stress in coil | MPa | 141 | 155 | 195 | 195 | 204 | 231
Min. pre-load for nominal operation
Max. pre-load for SS 1.9K
Structure can withstand high pre-load if required
Coil should be limited to ultimate current
v6.14.R2

## Slide 7: Peak stress in coil and Contacts (Nom.+UWP)
Pre-load | Pre-load
Cool-down | Cool-down
Nominal: 13.7 kA | UWP: 16.5 kA
Nominal: 13.7 kA | UWP: 16.5 kA
44 MPa
96 MPa
121 MPa
158 MPa
141 MPa
195 MPa
11 MPa
13 MPa
v6.14.R2

## Slide 8: Peak stresses in structure (SS 1.9 K)
110 < 180 MPa
124 < 180 MPa
205 > 180 MPa locally
S1 = 92 < 200 MPa at cold
S1 = 118 < 200 MPa at SS
82 < 480 MPa at warm
162 <690 MPa at cold

## Slide 9: Room for Tie Rods
 | At Room Temperature | After Cool-Down
Force/rod (4 rods) | -142.8 kN = 70 % EMF @ SS 1.9K | -204 kN = 100 % EMF @ SS 1.9K
Minimum diameter before yield: | 480 MPa 19.5 mm | 690 MPa 19.4 mm
 | At Room Temperature | After Cool-Down
Force/rod (4 rods) | -142.8 kN = 70 % EMF @ SS 1.9K | -204 kN = 100 % EMF @ SS 1.9K
N.b.: 18 mm is minimum diameter for 16.5 kA ultimate working point condition
24 mm has been chosen, giving 1.5 safety factor
(see 4, P. Manil for longitudinal pre-load concepts)
v6.14.R2

## Slide 10: 3D Model – Return End RE
RE, symmetric
LE, symmetric
LE, with jumps
ongoing
ongoing
This presentation

## Slide 11: VM Stress – 2D vs 3D (Ultimate)
Cool-down
16.5 kA Ultimate current
2D
3D
Profile and range very similar between 2D/3D
Difference 10-20 MPa in max. VM Stress attributed to 2D plane stress Vs 3D stress, 2D more pessimistic (conservative)
Difference <5 MPa in X Stress
0.60 mm Xinterf
0.05 mm Yinterf
96 MPa
158 MPa
195 MPa
79 MPa
149 MPa
178 MPa

## Slide 12: Pole Contact Pressure – 2D vs 3D (Ultimate)
Profile and range very similar between 2D/3D
Difference <5 MPa in min. contact pressure
 pre-load to be slightly corrected  +/-5 MPa on coil stress
Cool-down
16.5 kA Ultimate current
2D
3D
162 MPa
13.7 kA Nominal current
49 MPa
12.7 MPa
160 MPa
53 MPa
15.1 MPa

## Slide 13: VM Stress – 3D (Nominal)
Higher stresses in coil-ends than in straight section
To be checked with longitudinal pre-load study
Peak stress still < 150 MPa at Nominal
36 MPa
118 MPa
127 MPa
Cool-down
~ 130 MPa
0.25 mm Xinterf
~ 40 MPa
13.7 kA Nominal current
~135 MPa

## Slide 14: VM Stress – 3D (Ultimate)
Higher stresses in coil-ends than in straight section
To be checked with longitudinal pre-load study
Peak stress still < 200 MPa at ultimate
Cool-down
16.5 kA Ultimate current
0.60 mm Xinterf
~95 MPa
~185 MPa
~180 MPa
79 MPa
149 MPa
178 MPa

## Slide 15: Pole contact pressure – 3D (Nominal)
No gap
Small contact
Lorentz forces @ Nominal current: Fz,mag = 350 kN /end
Xpreload: 0.25 mm interf.
Z Preload:
  warm: 400 kN = 115 % Fz,mag
  Cold: 641 kN = 183 % Fz,mag
 Small >0 contact in the ends with relatively high pre-load
Goals of the longitudinal support:
Positive contact pressure
Stress < criteria

## Slide 16: Pole contact pressure – 3D (+ZPreload)
Lorentz forces @ Nominal current: Fz,mag = 350 kN /end
Xpreload: 0.25 mm interf.
Increasing Z Preload +40%:
  warm: 529 kN = 151 % Fz,mag
  Cold: 783 kN = 224 % Fz,mag
 contacts >0 in the ends if very high pre-load
contacts
>30 MPa
No gap

## Slide 17: Pole contact pressure – 3D (+X+ZPreload)
22 µm
No contact
Lorentz forces @ Nominal current: Fz,mag = 350 kN /end
Increasing X preload: 0.6 mm interf.
Increasing Z Preload:
  warm: 565 kN = 162 % Fz,mag
  Cold: 831 kN = 238 % Fz,mag
 But: contacts lost if transverse pre-load is too high

## Slide 18: Pole contact pressure – 3D (Ultimate)
41 µm
13 µm
No contact
Lorentz forces @ Ultimate current: Fz,mag = 477 kN /end
X preload: 0.6 mm interf.
Z Preload:
  warm: 565 kN = 119 % Fz,mag
  Cold: 831 kN = 174 % Fz,mag
 Need to considerably increase the pre-load to guarantee full contact in the ends
(see 4, P. Manil for longitudinal pre-load concepts)

## Slide 19: Conclusions
Attempt to assemble R2D2 coils in the F2D2 structure
  coil stress too high >200MPa
2D Parametric study to find the adequate shell and yoke radiuses
Peak stress in the coil <150 MPa at nominal, <200 at ultimate
Range of pre-load to guarantee 10 MPa coil-pole contact from nominal to SS operation
3D model to study coil-ends:
  Simplified RE symmetric geometry
  ‘Conventional’ tie-rods + end-plates
  Peak stress in coil-ends, but still below criteria
  Possible to guarantee full contact in the ends, but with very high forces in the rods
  Further studies required with detailed models

## Slide 20
Thank You!

## Slide 21: Model Flow
Input code
I/O text file
Output Images
Results file
R2D2_2d_magn
Mat_prop_magn
R2D2_2d_mecha
Mat_prop_mecha
partnames_%magnet_version%
Coil_model
Structure_model
Coil\coil_coords_%coil_version%
Structure\%part%_%struct_version%
Meshing
SOLUTION
EOF
Postproc_fmag
Postproc_magn
%filename%_fmag
%filename%_output
Contact_list
Contacts
(contact.mac)
Load_steps
EOF
Postproc_4
SOLUTION
R2D2_2d_magn_%magnet_version%.rmg
Contact pressure on coils, equivalent stress images
Geo_param
R2D2 v. 6.14.R2

## Slide 22: Symmetry Conditions and Mesh

## Slide 23: Minimum Rod Diameter Approximation
3D Magnetic Model: Full energy/length @ 1.9 K, Short Sample (18 kA) = 204 kJ/m per quadrant
Fz,mag = 816 kN.
Assuming resultant forces on end-shoes and end-plates are the same.
Assuming 30 % of efforts coming from differential contraction with Al rods (to be checked with mechanical model)
We aim at 100 % of magnetic forces in z after preload at room temperature (RT) + cool-down (CD)
Fz,RT+CD = Fz,mag = -816 kN
Assumption: 70% of forces are applied at room temperature:
Fz,RT = Fjack = -571 kN
Force on one rod:
Fz,rod = Fz,mag/Nrods = σ x Arod = σ x ϖdrod2/4

## Slide 24: Comparison 2D Vs 3D
2D
3D

## Slide 25: R2D2 3D – iso geometric

## Slide 26: Forces
 |  | Fx | Fy | Fz
coil1 | kN | 136 | -16.5 | 8.5
coil2 | kN | 415.3 | -126.8 | 36.7
coil3 | kN | 150.1 | -91.6 | 17.2
coil4 | kN | 28.6 | -319.6 | 25.1
coil | kN | 651.5 | -518.9 | 87.4
Opera | kN | 646 | -491 | -90.3
Forces imported from Opera 3D
RE,
nominal current 13.7 kA
Per octant
 |  | HF | LF | total
Fx | kN/m | 1698 | 112 | 1810
Fy | kN/m | -469 | -752 | -1221
Fz | kN/m | 41 | 77 | 118

## Slide 27: VM Stress – 2D vs 3D (Nominal)
0.40 mm Xinterf
0.05 mm Yinterf
Cool-down
Nominal current
2D
3D

## Slide 28: X Stress – 2D vs 3D (0.2 mm interf)

## Slide 29: Pole Contacts – 2D vs 3D (Nominal)
0.40 mm Xinterf
0.05 mm Yinterf
Cool-down
Nominal current
2D
3D

## Slide 30: Stresses in Structure – 2D vs 3D (0.2 mm)

## Slide 31: VM Stress – 3D

## Slide 32: VM Stress – 2D vs 3D (0.8 mm)
Cool-down
16.5 kA Ultimate current
2D
3D
0.80 mm Xinterf
0.05 mm Yinterf
104 MPa
168 MPa
201 MPa

## Slide 33: Longitudinal preload
Chart: rod disp [mm]
| 2.5 | 3.4 | 5.5
Room temperature | 107.4131 | 142 | 220
4.2 K | 171.8834 | 210 | 300
Room temperature | 100.0862 | 132.3138 | 210
4.2 K | 160.1664 | 195.6847 | 280
Chart: Rod disp [mm]
| 2.5 | 3.4 | 5.5
Press1 | 13.4 | 17.9 | 27
Press2 | 2.4 | 16.2 | 50
Nominal current
0.25 mm xinterf
0.6 mm xinterf
0.25 mm xinterf