## Slide 1: Injector RF and Synchrotron RF
Present Status, Activities, Plans

## Slide 2: Contents
Introduction
  What is “RF”?
  Main components of an RF system
Injector RF System
  Overview
  Status, Plans, Actions
Synchrotron RF System
  Overview
  Status, Plans, Actions
Summary and Outlook

## Slide 3: Introduction

## Slide 4: Recap: What is ‘RF’ ?
RF, short for: Radio Frequency
  Wave length comparable to physical dimensions
  Field quantities = function(time, space)
velocity of propagation
in a medium
wave length
frequency
Practical Example: Mobile Phone
Transmit energy by means of EM-fields.

## Slide 5: How to accelerate particles?
Force acting on a
charged particle
Force due to Electric Field
Magnetic Guidance Field
Charged particle dynamics are represented by Lorentz's Equation:
Confined volume
for EM-field + beam
1
2
Provide EM-field energy to volume
3
Control EM-field
ToDo:

## Slide 6: Main components of an RF System
Resonant structure = cavity
  To store energy (in form of EM-field)
  To apply E-field component in beam direction
RF amplifier
  To build up EM-field, i.e. to power the cavity
RF signal generation = LLRF
  Drives the RF amplifier
 LLRF (Low Level RF; means: low signal level)
Consists of closed loop controls,
to ensure HW performance
and beam stability/reproduceability
cavity
LLRF
1
2
3

## Slide 7: Work package RF
Accelerator
Injector RF
RF Amplifier
Resonant Structures
RF Feedback Loops
Synchrotron RF
RF Amplifier
Resonant Structures
RF Feedback Loops
Today
Today

## Slide 8: Injector RF

## Slide 9: Injector RF – Overview, RF signals
M&A 1
Digital LLRF
Amp 1
PLC
M&A 2
Amp 2
PLC
Amp 3
PLC
Amp 4
PLC
RF DRIVE 1
RF OUT 1
MO
Monitor Fwd/Refl
Monitor
Monitor
RF DRIVE 2
RF DRIVE 3
RF DRIVE 4
RF OUT 2
RF OUT 3
RF OUT 4
Monitor Fwd/Refl
Monitor Fwd/Refl
Monitor Fwd/Refl
Tank probe 1
Tank probe 2
Tank probe 3
Tank probe 4
Monitor
Monitor

## Slide 10: Injector RF – Present Status
Two-stage negotiated tendering procedure
  For RF amplifiers + LLRF
  About to be successfully completed
Definition of contract scope/optional items
  Amount of documentation we get
  On-site visits and system simulator access
  Provision of LLRF System “CERN” mid 2011

## Slide 11: Injector RF – Plans
Concentrate requirements in terms of controls
On-site tests (~2 weeks, close to Zürich)
Install and run LLRF “CERN” – Mid 2011
Delivery of RFQ amplifier for ITS – End 2011
  Run ITS at CERN (LLRF “CERN”)
Delivery of IH amplifier to Wiener Neustadt – End 2012
  RF conditioning of IH tank (LLRF “WN”)
Ship CERN equipment to Wiener Neustadt - End 2012
  Merge LLRF “CERN” and LLRF “WN”,
  Run Injector

## Slide 12: Injector RF - Actions
Contract Signature with Supplier
Requirements Document, WP CO
Define on-site tests (Supplier, WP-CO)
Prepare LLRF “CERN”
Short term
Mid term
Long term

## Slide 13: Synchrotron RF

## Slide 14: System Overview

## Slide 15: Synchrotron RF – Present Status
Identified synergies with CERN PS-Booster upgrades
in preparation: Collaboration Agreement between CERN RF-group and MedAustron
  Big effort, covers LLRF + cavity + amplifier
New team member started, working on
  LLRF hardware development
  Implementation of firmware components

## Slide 16: Synchrotron RF – Plans
Finalize Collaboration Agreement (CERN)
Requirements Document (WP-CO)
Develop LLRF prototype – Fall 2011
  For beam tests @CERN using CERN infrastructure
LLRF series production
  MACS integration – Spring 2012
Overall system tests
  LLRF+cavity+amplifer – Mid 2012
Wiener Neustadt
  Installation, commissioning, operation – 2013

## Slide 17: Synchrotron RF – Actions
Finalize Collaboration Agreement
Requirements Document, WP CO
Prepare LLRF tests for end 2011, CERN
(Build cavity prototype)
Short term
Mid term
Long term

## Slide 18: Summary and outlook

## Slide 19: Summary and Outlook
Injector RF and Synchrotron RF
  Two independent and different systems
Implementation approaches
  Synchrotron RF  build in-house
  Injector RF  purchase solution
Next big steps:
  Contract signature for Injector RF
  Accepted collaboration agreement for Synchrotron RF
  Requirements documents

## Slide 20: THank you!