## Slide 1: PVSS State Machine
A library for PVSS control scrips

## Slide 2: Control Structure
Virtual Accelerator
Working Set
State Driven Device (e.g. PCC)
Basic Device (e.g. PCO, VVS)

## Slide 3: General State Machine
Each state driven device MUST include the same state machine.
Each state driven device MUST include the same commanding interface.

## Slide 4: General State Machine
Each state driven device must understand a set of standard commands state:
  Commands for state transitions
  Prepare (in Op state only)
  Activate (in Op state only)
  Deactivate (in Op state only)
  Finalize (in Op state only)

## Slide 5: Concept
States
  enterState(): allocate needed resources
  leaveState(): deallocate needed resources
State transition
  Consists out of a leaveState() and a enterState() sequence

## Slide 6: Devices connected to NI PXI
Implementation as FEC using FECOS
Basic Devices
Processing tier (2)
Equipment tier (3)
Frontend tier (4)
State machine

## Slide 7: Problems
Equipment tier (3)
What to do with basic devices that are connected directly to PVSS?
What to do with PLCs where it is not convenient or possible to implement the state machine?
Basic Devices
Processing tier (2)
Equipment tier (3)
Frontend tier (4)
State machine
interface

## Slide 8: How to implement in PVSS?
With PVSS control scripts
Control scripts running in a PVSS control manager
State machine control script
Presentation tier (1)
Processing tier (2)
Equipment tier (3)

## Slide 9: Library and templates
PVSS state machine consists of 3 script files
State Machine library
  Covers all common state machine functions
Device Class template
  For defining device specific functions
Device instance script template
  For creating an instance of a device class

## Slide 10: State Machine library
Covers the general state machine
Provides the standard commanding interface
Handles received commands
Handles fail and fault conditions
Provides functions to register and deregister from data point elements
Provides logging functions to the PVSS log

## Slide 11: Device Class template
Provides blank functions for enter/leave states
Provides blank functions for the four standard commands
Provides the possibility to add device specific functions

## Slide 12: Running a PVSS state machine device
Example: device class VSE, device MR-01-001-VSE
state machine
library
device class
library
device instance
script

## Slide 13: Usage of the PVSS state machine
Vacuum control system
Integration of RF Amplifiers
Integration of special magnet slow control system
Vacuum Devices
RS485/422/232
Digital I/O

## Slide 14: Status/Conclusion
PVSS state machine provides the general state machine functions and commanding interface as all state driven devices within the MACS
Version 1.0.0 is released
All library and template files are available under: https://svn.cern.ch/reps/macs/trunk/SCS/PVSS/StateMachine
A programmers manual is available under: https://svn.cern.ch/reps/macs/trunk/sdp/documents/Deployment/PVSSStateMachine/doc