## Slide 1: KEKB crab RF architecture & controls
K.Nakanishi
KEK
Dec. 16 , 2010
LHC-CC10

## Slide 2: Comparison between crab and SCC
Qext of the cavities
Crab : 1.6~2x105 SCC : ~7x104
Tuning strategy
Crab : Insert the coaxial coupler. SCC : deform the cavity.
Required mode
Crab mode : 509MHz Lowest mode : ~410MHz acc mode : 509MHz
Beam loading
Crab : Depend on beam alignment, cavity phase and voltage.
SCC : Depend on the cavity phase and voltage.
Damped by the coaxial coupler
(Lowest mode)

## Slide 3: Crab RF system_1
Dependence of RF power on the loaded Q value and a horizontal beam orbit for a beam current of 2 A.
The required RF power to maintain the crabbing voltage is given as:
(for a simple case of β>>1, crab phase=π/2, and loading angle =0)
We have chosen QL=1~2 x105 for a good compromise.
  This value is suitable for operating the system with a possible error of ΔX=1mm, and
  A high power source of 200 kW is sufficient for conditioning the cavity up to 2 MV.
Typical parameters for the crab crossing.
KEKB review on 2008

## Slide 4: Crab Cavity & Coaxial Coupler in Cryo-module
Support Rod
Jacket Type Main He vessel
SUS316L
Jacket Type Sub He vessel
Coaxial Coupler (Nb)
Stub Support
Crab Cavity Cell
Notch Filter
Support Pipe
Tuning Rod
RF Absorber
Extract TM010, TE111 Mode
Frequency Tuning
Input Coupler
Bellows
KEKB review on 2007

## Slide 5: Schematic Drawing of Cryostat
KEKB review on 2007

## Slide 6: Cryostat Conceptual Design
Top View
RF Input coupler
Magnetic Shield
(Jacket Type)
80 K Liq. Nitrogen Shield
Coaxial Coupler
Stub Support
Bellows
Liq. He
RF Monitoring
Port
Frequency Tuning
by Adjusting Distance
Crab Mode Reject Filter
(Notch Filter)
HOM
Absorber
I.D. 240
I.D.100
Liq. He
HOM
Absorber
KEKB review on 2007

## Slide 7: Crab RF system_2
Two new RF stations, each for one crab cavity, were constructed in the D11 building.
  Two reused klystrons that have been tested up to 600 kW were set.
  The high-power system and most of the low-level RF system are similar to those of the SC accelerating cavity stations.
  Conventional amplitude and phase feedback loops are used to control the cavity field and the klystron output.
  The resonant frequency of the cavity is controlled by the main tuner system consisting of a motor and piezo element, which moves the coaxial beam pipe in the longitudinal direction with respect to the cavity cell.
  The interlock system includes a quench detector, arc sensors at the input coupler, vacuum pressure gauges, temperature sensors, etc.
KEKB review on 2008

## Slide 8
RF system for crab cavity will be similar.
KEKB review on 2006

## Slide 9: Diagram of tuning control system for crab cavity
Coaxial coupler mover
Frequency tuning
tuner
Adjust horizontally
Use component for SCC
Prepare similar component
for SCC control.
Prepare new component
KEKB review on 2006

## Slide 10: Tolerance_Timing (RF phase)
Timing error (RF phase error) gives rise to horizontal displacement at the IP.
  Here, fcross is the half crossing angle.
  A is the ratio of allowed offset to horizontal beam size, sx*.
  The value A should be determined from beam-beam view point.
 | KEKB | Super-KEKB | LC
sx* | 100mm | 70mm | 0.24mm
A (assumed) | 0.05? | ~0.05? | ~0.2?
fcross | +/- 11mrad | +/- 15mrad | +/- 3.5mrad
Dt | 1.5 ps | 0.8 ps | 0.05 ps
0.27 deg (509MHz)
KEKB review on 2006

## Slide 11: Frequency Tuning by Main Tuner
by A. Kabe
Main Tuner Position (mm)
Main Tuner Position (mm)
Resonance Frequency
Load [kg]

## Slide 12: Frequency Tuning by Piezo Tuner
by A. Kabe

## Slide 13: LER tuning mechanism problem
Distribution of tuner phase for Vc > 0.3 MV
HER
LER
manual
Piezo on
Problem of LER frequency tuner:
  Suffers from something like mechanical backlash. This results in a large fluctuation of tuner phase, even tuning feedback system is working.
  Although some efforts were effective to reduce it, we still have a tuning error of about ±15 degree.
Consequences:
  Cavity phase is successfully stabilized to a required level by a phase lock loop (next two slides).
  Cavity input power inevitably fluctuates to keep the cavity voltage constant.
  Some of the LER trips seem associated with this fluctuation (discussed later).
LER
LER

## Slide 14: Phase stability (histogram of phase detector signal)
HER
LER
0.007°
0.046°
Distribution of cavity phase (cavity feedback loops on)
Linear scale
Log scale
The required stability is 0.27degree.

## Slide 15: Phase stability (cavity pick up signal)
Span 3MHz
No significant sidebands seen.
Span 200 kHz
Sideband peaks at 32kHz, 64kHz.
Phase error < ± 0.01 deg (fast)
Span 200 Hz
Sideband peaks
at 32, 37, 46, 50, 100 Hz.
Phase error < ± 0.07 deg (slow)
LER
Spectrum of pick up signal is consistent with phase detector data.
The measured phase error is much smaller than the allowed values given by beam-beam simulation.
According to b-b simulation by Ohmi-san, allowed phase error
for N-turn correlation is 0.1×√N (degree).

## Slide 16: Crab RF system_3
Special cares are taken for the coaxial beam pipe.
  A sub tuner is added to align the coax horizontally in order to minimize the coupling of the crabbing mode between the cell and the coax.
  RF signals monitored at seven pickup ports located in the coax are connected to the fast interlock system. It protects the ferrite damper at the end of the coax from abnormally large crabbing-mode power that can leak through the coax on the occasion of a discharge at the coax or the notch filter.
Sub-tuner
Monitor ports
With band path filters
KEKB review on 2008

## Slide 17: Adjustment of Coaxial Coupler Position by Sub Tuner
by A. Kabe
By adjusting coaxial coupler on the axis of crab cavity,
the crab mode can be prevented going out.
The coupler position can be controlled by sub-tuner.

## Slide 18
HER
LER
Outer
Outer
Inner
Inner
40kHz
40kHz
5kHz
5kHz
Searching Field Center in Crab Cavity
Field center was searched by measuring the crabbing mode amplitude excited by a beam with the crab cavity detuned. Two measurements with different detuning frequencies agreed to each other.
A local bump orbit was set to make the beam aligned on the field center.
KEKB review on 2007

## Slide 19: Oscillation of high-current crabbing beams
A large-amplitude oscillation was observed in high-current crab-crossing operation in June.
  It caused unstable collision, short beam life time and luminosity degradation.
  Crab amplitude and phase were modulated at 540 Hz. Horizontal oscillation of beams was also observed at the same frequency.
  None of the beam orbit feedback systems is responsible, since their time constants are 1 to 20 sec, much slower than the oscillation.
  The oscillation occurred when the LER tuning phase migrated to the positive side. This gave us a hint to understand the phenomena.
Beam-beam kick is shaken.
KEKB review on 2008

## Slide 20: A remedy for the oscillation was found
Observations at a machine study
  The oscillation occurred only with high-current colliding beams: it never occurred with a single beam, even at a high current.
  Both beams oscillates coherently.
  The threshold for the oscillation is dependent on the crab phase and tuning phase (see left).
Cause and remedy
  We concluded that the oscillation is caused by beam loading on crab cavities together with beam-beam force at the IP (see, next slide).
  We found that it can be avoided by shifting the crabbing phase by +10° and controlling the tuning offset angle appropriately.
Both crab phase (degree)
LER tuning offset (degree)
HER tuning offset:
φtun (HER)
φtun (HER) = 0°
φtun (HER) = -10°
φtun (HER) = +10°
oscillation
occurs
stable
Dependence on the crab phase and tuning phase.
Beam current was 1150 mA (LER) and 620 mA (HER).
KEKB review on 2008

## Slide 21: Possible mechanism of the oscillation
Kick bunch
Horizontal displacement at crab and IP
Kick by beam-beam force
Beam-loading on crab cavity
Crab voltage
Crab phase
Phase control
Level control
Input rf phase
Input rf power
Kick bunch
Horizontal displacement at crab and IP
Beam-loading on crab cavity
Crab voltage
Crab phase
Input rf phase
Input rf power
LER
HER
Phase control
Level control
IP
KEKB review on 2008

## Slide 22: summary
The RF systems for crab cavities were established by using available components for SCC.
The required phase stability was obtained nevertheless the poor LER tuner performance.
In high beam current operation, a phase instability was observed. It was suppressed to adjust the tuning offset and the cavity phase.