## Slide 1: KEK-B crab trips & RF signals
K.Nakanishi
KEK
Dec. 16 , 2010
LHC-CC10

## Slide 2
Cavity voltage
Abort request
RF switch
Beam current (DCCT)
DCCT signal delay 80microsecond, when that is caught at RF station
Beam abort
~300 μs
~200 μs
In KEKB, the beam was aborted 300us after the RF trips.
It corresponds to 30 turns of beam circulation.

## Slide 3: Data taking
Various data measured by RF abort monitor and BOR are introduced in this report.
RF abort monitor
BOR
It is an oscilloscope attached to LLRF
It is triggered by beam decaying.
When a beam abort is required, the snapshot of an oscilloscope is saved.
DCCT
Trigger
Bunch by bunch feedback system
KEKB HER(High Energy Ring) and LER(Low Energy Ring) have a bunch-by-bunch feedback system respectively. The beam positions in 4096 turns of every bunches are stored in ring buffer of them.
When a beam loss is observed by DCCT, the data is saved.
At first, I searched characteristic signals in data of RF abort monitor. And corresponding data was find in the BOR data.
e+/-
BPM
LLRF
HER H:0.0118
HER V:0.00655
LER H:0.00570
LER V:0.0169 mm mA/count

## Slide 4
turns
Yellow :Klystron output power
Blue :Power form pick up antenna at the cavity.(∝Vc2)
Purple :Cavity phase
Green :Beam current
HER DCCT
The vertical axis shows a quantity related to a displacement and bunch current.
The beam was kicked when a quench was occurred.
10deg
~1mm
horizontal

## Slide 5
turns
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
Some turbulence occurred in the cavity. Corresponding displacement was observed.
Finally, the cavity phase was lost, and the beam was kicked.
Because the betatron tune is very close to half integer, the beam observed with alternative displacement turn by turn.
Beating structure is observed, because the betatron tune is not half integer.
40deg
~1.5mm
horizontal

## Slide 6
turns
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
10deg
When LLRF feedback was oscillated at 540Hz, corresponding displacement was observed.
~0.4mm
horizontal

## Slide 7
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
In this case, the beam was not aborted after turn off the RF.
After turned off the RF, a horizontal oscillation was started. And it seems decaying. Finally, the beam was aborted due to discharge caused by the beam induced field. The beam survived for 2msec after turned off the RF.
~1.5mm
~0.3mm
10deg
horizontal
vertical

## Slide 8: Crab kickによるCOD
Horizontal COD by crab kick
Arc部でのCOD
(COD at arc section)

## Slide 9: Crab Phase Scan (LER)
0
36
72
108
144
180
216
252
288
324
360
Phase 0：174.8 deg.
Vcrab set:1.0MV, estimated: 0.987MV
agree very well
crab
Horizontal orbit by crab kick
Horizontal kick by crab cavity (rad)
(Estimated from orbits around the ring)
crab
H. Koiso, A. Morita

## Slide 10
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Green :Beam current
Purple :Cavity phase
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Green :Beam current
Purple :Cavity phase
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Green :Beam current
Purple :Cavity phase
40deg
noise?
The HER beam was aborted by intentional abort request.
The expected decay time of stored energy was 42 μsec.
(84 μsec for cavity voltage)
The arc sensor was lighten by a LED.

## Slide 11
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Green :Beam current
Purple :Cavity phase
The HER beam was aborted.
Sometimes the cavity voltage decays cleanly.
What is different from previous page?
40deg

## Slide 12
40deg
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
The LER beam was aborted by intentional abort request.
The expected decay time of stored energy was 65 μsec.
(130 μsec for cavity voltage)
The beam induced field vanish here

## Slide 13
10deg
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
The RF power for LER crab cavity was turned off.
The beam was aborted in 50 msec.
Anyway the beam could circulate, and it seems to stabilized by the beam induced field.

## Slide 14: Beam loading depend on the beam position
Beam current [mA]
Beam current [mA]
RF power [kW]
RF power [kW]
LER
HER
The beam position is adjusted to center.
The conditions that the beam is offset 2mm for both sides are prepared.

## Slide 15: In LER negative beam loading case
40deg
~0.3mm
In LER negative beam loading case, opposite phase beam induced field was observed.
But the phase behavior was rather gentle.
Even in this condition, the beam was not kicked hard.
In case of on axis and positive beam loading, the beam was also not kicked.
horizontal

## Slide 16: In HER positive beam loading case
~1.3mm
In this case, the positive beam loading don’t help the phase stabilization.
In these experiments, other beam positions tests show same result.
horizontal

## Slide 17: summary
The beam oscillation due to decaying crabbing field was observed.
The beam oscillation was related to the turbulence of the crab cavity phase.
In most case, the crab cavity phase turbulence is observed at the HER crab cavity.
Possible hypothesis
Strong traveling wave RF field induce discharge at input coupler.

## Slide 18
The HER RF power is turned off without beam.
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current

## Slide 19
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
The LER RF power is turned off without beam.

## Slide 20
Yellow :Klystron output power
Blue :Pick up power(∝Vc2)
Purple :Cavity phase
Green :Beam current
20deg

## Slide 21
HER
LER
Outer
Outer
Inner
Inner
40kHz
40kHz
5kHz
5kHz
Searching Field Center in Crab Cavity
Field center was searched by measuring the crabbing mode amplitude excited by a beam with the crab cavity detuned. Two measurements with different detuning frequencies agreed to each other.
A local bump orbit was set to make the beam aligned on the field center.
KEKB review on 2007

## Slide 22
 | LER | HER | unit
β x* | 80 | 80 | cm
β x monitor | 21 | 39 | m
β x cavity | 73 | 162 | m
νx | 44.506 | 45.511 | -
I bunch | 1.0 | 0.75 | mA
φ cavity | 0.35 | 0.35 | rad
V cavity | 0.95 | 1.45 | MV
τ crab | 130 | 84 | μsec
Typical parameters