## Slide 1
WP3 update
Positron Source: Target and Capture System
Iryna Chaikovska
on behalf of the WP3 team
11 March 2021

## Slide 2: General updates
Common workspace (indico, cernbox, gitlab, notes, etc. ) is deployed for the FCC-injector studies/CHART collaboration (thanks to Andrea) and ready to be used by everybody. https://espace.cern.ch/FCC-ee-injectors/WP3/_layouts/15/start.aspx#/SitePages/Home.aspx
Work within the WP3 is mainly focused now on the benchmark of simulation codes and simulations of the capture system (different matching devices, RF structures, production schemes).
Setting up the working environment with CERN STI group => the general strategy for the target design should be clarified and validated.
Abstract of the IPAC-2021 has been submitted by Y. Zhao (Title: Comparison of Different Capture Schemes for the FCC-ee Positron Source Design) and contributions to the FCC-France workshop on 20-21 January 2021 (I. Chaikovska) and LCWS-2021 on 15-18 March 2021 (I. Chaikovska and Y. Zhao) was/will be given.

## Slide 3: Some highlights (work ongoing)
Conventional production scheme
L-band TW structures (same as CLIC)
Gradients: 22 MV/m for dec. 16.5 MV/m for acc. Already optimised to achieve the maximum positron yield, with the energy at the exit as close to 200 MeV as possible
HTS as the AMD
Design studies of the SC solenoid have been started @PSI. The HTS technology is proposed.
Two fieldmaps are provided by the PSI magnet group (with peak field of 7 and 10 T).
Goal: 4.2 ⨯ 1010 e+/bunch (7 nC)
The e- drive beam parameters are kept the following:
  6 GeV,
  beam spot size 1.8 mm,
  bunch length 1 mm*
  25-30 bunches per pulse,
  100 Hz rep. rate.
* zero bunch length was used in the presented simulations.
Next step: simulation of the radiation environment in target vicinity
Courtesy of J. Kosse and Y. Zhao

## Slide 4: Some highlights (work ongoing)
HTS as the AMD
Courtesy of Y. Zhao
Results obtained with the FC 7 T, B_TW = 0.7 T, DR acceptance 3.8% (ceteris paribus)
Effect of the magnetic field upstream the target has been evaluated:
px, py spread increased by a factor of 40 @Target entrance
Difference in positron yield @Target: the same, @Solenoid exit: ~0.1%, accepted by the DR: ~1%, PEDD: ~2% => small effect

## Slide 5: Some highlights (work ongoing)
Conventional scheme
Motivation: optimise conventional target thickness, as well as primary electron beam parameters.
Courtesy of Y. Zhao
AMD: FC with a small (7 T , 8 mm) and large aperture (5 T, 16 mm)
TW structures: CLIC-like L-band with 0.5 T DC field
Injector linac: analytic formula without simulation

## Slide 6: Some highlights (work ongoing)
Hybrid scheme
Design studies of the hybrid scheme for the FCC-ee have been started. Next steps: optimization of the crystal, distance between the targets, target-converter, drive beam parameters, large aperture AMD, etc.)
Courtesy of Y. Zhao and A. Sytov
The difference in positron yield is small (< 13%).
The difference in photon energy spectrum (low energy part E < 13 MeV) and transverse momenta of the charged particles after the crystal is under investigation.
Benchmark of the codes to simulate the radiation in the oriented crystals (FOT vs. Ferrara’s code) is ongoing
Crystal optimization