## Slide 1: Test results of MCBXFBP2b
Salvador Ferradás, Jerome Feuvrier, Jean-Luc Guyon, Franco Mangiarotti, Juan Carlos Pérez, Guillaume Pichon, Gerard Willering
WP3 Meeting – 03 March 2021
https://indico.cern.ch/event/1012233/
Test plan: EDMS #2466864

## Slide 2
Contents
Connection scheme
HV Tests
Protection scheme
Thermal transients
Cold powering
Conclusions

## Slide 3: 0. Intro
MCBXFBP2b vs 2a:
Inner and outer dipoles were recollared
  Ref: Coil geometry and shimming.
Inner dipole has instrumented collars
Targeted azimuthal pre-stress ~20 MPa higher at cold for both inner and outer dipoles:
  Ref: Mechanical measurements of MCBXFBP2b
The inner dipole was installed rotated 180 degrees.

## Slide 4: 1. Connection scheme
MCBXFBP2b
EDMS 2475766
LEAD
Inner
Magnet
-
+
+ LEAD
Outer
Magnet
- LEAD
Outer
Magnet
IC#5
IC#4
OC#4
OC#3
MCBXFBP2a
EDMS 2413181

## Slide 5: 2. Electrical insulation test (I/II)
Circuit | V [kV] | Time [s] | Resistance [GΩ]
Inner – GND | 0.4 | 60 | 379
Outer – GND | 0.4 | 60 | 373
@Reception
SM18 Hall
293 K, Air
MIT515
Voltage: 5 kV (+4%, -0%, ±10 V nominal test voltage at 1 GΩ load (0°C to 30°C)
Current: ±5% ±0.2 nA at all voltages (20 °C) [1].
[1] MIT515; 5 kV d.c. Insulation Resistance Testers; https://us.megger.com/5-kv-insulation-resistance-tester-mit525#technical
@Cryostat
Cluster D
293 K, Air
CD1 Before test
@Cryostat, Cluster D
4.5 K, He
CD1 Before test
Circuit | V [kV] | Time [s] | Resistance [GΩ]
Inner – GND | 0.4 | 60 | 378
Outer – GND | 0.4 | 60 | 398
Circuit | V [kV] | Time [s] | Resistance [GΩ]
Inner – GND | 1 | 60 | 34
Outer – GND | 1 | 60 | 25
MCBXFBP2b

## Slide 6: Electrical insulation test (II/II)
Circuit | V [kV] | Time [s] | Resistance [GΩ]
Inner – GND | 1 | 60 | 63
Outer – GND | 1 | 60 | 34
MIT515
Voltage: 5 kV (+4%, -0%, ±10 V nominal test voltage at 1 GΩ load (0°C to 30°C)
Current: ±5% ±0.2 nA at all voltages (20 °C) [1].
@Cryostat
Cluster D
4.5 K, He
CD1 After test
[1] MIT515; 5 kV d.c. Insulation Resistance Testers; https://us.megger.com/5-kv-insulation-resistance-tester-mit525#technical
MCBXFBP2b
@Cryostat
Cluster D
293 K, Air
After test
Circuit | V [kV] | Time [s] | Resistance [GΩ]
Inner – GND | 0.4 | 60 | >500
Outer – GND | 0.4 | 60 | 341

## Slide 7: 3. Protection scheme
2 kA PC 1
2 kA PC 2
Two quench detection systems:
  uQDS: Inductive cancellation of the total magnet voltage & diff signals
  PotAim cards (DAQ): Diff signals

## Slide 8: 4. Cooldown 1
Middle
Down
Down A
Up
Up A
Disclaimer: Approximate sensor positioning
Warmup 1

## Slide 9: 5. Summary of events
MCBXFBP2b:
Reached ultimate in both circuits, standalone
132 Events
Reached 99.9% + nominal torque. Proved unstable at high currents. Might point to a slightly decrease in performance
Reached 94.4% of -nominal torque
 | Training quenches |  | 
 | IC4 | IC5 | OC3
 | 9 (10%) | 76 (90%) | 0
Total | 85 |  | 
MCBXFBP2a:
Reached ultimate in both circuits standalone
Reached 1980 A Inner circuit stand alone
280 Events
Reached nominal + torque
Reached 97% of -nominal torque
 | Training quenches |  | 
 | IC4 | IC5 | OC3
 | 91 (51%) | 83 (47%) | 4 (2%)
Total | 177 |  | 

## Slide 10: Training Q1 (from event 0)
MCBXFBP2b:
35 quenches to 99.9%
After 41 quenches nominal was not attained yet
 | Training quenches |  | 
 | IC4 | IC5 | OC3
Total 35 | 3 (8%) | 32 (92%) | 0
MCBXFBP2a:
32 quenches to nominal
 | Training quenches |  | 
 | IC4 | IC5 | OC3
Total 32 | 20 (62%) | 11 (34%) | 1 (2%)

## Slide 11: Training Q2 right after
MCBXFBP2a:
31 quenches
First quench at 23% of nominal torque
Reached 94% of nominal torque
 | Training quenches |  | 
 | IC4 | IC5 | OC3
 | 11 (36%) | 18 (58%) | 2 (6%)
MCBXFBP2b:
28 quenches
First quench at 23% of nominal torque
Reached 94% of nominal torque
 | Training quenches |  | 
 | IC4 | IC5 | OC3
 | 4 (14%) | 24 (86%) | 0
Magnetic measurements

## Slide 12: QA
The magnetic measurement shaft is installed as a quench antenna. There are 5 segments of 500 mm. Segment 3 should be centered with the magnet. Segment 1 and 5 stick out of the magnet. We use 2,3 and 4 to distinguish towards which coil end the quench happened.

## Slide 13: Note on quench localization
Case 1:
Clear onset on the NCS pick-up coil
The gain is under investigation, and the amplitude of the orange signal
Quench at 56% of nominal torque. Event na006.

## Slide 14: Note on quench localization
Case 1:
Clear onset on the NCS pick-up coil
The gain is under investigation, and the amplitude of the orange signal
Quench at 91% of nominal torque. Event na034.
As the current increases, central segment of the QA approaches in time to the onset of the NCS segment.

## Slide 15: Note on quench localization
Case 1 high current:
Undistinguishable

## Slide 16: Note on quench localization
Case 2:
Clear detection in the CS side

## Slide 17: Note on quench localization
Case Extra I:
Preceding vibrations do not decay, and it is difficult to assess the quenching segment

## Slide 18: Note on quench localization
Case Extra II:
Preceding vibrations do not decay, Central segment gets most of the signal

## Slide 19: Note on quench localization
Summary:
During training in P2b Q1:
  NCS Onset: 47 %
  CS Clear: 22%
  Indistinguishable: 31%
Study case: training P2a Q1 in CD1 (Example ->)
  Not even 1 undistinguishable case
Case Extra III in 2a:

## Slide 20: Recap… summary of events
MCBXFBP2b:
Reached ultimate in both circuits, standalone
132 Events
Reached 99.9% + nominal torque
Reached 94.4% of -nominal torque
 | Training quenches |  | 
 | IC4 | IC5 | OC3
 | 9 | 76 | 0
Total | 85 |  | 
MCBXFBP2a:
Reached ultimate in both circuits standalone
Reached 1980 A Inner circuit stand alone
280 Events
Reached nominal + torque
Reached 97% of -nominal torque
 | Training quenches |  | 
 | IC4 | IC5 | OC3
 | 91 | 83 | 4
Total | 177 |  | 
Retrain in Q1 to reposition the assembly again

## Slide 21: J. Verification of the quench free region (I/III)
MCBXFBP2a:
  Quench free cycle of 4 points (diagonals) 20, 23, 26, 29, 32, 35% of nominal torque
  Quench when attempting 38%
Quench at 38%

## Slide 22: Verification of the free cycle (II/II)
MCBXFBP2a:
After the quench at 38% in the 4 point cycle:
  Quench free cycle attempt of 12 points at 35%, quench when ramping the outer to nominal current.
  Quench free cycle of 12 points at 32% OK
Quench at 35%

## Slide 23: 6. Conclusions
Similar to P2a:
  Good margin in standalone configuration
    No quench inner nor outer
  ~ same number of training quenches in both torque directions
  Quench free region:
    Q1/Q3: ~32% of nominal torque Q2/Q4: ~32% of nominal torque
Different from P2a:
  Unstable at high currents
  IC 5 quenching 90% of the time

## Slide 24: Summary of events, for completeness