## Slide 1: Study of dose-enhancing agents on bremsstrahlung photons from SL75-5MT medical accelerator
INR RAS
лекция
Skorkin V.M.
LXXI International conference ”NUCLEUS – 2021. Nuclear physics andelementary particle physics. Nuclear physics technologies”

## Slide 2: Contrast-enhanced radiotherapy allows to enhance the radiation dose absorbed by the tumor when using the hard elements for a photon absorption.
The dose-enhancing agents (I, Gd, Au, Bi, etc.) have a better absorption capacity, than biological tissues and thus sparing the surrounding healthy cells.

## Slide 3: Normally, increase dose absorbed by dose-enhancing agent concentrations employ up to 15 mg/ml at using bremsstrahlung photons generated by the clinical linear electron accelerator SL75-5MT. .
Increase dose absorbed (on 13%) by iodinated water (for 50 mg/ml iodine concentrations) was obtained in a work (Vorobyeva E.S. at al, Bulletin of RSMU. 4, 57 (2017).

## Slide 4: The study is aimed at studying the features of using metal-organic composites to increase the absorption of SL75-5MT bremsstrahlung photons.
In the work investigated the possibility of using dose increasing agents (Gd, Au, W, Bi, Pb, D2O) to increase the absorption of SL75-5MT accelerator radiation. .

## Slide 5: The SL75-5MT bremsstrahlung radiation created 2 Gray/min absorbed dose at a distance of 1 m.
The 80% of flux photon of the accelerator have 0.5-4.5 MeV energy.

## Slide 6: The energy fluence distribution from SL75 accelerator

## Slide 7: The photons of the linear electron accelerator create secondary X-ray and electrons in the dose-enhancing metallic agents.
This is enhanced the radiation dose absorbed by the tumor.

## Slide 8
DNA
Gd ion
e
e
Radiation
electrons
X ray
Cell
nucleus
≥ 50 m
X-ray and electrons from dose-enhancing agents are enhanced the radiation dose absorbed by the tumor cells.

## Slide 9: X-ray characteristic radiation for the lead material from lead composite material (energies 75 keV, 85 keV)
The intensity of the characteristic radiation for the Pb-composite, measured by a Ge detector was more than 15% from a attenuation radiation.

## Slide 10: Spectrum of radiation from the bismuth material
The intensity of the characteristic radiation for the Bi-material (at large attenuation gamma raу). was about 50% from a attenuation radiation.

## Slide 11: Bismuth dose-enhancing agent material

## Slide 12: Spectrum of radiation from the bismuth material
The intensity of the characteristic radiation for the Bi-material (at large attenuation gamma raу). was about 50% from a attenuation radiation.

## Slide 13: The photon absorbed dose measured by clinical ionization chambers in tissue-equivalent phantom and PTW MULTIDOS dosimetry chambers.
The dose measured using fantom with irradiated dose-enhancing metallic agents (Gd, Au, W, Bi, Pb)

## Slide 14: In addition, a gamma radiation from the phantom were measured using BDMG-08R gamma detectors.
Dose increasing agents (Gd, Au, W, Bi, Pb, D2O) . .
γ
γ

## Slide 15: The proton irradiation of a metal and material creates γ –rays and radionucledes
The interaction of γ pulse with metallic agents create gamma, measured by the BDMG-08 gamma detector

## Slide 16: A dose load from gamma emitting isotopes in a metal shell and organic material
A gamma dose load from long life 54Mn, 56, 57Co nuclides generated in steel protective shell (54Fe, 56Fe, 57Fe)
The gamma dose load from 11C, 14N, 15O short life positron isotopes
Tritium can be formed in containers with water under cosmic irradiation

## Slide 17: For Au, Bi, Pb dose-enhancing agents the absorbed dose increased by 10-20%. The significant increase in the absorbed dose (> 50%) was observed from d(γ,n)p reaction when using deuterated water instead of tissue-equivalent phantom.
About 30% of the bremsstrahlung photons have energies above the deuteron breakup threshold. As a result, the fast photons in D2O target create protons and neutrons.

## Slide 18: The irradiation facility consists of the heavy water target (30×30×30 cm), surrounded by a graphite reflector and lead absorber
1 - D2O target; 2 - a graphite reflector; 3 – lead absorber; 4 – the bremsstrahlung photons; 5 - a neutron detector;
6 - a gamma detector.

## Slide 19: Diagram of the gamma radiation dose rate from photoneutron target
1, 4 - the gamma detector into D2O target; 2, 3- the gamma detector into H2O target; 5- the gamma detector out the water target; 6- the gamma detector out D2O target. .

## Slide 20: Diagram of the neutron dose rate from photoneutron target
1- neutron detector into D2O target; 2, 3- the neutron detector into H2O target; 4, 6- the neutron detector out D2O target; 5- the neutron detector out the water target.
. .

## Slide 21: The particles of the cholesteric double-stranded DNA liquid-crystalline dispersions, containing Gd and Au ions have been obtained in Engelhardt Institute of Molecular Biology of the RAS.
ion Gd ion Au

## Slide 22
Table.1. Energy, formation probability and maximum range of electrons in the 1 neutron capture by nanostructures.
Approximately half of all electrons with energy less than 6 keV are absorbed in the microparticles themselves.
Еe, keV | 200 | 80 | 30 | 7 | 6 | 5 | 4 | 2 | 1
Р, % | 5.7 | 42.3 | 20.8 | 4.3 | 17.3 | 23.7 | 1 | 31.4 | 16
Rм, µm | 439 | 92 | 16 | 1.2 | 0.90 | 0.65 | 0.44 | 0.12 | 0.06

## Slide 23
The absorbed dose of electrons from the reaction 157Gd (n, ) 158Gd depending on the electrons range
1- dose taking into account Auger electron channeling effect 2- dose without the electron channeling.

## Slide 24
High-energy conversion electrons (≥1 MeV) slowing down in DNA-Gd and DNA-Au microparticles, generate bremsstrahlung with a wide spectrum.
Channeled electrons traveling along DNA chains metal with metal ions can make periodic movements and emit photons in a narrow cone of angles (≤ 5).
The wavelength of monochromatic X-ray radiation (m) at zero angle is determined by the channel radius (rc) and the relativistic factor (): m  rc /23/2

## Slide 25
Conclusion
An increase of the cell irradiation dose is due to Auger electrons channeling effect in DNA-Gd.
In liquid-crystalline DNA-Au nanostructures conversion electrons can emit photons with a wavelength  0.3 nm.
By changing the orientation of DNA-Gd using a magnetic field, one can increase the monitor the effectiveness of cancer therapy.