## Slide 1
Reactor PIK status and
scientific program for elementary particle and nuclear physics
Vladimir Voronin
NRC “Kurchstov institute”-PNPI
Notes: 1
1

## Slide 2
2021 – 50 years of PNPI

## Slide 3
Член-корр. РАН - 2
Доктора наук – 75
Кандидаты наук – 260
Научные сотрудники - 530
Инженеры – >600
Всего в ПИЯФ – 2100 (+ 100 совм.)
Instrumental facilities Research nuclear reactor for 18 MW; Research nuclear reactor for 100 MW (commissioning stage); Proton accelerator at 1 GeV; Cyclotron 80 MeV. Main research direction: physics of elementary particles and fundamental interactions; physics of the atomic nucleus and nuclear reactions; neutron physics; physics of the condensed state of matter; molecular and radiation biophysics; theoretical physics; physics and technology of reactors and accelerators; radiation medicine; applied developments and instrumentation. Staff Total – 2100 Engineers - 600 Scientists - 530

## Slide 4: Reactor PIK as a neutron source

## Slide 5: High flux research reactor PIK
Reactor core
Heavy water moderator
Light water coolant
Neutron beam
PIK is aimed for production of neutron beams with the maximal possible fluxes.
We need:
High neutron fluxes inside the reactor
Neutron thermalization system to provide required energy
Neutron transportation system
Neutron scattering station

## Slide 6
Reactor PIK parameters
 | Value
Power | 100 MW
Reactor core volume | 50 l
Core height | 500 mm
Coolant | Н2О
Reflector | D2О
Maximal neutron flux in moderator | 1.3х1015 n/cm2c
Maximal neutron flux in central trap | 5х1015 n/cm2c
Operation cycle | ~30 day
Experimental channels - Horizontal (HEC) - Vertical (VEC) Inclined (IEC) Central (CEC) | 10 6 6 1

## Slide 7
Comparison of PIK with the best reactors
Facility/ Location | Commissioning Date | Power | Maximum Flux Density | Number of Instruments on Beams
PIK Gatchina, Russia | 2021 (under commissioning) | 100 MW | 51015 n/сm2s | Up to 50
HFR Grenoble, France | 1971 | 58 MW | 1.51015 n/сm2s | 40
HFIR Oak Ridge, USA | 1965 (updated 2007) | 85 MW | 2.51015 n/сm2s | 12
FRM2 Munich, Germany | 2005 | 20 MW | 0.81015 n/сm2s | 27
BER2 Berlin, Germany | 1973 | 10 MW | 0.0861015 n/сm2s | 25
OPAL Sydney, Australia | 2006 | 20 MW | 0.41015 n/сm2s | 7
CARR Beijing, China | 2010 | 60 MW | 0.81015 n/сm2s | 6
WWR-M Gatchina. Russia | 1959 | 18 MW | 0.451015 n/сm2s | 14
Europe without PIK
(from C.Carlile, NOP-2017, Nara, Japan)

## Slide 8: Current status of PIK commissioning

## Slide 9
8 February 2021.
The energetic regime was started by Russia president Vladimir Putin
2019 – 100 kW
2021 – 10 MW
2023 – 100 MW

## Slide 10
Roadmap of PIK commissioning
We are here
First neutron beam
experiment
5 stations
for CM
5+20 stations

## Slide 11
TEX-3
Test neutron reflectometer
DPN
5 “first day” stations
NERO-2
Tspectrum

## Slide 12
Status of the “first day” stations
TNR test neutron reflectometer
NERO Polarized Neutron Reflectometer (GKSS)
DPN polarized neutron diffractometer
Texture Diffractometer TEX-2 (GKSS)
Test neutron spectrometer
2
3
4
5
1
Commissioned at the December 2020
First “demonstration” experiments at 100kW power were carried out
All results coincide with the theoretical predictions
Program for updates of these stations to the power of 100 MW is developed

## Slide 13: Instrumental program status
The design of the project obtained a positive state expertise decision in September 2020
Construction of the first phase instruments started January 2021
Second phase instruments started June 2021
The third phase will start at the beginning of 2022

## Slide 14: Road map of instrumental program
# |  |  | 2019 |  | 2020 |  |  |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  | 
 |  |  | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV | I | II | III | IV
0 |  | Reactor PIK commissioning | 100 kW |  |  |  |  |  | 10MW |  |  |  |  |  |  |  | 10-100MW |  |  |  | ~100MW |  |  | 
1 |  | Project of instruments |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  | Experimental channel |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  | HNC HEC-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  | UCNS HEC-4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  | CNS HEC-2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  | CNS HEC-3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  | Neutronguide system |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Neutron stations |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  | SESANS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Commissioning
4 |  | INAA |  |  |  |  |  |  |  | Phase 1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  | «Нейтрино» (Neutrino) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  | D1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  | DC-1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  | D3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  | IN-1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  | IN-2 |  |  |  |  |  |  |  |  |  |  | Phase 2 |  |  |  |  |  |  |  |  |  |  | 
10 |  | ИРИНА (IRINA) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
11 |  | DEDM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  | FISCO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
13 |  | Tenzor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  | Мембрана – 2 (Membrane – 2) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
14 |  | IN-3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
15 |  | IN-4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
16 |  | SONATA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
17 |  | SEM |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Phase 3 |  |  |  |  |  |  | 
18 |  | Harmony |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
19 |  | PROGRAS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
20 |  | «Бета-распад нейтрона» (neutron beta decay) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15
The scientific case was published in 2015. (v.3 and v.4) There are not serious changes for 2021.

## Slide 16: What do we get for particle and nuclear physics?

## Slide 17
5 “first day” stations (2020)
Main program (2020-2024)
Neutron sources –
Two cold neutron source (HEC 2 and HEC 3)
Hot neutron source – HEC 8
Ultra cold neutron source – HEC 4
Instrumentation base (20 stations)
Experimental stations for condensed matter (13)
• Diffractometers (3)
• Spectrometers of inelastic scattering (5)
• SANS machines (3)
• Reflectometers (2)
Experimental stations for nuclear and particle physics (7)
  Stations with CN (2)
  Neutrino physics facility (1)
  Stations for nuclear spectroscopy (3)
  Fission physics (1)
National Instrument Program
Realized at the the framework of national program of the development of neutron and synchrotron research in Russia (2020-2027)

## Slide 18
ULTRACOLD NEUTRON SOURCE
UCN source parameters:
Parameter | Value
UCN converter temperature, K | 1,15
Thermal neutron flux, cm-2s-1 | 2,8∙1010
9Å flux density, cm-2s-1Å-1 | 5∙108
UCN density in UCN source, cm-3 | 1,3∙103
UCN density in the EDM trap, cm-3 | 3,5∙102
Energy release in the helium chamber, W | 3,85
Energy release in the pre-moderator chamber, W | 10,7
Energy release in the lead shield, W | 267
Superfluid 4Не convertor at HEC-4
Т-1.15К
V~35 litre

## Slide 19
UCN source on PIK reactor and the program of research of fundamental interactions
n-n’ oscillations
EDM spectrometer
asymmetry of β-decay
UCN
gravitational
trap
UCN
magnetic trap
UCN source
EDM spectrometer
UCN magnetic trap
n-n’ oscillations
UCN gravitational
trap

## Slide 20: Neutron beta-decay
Supermirror Polarizer
Shutter
Monochromator
Breaker
Spin Flipper
Superconducting solenoid
Beam polarization measuring device
Helium refrigerator
Helium Dewar
Vacuum pump
Beam stop
NEUTROM BETA DECAY
Study the correlation in neutron decay with accuracy about 10-3

## Slide 21
NEUTRINO
Parameter | Value
Detector section size, cm | 22х22
Energy resolution | 20% for 1 MeV
Fast neutron background inside the detector shielding | less then 6·10-5 s-1cm-2
Thermal neutron background inside the detector shielding | less then 4·10-5 s-1cm-2
The ratio of the neutrino level signal to the correlated background | more then 1
The ratio of the neutrino level signal to the background of random coincidences | more then 0,6
NEUTRINO parameters:
Study the short range neutrino oscillations

## Slide 22
1. Beam shutter
2. Velocity selector
3. Double-crystal monochromator
4. Neutron guide
5. SM polarizer
6. Spin-flipper
7. CRYOPAD (3D polarization analyze)
8. Working crystal (sample)
• Working mode: wavelength 3-5 Å or white spectrum, polarized/non-polarized beam.
• Polarizer/analyzer: super-mirror multi-slit, P ~ 98-99%.
• CRYOPAD: system with a double superconducting magnetic shield and rotating coils for 3D polarization analysis. Max sample size is 100 × 100 × 500 mm3.
9. Non magnetic hexapod positioner
10. Monochromator
11. Transparent SM analyzer
12. Spin-rotating coil
13. Crystal-reflector
14. PSD detector
15. Granite plate
16. Beam stop
• Velocity selector: transmission ~ 95%, Δλ/λ ~ 10%.
• Monochromator: Dual pyrolytic graphite (PG), size 100 × 100 mm2, mosaicity ~1°.
• Detector: 2D position-sensitive, 250 × 250 mm2, resolution ~ 1-2 mm, efficiency > 90%.
• Hexapod Positioner: non magnetic, not heat.
• Spin-flipper: radio frequency, f ~ 99.9%
DEDM Setup for Crystal Diffraction Experiments at PIK Reactor Complex
DEDM

## Slide 23
Project of DEDM-CRYOPAD
(3D polarization analysis)collaboration with ILL (Grenoble, France) for large composite crystal.
Large tested composite working crystal (15 items with 35×100×100 mm3).
Interplanar space dispersion is
 d/d=  2  10-6 over the all crystal.
3D model of the DEDM setup
A high-priority task is to conduct an experiment on the neutron EDM search using the diffraction in a noncentrosymmetric quartz crystal. The sensitivity can reach about 2.5×10-25 e∙cm/day for the full scale experiment.
DEDM Setup for Crystal Diffraction Experiments at PIK Reactor Complex

## Slide 24
Calculated yields of isotopes expected at the IRINA facility
1–heat shield; 2-insulator; 3-niobium support disk; 4-niobium frame;
5-tantalum target body; 6-UC target inside graphite container;
7,8-pyrolytic graphite plugs; 9-tantalum target shield;10-tantalum
target holder; 11-plate from pyrolytic graphite; 12-extraction electrode;
13,14,15- focusing lens electrodes; 16,17-insulators;18-flange of lens
electrode; 19- the rod-holder.
Target – ion optic system
The IRIN goal:
to investigate neutron-rich isotopes with neutron number close to the magic number N=82 in the region of border of neutron stability;
isotopes in the valley of nuclei with the proton magic number Z=28 and neutron magic number N=50 to establish the influence the shell effect on the nucleus form;
to develop new methods of radioisotopes production for medicine;
production radioisotope for research in solid state physics
Исследование Радиоактивных Изотопов на НейтронАх (ИРИНА)
Investigation Radioactive Isotopes with Neutron (IRINA) facility project at the PIK reactor
Target is a high density uranium carbide of highly enriched 235U.
The neutron flux through the target is (3-5)х1013 n/сm2s.
Power dissipated on the target about 2,5 кW,
The target temperature up to 2200 °С.

## Slide 25
Laser ion source and 238UC target material tested at the IRIS facility
The target of 238UC of
of a high density
Method of laser resonance spectroscopy in the laser ion source firstly developed and used at IRIS facility in PNPI will be used.

## Slide 26
FISCO facility (FISsion COrrelations) – Detectors
(A) Detector of the fission neutrons multiplicity
(B) The multi-section detector of fission neutron and γ-quanta
Studies of the angular correlations of light charged particles in ternary fission induced by cold polarized neutrons (ROT, TRI and PNC effects).
Studies of the angular correlations in γ -quanta and neutrons emission in fission induced by polarized neutrons with resonance energies (ROT effect).
Study of the angular correlations in the prompt neutron emission in the spontaneous fission of 252Cf.
Measurements of the Fission Neutron Multiplicity Distribution in Spontaneous Fission and in Fission by Thermal and Low Energy Neutrons.
The fission fragment detector

## Slide 27
INAA setup (Instrumental Neutron Activation Analysis)
Automation of instrumental neutron activation analysis using a pneumatic transport unit. The reduced transport time of the sample and to avoid contact of personnel with radioactive samples.
The installation will allow determining the content of Li, B, N, O, F, Ne, Al, V, and Pb in samples by their short-lived isotopes and will increase the number of elements determined by neutron activation analysis. This opens up a unique opportunity to determine these elements in superhard and heat-resistant alloys on the content of which their properties depend, to study geological samples and biological objects.
Nuclear spectroscopic studies are supplemented by x-ray fluorescence analysis of the elemental composition of samples. Development of technology for the production of isotopes 75Se and 192Ir, which are used in the production of non-destructive gamma-ray flaw detectors. Development of technology for the production of radiopharmaceuticals 32P, 64Cu, 66.67Ga, 90Y.
General view of the pneumatic transport installation and container for irradiation.

## Slide 28
PROGRAS
General layout
of semiconductor gamma-ray spectrometers on the inclined channel of the PIK (b) reactor and experimental equipment:
1-neutron polarizer, 2-flipper, 3- collimator, 4 – trap, 5, 6 –radiation detectors.
A unique opportunity to identify and quantify light elements in (n,g) reactions, prompt gamma analysis, studies of nuclear reactions in gamma-gamma coincidences.
Hall of IEC
1
2
3
4
5, 6
Study the nucleus structure with (n,)-reaction by thermal neutron in (-) coincidence.
PROGRAS
INAA

## Slide 29: Thanks