## Slide 1: On the Normal conducting RF for muon collider
Alexej Grudiev (CERN)

## Slide 2: RF system for muon capture and cooling
Region | Length [m] | N of cavities | Frequencies [MHz] | Peak Gradient [MV/m] | Peak RF power [MW/cavity]
Buncher | 21 | 54 | 490 - 366 | 0 - 15 | 1.3
Rotator | 24 | 64 | 366 - 326 | 20 | 2.4
Initial Cooler | 126 | 360 | 325 | 25 | 3.7
Cooler 1 | 400 | 1605 | 325, 650 | 22, 30 | 
Bunch merge | 130 | 26 | 108 - 1950 | ~ 10 | 
Cooler 2 | 420 | 1746 | 325, 650 | 22, 30 | 
Final Cooling | 140 | 96 | 325 - 20 |  | 
Total | ~1300 | 3951 |  |  | ~4000 x ~3MW => ~12GW
It is a very large and complex RF system with high peak power
Summarized from:
David Neuffer
Chris Rogers

## Slide 3: RF cavities for muon cooling
Challenges:
High Gradient
High magnetic field
High radiation
Technology far from been common
---------------------
State of the art (not complete):
MICE 200 MHz RF module prototype: 4T, 10 MV/m, 1ms@1Hz
800 MHz beryllium cavity:
3T, 50 MV/m, 30us@10Hz
Gas filled RF cavity:
Small gap, 200 MHz, >50 MV/m

## Slide 4: R&D directions and test facility towards feasibility demonstration of muon cooling
Stage 1: High gradient RF test facility
  Frequency: 200 - 800 MHz
  Magnetic field: 0 - 5T, different field configurations
  Different materials: Cu, Be, Al, …
  Different temperatures: Cryogenic NC, HTS RF, …
  Different gases and pressure: 0 – few Bars
  Different designs
Stage 2: Prototype(s) for cooling test facility
  Design of realistic cavity prototypes: frequency, beam aperture, integration
  Parameters defined based on the results of Stage 1 and the (re-)design of the muon cooling complex (higher gradient,…)
  May include irradiation capability to check its impact on the performance
Stage 3: Muon cooling demonstrator

## Slide 5: Cryogenic operation of NC cavities
RF breakdown (BD) strength in high magnetic field depends on thermo-mechanical properties
Field emission induced pulsed heating model predicts (PRAB 23, 072001):
Cu
Local temperature rise
Threshold: (38K for Cu@300K)
Higher gradients require even higher RF power:
  V=const, G x 2 => P x 2
Low temperature reduce ohmic losses: P x 1/3 or even lower
Cu
Low temperature improves thermal and mechanical properties
=> Higher BD strength
RF technology challenges discussion, MC workshop, 2019 (cern.ch)
Cavities are already in the cryogenic environment of the SC solenoids

## Slide 6: HTS for RF applications
HTS coated conductor at 8 GHz
From: Teresa Puig – ICMAB. Developments of HTS Coated Conductors for the FCC-hh beam screen impedance mitigation
Cu RRR=100 @ 70 K
Cu RRR=100 @ 20 K
Frequency scaling HTS vs Cu at 9 T
Cu RRR=100 @ 300 K: 25 m

## Slide 7: Soldering of HTS coated conductors
T = 50 K, GHz
FCC Cu
CC 2
CC 4
CC 5
Standard sample
Soldered sample
Soldering mostly preserves properties
This could be used in a cavity made in sectors