## Slide 2: A Quick Introduction to PS-BGI
Swann Levasseur
CERN BE-BI-BL
Acknowledgements:
J. Storey, H. Sandberg

## Slide 3: PS-BGI – In a few words
What is it?
Proton Synchrotron Beam Gas Ionization Profile Monitor
Measures the transverse profile of a beam of particles (p+ or Ions)
Why do we need?
Make sure the beam is what we want it to be.

## Slide 4: PS-BGI – In a few words
Raw detector image (2D Projection of the beam)
Measured beam profile (1D integration of raw image)

## Slide 5: PS-BGI – In a few words
Timepix3 Hybrid Pixel Detector:
Hybrid: Combination of a pixelated sensor and readout chip.
Incoming ionizing radiation create e-/hole pair in the sensor.
The readout chip measures the charge deposited and digitize it.
  It measures Position (column and row), time of arrival and energy
Timepix3 Hybrid Pixel Detector
Hybrid Pixel Detector representation

## Slide 6: PS-BGI – In a few words
How does it work?
Beam traverse the instrument and ionizes the rest gas and creates electron ion pairs.
Assuming that the rest gas is homogeneously spread in the vacuum chamber, the distribution of the generated electron/ion pair is representative of the particle distribution in the beam.
A vertical electric and magnetic field direct the electrons to a detector.
The detector measures the position, time-of-arrival and energy of each electron.
The back-end computer, extract the beam profile from this information.
What is the working environment?
UHV around 10^-10 mBar
Mixed field ionizing radiation (1 to 10 kGy/yr)
  Access impossible most of the year (two/three opportunity/year)

## Slide 7: PS-BGI – How does it looks?
Cathode (-20kV)
Anode
(GND)
Flange
Support arms
Faraday cage
Detector opening/honeycomb

## Slide 8: PS-BGI – How does it looks?
Flexible Cables (2x) (data-in/out)
TPX3 Detector modules (4x)
(detect e-)
Cooling plate @ 6 °C
(keep detectors cool)
Low-voltage distribution
(power-in/out)

## Slide 9: PS-BGI – How does it looks?
Low-voltage distribution
(power-in/out)

## Slide 10: PS-BGI – How does it looks?
Detector module

## Slide 11: PS-BGI – How does it looks?
Detector module

## Slide 12: PS-BGI – How does it looks?
MkIII Detector

## Slide 13: PS-BGI – How does it looks?
MkIII Detector

## Slide 14: PS-BGI – How does it looks?
Full Instrument PS-BGIH

## Slide 15: PS-BGI – How does it looks?
MKII detector (older version)