## Slide 1: Relative Formation Probabilities for Fluoride and Oxyfluoride Anions of U, Np, Pu and Am in Accelerator Mass Spectrometry Measurements at VERA
Andreas Wiederin1
R. Golser1 , M. Kern1, K. Hain1, M. Martschini1, A. Sakaguchi2, P. Steier1, A. Yokoyama3
1University of Vienna, Austria 2University of Tsukuba, Japan 3Kanazawa University, Japan
Joint Annual Meeting of ÖPG and SPS 2021
Joint annual Meeting APS SPS Innsbruck 2021
Presenting author email: andreas.wiederin@univie.ac.at

## Slide 2: Why is this interesting? 237Np spike project
Second most abundant anthropogenic actinide in the environment?
Released by nuclear weapons tests and industry
Potential environmental tracer
    Long lived and highly mobile in water
Magill et al., Nucleonica GmbH, 2006
1

## Slide 3: Why is this interesting? 237Np spike project
Second most abundant anthropogenic actinide in the environment?
Released by nuclear weapons tests and industry
Potential environmental tracer
    Long lived and highly mobile in water
Challenging to measure in general environment:
  Decay counting: very large samples (T1/2!)
  MS: background from 238U, 235UH2
  AMS: Lack of isotopic spike hinders quantification
Magill et al., Nucleonica GmbH, 2006
1

## Slide 4: Why is this interesting? 237Np spike project
Second most abundant anthropogenic actinide in the environment?
Released by nuclear weapons tests and industry
Potential environmental tracer
    Long lived and highly mobile in water
Challenging to measure in general environment:
  Decay counting: very large samples (T1/2!)
  MS: background from 238U, 235UH2
  AMS: Lack of isotopic spike hinders quantification
    Different isotope of Np to add to sample for relative measurements
Severely understudied!
Magill et al., Nucleonica GmbH, 2006
1

## Slide 5: Why is this interesting? 237Np spike project
Plan: Develop isotopic spike for 237Np
  Joint Project: Universities of Vienna, Tsukuba and Kanazawa
  Current focus: 232Th(7Li,3n)236Np reaction
Magill et al., Nucleonica GmbH, 2006
2

## Slide 6: Why is this interesting? 237Np spike project
Plan: Develop isotopic spike for 237Np
  Joint Project: Universities of Vienna, Tsukuba and Kanazawa
  Current focus: 232Th(7Li,3n)236Np reaction
Problem: Isobaric interference from 236U
  Co-production in irradiation for spike production?
    Need a method to distinguish 236U and 236Np!
  236U in environmental samples
    U – Np Isobar separation necessary for 236Np spike
      ILIAMS?
Magill et al., Nucleonica GmbH, 2006
2

## Slide 7: Fluoride molecular anions of actinides
AMS: negative ions
  Actinides do not form sufficient atomic anions
Molecular anions
3

## Slide 8: Fluoride molecular anions of actinides
AMS: negative ions
  Actinides do not form sufficient atomic anions
Molecular anions
Fluoride molecular anions for actinides?
    [X.-L. Zhao et al., Nucl Instrum Methods Phys Res B 294 (2013), 356-360]
    [R.J. Cornett et al., Nucl Instrum Methods Phys Res B 361 (2015), 317-321]
3

## Slide 9: Fluoride molecular anions of actinides
AMS: negative ions
  Actinides do not form sufficient atomic anions
Molecular anions
Fluoride molecular anions for actinides?
    [X.-L. Zhao et al., Nucl Instrum Methods Phys Res B 294 (2013), 356-360]
    [R.J. Cornett et al., Nucl Instrum Methods Phys Res B 361 (2015), 317-321]
  Research at VERA is focused on mixing oxide materials in Fe2O3 with PbF2
    In situ fluoridization inside the Cs-sputter ion source
    [M. Kern, this meeting]
3

## Slide 10
The relative formation probabilities for a range of (oxy-)fluoride molecular anions of U, Np, Pu and Am have been systematically investigated
An stands for U, Np, Pu or Am
AnF5– | AnF4O– | AnF3O2–
AnF3O– | AnF2O2– | AnF4–
Fluoride molecular anions of actinides
4

## Slide 11
The relative formation probabilities for a range of (oxy-)fluoride molecular anions of U, Np, Pu and Am have been systematically investigated
An stands for U, Np, Pu or Am
Isobaric contaminations can be monitored with this data
  First application:236U in prospective 236Np spike material
UF4– , NpF4– candidates for U – Np separation with ILIAMS
AnF5– | AnF4O– | AnF3O2–
AnF3O– | AnF2O2– | AnF4–
Fluoride molecular anions of actinides
4

## Slide 12: Materials and Methods

## Slide 13: Sample preparation
Reference material
  236U, 237Np, 242Pu, 243Am (3x108 at) in nitric sol.
  Dried with 300µg Fe
  Ignition (800°C)
  Mixed with PbF2 (1:9 mass ratio)
  Required in every beamtime
5

## Slide 14: Sample preparation
Reference material
  236U, 237Np, 242Pu, 243Am (3x108 at) in nitric sol.
  Dried with 300µg Fe
  Ignition (800°C)
  Mixed with PbF2 (1:9 mass ratio)
  Required in every beamtime
Material from 232Th(7Li,3n)236Np irradiation
  RIKEN Nishina Center for Accelerator Based Science
    Chemical purification at University of Tsukuba
  Previously measured at VERA in oxide form
    Residue mixed with PbF2 for isobar analysis
5

## Slide 15: Measurements at VERA
+1.7 MV
6
AnFmOn1- selected by low energy mass spectrometer

## Slide 16: Measurements at VERA
+1.7 MV
6
AnFmOn1- selected by low energy mass spectrometer
He-stripping destroys molecules

## Slide 17: Measurements at VERA
+1.7 MV
6
AnFmOn1- selected by low energy mass spectrometer
He-stripping destroys molecules
High energy mass spectrometer selects An3+

## Slide 18: Measurements at VERA
+1.7 MV
6
AnFmOn1- selected by low energy mass spectrometer
He-stripping destroys molecules
High energy mass spectrometer selects An3+
An3+ detected in Bragg type ionization chamber

## Slide 19: Measurements at VERA
AnFmOn1- selected by low energy mass spectrometer
He-stripping destroys molecules
High energy mass spectrometer selects An3+
An3+ detected in Bragg type ionization chamber
24 machine setups with masses 306u to 338u measured on each target
  Only electrostatic components were adjusted
    magnetic rigidity constant for all setups
+1.7 MV
6

## Slide 20: Results
All results are stated in the form of AnFmOn/AnF5 ratios

## Slide 21: Formation distribution: reference materials
  Characteristic UFmOn– /UF5– ratios
7

## Slide 22
  Characteristic AnFmOn– /AnF5– ratios for U, Np
7
Formation distribution: reference materials

## Slide 23: Formation distribution: reference materials
  Characteristic AnFmOn– /AnF5– ratios for U, Np, Pu
7

## Slide 24: Formation distribution: reference materials
  Characteristic AnFmOn– /AnF5– ratios for U, Np, Pu, Am
7

## Slide 25: Formation distribution: reference materials
  Characteristic AnFmOn– /AnF5– ratios for U, Np, Pu, Am
    Isobaric contaminations shift formation ratios
    AnF4–/AnF5–!
7

## Slide 26: Formation distribution: reference materials
7
  Characteristic AnFmOn– /AnF5– ratios for U, Np, Pu, Am
    Isobaric contaminations shift formation ratios
    AnF4–/AnF5–!
  UF4 –, NpF4 – for ILIAMS?
    Hypothesis: correlation anion formation ratio to e– detachment energy?
    Suppression of U vs Np by one order of magnitude in ion source

## Slide 27: Analysis of irradiated samples
Ratios shift between beamtimes, separation for AnF44– remains stable
  reference materials for every beamtime
8

## Slide 28: Analysis of irradiated samples
Ratios shift between beamtimes, separation for AnF4–/AnF5– is stable
  Reference materials for every beamtime
8

## Slide 29: Analysis of irradiated samples
Ratios shift between beamtimes, separation for AnF4–/AnF5– is stable
  Reference materials for every beamtime
QC for measurement: m237 on irradiated targets (~ 10% of m236)
    Co-produced 237Np!
  m237 AnF4–/AnF5– ratio compatible with reference Np (1σ)
8

## Slide 30: Analysis of irradiated samples
9
  m236 AnF4–/AnF5– ratio is compatible with ref. Np (1σ)
    Isobaric 236U interference is negligible

## Slide 31: Analysis of irradiated samples
9
  m236 AnF4–/AnF5– ratio is compatible with ref. Np (1σ)
    Isobaric 236U interference is negligible
  The production and separation of 236Np was successful

## Slide 32: Conclusion and outlook
The relative formation probabilities for
are characteristic for U, Np, Pu and Am
  This distribution can be used to identify isobaric contaminations
This method could show that 236Np was successfully produced and chemically separated from 236U
  Isotopic spike for environmental 237Np?
The next steps:
  ILIAMS separation of U and Np
  Maximize NpF4– formation
AnF5– | AnF4O– | AnF3O2–
AnF3O– | AnF2O2– | AnF4–
10

## Slide 33: Appendix

## Slide 34: How stable are the ratios with increasing duration of the measurement?

## Slide 35
Ratios change significantly after the first two sequences
All targets should be measured for 2 sequences (~2.5h) for consistent results
How stable are the ratios with increasing duration of the measurement?

## Slide 36: How stable are the ratios for different mixing rates with PbF2?
Reducing mixing ratios to 1:4.5 increases lower fluorides/oyxfluorides
    Similar to long measurement duration
    Fluorine supply affects formation probablilities
Increasing PbF2 further (1:18) has no significant effect

## Slide 37: How stable are the ratios between Beamtimes
AnFmOn–/AnF5– ratios change between beamtimes
  Ion source conditions?
  Tuning?
Separation for AnF4/AnF5 remains stable
  Method is robust against tuning variations!
Reference samples have to be included in every measurement