## Slide 1
“Consideration on optimal dipole length from the point of view of optics”
Jérémie Bauche, Antoine Chance, Barbara Dalena, Roberto Kersevan, Bastian Harer, Mike Koratzinos, Attilio Milanese, Katsunobu Oide, Dmitry Shatilov, Frank Zimmermann
FCC technologies meeting, 26 March 2021

## Slide 2
FCC-ee CDR baseline parameters
parameter | Z |  | WW | ZH |  | LEP2
energy/beam [GeV] | 45.6 | 80 |  | 120 | 182.5 | 105
bunches/beam | 16640 | 2000 |  | 328 | 48 | 4
beam current [mA] | 1390 | 147 |  | 29 | 5.4 | 3
luminosity/IP x 1034 cm-2s-1 | 230 | 28 |  | 8.5 | 1.6 | 0.0012
energy loss/turn [GeV] | 0.036 | 0.34 |  | 1.72 | 9.2 | 3.34
synchrotron power [MW] | 100 |  |  |  |  | 22
RF voltage [GV] | 0.1 | 0.75 |  | 2.0 | 4.0 + 6.9 | 3.5
rms bunch length (SR,+BS) [mm] | 3.5, 12 | 3.0, 6.0 |  | 3.2, 5.3 | 2.0, 2.5 | 12, 12
rms emittance ex,y [nm, pm] | 0.27, 1 | 0.84, 1.7 |  | 0.63, 1.3 | 1.5, 2.9 | 22, 250
arc phase advance per FODO cell x/y recent proposal | 60/60 45/45 | 60/60 45/45 |  | 90/90 | 90/90 | e.g. 102/90
parameter | Z |  | WW | ZH |  | LEP2
energy/beam [GeV] | 45.6 | 80 |  | 120 | 182.5 | 105
bunches/beam | 16640 | 2000 |  | 328 | 48 | 4
beam current [mA] | 1390 | 147 |  | 29 | 5.4 | 3
luminosity/IP x 1034 cm-2s-1 | 230 | 28 |  | 8.5 | 1.6 | 0.0012
energy loss/turn [GeV] | 0.036 | 0.34 |  | 1.72 | 9.2 | 3.34
synchrotron power [MW] | 100 |  |  |  |  | 22
RF voltage [GV] | 0.1 | 0.75 |  | 2.0 | 4.0 + 6.9 | 3.5
rms bunch length (SR,+BS) [mm] | 3.5, 12 | 3.0, 6.0 |  | 3.2, 5.3 | 2.0, 2.5 | 12, 12
rms emittance ex,y [nm, pm] | 0.27, 1 | 0.84, 1.7 |  | 0.63, 1.3 | 1.5, 2.9 | 22, 250
arc phase advance per FODO cell x/y recent proposal | 60/60 45/45 | 60/60 45/45 |  | 90/90 | 90/90 | e.g. 102/90
new proposal would impact the sextupoles

## Slide 3
arc supercell for Z+W and for ZH+top operation
CDR
K. Oide

## Slide 4
three types of short straight sections
All sextupole pairs are independently powered. There are 584 and 416 independent pairs per half ring for 90◦/90◦ and 60◦/60◦, respectively.
CDR
K. Oide
dipole length [m] | #units
21.232 | 1152
22.732 | 492
24.432 | 1256
half cell length
constant
27.9324 m
magnetic length

## Slide 5
parameters of the main arc dipole magnets
CDR
A. Milanese
K. Oide

## Slide 6
cross section of collider arc dipole magnet
CDR
A. Milanese

## Slide 7
prototype collider arc dipole
two busbars
(plus shielding)
and two plates
-
could be assembled in the tunnel
access “gap” needed? –
for photon stops (every 4-5 m), water cooling, bellows, flanges, vacuum equipment etc.?
A. Milanese et al.

## Slide 8
impact of equal & shorter dipoles on performance
example:
suppose we replace all dipoles by 3 dipoles of 6.70 m length
each with 55 cm separation between dipoles (total length 21.2 m)
→ we lose the following dipole length:
1152x(21.232-20.10)+492x(22.732-20.10)+1256x(24.432-20.10) m
=8040 m = 8.04 km
out of a total of
1152x(21.232)+492x(22.732)+1256x(24.432) m =66330 m
which is 12%
→ 12% more energy loss per turn, 12% higher RF voltage (expensive at the ttbar),
12% less luminosity, 12% higher field, 12% more dipole magnet electric power

## Slide 9
full energy booster
dipole length [m] | #units
11.1 | 5176
CDR
B. Harer
A. Chance
B. Dalena
field at injection 0.006 T
peak field 0.058 T
two optics for the high-energy booster similar to the collider: 60°/60° for Z & WW operation. 90°/90° for ZH & ttbar operation
The booster arc FODO cells are a bit shorter than in the collider: 54 m versus 55.865 m.
Smaller equilibrium emittance: 1.3 nm against 1.48 nm at 182.5 GeV
0.27
magnetic length

## Slide 10
conclusions
filling available arc space with dipoles gives maximum performance
long dipoles, ~22-24 m, could be installed in situ without gap if no other constraints
if there are other constraints, what are these – photon stops, cooling bellows? flanges…? which locations and gaps are required for these? which maximum continuous dipole length is allowed?
it might be advantageous to make the booster cell as long as collider cell; however, this would remove the emittance margin