## Slide 1: PSI Muon Facilities
Daniela Kiselev :: ASA/GFA :: Paul Scherrer Institut
Workshop on Muon Collider test opportunities, 24.3.2021

## Slide 2
Accelerator Facilities at PSI
p-Therapy
250MeV, <1A
Swiss Light Source
2.4GeV, 400mA
High Intensity Proton Accelerator
590 MeV, max. 2.4mA
SWISSFEL
5.8 GeV
Central control room
SINQ Spallation Neutron Source
UCN

## Slide 3
The PSI Proton Accelerator Facilities
HIPA (High Intensity Proton Accelerator)
- CW (50.63 MHz), 590 MeV,
- up to 2.4 mA(1.44 MW)
2 meson production targets
7 secondary beam lines
- SINQ and UCN spallation source
Page 3
PROSCAN (Proton therapy): since 2007
Comet: superconducting cyclotron
CW, 250 MeV, up to 1 mA protons
medical treatment:
3 Gantries, 1 Eye Cancer Treatment Station
Irradiation Station: PIF
PIF
Secondary
Beam Lines
hot cell HIPA
Gantry 1, 2 3
Target M
Comet
Target E
Spallation neutron source SINQ
Injector II
Injector I
ECR-source &
Cockroft-Walton
OPTIS
Ring
UCN

## Slide 4
Challenges for meson production targets
Power deposition:
at 2.4 mA, 590 MeV protons ~ 50 kW on Target E
 cooling
 high temperature resistant material
 thermal stress
Radiation damage:
 embrittlement
 deformation (also due to heating)
 loss of conductivity
Approach:
distribute power:
rotating wheel with 1 Hz  needs bearings
cooling by radiation:
- independent of conductivity
- local shielding (Cu) is cooled by water
p-beam
Target E

## Slide 5
Drive shaft
Motor
Motor:
2.5 m above the beam line
Functioning is not affected by irradiation
life time ~ 5 – 8 years
Target
wheel
Water
cooling
Local
shielding
deep groove
ball bearings
angular contact
ball bearings
140 oC
50 oC
Challenges for meson production targets
Wheel deformation reduced by
- polycrystalline graphite  isotropic properties
- slits in wheel rim für thermal expansion
- spokes: allows thermal expansion of target cone
hollow to avoid high temperature at bearing
12 segments with 1 mm slit
1700 K
Notes: deep groove ball bearing: Rillenkugellager: Die vorderen sind Radiallager, können wenig axiale Last aufnehmen
angular contact bearings: Schrägkugellager: Kugeln liegen um 23o geneigt, nehmen axiale und radiale Last auf, wirken noch etwas zentrierend
deep groove ball thrust bearing: Axial-Rillenkugellager, für Axiallast, haben wir nicht. Man könnte ein Schrägkugellager durch ein Axial- und Radiallager ersetzen.

## Slide 6
Critical components: Bearings
No grease as lubrication!  brittle due to hard irradiation
so called radiation hard grease does not help  proofed
Balls Si3N4, GMN, Germany
Coating: MoS2, Ag for ring & cage
1 -2 x exchange/year
 Graphite wheel lasts much longer: ~ 4Years
(39 Ah record)
Ball bearings:
in use:
Shun Makimura
(JPARC)
in test:
Balls stainless steel + WS2 blocks
Koyo, Japan
Test (without radiation): > 420 days
Test in beam at PSI planned this year
Notes: Dosis an Target E: 10000 Gy/h bei 1 mA (nach Gerd’s Abschätzung)

## Slide 7: Exchange of the high-activated components
Exchange flask:
45 t, shielded with 40 cm steel
remotely operated
Working platform:
~ 2m above beamline, shielded with steel
Accessible after removing 3 – 4 m of concrete
"Bridge":
contains contamination protection
door to close lifting hole
sticks for positioning of the flask

## Slide 8
Transport to hotcell PSI West (ATEC)
Exchange of bearings with manipulator
View into hotcell of ATEC
Hub
Remote handling necessary: up to 3 Sv/h
Handing over from flask to hotcell via sluice
Usually only the hub needs to be exchanged
 not much radioactive waste (up to 200 mSv/h)

## Slide 9
μ/π Secondary Beam Lines
Seite 9
Target E
p-Beam
Spin rotator
πE1
μE1
μE4
πM1
πM3
πE5
Target M
πE3
Target M:
πM1: 100-500 MeV/c Pions
πM3: 28 MeV/c Surface Muons
Target E:
πE1: 10 - 500 MeV/c High Intensity Pions und Muons μE1: Polarized Muon Beam
πE3: 28MeV/c Surface polarized Muons
μE4: 30 - 100 MeV/c High Intensity Polarized Muons πE5: 10 - 120 MeV/c High Intensity Muons

## Slide 10: Overview of Secondary Beam Lines
 | PiM1 | PiE5 | PiE1 | PiE3 | PiM3 | MuE4 | MuE1
Target | M | E | E | E | M | E | E
Particle Type | π/e/μ/p | μ/π | π/μ/p | μ, p | μ | μ | μ (cloud)
Momentum Range | 10-500 MeV/c (max 300 MeV/c for positive particles) | 20-120 MeV/c | 10-500 MeV/c ustream ASK 10-120 MeV/c downstream ASK | μ:10-40 MeV/c p: 50 – 250 MeV/c | 10-40 MeV/c | 10-40 MeV/c | 60-120 MeV/c
Typical Momentum | 15-300 MeV/c | 28-85 MeV/c | PP: 10-50 MeV/c μSR: 28 MeV/c Irrad: 300 MeV/c | 28 MeV/c | 28 MeV/c | 28 MeV/c | 60-125 MeV/c
Max Rate [mA-1 s-1] | @ 350 MeV/c π+::2x108 | @120MeV/c p+:2x1010 m+:5x108 | @ 300 MeV/c p+:4x109 | m+:3x107 p+ :2x109 @ 170 MeV/c | m+:3x106 | m+:4x108 | @ 300 MeV/c m-:6x107
Typical Use | Particle Physics Test Experiments, Detector/Material Irradiation | Particle Physics Experiments | μSR Dolly Particle Physics Experiment, Detector Irrad. | μSR HAL 9500 (High Field) | μSR GPS and LTF | μSR LEM Facility | μSR GPD Facility
Particle physics: (CHRISP facility)
μSR (Muon Spin Rotation),
SmS (Swiss Muon Source)

## Slide 11: PiM1 Beamline
Often used as Test Beam line at PSI
e/μ/π/p momentum range 20 – 500 MeV/c
Particle separation by energy loss in material & momentum selection
Momentum < 115 MeV/c: dominated by e
115 - 280 MeV/c Beam dominated by μ/π
> 280 MeV/c Beam dominated by π/p
Measured Particle Rates
(R.A. Schumacher, U. Sennhauser, 1987)
Beam scanner
p- acceptance: 2.9 %
p-resolution: 0.1 %
Size at Target: hor: 15 mm,
vert: 10 mm
Divergence : hor: 35 mrad
vert: 75 mrad

## Slide 12: PiE1 Beamline
High intensity μ/π beam line at TE
< 120 MeV/c: Beam dominated by e/μ
120 - 280 MeV/c Beam dominated by μ/π
> 280 MeV/c Beam dominated by π/p
Momentum acceptance (1σ): 4%
Max. particle flux: 4x109 π+ @ 300 MeV/c
Beam spot (RMS): 7mm (x), 4mm (y)
Wien Filter
SpinRot (45° @ 28 MeV/c)
ASK Dipole
Dolly (µSR)
Particle Physics
Pion Irradiation
Mode A
Mode B
surface m
ASK
at 10°forward angle

## Slide 13: PiE5 Overview
Fixed Part of the Beam Line
Experimental Area
2. beam line
AST
Low energy (10-120 MeV/c), high intensity μ/π beam line at TE (175° backward angle)
Momentum acceptance (1σ): 5%
Max. particle flux: 6x109 π+ @ 120 MeV/c
Spot size after triplet I (RMS): 8mm (x), 10mm (y)
High neutron background (150 n/mA/s/cm2
Wien Filter (or Muon Spin Rotator)
XY Beam Scanner

## Slide 14: mucool: compression of m phase space
Aim: to improve the quality of the m beam
Longitudinal and transverse phase space reduction of a μ+ beam
by a factor of 1010 with 10−3 efficiency.
Transverse compression:
vertically 14 mm was reduced to a 0.25 mm size (rms) within 3.5 μs.
lower density He
higher density He
~5 mbar He
5 T magnetic field
E x B
Ex = Ey= 1kV/cm
Due to He density gradient m collide
with He less on the top
than on the bottom.
Energy loss compensated
by electric field
predominately drift in ExB direction
A. Antognini et al (muCool Collaboration), Phys. Rev. Lett. 125, 164802 (2020)
20 cm long muon stop distribution
reduced to a sub-mm extent within 2 μs
Longitudinal compression:
Belosevic et al, (muCool Collaboration),
Eur. Phys. J. C 79, 430 (2019)
E = 50V/cm
12.5 MeV/c
muons
muon drift
Contacts: A. Antognini, K. Kirch, A. Knecht, A. Papa

## Slide 15: πE3 Extension for the High-Field μSR Facility (2011)
Beam Line
Beam size at sample: σx,y ≈ 15mm
Large beam transmission
Momentum Bite at sample:
Δp/p ≈ 2%
  ‏ Worldwide unique 9.5T External Field
  Sample extremely small
Material T range: 0.02 K - 320K
Transverse beam polarization
at the sample material:
 2 Spin rotators required!
surface
muons
Sample
High Field μSR (Muon Spin Rotation/Relaxation/Resonance)

## Slide 16: Possibilities for testing at PSI
Detector tests
- convenient in PM1 (test area)
- beam scanner available
Test of diagnostics
mucool: a cooling method at low energy
2027: Likely no beam because of HIMB (High Intense Muon Beam)
 Redesign of PiM1
 Use for particle physics program
No possibility of testing the target with high intense proton beam

## Slide 17: HIMB in short
TgM (5 mm)  TgM* (20 mm)
Old type  Slanted type
PiM3
PiM1
22.5o
22.5o
2 mm
present TgM
Slanted target type
 Tested
successfully at
Target E
5-8o
Large acceptance due to large capture solenoids close to target
Central field of solenoids ~0.35 T
Field at target ~0.1 T
Muon/pion beamline out of
large diameter solenoids
Factor ~100 more
Surface muons
A. Knecht

## Slide 18
Present Target-M
P-BEAM
Target M:
Mean diameter: 320 mm
Target thickness: 5.2 mm
Target width: 20 mm
Graphite density: 1.8 g/cm3
Beam loss: 1.6 %
Power deposition: 2.4 kW/mA
Temperature: 1100 K
Irradiation damage: 0.1 dpa/Ah
Rotational Speed: 1 Hz
Current limit: 5 mA
Life time: up to several years
up to ~ 60 Ah ~ 6 DPA
.
Improved design
(2013)
Notes: beam loss target: 0.5 %
collimators/region: 1.6 %

## Slide 19: Slanted/Standard (for TargetE 40 mm)
Seite 19
Slab Tg E (standard)
Slanted TgE
TgE
+30%
+30%
+60%
+35%
Significant increase of
surface muon rate
Simulation confirmed
by measurement (2019):
40 – 50 % increase

## Slide 20: Preliminary layout
MuH3 (PiM3)
MuH2
(PiM1)
water cooling &
cryogenics
Spinrotator
Water cooling cycle and liquid He filling platform have to be removed.
Geant4, Transport, COSY Infinity
BDSIM, Turtle, MCNP, ZGOUBI

## Slide 21
Summary
Introduction to the PSI High Intensity Proton Accelerator (HIPA)
Extraction from the Ring Cyclotron
Beam transfer to the meson production targets M/E and SINQ spallation source
Beam diagnostics for setup & optimization
Feasibility study of beam rotation for SINQ
Beam switchover to the UCN source
Conclusion
Page 21
Challenges for the muon target at 50 kW:
- Cooling, Deformation, Bearings still need to be improved!
Some test opportunities at PiM1: pions,muons, electrons, (protons)
Feasibility study HIMB for Swiss Roadmap
100 x more surface muons

## Slide 22: PiM1 beam fractions

## Slide 23: HiMB Slanted Target Tests
HiMB 40 mm slanted target installed on November 25
Muon beam rates:
30-60% increase in surface muon rate expected
First measurements confirm this increase for μE4, πE5, πE3 and πE1 (μE1 not affected as it relies on pion collection) 40 mm slanted target as good as 60 mm standard target!
Proton beam impact:
Setup of proton beam well under control
Increased safety margins confirmed
Future:
To be seen: Impact of higher thermal stress on long term stability of target wheel
We are looking forward to continue this work within the recently CROSS-funded HiMB study to increase surface muon rates by almost two orders to 1010 μ+/s!
TgE
+30%
+30%
+60%
+35%
slanted
standard

## Slide 24: HiMB Slanted Target Design
protons
protons
Standard 40 mm TgE
Slanted 40 mm TgE
Involved people:
NUM: P.-R. Kettle, A. Knecht, A. Papa, T. Rostomyan, P. Schwendimann
GFA: P. Baumann, S. Joray, D. Kiselev, D. Laube, R. Sobbia, D. Reggiani
Goals:
Change of geometry of TgE to increase surface muon rates for all connected beam lines
Increase safety margin for “missing” TgE with the proton beam

## Slide 25: Transport of 2. target insert to beamline
open
closed
parking lot
sluice to hotcell
To save time:
Spare Target E insert is taken out from the parking lot
Exchange flask on parking lot
At the same time:
Reparing of the insert from beamline in hotcell

## Slide 26: Design of the hotcell ATEC
ATEC: 2. service cell in 2019
wall in between can be opened vertically
Advantage:
in case of unavoidable access to one service cell (in case of failure),
radioactive components are moved to the other service cell.
less personal dose rate during cleaning:
drums with rad. waste can be moved temporarly to the other service cell.
2. Service cell
1. Service cell
Sluice in between
Sluice for Target E
Room for personal
Sluice pulled up by external crane
Moved by
ATEC crane

## Slide 27
Standard equipment of hotcell ATEC
6 high-resolution cameras/service cell
1 power manipulator/
service cell
"cold" hand
in control room
"hot" hand
in service cell
for wall shielding
+ 1 leadglass window
+ 1 dosimeter
+ a trolley to move things around
(up to 60 t)
+ 1 crane/cell
movable over 2 service cells
(important, if 1 crane fails)
Grip
for camera

## Slide 28
Meson production targets: Target E and Target M
Production of muons:
Surface muons:
produced from pion decay at rest at the
surface of the target (d < 1 mm)
p+
m+
n
- almost monochromatic:
max. at 28 MeV/c (= 3.7 MeV)
- 100% polarized
(spin in opposite direction to momentum)
in reality: 90 – 95 % polarization due to
pion decays in flight
World’s highest intensity surface muon beams > 108 µ/s
590 MeV
Cloud muons: decay of pions in flight
Low energy muons (LEM): 0.5 -30 keV
moderated by a cryogenic target
Besides this, there are pions, positrons (and sometimes protons)
Notes: surface muons are 100 % polarized (if the neutrino has no mass(!)). The point is that I had the real muon beam in mind. Here one has contributions from muons, which originate from a pion decay in flight. The polarization of the muon beam at the experimental stations is 90-95% as I know from Thomas Prokscha.
E=0.1 - 4 MeV energy distribution of surface muons
range width in matter ~180 mg/cm2
LEM: Einfang von e, muonium