## Slide 1: RF R&D for muon collider needs and opportunities
Alexej Grudiev (CERN)
25/02/2021
Workshop on Muon collider testing opportunities

## Slide 2: Outline
Muon collider layout and RF
  MAP scheme: proton driven muon source
  LEMMA scheme: positron driven muon source
RF system for proton driver
RF system for positron driver
RF system for muon cooling
RF system for acceleration and collider

## Slide 3: Muon Colliders and RF systems
Proton driven Muon Collider Concept (MAP collaboration)
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
Positron driven Muon Collider concept (LEMMA)
22 GeV
RF
RF
RF
RF
RF
RF
Muon cooling
Acceleration and collider rings
Positron Driver

## Slide 4
Challenges:
Few MW beam power
….
---------------------------------------------------------
State of the art RF technology (SNS, ESS, SPL, …)
Required RF Test facility for feasibility demonstration
NO
SPL@CERN
RF
RF
RF
RF

## Slide 5
Challenges:
Positron production
Target
Muon accumulation and merging
….
----------------------------------
State of the art RF technology for electron positron linacs:
Normal conducting: S-, C-band (LCWS, SwissFEL,…)
Superconducting: L-band (XFEL, ILC,…)
Required RF Test facility for feasibility demonstration
NO
Positron Driver

## Slide 6: RF system for muon capture and cooling
Region | Length [m] | N of cavities | Frequencies [MHz] | Peak Gradient [MV/m] | Peak RF power [MW/cav.]
Buncher | 21 | 54 | 490 - 366 | 0 - 15 | 1.3
Rotator | 24 | 64 | 366 – 326 | 20 | 2.4
Initial Cooler | 126 | 360 | 325 | 25 | 3.7
Cooler 1 | 400 | 1605 | 325, 650 | 22, 30 | 
Bunch merge | 130 | 26 | 108 - 1950 | ~ 10 | 
Cooler 2 | 420 | 1746 | 325, 650 | 22, 30 | 
Final Cooling | 140 | 96 | 325 - 20 |  | 
Total | ~1300 | 3951 |  |  | => ~12GW
It is a very large and complex RF system with high peak power
Very high bunch charge: (40->4)e12 => Collective effects (?)
Summarized from:
David Neuffer
Chris Rogers

## Slide 7: RF cavities for muon cooling
Challenges:
High Gradient
High magnetic field
High radiation
Technology far from been common
---------------------
State of the art :
MICE 200 MHz RF module prototype: 4T, 10 MV/m, 1ms@1Hz
800 MHz beryllium RF cavity:
3T, >50 MV/m, 30us@10Hz
800 MHz Gas filled RF cavity:
Small gap, 3T, >50 MV/m
PRAB23, 072001 (2020)
PRAB19, 062004 (2016)

## Slide 8: R&D directions and test facilities
High gradient RF test facility with magnetic field up to ~10T (NO BEAM)
Stage 1: Test cavities for technology development
  Frequency: 200 - 800 MHz
  Magnetic field: 0 - 10T, different field configurations
  Different materials: Cu, Be, Al, …
  Different temperatures: 300K -> 70K ->…
  Different gases and pressure
Stage 2: Prototype(s) for muon cooling test facility
  Design of realistic cavity prototypes: frequency, beam aperture, integration
  Parameters defined based on the results of Stage 1 and the design of the muon cooling test facility
  Validation of high gradient in magnetic field performance
Muon cooling test facility
  Validates performance with the beam
Required RF Test facility for feasibility demonstration
YES

## Slide 9: What kind of facility we need
Magnet
RF modulator
RF power source
RF cavity
RF infrastructure
Power converter
Superconducting magnet infrastructure
Cryogenics

## Slide 10: Proposal mentioned by Johannes Bernhard
proposal_rf.dvi (inspirehep.net)
Proposal might be reconsidered
RF must be brought to the magnet
Cost estimate 2010: ~0.5MCHF

## Slide 11: RF test infrastructure at CERN: an example CERN 3 MeV test stand with L4-RFQ RF station
Commissioned in 2014
L4-RFQ 352 MHz fed by
LEP klystron 1.2 MW
Dismounted after
L4-RFQ Spare project – a new project initiated in 2020
Short-term goals:
  Construct a spare copy of L4-RFQ (2021 – 2022)
  Commission new RFQ with RF and beam in reinstalled 3 MeV test stand (2022 – 2023)
  Make L4-RFQ spare available for replacement in L4
Long-term goals: Develop a new RFQ with better expected performance in terms of
  beam acceptance
  resilience to RF breakdowns under H- irradiation
There is a potential for synergies:
  High gradient under irradiation (p, H-)
  Different material (Cu, CuCrZr, CuBe, Ta, Nb, Ti6Al4V)
  Resources, infrastructure
NO MAGNET, NO CRYOGENICS
NO RADIATION SCHELDING
CERN-ACC-2013-0259.pdf

## Slide 12: Acceleration
Limited muon lifetime requires highest possible acceleration rate
Although the rate is defined mainly by the magnets ramping rate, the SRF must follow with required (very high) voltage
Small number of turns (~100) for very high collision energy ~10 TeV requires very high voltage: ~100 GV
It operates in quasi pulsed mode;
  RF is on only during acceleration (~ 10 ms)
  Transients
Longitudinal bunch compression/manipulation require additional voltage
Highest gradient for ‘compact’ RF system

## Slide 13: Acceleration (cont.)
Very large bunch charge:
  In collider ring: 2x1012
  In accelerators: (4->2)x1012
Short bunch length: 1 mm
Cause strong collective effects which must be mitigated
  Large Aperture
  Highest possible gradient
  Novel designs
FCC-ee
0.2
2.4
Single bunch beam loading (energy spread):
Energy spread ~ Loss factor x Bunch charge

## Slide 14: R&D directions for SRF for muon acceleration
Highest possible gradient
  Pulsed operation of ~0.1ms (LA) -> ~10ms (RCS) may help
Large aperture, low loss factor
Design of the cavities combining the above (contradicting) points must be driven by
  High gradient considerations
  Longitudinal beam dynamic requirements
  Overall design of the RF system
  Efficiency and Cost
The design might need (must have) high gradient validation
Required RF Test facility for feasibility demonstration
MAYBE (YES)

## Slide 15: Acknowledgements
I would like to acknowledge usage of material from:
  MAP collaboration: Muon Accelerator Program
  International Muon Collider Collaboration: Accelerator Design
Thank you !

## Slide 16: Spare slides

## Slide 17: Cryogenic operation of NC cavities
RF breakdown (BD) strength in high magnetic field depends on thermo-mechanical properties
Field emission induced pulsed heating model predicts (PRAB 23, 072001):
Cu
Local temperature rise
Threshold: (38K for Cu@300K)
Higher gradients require even higher RF power:
  V=const, G x 2 => P x 2
Low temperature reduce ohmic losses: P x 1/3 or even lower
Cu
Low temperature improves thermal and mechanical properties
=> Higher BD strength
RF technology challenges discussion, MC workshop, 2019 (cern.ch)
Cavities are already in the cryogenic environment of the SC solenoids

## Slide 18: HTS for RF applications
HTS coated conductor at 8 GHz
From: Teresa Puig – ICMAB. Developments of HTS Coated Conductors for the FCC-hh beam screen impedance mitigation
Cu RRR=100 @ 70 K
Cu RRR=100 @ 20 K
Frequency scaling HTS vs Cu at 9 T
Cu RRR=100 @ 300 K: 25 m

## Slide 19: Soldering of HTS coated conductors
T = 50 K, GHz
FCC Cu
CC 2
CC 4
CC 5
Standard sample
Soldered sample
Soldering mostly preserves properties
This could be used in a cavity made in sectors

## Slide 20: Initial acceleration
Limited muon lifetime requires highest possible accelerating gradient to reach higher energies
Large emittance require large acceptance
  Additional voltage
  Low frequency
  Large aperture
Very large bunch charge: ~5x1012 causes collective effects which must be addressed
Transmission and decay beam losses
Strong focusing magnets with large apertures
  Stray magnetic fields
  Low filling factor
  Cryogenic NC RF might help in the linac