CZT implementations in C and python
and python performance
BLonD Meeting
M. Vadai

---
Recap on CTA
- Previous presentation with math and examples (also CZT): https://indico.cern.ch/event/996624/
- CTA: chirp transform algorithm. Calculates the Fourier transform with arbitrary start and stop frequencies on the unit circle and an equal spacing between them.
- Usual calculation (1960s algorithm) ~ 2xFFT + 1xIFFT.
- Expectation on run time: computationally more efficient than the FFT when the zoom is larger than roughly 3-4 compared to the equivalently padded FFT.

---
Illustration
- 75/128 and 78.5/128 frequency sinusoids with 1 and ¾ amplitude added. Signal length: 256 samples.
- Hanning window + FFT.
- CTA calculated for the 256(+50) point signal. ~6x resolution.
- Calculating an only two point CTA would have been sufficient in this example.
\omega_0
\Delta \omega
\times e^{-j \frac{1}{2} \frac{2\pi n}{256}}

---
Recap on CZT
- CZT: calculates a more general transform than Fourier with arbitrary start and stop frequencies. The transform operates along a spiral contour in the z plane vs the circle arc of the CTA.
- Usual calculation ~ 2xFFT + 1xIFFT.
- New since 2019: there is an efficient inverse N log N, potentially improving on the 3-4x limitation. Efficient implementations are not really available yet.

---
Use cases
- Astronomy: long acquired data, but only certain parts are interesting. Sometimes can be similar to our use cases.
- The original 1960s CZT was used in CCD sensors with applications in space and astronomy.
- Same thing seems to be happening now with the inverse, just for data analysis in astronomy.

---
Implementations in python
- A summary: https://gist.github.com/endolith/2783807
- Scipy: https://github.com/scipy/scipy/issues/4288
- The new inverse computation is implemented: https://pypi.org/project/czt/ or the same on github: https://github.com/garrettj403/CZT . Needs testing at the moment. But development is active, improved since my last presentation.
- There’s also my own implementation for the classic algorithm in examples, development code.

---
C / C++ implementations
- Problem of research: there are many CZT acronyms, so you have to check the code (even after filtering the obvious false positives).
- https://github.com/mickey305/CZTransform
  - Pure C. Classic algorithm.
  - Tested, compiles and works for CTA.
  - The FFT is custom, so probably was developed for a very specific purpose. The tests and source code comments are in Japanese, so I was relying on Google. Otherwise there is no other documentation.
  - Based on the calculations this seems to be CTA at first sight. This is correct technically, since CTA is a special case of CZT.
- https://github.com/thejonaslab/pychirpz
  - Python and C++. Classic algorithm.
  - Based on FFTW and numba https://numba.pydata.org/ .
  - Benchmarks for CTA vs FFT, confirming the zoom speed-up compared to FFT. As it can be shown based on the algorithm, too.
  - Tested, compiles and works for CTA and CZT, better documented.
- No new inverse CZT found in C / C++, and no time yet to write it myself.

---
Test setup
- Test aim: confirming algorithmic speed up.
- FFT vs CTA using the same numpy.fft / numpy.ifft for CTA, too, so the comparison has the same systematic errors from the software point of view. Therefore using my own CTA implementation.
- Increasing the length of the FFT, and see where CTA catches up on average.
- 9 different zoom settings for CTA for one run, two sets of settings.
  - Reproducibility on the same computer. (9 settings with CTA and FFT repetitions).
  - Decimation (in time or in frequency) FFT run time is highly sensitive to the length even for roughly the same size. (2x9 slightly different zoom settings).
- 10k point scan for FFT length corresponding to different paddings to achieve higher resolution in binning.
- Scan repeated for 2 signal sizes 256 and 2560 to check for transient effects (e.g. computer switching to performance mode) and to see the effect on reproducibility.
- perf_counter_ns() for time measurements, single thread performance for algorithm comparison.

---
Measurements
- Measurements:
  - How well does the algorithm behave?
    - Checking systematic deviation due to different partitioning of the DFTs because of the different FFT lengths.
  - How well does the computer behave?
    - Checking reproducibility for both FFT and CZT for the same partitioning.
  - How is the measured algorithm performance?
    - Comparing equivalent FFT and CZTs for a given zoom.

---
Results, raw timings
- Line: CTA
- Dotted: FFT.
- L = 256
- There are temporary slowdowns when system adapts to load. Draws some power from the network, spins up fan, etc. Systematics.
- As expected from a decimation algorithm, FFT size is critical in both FFT and CTA as seen from FFT spread here (CTA later).

---
Results, raw timings
- Line: CTA
- Dotted: FFT.
- L = 2560
- As expected from a decimation algorithm, FFT size is critical in both FFT and CTA as seen from FFT spread here.
- Here the raw spread of the CTA (straight lines) can also be seen.

---
Gradient of linear fits
- Reproducible computer behaviour on average.
- Line: CTA.
- Dotted: FFT.
- L = 256.
- About 13% spread in FFT gradient.
- About the same deviation for the CTA, which should be ideally constant.
- Especially visible in CTA: the different zooms can take a very different time to run (10k repetition of the same calculation). This is because of the behaviour of the underlying FFTs.
- If a better partitioning exists, a slightly longer FFT will run much faster – here up to 5x.

---
Gradient of linear fits
- Line: CTA.
- Dotted: FFT.
- L = 2560.
- Spreads tighten with larger FFT and CTA sizes as size and transient effect become less relevant.

---
Equivalent FFT size for a given CTA zoom
CTA: x
- FFT: o
- L = 256
- As expected from the algorithm, the larger the zoom, the faster the CTA is compared to an equivalent FFT.
- The larger spread in CTA is due to systematics, much larger than reproducibility.
- The reason is the FFT sizes. The base signal length is 256, and CTA does not need a lot more points for a much larger zoom, where some FFT sizes are much faster than others. But the trend is representative of bigger sizes, too.
- Hence a zoom 24 can be almost as fast as a zoom 6...

---
Equivalent FFT size for a given CTA zoom
CTA: x
- FFT: o
- L = 2560
- As expected from the algorithm, the larger the zoom, the faster the CTA is compared to an equivalent FFT.
- Even better seen that the larger spread in CTA is due to systematics, because the algorithm scales exceptionally well with zoom, therefore the effects of the underlying implementation are seen.

---
Conclusions
- Existing Python and C / C++ implementations of the CZT were surveyed, there are not many.
- The new inverse is only implemented in Python and it is still at the early stages of development, but it is in active development.
- A test to compare the performance of the forward CZT with the FFT in numpy was carried out.
- On average, the algorithms perform as expected from theory.
- The running time – as expected – is highly sensitive (up to 5x) to the precise length of the FFT for a given approximate length.

---
Next steps
- For a fair benchmark a proper ICZT with C performance is to be implemented.
  - Idea: use numba for all calculations.
  - With that ICZT can be implemented fast and the rest of the calculations will use the same optimisation, too.
  - Multi thread capability is promised out of the box, not tested.
- Then compare performance in BLonD.