## Slide 1: Busbars, internal routing, supports and expansion loops
H. Prin
  E. Todesco, R. Principe, J. Fleiter
  IT quads: R. Bossert (FNAL), A. Temporal for the integration
  D1: T. Nakamoto (KEK), Y. Leclercq, D. Duarte Ramos
  D2: O. Id Bahmane for the integration
  MCBXFA/B: J.-C. Perez, F. Toral
  MCBRD: G. Kirby, A. Musso
Busbars and Splice Review 14/04/2021
https://indico.cern.ch/event/1021628/

## Slide 2: Outline
Powering Circuits Overview
  18kA Main Circuit & Trims for the Inner Triplet
    Layout and Routing for the flat and round busses
    Supporting
    Expansion loops
  13kA Circuits for the D1 Separation Dipole
  2kA Circuits for the IT Orbit Correctors
  120 and 200A for the CP HO Correctors
  13kA and 600A Circuits for the D2 cold mass
Busbars and related components Drawing Status
Lessons learnt form LHC

## Slide 3: Powering Circuits Overview
18kA IT MQXFA/B Quadrupoles Circuit 2 busses
2kA IT Trim Circuits 2+1 busses
13kA D1 MBXF Separation Dipole Circuit 2 busses
2kA IT MCBXFA/B Orbit Correctors Circuits 3x 4 busses
DFX
DSHx Link
13kA D2 MBRD Separation Dipole Circuit 2 busses
600A D2 MCBRD Orbit Correctors Circuits 2x 4 busses
DFM
DSHm Link
120 & 200A CP HO Correctors Circuits 9x 2 busses
Local powering through conduction cooled leads

## Slide 4: 18kA Main Circuit & Trims for the Inner Triplet Layout and routing
MQXFA “pizza box”
Magnet leads
MQXFB connection box
(LHCLMQXF_E0009)
Round busbars
Flat busbars

## Slide 5: 18kA Main Circuit & Trims for the Inner Triplet Supporting
3x 18kA individual cables
2x 18kA twisted cables
+ core
2x 18kA twisted cables
Q2 Busses installation test in October 20
G10 tube
Styecast 2850FT blue epoxy
G11 Bus Housing Base
G11 Bus Housing Cap
Al Bus Housing Clip
MQXFA/B
3 individual + 2 twisted cables + core insertion test in April 21
MCBXFB
Flat busbars
Round busbars
Q2 Busses from FNAL
Samples from J. Fleiter and J. Hurte

## Slide 6: 18kA Main Circuit & Trims for the Inner Triplet Expansion Loops
Calculation of the expansion loop movements according to temperature assumptions presented during the 8th HiLumi Collaboration Meeting by R. Bossert and H. Prin (https://indico.cern.ch/event/742082/)
FNAL Cold mass leads and busbars mock-up
CERN Interconnection mock-up

## Slide 7: 13kA Circuits for the D1
Magnet leads
Flat busbars
Courtesy of Yann Leclercq
D1 service module
DCM
“S” shape expansion loop proposed by CERN
Holding fixtures along the routing
Supporting TDB
Round busbars
18kA round busses twisted by pair

## Slide 8: 2kA Circuits for the IT Orbit Correctors
Magnet leads
Round busbars
MCBXFB lead forming tool in November 2020
Lyre shape expansion loop
Leads holding fixtures

## Slide 9: Busbar Cable Support/Spacer
LHC “Spider”
11T “Pipistrelle”
Q1/Q2/Q3 MQXFA/B CS
Q2/CP MCBXFA/B Corr CS
D1
?

## Slide 10: 120 and 200A for the CP HO Correctors
Splices between round cables and conduction cooled leads inspired from the ones used for the 60 and 120A orbit corrector circuits or the 230A trim leads in the 11T
Conduction cooled leads
Connection to magnet Sc leads
1st pair for MC_XF
2nd pair for MC_SXF
5 x LHC Sc 600A cable Ø5.6mm (4wires) for HO correctors
Connection to one of the
5 conduction cooled leads (Cu)
Plyospire sleeve

## Slide 11: 13kA and 600A Circuits for the D2 cold mass
Busbars for the cold test junction to the CFB in SM18
MBRD leads
MCBRD leads
600A round busbars
Magnet leads
Round busbars
18kA round busbars
Expansion loop
Leads holding fixtures
18kA round busses
MBRD leads
600A round busses

## Slide 12: Busbars and related components Drawing Status
 | Q1/Q3 | Q2 | CP | D1 | D2
3D models and integration |  |  | June 2021 |  | 
Subcomponents fabrication drawings |  |  | June 2021 |  | 
Cold mass Integration drawings |  Under revision | July 2021 | July 2021 |  cold mass Extension to DCM Sep 21 | July 2021
Interconnection 3D models | Nov 2021 |  |  |  | July 2021
Interconnection drawings | Dec 2021 |  |  |  | Aug 2021

## Slide 13: Lessons learnt from LHC
Issue in the LHC | Mitigation for HL-LHC
Busses alignment in the splices | Round cable cross section Cable flexibility
Sharp edges | Chamfered or rounded corners in particular inside the end covers
Busbars proximities with other equipment (MB busses/MCS, SSS busses/HX tube, spools/shell…) | Volumes for MQXFA and B expansion loops increased by moving the connection boxes towards the magnets. Very comfortable for the other magnets. Checks on mock-ups
Spider legs | Spacers design inspired from one used in the present LHC Inner Triplet No metallic contact to ground Centring system using springs
Lorentz forces in the connection cryostat and the splices | 18kA busses of the main circuit are twisted from the DCM up to Q3 Holding fixtures are distributed along the magnet lead path and the splice insulation boxes
N-line filling factor in the DS | Insertion easier without core associated to the twisted pair NOMEX, Basalt or Siligaine sleeves rather than glass fibre (toughness, friction)
SSS series 500 busbars length adjustment | Cable cutter to adjust flat and round cables rather than milling machine on surface or saw and file in the tunnel for the copper stabiliser
600A and 6kA cable metallic sleeves | Except the existing 600A busses used inside the CP and the D2, all cables will be delivered insulated without metallic braid

## Slide 14: Summary
Busbars typology and routing is clearly defined
  Designed to minimise the number of splices and the ergonomic during installation,
  Integration according to the HL-LHC WP3 Bus Bars technical specification and conceptual lay out (edms 2029211) and compliant with the splice catalogue study (edms 2492410 see Rosario’s talk).
Magnet lead routing and integration is discussed and agreed with the Project Engineers and external collaborators.
Round busbars insertion test inside the N-line is conclusive for 18kA at the moment
  4x 2kA insertion test to be performed
  It needs to be realised along the IT full length (~52m)
Supporting inside the CP and between the D1 and DFM will be finalised in June 21.
Busbars integration drawings in the cold masses will be completed in July 21, interconnection ones for the tunnel (and the string) by the end of the year.
No show stopper identified

## Slide 15: Spare slides

## Slide 16: Material and Presentation Library
Quadrupoles and orbit correctors bus bars routing along the inner triplet string (WP3 Meeting 2015-12-10)
https://lhc-div-mms.web.cern.ch/lhc-div-mms/tests/MAG/docum/hilumi/Presentations/2015-12-10_hp_busbar.pptx
Quadrupoles and orbit correctors bus bars routing (MQXF Workshop at CERN 2016-02-03)
https://indico.cern.ch/event/478951/
Q1/Q2/Q3 Bus bar outstanding issues: https://indico.cern.ch/event/946104/
Room for the bus bar expansion loop: https://indico.cern.ch/event/746549//
Q1/Q3 bus work update: https://indico.cern.ch/event/805403/
Third Lead (CM Meeting 2019-01-18): https://indico.cern.ch/event/790483/
Busbars in D2 cold mass and cryostat (WP3 Meeting 2020-04-22) https://indico.cern.ch/event/910314/
Superconducting Bus Bars Inside Cryostats (Int. Review of the HL-LHC Magnet Circuits 2019-09-09): https://indico.cern.ch/event/835702/contributions/3503952/
Nb-Ti busbars design and interfaces (7th HiLumi Collab Meeting) https://indico.cern.ch/event/647714/contributions/2646576/
Expansion loops (8th HiLumi Collab Meeting): https://indico.cern.ch/event/742082/contributions/3141508/
Q2 busbars drawing folder: https://edms.cern.ch/document/2515485/
Busbars installation procedure (FNAL): https://indico.cern.ch/event/963060/
LHC 13 kA circuit Risk Analysis https://edms.cern.ch/document/1144154

## Slide 17: Busbars Layout Summary in the Inner Triplet
600A round busbars for the 120 and 200A HO correctors (L1/L2)
120 and 200A HO correctors conduction cooled current leads
18kA round busbars for the quads and trim leads (N1)
2kA round busbars for the orbit correctors (N2)
MCBXFA/B orbit corrector leads (M)
MQXFA/B quad lead
+ 18kA flat bus (M)
18kA flat busses
N1
N2
M
Ø139.7mm

## Slide 18: 18kA Flat Busbars
3.9 mm
3.9 mm
975 µm
18.2 mm
19.2 mm
9.78 mm
3 layers of 125 µm thick Kapton = 375 µm
1 layer of 50 µm thick Kapton with 66% overlap = 150 µm
1 layer of 50 µm thick Kapton with 66% overlap = 150 µm
1 layer of 50 µm thick Kapton with 75% overlap = 200 µm

## Slide 19: D1 leads and 13kA Flat Busbars

## Slide 20: LMQXFA (Q1/Q3) extremities (Mock-up)

## Slide 21: LMQXFA (Q1/Q3) extremities (Prototype)
LMQXFA01 Qa end
LMQXFA01 Qb end

## Slide 22: LMQXFB (Q2) Cold Mass Extremities

## Slide 23: MQXFB connection box displacement in 2018 to gain volume for the expansion loops

## Slide 24: 18 and 2kA round busses inside N1 and N2

## Slide 25: 18kA round busbars insertion test

## Slide 27: D2 Cold Mass from Test to Tunnel configuration

## Slide 28: LMBRD (D2) Busbars integration

## Slide 29: CLIQ and k-mod Leads
K-mod
CLIQ
IFS

## Slide 30: Interconnection Mock-up in LMF
LHCQQQIH0003