## Slide 1: Scattering cross-sections and detector simulation
S.F.Biagi Rd51 April 2021

## Slide 2
High precision detectors :
Drift , tpcs, Mwpc
Low precision detectors:
RPC , streamer, geiger

## Slide 3
High precision detectors:
Drift velocity +- 0.5%
diffusion +- 2%
townsend coeficients +-3%
lorentz angle +- 1 degree
data base satisfies above constraints
mixtures of Ar, He,Ne,Kr and Xe
molecular gases :
N2,CO2, CH4,CO,DME,CF4,H2,D2,O2
slightly reduced accuracy on :
TMA,C2H6,C3H8,C4H10,C3H6,NH3,N2O,TMA,H2O,
Alcohols,SF6,O3,GeH4,BF3,NO,Methylal,C2H4
Fluorocarbons: C2F6,C3F8,CHF3,R134a soon:HFO

## Slide 4
Low precision detectors:
drift velocity +- 5%
diffusion +- 10%
townsend gain +-4%
attachment +-4%
lorentz angle +- 5 degree

## Slide 5
Rpc simulation requirements satisfied by the lower precision .
The main parameters required are the gain and attachment (see Regler and Veenhof)
the cross-sections sets also allow for the calculation of the primary Cluster size and spacing for the incident particle using degrade
There are also important non-equilibrium effects in RPCs that are automatically taken into account by using Garfield++ and the magboltz database.

## Slide 6
Interest in Hydro Fluorocarbons for reduced global warming:
2006 :
created R134a (C2H2F4) x-section file
derived from C2F6 (2002)
2010 :
updated R134a file with better mixture data
2021:
updating C3F8(2002) then use for HFO

## Slide 7
Updates planned:
2021 (May) C3F8
2021 summer HFO
2021 autumn C2F6 then R134a

## Slide 8
Analysis improvements for Fluorocarbons :
A) 3 body attachment now includes the critical density dependence of the attachment x-section
scaled by : 1/((Nc/N)+1)
this now replaces the N dependence of the
3body x-sections..
B) Using dipole screened coulomb angular distribution for the vibrational scattering rather than Capitelli-Longo algorithm.

## Slide 9
Requirements for standard measurements:
Hydrofluorocarbons: good purity 99%
Mixture data with Helium and Argon :
90/10, 95/5 and 99/1
ratio must be accurately measured to 1% of the smaller component :
ie 99/1 requires 1 be to +- 0.01
Temperature and pressure to better than 1KPa and 2 degrees C.
water and nitrogen measured to +- 50 ppm.
townsend as function of pressure (very important)

## Slide 10
Additional measurements required:
Electron scattering experiments :
locate the attachment resonance energies.
Measure ionisation x-sections
BEB ionisation model can be used but not accurate to better than 10%..

## Slide 11
Conclusion:
possible to create x-section sets for the hydrofluorocarbons adequate to use in RPC simulation but not accurate enough for precision simulation of other detector stuctures.
experimental measurements required are
accurate mixture data with argon and helium
pressure dependent townsend measurements
A recent report on the CO update is attached to this talk and discusses some techniques used in the derivation of x-sections.