## Slide 1
David Alesini
(INFN-LNF, Frascati, Rome, Italy)
Linear Accelerators

## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution. Nevertheless the material represent entirely standard teaching material known for more than ten years. Naturally some figures will look alike those produced by other teachers.
Copyright statement and speaker’s release for video publishing

## Slide 3
LINAC APPLICATIONS
Injectors for synchrotrons
Medical applications: radiotherapy
Industrial applications
National security
Material treatment
Ion implantation
Material/food sterilization
Free Electron Lasers
Spallation sources for neutron production
Material testing for fusion nuclear reactors
Nuclear waste treatment and controlled fission for energy production (ADS)
104 LINACs operating around the world

## Slide 4
LINAC: BASIC DEFINITION AND MAIN COMPONENTS
LINAC (linear accelerator) is a system that allows to accelerate charged particles through a linear trajectory by electromagnetic fields.
Particle source
Accelerated beam
Accelerating structures
Focusing elements: quadrupoles and solenoids
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
LINAC BEAM DYNAMICS
LINAC COMPONENTS AND TECHNOLOGY
1st PART OF THE LECTURE
2nd PART OF THE LECTURE

## Slide 5
LINAC TECHNOLOGY COMPLEXITY
The overall LINAC has to be designed to obtain the desired beam parameters in term of:
-output energy/energy spread
-beam current (charge)
-long. and transverse beam dimensions/divergence (emittance)
…
Having, in general, constraints in term of:
-space
-cost
-power consumption
-available power sources
…

## Slide 6
ACCELERATION
BENDING AND FOCUSING
Transverse Dynamics
Longitudinal Dynamics
LORENTZ FORCE: ACCELERATION AND FOCUSING
The basic equation that describes the acceleration/bending/focusing processes is the Lorentz Force.
Particles are accelerated through electric fields and are bended and focused through magnetic fields.
To accelerate, we need a force in the direction of motion
2nd term always perpendicular to motion => no energy gain

## Slide 7
The first historical linear particle accelerator was built by the Nobel prize Wilhelm Conrad Röntgen (1900). It consisted in a vacuum tube containing a cathode connected to the negative pole of a DC voltage generator. Electrons emitted by the heated cathode were accelerated while flowing to another electrode connected to the positive generator pole (anode). Collisions between the energetic electrons and the anode produced X-rays.
The energy gained by the electrons travelling from the cathode to the anode is equal to their charge multiplied the DC voltage between the two electrodes.
ACCELERATION: SIMPLE CASE
+
Electric field
Voltage V
Cathode
Anode
Particle energies are typically expressed in electron-volt [eV], equal to the energy gained by 1 electron accelerated through an electrostatic potential of 1 volt:
1 eV=1.6x10-19 J

## Slide 8
PARTICLE VELOCITY VS ENERGY: LIGHT AND HEAVY PARTICLES
Light particles (as electrons) are practically fully relativistic (1, >>1) at relatively low energy and reach a constant velocity (c). The acceleration process occurs at constant particle velocity
Heavy particles (protons and ions) are typically weakly relativistic and reach a constant velocity only at very high energy. The velocity changes a lot during the acceleration process.
rest mass m0
rest energy E0 (=m0c2)
total energy E
relativistic mass m
velocity v
momentum p (=mv)
Kinetic energy W=E-E0
Relativistic factor =v/c (<1)
Relativistic factor =E/E0 (1)
Single particle
This implies important differences in the technical characteristics of the accelerating structures and in the beam dynamics. For protons and ions we need accelerating structures, optimized for different velocities while for electrons the particles travel at the velocity of light after few MeV.
+
Heavy particles
Light particles
Kin. Energy [MeV]
e-
p+
1


## Slide 9
To increase the achievable maximum energy, Van de Graaff invented an electrostatic generator based on a dielectric belt transporting positive charges to an isolated electrode hosting an ion source. The positive ions generated in a large positive potential were accelerated toward ground by the static electric field.
DC voltage as large as 10 MV can be obtained (E10 MeV). The main limit in the achievable voltage is the breakdown due to insulation problems.
APPLICATIONS OF DC ACCELERATORS
(ELECTROSTATIC ACCELERATORS)
750 kV Cockcroft-Walton
Linac2 injector at CERN from 1978 to 1992
LIMITS OF ELECTROSTATIC ACCELERATORS
DC particle accelerators are in operation worldwide, typically at V<15MV (Emax=15 MeV), I<100mA.
They are used for:
 material analysis
 X-ray production,
 ion implantation for semiconductors
 first stage of acceleration (particle sources)

## Slide 10
RF Accelerators : Wideröe “Drift Tube LINAC” (DTL)
Basic idea: the particles are accelerated by the electric field in the gap between electrodes connected alternatively to the poles of an AC generator. This original idea of Ising (1924) was implemented by Wideroe (1927) who applied a sine-wave voltage to a sequence of drift tubes. The particles do not experience any force while travelling inside the tubes (equipotential regions) and are accelerated across the gaps. This kind of structure is called Drift Tube LINAC (DTL).
L1
Ln
(protons and ions)
If the length of the tubes (or, equivalently, the distances between the centers of the accelerating gaps) increases with the particle velocity during the acceleration such that the time of flight between gaps is kept constant and equal to half of the RF period, the particles are subject to a synchronous accelerating voltage and experience an energy gain of ∆E=q∆V at each gap crossing.
In principle a single RF generator can be used to indefinitely accelerate a beam, avoiding the breakdown limitation affecting the electrostatic accelerators.
The Wideroe LINAC is the first RF LINAC

## Slide 11
DC ACCELERATION: ENERGY GAIN
We consider the acceleration between two electrodes in DC.
Ez
source
rate of energy gain per unit length
z (direction of acceleration)
energy gain per electrode pair
DV
+
-
z
Ez
gap
t
E
W=E-E0
Energy-momentum relation
Lorentz force

## Slide 12
We consider now the acceleration between two electrodes fed by an RF generator
Ez
source
z
z
gap
RF ACCELERATION: BUNCHED BEAM
tinj
E
Only these particles are accelerated
These particles are not accelerated and basically are lost during the acceleration process
t
charge
DC acceleration
t
charge
RF acceleration
Bunched beam (in order to be synchronous with the external AC field, particles have to be gathered in non-uniform temporal structure)
RF period

## Slide 13
We consider now the acceleration between two electrodes fed by an RF generator
Ez
source
z
z
gap
RF ACCELERATION: ACCELERATING FIELD CALCULATION
-L/2
+L/2
Hyp. of symmetric accelerating field
Peak gap voltage
T<1
Transit time factor
Injection phase
Average accelerating field in the gap
Average accelerating field seen by the particle
t=z/v

## Slide 14
DRIFT TUBE LENGTH AND FIELD Synchronization
+
-
Ez
z
vn
Ln
Ln+1
Ln+2
+
-
Ez
z
Ln
Ln+1
Ln+2
vn+1
If now we consider a DTL structure, we have that at each gap the maximum energy gain is En=qVacc and the particle increase its velocity accordingly to the previous relativistic formulae. It is convenient to refer to the center of each gap as follows:
z
E
En
qVacc
z
v
vn
 In order to be synchronous with the accelerating field at the center of each gap, the distance between the centers of the gaps (Ln) has to be increased as:
The energy gain per unit length (i.e. the average accelerating gradient times q) is given by:
[eV/m]
(protons and ions or electrons at extremely low energy)
En+1
vn+1
Gap n
Gap n+1
=average particle velocity between the gap n and n+1

## Slide 15
ACCELERATION WITH HIGH rf FREQUENCIES: RF CAVITIES
There are two important consequences of the previous obtained formulae:
The condition Ln<<RF (necessary to model the tube as an equipotential region) requires <<1. The Wideröe technique can not be applied to relativistic particles.
Moreover when particles get high velocities the drift spaces get longer and one looses on the efficiency. The average accelerating gradient (Eacc [V/m]) increase pushes towards small RF (high frequencies).
High frequency, high power sources became available after the 2nd world war pushed by military technology needs (such as radar). Moreover, the concept of equipotential DT can not be applied at small RF and the power lost by radiation is proportional to the RF frequency.
As a consequence we must consider accelerating structures different from drift tubes.
The solution consists of enclosing the system in a cavity which resonant frequency matches the RF generator frequency.
Each cavity can be independently powered from the RF generator
waveguide
Ez
Ez

## Slide 16
RF CAVITIES
High frequency RF accelerating fields are confined in cavities.
The cavities are metallic closed volumes were the e.m fields has a particular spatial configuration (resonant modes) whose components, including the accelerating field Ez, oscillate at some specific frequencies fRF (resonant frequency) characteristic of the mode.
The modes are excited by RF generators that are coupled to the cavities through waveguides, coaxial cables, etc…
The resonant modes are called Standing Wave (SW) modes (spatial fixed configuration, oscillating in time).
The spatial and temporal field profiles in a cavity have to be computed (analytically or numerically) by solving the Maxwell equations with the proper boundary conditions.
B
E
Courtesy E. Jensen

## Slide 17
Alvarez's structure can be described as a special DTL in which the electrodes are part of a resonant macrostructure.
ALVAREZ STRUCTURES
The DTL operates in 0 mode for protons and ions in the range =0.05-0.5 (fRF=50-400 MHz, RF=6-0.7 m) 1-100 MeV;
The beam is inside the “drift tubes” when the electric field is decelerating. The electric field is concentrated between gaps;
The drift tubes are suspended by stems;
Quadrupole (for transverse focusing) can fit inside the drift tubes.
In order to be synchronous with the accelerating field at each gap the length of the n-th drift tube Ln has to be:
Ez
z
© Encyclopaedia Britannica, inc
(protons and ions)
Example =0.1, fRF=100 MHz, RF=3 m, Ln=-0.3 m)

## Slide 18
ALVAREZ STRUCTURES: EXAMPLES
CERN LINAC 4: 352 MHz frequency, Tank diameter 500 mm, 3 resonators (tanks), Length 19 m, 120 Drift Tubes, Energy: 3 MeV to 50 MeV, =0.08 to 0.31  cell length from 68mm to 264mm.
Ion species H-
Output energy 160 MeV
Bunch frequency 352.2 MHz
Max. rep.-rate 2 Hz
Beam pulse length 400 s
Max. beam duty cycle 0.08%
Linac current 40mA
Average current 0.032mA

## Slide 19
HIGH  cavities: CYLINDRICAL STRUCTURES
When the  of the particles increases (>0.5) one has to use higher RF frequencies (>400-500 MHz) to increase the accelerating gradient per unit length
the DTL structures became less efficient (effective accelerating voltage per unit length for a given RF power);
Cylindrical single or multiple cavities working on the TM010-like mode are used
H
E
For a pure cylindrical structure (also called pillbox cavity) the first accelerating mode (i.e. with non zero longitudinal electric field on axis) is the TM010 mode. It has a well known analytical solution from Maxwell equation.
Real cylindrical cavity
(TM010-like mode because of the shape and presence of beam tubes)
(electrons or protons and ions at high energy)

## Slide 20
QUALITY FACTOR
SHUNT IMPEDANCE
The shunt impedance is the parameter that qualifies the efficiency of an accelerating mode. The higher is its value, the larger is the obtainable accelerating voltage for a given power. Traditionally, it is the quantity to optimize in order to maximize the accelerating field for a given dissipated power:
ACCELERATING VOLTAGE (Vacc)
DISSIPATED POWER (Pdiss)
STORED ENERGY (W)
  NC cavity Q104
  SC cavity Q1010
  NC cavity R1M
SW CAVITIES PARAMETERS: R, Q
  SC cavity R1T
Example:
  R1M
Pdiss=1 MW
Vacc=1MV
For a cavity working at 1 GHz with a structure length of 10 cm we have an average accelerating field of 10 MV/m
Vacc
SHUNT IMPEDANCE PER UNIT LENGTH

## Slide 21
MULTI-CELL SW CAVITIES
R
nR
In a multi-cell structure there is one RF input coupler. As a consequence the total number of RF sources is reduced, with a simplification of the layout and reduction of the costs;
The shunt impedance is n time the impedance of a single cavity
They are more complicated to fabricate than single cell cavities;
The fields of adjacent cells couple through the cell irises and/or through properly designed coupling slots.
Pin
.
Pin
(electrons or protons and ions at high energy)

## Slide 22
MULTI-CELL SW CAVITIES:  MODE STRUCTURES
The N-cell structure behaves like a system composed by N coupled oscillators with N coupled multi-cell resonant modes.
The modes are characterized by a cell-to-cell phase advance given by:
.
The multi cell mode generally used for acceleration is the , /2 and 0 mode (DTL as example operate in the 0 mode).
In this case as done for the DTL structures the cell length has to be chosen in order to synchronize the accelerating field with the particle traveling into the structure at a certain velocity
Ez
z
Ez
z
0 mode
 mode
For ions and protons the cell length has to be increased and the linac will be made of a sequence of different accelerating structures matched to the ion/proton velocity.
For electron, =1, d=RF/2 and the linac will be made of an injector followed by a series of identical accelerating structures, with cells all the same length.
(electrons or protons and ions at high energy)

## Slide 23
 MODE STRUCTURES: EXAMPLES
100 MeV
160 MeV
1.28 m
1.55 m
12 tanks
European XFEL (Desy): electrons
All identical =1
Superconducting cavities

## Slide 24
MULTI-CELL SW CAVITIES: /2 MODE STRUCTURES
It is possible to demonstrate that over a certain number of cavities (>10) working on the  mode, the overlap between adjacent modes can be a problem (as example the field uniformity due to machining errors is difficult to tune).
The criticality of a working mode depend on the frequency separation between the working mode and the adjacent mode
the /2 mode from this point of view is the most stable mode. For this mode it is possible to demonstrate that the accelerating field is zero every two cells. For this reason the empty cells are put of axis and coupling slots are opened from the accelerating cells to the empty cells.
this allow to increase the number of cells to >20-30 without problems
 mode
0 mode
fres
fres_
/2 mode
fres_/2
z
Ez
Side Coupled Cavity (SCC)
fRF=800 - 3000 MHz for proton (=0.5-1) and electrons
Phase advance per cell
(electrons or protons and ions at high energy)
Dispersion curve
Multi cell cavity modes

## Slide 25
SCC STRUCTURES: EXAMPLES
Spallation Neutron Source Coupled Cavity Linac (protons)
4 modules, each containing 12 accelerator segments CCL and 11 bridge couplers. The CCL section is a RF Linac, operating at 805 MHz that accelerates the beam from 87 to 186 MeV and has a physical installed length of slightly over 55 meters.
segment
Accelerating cell
Coupling cell

## Slide 26
TRAVELLING WAVE (TW) STRUCTURES
To accelerate charged particles, the electromagnetic field must have an electric field along the direction of propagation of the particle.
The field has to be synchronous with the particle velocity.
Up to now we have analyzed the cases standing standing wave (SW) structures in which the field has basically a given profile and oscillate in time (as example in DTL or resonant cavities operating on the TM010-like).
Ez
z
Direction of propagation
Ez
z
P RF in
P RF in
P RF out
P RF TW
There is another possibility to accelerate particles: using a travelling wave (TW) structure in which the RF wave is co-propagating with the beam with a phase velocity equal to the beam velocity.
Typically these structures are used for electrons because in this case the phase velocity can be constant all over the structure and equal to c. On the other hand it is difficult to modulate the phase velocity itself very quickly for a low  particle that changes its velocity during acceleration.
field profile
Time oscillation
(electrons)

## Slide 27
TW CAVITIES: CIRCULAR WAVEGUIDE AND DISPERSION CURVE
In TW structures an e.m. wave with Ez0 travel together with the beam in a special guide in which the phase velocity of the wave matches the particle velocity (v). In this case the beam absorbs energy from the wave and it is continuously accelerated.
As example if we consider a simple circular waveguide the first propagating mode with Ez0 is the TM01 mode.
Nevertheless by solving the wave equation it turns out that an e.m. wave propagating in this constant cross section waveguide will never be synchronous with a particle beam since the phase velocity is always larger than the speed of light c.
(propagation constant)
=2f (f=RF generator frequency)
k*
CIRCULAR WAVEGUIDE
RF
tan()=vph
k2*
RF_2
Dispersion curve
Ez
z
cut-off
(electrons)
k

## Slide 28
In order to slow-down the wave phase velocity, iris-loaded periodic structure have to be used.
MODE TM01
MODE TM01-like
IRIS LOADED STRUCTURE
Periodic (in z) wih period D (from Floquet theorem)
TW CAVITIES: IRIS LOADED STRUCTURES
CIRCULAR WAVEGUIDE
The field in this type of structures is that of a special wave travelling within a spatial periodic profile.
The structure can be designed to have the phase velocity equal to the speed of the particles.
This allows acceleration over large distances (few meters, hundred of cells) with just an input coupler and a relatively simple geometry.
RF
k*
k
/D

(electrons)
D
Beam direction
Metal irises
They are used especially for electrons (constant particle velocityconstant phase velocity, same distance between irises, easy realization)

## Slide 29
TW CAVITIES PARAMETERS: r, , vg
Similarly to the SW cavities it is possible to define some figure of merit for the TW structures
Group velocity [m/s]: the velocity of the energy flow in the structure (1-2% of c).
Shunt impedance per unit length [/m]. Similarly to SW structures the higher is r, the higher the available accelerating field for a given RF power.
Field attenuation constant [1/m]: because of the wall dissipation, the RF power flux and the accelerating field decrease along the structure.
Working mode [rad]: defined as the phase advance over a period D. For several reasons the most common mode is the 2/3

## Slide 30
TW CONSTANT GRADIENT STRUCTURES PARAMETRS , vg
In a TW structure, the RF power enters into the cavity through an input coupler, flows (travels) through the cavity in the same direction as the beam and an output coupler at the end of the structure is connected to a matched power load.
If there is no beam, the input power reduced by the cavity losses goes to the power load where it is dissipated.
In the presence of a large beam current, however, a fraction of the TW power is transferred to the beam.
In a purely periodic structure, made by a sequence of identical cells (also called “constant impedance structure”), the RF power flux and the intensity of the accelerating field decay exponentially along the structure :
It is possible to demonstrate that, in order to keep the accelerating field constant along the structure, the iris apertures have to decrease along the structure.
(electrons)
L

## Slide 31
LINAC TECHNOLOGY

## Slide 32
The cavities (and the related LINAC technology) can be of different material:
copper for normal conducting (NC, both SW than TW) cavities;
Niobium for superconducting cavities (SC, SW);
We can choose between NC or the SC technology depending on the required performances in term of:
accelerating gradient (MV/m);
RF pulse length (how many bunches we can contemporary accelerate);
Duty cycle (see next slide): pulsed operation (i.e. 10-100 Hz) or continuous wave (CW) operation;
Average beam current.
…
ACCELERATING CAVITY TECHNOLOGY
Dissipated power into the cavity walls is related to the surface currents
Frequency [GHz]
NIOBIUM
Between copper and Niobium there is a factor 105-106
COPPER

## Slide 33
RF STRUCTURE AND BEAM STRUCTURE: NC vs SC
The “beam structure” in a LINAC is directly related to the “RF structure”. There are two possible type of operations:
CW (Continuous Wave) operation  allow, in principle, to operate with a continuous (bunched) beam
PULSED operation  there are RF pulses at a certain repetition rate (Duty Cycle (DC)=pulsed width/period)
SC structures allow operation at very high Duty Cycle (>1%) up to a CW operation (DC=100%) (because of the extremely low dissipated power) with relatively high gradient (>20 MV/m). This means that a continuous (bunched) beam can be accelerated.
NC structures can operate in pulsed mode at very low DC (10-2-10-1 %) (because of the higher dissipated power) with, in principle, larger peak accelerating gradient(>30 MV/m). This means that one or few tens of bunches can be, in general, accelerated. NB: NC structures can also operate in CW but at very low gradient because of the dissipated power.
Bunch spacing
RF pulses
RF power
t
Amplitude
103-108 RF periods
time

## Slide 34
EXAMPLES: EUROPEAN XFEL

## Slide 35
EXAMPLE: SWISSFEL LINAC (PSI)
Courtesy T. Garvey

## Slide 36
LINAC: BASIC DEFINITION AND MAIN COMPONENTS
LINAC (linear accelerator) is a system that allows to accelerate charged particles through a linear trajectory by electromagnetic fields.
Particle source
Accelerated beam
Accelerating structures
Focusing elements: quadrupoles and solenoids
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
LINAC BEAM DYNAMICS
LINAC COMPONENTS AND TECHNOLOGY

## Slide 37
ELECTRON SOURCES: RF PHOTO-GUNS
RF guns are used in the first stage of electron beam generation in FEL and acceleration.
Multi cell: typically 2-3 cells
SW  mode cavities
operate in the range of 60-120 MV/m cathode peak accelerating field with up to 10 MW input power.
Typically in L-band- S-band (1-3 GHz) at 10-100 Hz.
Single or multi bunch (L-band)
Different type of cathodes (copper,…)
The electrons are emitted on the cathode through a laser that hit the surface. They are then accelerated trough the electric field that has a longitudinal component on axis TM010.
cathode

## Slide 38
RF PHOTO-GUNS: EXAMPLES
LCLS
Frequency = 2,856 MHz
Gradient = 120 MV/m
Exit energy = 6 MeV
Copper photocathode
RF pulse length 2 s
Bunch repetition rate = 120 Hz
Norm. rms emittance
0.4 mmmrad at 250 pC
PITZ L-band Gun
Frequency = 1,300 MHz
Gradient = up to 60 MV/m
Exit energy = 6.5 MeV
Rep. rate 10 Hz
Cs2Te photocathode
RF pulse length 1 ms
800 bunches per macropulse
Normalized rms emittance
1 nC 0.70 mmmrad
0.1 nC 0.21 mmmrad
Solenoids field are used to compensate the space charge effects in low energy guns. The configuration is shown in the picture

## Slide 39
THERMOIONIC GUNS

## Slide 40
LINAC: BASIC DEFINITION AND MAIN COMPONENTS
LINAC (linear accelerator) is a system that allows to accelerate charged particles through a linear trajectory by electromagnetic fields.
Particle source
Accelerated beam
Accelerating structures
Focusing elements: quadrupoles and solenoids
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
LINAC BEAM DYNAMICS
LINAC COMPONENTS AND TECHNOLOGY

## Slide 41
SYNCHRONOUS PARTICLE/PHASE
Let’s assume that the “perfect” synchronism condition is fulfilled for a phase s (called synchronous phase). This means that a particle (called synchronous particle) entering in a gap with a phase s (s=RFts) with respect to the RF voltage receive an energy gain (and a consequent change in velocity) that allow entering in the subsequent gap with the same phase s and so on.
for this particle the energy gain in each gap is:
Let us consider a SW linac structure made by accelerating gaps (like in DTL) or cavities.
In each gap we have an accelerating field oscillating in time and an integrated accelerating voltage (Vacc) still oscillating in time than can be expressed as:
TRF
Vacc
t
s*
s
Vacc_s
obviously both s and s* are synchronous phases.

## Slide 42
PRINCIPLE OF PHASE STABILITY
Vacc
t
s*
s
Let us consider now the first synchronous phase s (on the positive slope of the RF voltage). If we consider another particle “near” to the synchronous one that arrives later in the gap (t1>ts, 1>s), it will see an higher voltage, it will gain an higher energy and an higher velocity with respect to the synchronous one. As a consequence its time of flight to next gap will be shorter, partially compensating its initial delay.
Similarly if we consider another particle “near” to the synchronous one that arrives before in the gap (t1<ts, 1<s), it will see a smaller voltage, it will gain a smaller energy and a smaller velocity with respect to the synchronous one. As a consequence its time of flight to next gap will be longer, compensating the initial advantage.
On the contrary if we consider now the synchronous particle at phase s* and another particle “near” to the synchronous one that arrives later or before in the gap, it will receive an energy gain that will increase further its distance form the synchronous one
The choice of the synchronous phase in the positive slope of the RF voltage provides longitudinal focusing of the beam: phase stability principle.
The synchronous phase on the negative slope of the RF voltage is, on the contrary, unstable
Relying on particle velocity variations, longitudinal focusing does not work for fully relativistic beams (electrons). In this case acceleration “on crest” is more convenient.
1
2
(protons and ions or electrons at extremely low energy)

## Slide 43
ENERGY-PHASE EQUATIONS (1/2)
In order to study the longitudinal dynamics in a LINAC, the following variables are used, which describe the generic particle phase (time of arrival) and energy with respect to the synchronous particle:
The energy gain per cell (one gap + tube in case of a DTL) of a generic particle and of a synchronous particle are (we put =0 in the generic expression of the accelerating voltage just for simplicity ):
Energy of the synchronous particle at a certain position along the linac
Energy of a generic particle at a certain position along the linac
Arrival time (phase) of the synchronous particle at a certain gap (or cavity)
Arrival time (phase) of a generic particle at a certain gap (or cavity)
L (accelerating cell length)
z
subtracting
Dividing by the accelerating cell length L and assuming that:
Average accelerating field over the cell (or accelerating gradient)
Approximating
(protons and ions or electrons at extremely low energy)

## Slide 44
On the other hand we have that the phase variation per cell of a generic particle and of a synchronous particle are:
v, vs are the average particles velocities
This system of coupled (non linear) differential equations describe the motion of a non synchronous particles in the longitudinal plane with respect to the synchronous one.
t is basically the time of flight between two accelerating cells
subtracting
Dividing by the accelerating cell length L
MAT
Approximating
ENERGY-PHASE EQUATIONS (2/2)
(protons and ions or electrons at extremely low energy)

## Slide 45
SMALL AMPLITUDE ENERGY-PHASE OSCILLATIONS
Assuming small oscillations around the synchronous particle that allow to approximate
Deriving both terms with respect to z and assuming an adiabatic acceleration process i.e. a particle energy and speed variations that allow to consider
harmonic oscillator equation
The condition to have stable longitudinal oscillations and acceleration at the same time is:
Vacc
t
s
Vacc_s
if we accelerate on the rising part of the positive RF wave we have a longitudinal force keeping the beam bunched around the synchronous phase.
(protons and ions or electrons at extremely low energy)
The angular frequency is simply: T= ssc;
The angular frequency scale with 1/3/2 that means that for ultra relativistic electrons shrinks to 0 (the beam is frozen)

## Slide 46
The energy-phase oscillations can be drawn in the longitudinal phase space:
w

The trajectory of a generic particle in the longitudinal phase space is an ellipse.
The maximum energy deviation is reached at =0 while the maximum phase excursion corresponds to w=0.
the bunch occupies an area in the longitudinal phase space called longitudinal emittance and the projections of the bunch in the energy and phase planes give the energy spread and the bunch length.
Gain energy with respect to the synchronous one
Loose energy
move backward
move forward
w

0
Number of particles
Bunch length
Energy spread
0
Longitudinal emittance is the phase space area including all the particles

w
ENERGY-PHASE OSCILLATIONS IN PHASE SPACE
Synchronous particle
(protons and ions or electrons at extremely low energy)

## Slide 47



s
-s
To study the longitudinal dynamics at large oscillations, we have to consider the non linear system of differential equations without approximations. In the adiabatic acceleration case it is possible to easily obtain the following relation between w and  that is the Hamiltonian of the system related to the total particle energy:
LARGE OSCILLATIONS AND SEPARATRIX
For each H we have different trajectories in the longitudinal phase space
the oscillations are stable within a region bounded by a special curve called separatrix: its equation is:
the region inside the separatrix is called RF bucket. The dimensions of the bucket shrinks to zero if s=0.
trajectories outside the RF buckets are unstable.
we can define the RF acceptance as the maximum extension in phase and energy that we can accept in an accelerator:
Small amplitude oscillations
RF bucket

## Slide 48
From previous formulae it is clear that there is no motion in the longitudinal phase plane for ultrarelativistic particles (>>1).
It is interesting to analyze what happen if we inject an electron beam produced by a cathode (at low energy) directly in a TW structure (with vph=c) and the conditions that allow to capture the beam (this is equivalent to consider instead of a TW structure a SW designed to accelerate ultrarelativistic particles at v=c).
Particles enter the structure with velocity v<c and, initially, they are not synchronous with the accelerating field and there is a so called slippage.
This is the case of electrons whose velocity is always close to speed of light c even at low energies.
Accelerating structures are designed to provide an accelerating field synchronous with particles moving at v=c. like TW structures with phase velocity equal to c.
LONGITUDINAL DYNAMICS OF LOW ENERGY ELECTRONS
After a certain distance they can reach enough energy (and velocity) to become synchronous with the accelerating wave. This means that they are captured by the accelerator and from this point they are stably accelerated.
z
If this does not happen (the energy increase is not enough to reach the velocity of the wave) they are lost
Eacc

## Slide 49
LONGITUDINAL DYNAMICS OF LOW ENERGY ELECTRONS: PHASE SPLIPPAGE
The accelerating field of a TW structure can be expressed by
The equation of motion of a particle with a position z at time t accelerated by the TW is then
It is useful to find which is the relation between  and  from an initial condition (in) to a final one (fin)
Suppose that the particle reach asymptotically the value fin=1 we have:

Eacc
in
in
fin
fin=1
z
Eacc
Should be in the interval [-1,1] to have a solution for fin
This quantity is >0
This limits the possible injection phases (i.e. the phase of the electrons that is possible to capture)
We always have that

## Slide 50
LONGITUDINAL DYNAMICS OF LOW ENERGY ELECTRONS: CAPTURE EFFICIENCY AND BUNCH COMPRESSION
Ez
in<1
fin=1

During the capture process, as the injected beam moves up to the crest, the beam is also bunched, which is caused by velocity modulation (velocity bunching). This mechanism can be used to compress the electron bunches (FEL applications).
Bunch length variation
in=0.01
fin1
These particle are lost during the capture process
BUNCH COMPRESSION
CAPTURE EFFICIENCY
All particles are captured
in=0.01
fin1

## Slide 51
In order to increase the capture efficiency of a traveling wave section, pre-bunchers are often used. They are SW cavities aimed at pre-forming particle bunches gathering particles continuously emitted by a source.
I
t
I
t
T
RF
I
t
T
RF
Continuous beam
with velocity modulation
Bunching is obtained by modulating the energy (and therefore the velocity) of a continuous beam using the longitudinal E-field of a SW cavity. After a certain drift space the velocity modulation is converted in a density charge modulation. The density modulation depletes the regions corresponding to injection phase values incompatible with the capture process
A TW accelerating structure (capture section) is placed at an optimal distance from the pre-buncher, to capture a large fraction of the charge and accelerate it till relativistic energies. The amount of charge lost is drastically reduced, while the capture section provide also further beam bunching.
Once the capture condition ERF>ERF_MIN is fulfilled the fundamental equation of previous slide sets the ranges of the injection phases in actually accepted. Particles whose injection phases are within this range can be captured the other are lost.
BUNCHER AND CAPTURE SECTIONS
Thermionic
Gun
Continuous beam
Buncher
(SW Cavity)
Drift L
Bunched beam
Capture section
(SW or TW)
Bunched and captured beam
(electrons)
v
t
vE
t
TRF

## Slide 52
LINAC: BASIC DEFINITION AND MAIN COMPONENTS
LINAC (linear accelerator) is a system that allows to accelerate charged particles through a linear trajectory by electromagnetic fields.
Particle source
Accelerated beam
Accelerating structures
Focusing elements: quadrupoles and solenoids
Transverse dynamics of accelerated particles
Longitudinal dynamics of accelerated particles
LINAC BEAM DYNAMICS
LINAC COMPONENTS AND TECHNOLOGY

## Slide 53
RF TRANSVERSE FORCES
The RF fields act on the transverse beam dynamics because of the transverse components of the E and B field
z
According to Maxwell equations the divergence of the field is zero and this implies that in traversing one accelerating gap there is a focusing/defocusing term
fRF=350 MHz
=0.1
L=3cm
r


## Slide 54
RF DEFOCUSING/FOCUSING
t
s
Transverse momentum increase
Gap length
Defocusing force since sin<0
Defocusing effect
transverse defocusing scales as 1/2 and disappears at relativistic regime (electrons)
At relativistic regime (electrons), moreover, we have, in general, =0 for maximum acceleration and this completely cancel the defocusing effect
Also in the non relativistic regime for a correct evaluation of the defocusing effect we have to:
      take into account the velocity change across the accelerating gap
      the transverse beam dimensions changes across the gap (with a general reduction of the transverse beam dimensions due to the focusing in the first part)
      Both effects give a reduction of the defocusing force
From previous formulae it is possible to calculate the transverse momentum increase due to the RF transverse forces. Assuming that the velocity and position changes over the gap are small we obtain to the first order:

## Slide 55
RF FOCUSING IN ELECTRON LINACS
-RF defocusing is negligible in electron linacs.
-There is a second order effect due to the non-synchronous harmonics of the accelerating field that give a focusing effect. These harmonics generate a ponderomotive force i.e. a force in an inhomogeneous oscillating electromagnetic field.
Ez
z
Direction of propagation
P RF in
Is equivalent to the superposition of two counterpropagating TW waves
Ez
z
Direction of propagation
The forward wave only contribute to the acceleration (and does not give transverse effect).
The backward wave does not contribute to the acceleration but generates an oscillating transverse force (ponderomotive force)
With accelerating gradients of few tens of MV/m can easily reach the level of MV/m2
The Lorentz force is linear with the particle dispacemement
MECHANISM
Transverse equation of motion
RF harmonics

z
r
This generate a global focusing force
NON-SYNCHRONOUS RF HARMONICS: SIMPLE CASE OF SW STRUCTURE
Average focusing force
Particle trajectory

## Slide 56
COLLECTIVE EFFECTS: SPACE CHARGE AND WAKEFIELDS
 Effect of Coulomb repulsion between particles (space charge).
 These effects cannot be neglected especially at low energy and at high current because the space charge forces scales as 1/2 and with the current I.
EXAMPLE: Uniform and infinite cylinder of charge moving along z
z
r
Er
B
rq
Rb
I
In this particular case it is linear but in general it is a non-linear force
Collective effects are all effects related to the number of particles and they can play a crucial role in the longitudinal and transverse beam dynamics
SPACE CHARGE
WAKEFIELDS
The other effects are due to the wakefield. The passage of bunches through accelerating structures excites electromagnetic field. This field can have longitudinal and transverse components and, interacting with subsequent bunches (long range wakefield), can affect the longitudinal and the transverse beam dynamics. In particular the transverse wakefields, can drive an instability along the train called multibunch beam break up (BBU).
z
wT
Several approaches are used to absorb these field from the structures like loops couplers, waveguides, Beam pipe absorbers

## Slide 57
MAGNETIC FOCUSING AND CONTROL OF THE TRANSVERSE DYNAMICS
Defocusing RF forces, space charge or the natural divergence (emittance) of the beam need to be compensated and controlled by focusing forces.
This is provided by quadrupoles along the beam line.
At low energies also solenoids can be used
In a linac one alternates accelerating structures with focusing sections.
Quadrupoles are focusing in one plane and defocusing on the other. A global focalization is provides by alternating quadrupoles with opposite signs
F
D
F
D
F
s
x
The type of magnetic configuration and magnets type/distance depend on the type of particles/energies/beam parameters we want to achieve.

## Slide 58
Due to the alternating quadrupole focusing system each particle perform transverse oscillations along the LINAC.
The equation of motion in the transverse plane is of the type:
The single particle trajectory is a pseudo-sinusoid described by the equation:
Term depending on the magnetic configuration
RF defocusing/focusing term
Characteristic function (Twiss -function [m]) that depend on the magnetic and RF configuration
Depend on the initial conditions of the particle
The final transverse beam dimensions (x,y(s)) vary along the linac and are contained within an envelope
TRANSVERSE OSCILLATIONS AND BEAM ENVELOPE
Space charge term
Transverse phase advance per period Lp. For stability should be 0<<
Focusing period (Lp)= length after which the structure is repeated (usually as N).
Distance [mm or m]

## Slide 59
SMOOTH APPROXIMATION OF TRANSVERSE OSCILLATIONS
In case of “smooth approximation” of the LINAC (we consider an average effect of the quadrupoles and RF) we obtain a simple harmonic motion along s of the type ( is constant):
x
Phase advance per unit length (/Lp)
s
Magnetic focusing elements (for a FODO)
RF defocusing term
If we consider also the Space Charge contribution in the simple case of an ellipsoidal beam (linear space charges) we obtain:
I= average beam current (Q/TRF)
rx,y,z=ellipsoid semi-axis
f= form factor (0<f<1)
Z0=free space impedance (377 Ω)
Space charge term
For ultrarelativistic electrons RF defocusing and space charge disappear and the external focusing is required to control the emittance and to stabilize the beam against instabilities.
G=quadrupole gradient [T/m]
l=quadrupole length
NB: the RF defocusing term f sets a higher limit to the working frequency
Lp
l

## Slide 60
GENERAL CONSIDERATIONS ON LINAC OPTICS DESIGN (1/2)
Beam dynamics dominated by space charge and RF defocusing forces
Focusing is usually provided by quadrupoles
Phase advance per period () should be, in general, in the range 30-80 deg, this means that, at low energy, we need a strong focusing term (short quadrupole distance and high quadrupole gradient) to compensate for the rf defocusing, but the limited space () limits the achievable G and beam current
As  increases, the distance between focusing elements can increase ( in the DTL goes from 70mm (3 MeV, 352 MHz) to 250mm (40 MeV), and can be increased to 4-10 at higher energy (>40 MeV).
A linac is made of a sequence of structures, matched to the beam velocity, and where the length of the focusing period increases with energy. As  increases, longitudinal phase error between cells of identical length becomes small and we can have short sequences of identical cells (lower construction costs).
Keep sufficient safety margin between beam radius and aperture
PROTONS AND IONS
Courtesy A. Lombardi

## Slide 61
Space charge only at low energy and/or high peak current: below 10 MeV (injector) the beam dynamics optimization has to include emittance compensation schemes with, typically solenoids;
At higher energies no space charge and no RF defocusing effects occur but we have RF focusing due to the ponderomotive force: focusing periods up to several meters. EMITTANCE DOMINATED DYNAMICS.
Optics design has to take into account longitudinal and transverse wakefields (due to the higher frequencies used for acceleration) that can cause energy spread increase, head-tail oscillations, multi-bunch instabilities,…
Longitudinal bunch compressors schemes based on magnets and chicanes have to take into account, for short bunches, the interaction between the beam and the emitted synchrotron radiation (Coherent Synchrotron Radiation effects)
All these effects are important especially in LINACs for FEL that requires extremely good beam qualities
GENERAL CONSIDERATIONS ON LINAC OPTICS DESIGN (2/2)
ELECTRONS
Courtesy C. Vaccarezza
Courtesy M. Ferrario

## Slide 62
RADIO FREQUENCY QUADRUPOLES (RFQ)
At low proton (or ion) energies (0.01), space charge defocusing is high and quadrupole focusing is not very effective. Moreover cell length becomes small and conventional accelerating structures (DTL) are very inefficient. At this energies it is used a (relatively) new structure, the Radio Frequency Quadrupole (1970).
These structures allow to simultaneously provide:
Acceleration
Transverse Focusing
Bunching of the beam
Electrodes
Courtesy M. Vretenar

## Slide 63
1-Focusing
The resonating mode of the cavity (between the four electrodes) is a focusing mode: Quadrupole mode (TE210). The alternating voltage on the electrodes produces an alternating focusing channel with the period of the RF (electric focusing does not depend on the velocity and is ideal at low )
RFQ: PROPERTIES
2-Acceleration
The vanes have a longitudinal modulation with period = RF this creates a longitudinal component of the electric field that accelerate the beam (the modulation corresponds exactly to a series of RF gaps).
3-Bunching
The modulation period (distance between maxima) can be slightly adjusted to change the phase of the beam inside the RFQ cells, and the amplitude of the modulation can be changed to change the accelerating gradient. One can start at -90 phase (linac) with some bunching cells, progressively bunch the beam (adiabatic bunching channel), and only in the last cells switch on the acceleration.
The RFQ is the only linear accelerator that can accept a low energy continuous beam.
Courtesy A. Lombardi
Courtesy M. Vretenar and A. Lombardi

## Slide 64
RFQ: EXAMPLES
The 1st 4-vane RFQ, Los Alamos
1980: 100 KeV - 650 KeV, 30 mA , 425 MHz
TRASCO @ INFN Legnaro
Energy In: 80 keV
Energy Out: 5 MeV
Frequency 352.2 MHz
Proton Current (CW) 30 mA
The CERN Linac4 RFQ
45 keV – 3 MeV, 3 m
80 mA H-, max. 10% duty cycle

## Slide 65
In general the choice of the accelerating structure depends on:
 Particle type: mass, charge, energy
 Beam current
 Duty cycle (pulsed, CW)
 Frequency
 Cost of fabrication and of operation
Cavity Type |  Range | Frequency | Particles
RFQ | 0.01– 0.1 | 40-500 MHz | Protons, Ions
DTL | 0.05 – 0.5 | 100-400 MHz | Protons, Ions
SCL | 0.5 – 1 | 600 MHz-3 GHz | Protons, Electrons
SC Elliptical | > 0.5-0.7 | 350 MHz-3 GHz | Protons, Electrons
TW | 1 | 3-12 GHz | Electrons
THE CHOICE OF THE ACCELERATING STRUCTURE
Moreover a given accelerating structure has also a curve of efficiency (shunt impedance) with respect to the particle energies and the choice of one structure with respect to another one depends also on this.
As example a very general scheme is given in the Table (absolutely not exhaustive).

## Slide 66
STRUCTURE PARAMETERS SCALING WITH FREQUENCY
We can analyze how all parameters (r, Q) scale with frequency and what are the advantages or disadvantages in accelerate with low or high frequencies cavities.
linear dimensions f-1
frequency f
parameter | NC | SC
Rs |  f1/2 |  f2
Q |  f-1/2 |  f-2
r |  f1/2 |  f-1
r/Q |  f | 
w// |  f2 | 
w┴ |  f3 | 
Wakefield intensity: related to BD issues
r/Q increases at high frequency
for NC structures also r increases and this push to adopt higher frequencies
for SC structures the power losses increases with f2 and, as a consequence, r scales with 1/f this push to adopt lower frequencies
On the other hand at very high frequencies (>10 GHz) power sources are less available
Beam interaction (wakefield) became more critical at high frequency
Cavity fabrication at very high frequency requires higher precision but, on the other hand, at low frequencies one needs more material and larger machines
short bunches are easier with higher f
SW SC: 500 MHz-1500 MHz
TW NC: 3 GHz-6 GHz
SW NC: 0.5 GHz-3 GHz
Compromise
between several requirements

## Slide 67
Medical applications
Security: Cargo scans
Industrial applications:
Ion implantation for semiconductors
Injectors for colliders and synchrotron light sources
Neutron spallation sources
FEL
THANK YOU FOR YOUR ATTENTION

## Slide 68
ACKNOWLEDGEMENTS
Several pictures, schemes, images and plots have been taken from papers and previous presentations of the following authors that I would like to thank.
I would like to acknowledge in particular the following authors:
Hans Weise, Sergey Belomestnykh, Dinh Nguyen, John Lewellen, Leanne Duffy, Gianluigi Ciovati, Jean Delayen, S. Di Mitri, R. Carter, G. Bisoffi, B. Aune, J. Sekutowicz, H. Safa, D. Proch, H. Padamsee, R. Parodi, Paolo Michelato, Terry Garvey, Yujong Kim, S. Saitiniyazi, M. Mayierjiang, M. Titberidze, T. Andrews, C. Eckman, Roger M. Jones, T. Inagaki, T. Shintake, F. Löhl, J. Alex, H. Blumer, M. Bopp, H. Braun, A. Citterio, U. Ellenberger, H. Fitze, H. Joehri, T. Kleeb, L. Paly, J.Y. Raguin, L. Schulz, R. Zennaro, C. Zumbach. Detlef Reschke, David Dowell, K. Smolenski, I. Bazarov, B. Dunham, H. Li, Y. Li, X. Liu, D. Ouzounov, C. Sinclair
A. Gallo, E. Jensen, A. Lombardi, F. Tecker and M. Vretenar
I would like also to acknowledge the following authors:

## Slide 69
REFERENCES
Reference Books:
T. Wangler, Principles of RF Linear Accelerators (Wiley, New York, 1998).
P. Lapostolle, A. Septier (editors), Linear Accelerators (Amsterdam, North Holland, 1970).
General Introduction to linear accelerators
M. Puglisi, The Linear Accelerator, in E. Persico, E. Ferrari, S.E. Segré, Principles of Particle Accelerators (W.A. Benjamin, New York, 1968).
P. Lapostolle, Proton Linear Accelerators: A theoretical and Historical Introduction, LA-11601-MS, 1989.
P. Lapostolle, M. Weiss, Formulae and Procedures useful for the Design of Linear Accelerators, CERNPS-
2000-001 (DR), 2000.
P. Lapostolle, R. Jameson, Linear Accelerators, in Encyclopaedia of Applied Physics (VCH Publishers,
New York, 1991).
CAS Schools
D. Alesini, CAS proceedings this school.
S. Turner (ed.), CAS School: Cyclotrons, Linacs and their applications, CERN 96-02 (1996).
M. Weiss, Introduction to RF Linear Accelerators, in CAS School: Fifth General Accelerator Physics
Course, CERN-94-01 (1994), p. 913.
N. Pichoff, Introduction to RF Linear Accelerators, in CAS School: Basic Course on General Accelerator
Physics, CERN-2005-04 (2005).
M. Vretenar, Differences between electron and ion linacs, in CAS School: Small Accelerators, CERN-
2006-012.
M. Vretenar, Low-beta Structures, in CAS RF School, Ebeltoft 2010
J. Le Duff, High-field electron linacs, CAS School: Fifth Advanced Accelerator Physics Course, CERN 95-06, 1995.
J. Le Duff, Dynamics and acceleration in linear structures, CAS School: Fifth General Accelerator Physics Course, CERN 94-01, 1994.
D. Alesini, “Linear Accelerator Technology”, CERN Yellow Reports: School Proceedings, v. 1, p. 79, CERN-2018-001-SP (CERN, Geneva, 2018).