## Slide 1: RF Systems I
H. Damerau
CERN
3 October 2021
Introduction to Accelerator Physics

## Slide 2
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution. Nevertheless the material represent entirely standard teaching material known for more than ten years. Naturally some figures will look alike those produced by other teachers.
Copyright statement and speaker’s release for video publishing

## Slide 3
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
  Local feedbacks
Longitudinal beam control system
  Building blocks: RF source and receiver
  Phase, radial and synchronization loops
Summary
Outline

## Slide 4
Introduction

## Slide 5
Introduction
What is below?
How are RF signals generated which make the beam feel comfortable?
The radiofrequency (RF) system transforms a string of magnets into an accelerator
Cavity most is the most visible part of an RF system
  On top of the RF system food chain
  Interacts directly with beam
Cavity
Power amplifier
Low-level RF
system
Beam
Beam

## Slide 6
Frequency and wavelength ranges
100 kHz 3 km
1 MHz 300 m
10 MHz
30 m
100 MHz
3 m
1 GHz
30 cm
10 GHz 3 cm
100 GHz
3 mm
SPS 200 MHz
PS main RF system
PS longitudi- nal damper
CLIC 12 GHz
Long wave
Medium/ short wave
VHF
Microwave links

## Slide 7
Amplitude ranges
1 mV
1 mV
1 V
1 kV
1 MV
1 GV
LEP: 3.6 GV total
LLRF systems
Signals from beam pick-ups
ILC and CLIC: several TV
LHC: 16 MV
Cooled hadron beams (ELENA)
Electron light
sources
SLS
LHC
Low/Medium energy hadron RF

## Slide 8
Particle velocity depends on its type:
Old television set (30 kV): Electrons at 30% of c0
            Protons just at 0.7%
Small synchrotron (500 MeV): Electrons at 99.99995%
              Protons at 75.8%
Most electron accelerators at ‘fixed’ frequency
Particle velocity
p+
e-
p+
e-

## Slide 9
Parameter choices

## Slide 10
Accelerator type
Linear
(single pass)
RF system for high-energy accelerators
Hadrons
Electron
Maximum RF voltage, constant velocity
Maximum RF voltage, variable velocity
Circular
(multi-pass)
Compensate synchrotron radiation losses
Sweep frequency with beam
Hadrons
Electron
*Exceptions (rare) exist
*

## Slide 11
Choice of frequency (range)

## Slide 12
Advantages | Disadvantages
Large beam aperture Long RF buckets, large acceptance Wide-band or wide range tunable cavities possible Power amplification and transmission straightforward | Bulky cavities, size scales 1/f, volume 1/f3 Lossy material to downsize cavities Moderate or low acceleration gradient Short particle bunches difficult to generate
Advantages | Disadvantages
Large beam aperture Long RF buckets, large acceptance Wide-band or wide range tunable cavities possible Power amplification and transmission straightforward | 
Why choose a low RF frequency?
  RF frequencies below ~200 MHz for
  Some hadron linear accelerators
  Cyclotrons
  Low- and medium energy hadron synchrotrons

## Slide 13
Advantages | Disadvantages
Cavity size scales 1/f, volume 1/f3 Break down voltage increases High gradient per length Particle bunches are short | Maximum beam available aperture scales 1/f No technology for wide-band or tunable cavities Power amplifiers more difficult Power transmission losses
Advantages | Disadvantages
Why choose a high RF frequency?
  RF frequencies above ~200 MHz used for
  Linear accelerators
  Electron storage rings
  High energy hadron storage rings

## Slide 14
Limits to maximum gradient
Kilpatrick 1957,
f in GHz, Ecrit in MV/m
Wang & Loew, SLAC-PUB-7684, 1997
Surface electric field in vacuum
1000
500
200
100
50
20
10
0.01
0.1
1
10
100
f [GHz]
Ecrit [MV/m]
High frequencies preferred for large gradient
E. Jensen

## Slide 15
If exact RF frequency not critical, choose standard value
Off-the-shelf RF components easily available in frequency ranges used by industry
Exchange of developments and equipment amongst research laboratories
Some standard frequencies
Accelerator | Frequency
Hadron synchrotrons (PSB, PS, JPARC RCS, MR) | <10 MHz
Hadron accelerators and storage rings (RHIC, SPS) | ~200 MHz
Electron storage rings (LEP, ESRF, Soleil) | 352 MHz
Electron storage rings (DORIS, BESSY, SLS,…) | 499.6…499.8 MHz
Superconducting electron linacs and FELs (X-FEL, ILC) | 1300 MHz
Normal conducting electron linacs (SLAC) | 2856 MHz
High-gradient electron linac (CLIC) | 11.99 GHz

## Slide 16
RF voltage

## Slide 17
RF system expected to provide given energy gain
On-crest acceleration
Used in some linear accelerators
Insufficient in a circular accelerator
More voltage provided to avoid on-crest acceleration
Off-crest acceleration
Needed for circular accelerator
Higher voltage for given energy gain
Minimum voltage requirement


## Slide 18
Bucket area dependence on stable phase
In a circular accelerator the area in energy-time phase space (bucket area) depends on the stable phase
Below transition, fS = 0…90°
Below transition, fS = 90°…180°
Typical synchronous phase with respect to 0° or 180°
  Hadron accelerators: < 40°
  Electron storage rings: ~ 20°

## Slide 19
Minimum voltage requirement (circular)
The RF system must compensate
Energy gain per turn due to changing magnetic field
Energy loss, e.g., due to synchrotron radiation (electrons)
(mp/me)4 = 18364 ~ 1.1 ∙ 1013 times less for protons

## Slide 20
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 21
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 22
RF cavity

## Slide 23
Cavity parameters
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
R
C
L
Z(w)
with

## Slide 24
Cavity parameters
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
Resonant circuit can also be described by R, R/Q, w0 or any other set of three parameters
R
C
L
Z(w)
with

## Slide 25
Cavity parameters
The resonance of a cavity can be understood as simple parallel resonant circuit described by R, L, C
Resonant circuit can also be described by R, R/Q, w0 or any other set of three parameters
R
C
L
Z(w)
Dw

## Slide 26
Cavity parameters
Most common choice by cavity designers w0, R, R/Q – why?
Resonance frequency, w0
  Exactly defined for given application, e.g. hfrev
Shunt impedance, R
  Power required to produce a given voltage without beam
“R-upon-Q”, R/Q
  Defined only by the cavity geometry
  Criterion to optimize a geometry
  Detuning with beam proportional to R/Q

## Slide 27
Why R/Q?
Charged particle experiences cavity gap as capacitor
Cavity geometry with small R/Q to reduce beam loading
q
Cavity
Beam induced voltage

## Slide 28
RF wavelength large below ~10 MHz: >30 m
Would need huge cavities  too large for accelerators
Line resonators: l/4 resonator
  Short circuit on one side  Voltage is zero
  Open end on other  No current but voltage
Why is this resonator so common in particle accelerators?
RF cavities in low frequency range
Voltage
Current
Transmission line, impedance ZL
l/4 length
Z(w)
Short- circuit

## Slide 29
Coaxial structure with inner conductor as beam pipe
RF cavities in low frequency range
Z(w)
Accelerating gap, isolated
Beam axis
Short- circuit
Still rather long geometry, 7.5 m at 10 MHz
Add capacitive or inductive shortening
Plate capacitor
Ferrite inductivity

## Slide 30
Capacitive loading
Add capacitor at gap of cavity to shorten the resonator
Significantly reduces cavity size
Fixed frequency only
Small losses due to capacitor
Cavity in vacuum
NSLS, 52.88 MHz
DESY PIA, 10.4 MHz, inner cond.
Outer cond.
~1 m
ACOL, 9.53 MHz
M. Nagl

## Slide 31
Inductive loading with magnetic material shortens resonator from tens of meters to a device, lossy though
Inductive loading
CERN PSB Finemet cav., 0.6-18 MHz
CERN PS, double gap, 2.8-10 MHz
Additional advantage: permeability of ferrite can be controlled by DC bias current  variable inductivity
  Cavity with programmable resonance frequency
  Essential for hadron acceleration in low-energy accelerators
M. Paoluzzi

## Slide 32
Remove inductive or capacitive loading
C. C. Friedrichs et al., PAC91, p. 1020
R. L. Madrak, IPAC16, p. 130
SSC Low Energy Booster, ~47 MHz to 60 MHz
FNAL Booster 2nd harmonic, 76 MHz – 106 MHz, 100 kV
Tunable cavities at higher frequencies
Upper frequency limit for cavities with large tuning range

## Slide 33
Remove inner conductor from coaxial set-up
The resonator becomes a pill-box cavity
The basis for cavity resonators
Further increase frequency
Electric field, TM010-mode
Magnetic field, TM010-mode
E. Jensen
Beam axis
Beam axis
DORIS cavity

## Slide 34
Example: 400 MHz cavities in LHC
Reduce beam loading in RF cavities
Shunt impedance, R, low for small R/Q with normal conducting cavities  superconducting cavities in LHC
Bell shape: R/Q ~ 44 W, 400 MHz
28 cavities, 5.3 MV/m
~o

## Slide 35
RF cavities in linear accelerators
Beam only passes once  Maximize gradient
Many accelerating cells to best reuse RF voltage
Cavity is the contrary to ‘one size fits all’
Many, many more variants
SuperHILAC, ~70 MHz, Berkley
CLIC, 12 GHz, ~100 MV/m

## Slide 36
Coupling power into a cavity

## Slide 37
Attack inductivity or capacitance of resonator, or combined
Coupling loop forms transformer with resonator inductivity
Coupling power into a cavity
C
Lc
M
RF power
L. Stigelin
Main coupler PSI cyclotron
~1 MW at 50 MHz
R
L
A. Rodchenko

## Slide 38
Attack inductivity or capacitance of resonator, or combined
Capacitive divider to gap to transform generator impedance to cavity shunt impedance
Beam also couples capacitively via the gap
Coupling power into a cavity
R
C
L
RF power
Cc
Beam
Coupler of CERN PS 40 MHz
Coupler forms one half of capacitor with the gap

## Slide 39
Coupling through an electric antenna
Capacitive (electric) coupling
Electrical coupler to space
Power coupler of LHC cavities 300 kW at 400 MHz
Coupler antenna transmits directly into the cavity
2 MW at 540 kHz
https://en.wikipedia.org/wiki/Transmitter_Solt

## Slide 40
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 41
Power amplifiers

## Slide 42
Power to accelerate beam  Wanted
Compensate beam-induced voltage  Refl. P
Compensate electrical losses in cavity  Heat
Compensate electrical losses in distribution  Heat
How much power is required?
(ideally)

## Slide 43
Basically
Pout = g ∙ Pin or Vout = ∙ Vin
The ideal power amplifier
  Large bandwidth: amplifies all frequencies equally
  No saturation, infinite power
  Zero delay
  No added noise
  Unconditionally stable and resistant to reverse power
  Radiation-hard
Unfortunately such a device has not been invented yet
Let us have a look at some real amplifiers
Power amplifiers

## Slide 44
Cathode and filament
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
e-
e-
e-
e-
e-
Ua*
anode
e-
e-
e-
e-
e-
e-
Basics of grid tube
Ia
From diode to tetrode amplifier
E. Montesinos
*For tube amplifier designs voltages are named U instead of V

## Slide 45
Ia
Cathode and filament
Vacuum tube
Heater + Cathode
  Heated cathode
    Coated metal, carbides, borides,…
  thermionic emission
  Electron cloud
Anode
Diode
e-
e-
e-
Ua
anode
Basics of grid tube
From diode to tetrode amplifier
E. Montesinos

## Slide 46
Cathode and filament
e-
e-
e-
Ua
anode
Ug1 control grid
e-
e-
e-
e-
Triode
  Modulating the grid voltage proportionally modulates the anode current
  Transconductance
    Voltage at grid
    Current at anode
  Limitations
    Parasitic capacitor from anode to control grid (g1)
    Tendency to oscillate
Basics of grid tube
From diode to tetrode amplifier
E. Montesinos

## Slide 47
Cathode and filament
e-
e-
e-
Ua
anode
Ug1 Control grid
e-
e-
Basics of grid tube
Ug2 Screen grid
Tetrode
  Screen grid
    Positive (lower anode)
    Decouple anode and g1
    Higher gain
  Limitations
    Secondary electrons
    Anode treated to reduce secondary emission
e-
e-
e-
e-
From diode to tetrode amplifier
E. Montesinos

## Slide 48
Tetrode based power amplifier
Ua
Anode
Grounded screen grid
RF in
RF out
Cathode and filament
Example of SPS 200 MHz amplifier, tetrode RS2004
Very simplified block diagram
Ug1 Control grid
Ug2 Screen grid
E. Montesinos

## Slide 49
Example: Tetrode amplifier driving SPS RF
Two transmitters, 2  1 MW at 200 MHz (almost continuous)
Eight tetrodes per amplifier
In operation since 1976
RS2004 tetrode
Amplifier trolley
Complete transmitter
E. Montesinos

## Slide 50
Tetrode amplifier driving PS RF
Frequency range 2.8…10 MHz, ~60 kW per cavity, 11 units
Space constraints to have amplifier installed below cavity
Tetrode is obvious choice
  High power in small volume
  Operates in radioactive environment
Amplifier trolley

## Slide 51
Basics of linear beam tube
Klystron: a complete mini-accelerator
E. Montesinos
Cathode and filament
Ubeam
Uanode
Electron Gun
Drift Space
Collector
Klystrons velocity modulation
  Converts the kinetic energy into RF power
Vacuum tube
Electron gun
  Thermionic cathode
  Anode
Electron beam
Drift space
Collector
e- constant speed until the collector

## Slide 52
Basics of linear beam tube
Klystron: a complete mini-accelerator
E. Montesinos
Cavity
Coupling
loop
Accelerating
gap
Beam
line
Ubeam
Uanode
Cathode and filament
Cavity resonators and drift
RF input cavity (Buncher)
  Modulates electron velocity
Drift space
  Faster electrons catch up
  Slower electrons fall behind
RF output cavity (Catcher)
  Resonating atsame frequency as input cavity
  At place where electrons are maximally bunched
  Kinetic energy converted into voltage and extracted

## Slide 53
Basics of linear beam tube
Klystron: a complete mini-accelerator
E. Montesinos
Cavity resonators and drift
RF input cavity (Buncher)
  Modulates electron velocity
Drift space
  Faster electrons catch up
  Slower electrons fall behind
RF output cavity (Catcher)
  Resonating atsame frequency as input cavity
  At place where electrons are maximally bunched
  Kinetic energy converted into voltage and extracted

## Slide 54
Example: Klystrons driving accelerators
2  8 cavities, each driven by separate 400 MHz klystron, 330 kW
First klystron amplifiers powering a hadron collider
Significantly more power was required to feed LEP (until 2000)
About 50 MW CW was installed at 352 MHz
E. Montesinos
G. McMonagle
12 GHz pulsed klystron for CLIC
50 MW in 1.5 ms

## Slide 55
In a push-pull circuit the RF signal is applied to two devices
  One of the devices is active on the positive voltage swing and off during the negative voltage swing
  The other device works in the opposite manner so that the two devices conduct half the time
  The full RF signal is then amplified
Needs two different type of devices
Basics of RF solid state amplifiers
NPN BJT
PNP BJT
Vin
VDC
Vout
E. Montesinos
BJT: Bipolar Junction Transistor

## Slide 56
Another push-pull configuration is to use a balun (balanced-unbalanced)
  Power splitter, equally dividing the input power between the two transistors
  Balun keeps one port in phase and inverts the second port in phase
Since the signals are out of phase only one device is On at a time
This configuration is easier to manufacture since only one type of device is required
Basics of RF solid state amplifiers
Vdc
Input balun
(Unbalanced-Balanced)
Output balun
(Balanced-Unbalanced)
0 ⁰
0 ⁰
180 ⁰
180 ⁰
NPN BJT
NPN BJT
Vin
Vout
E. Montesinos
NXP Semi- conductors AN11325 2-way Doherty amplifier with BLF888A

## Slide 57
Example: Soleil 45 kW, 352 MHz
DU1029UK
Electron storage ring running at 352 MHz
600 W, 300 VDC/30 VDC converter
330 W amplifier module

## Slide 58
Example: Soleil 45 kW, 352 MHz
Large scale solid state amplifier installations
45 kW per tower (2004 and 2007)
150 kW per tower (2012)
E. Montesinos
Requires a series of power combiners to moderate power per amplifier module to several tens of kilowatts

## Slide 59
Example: BESSY II
500 MHz solid state amplifiers: 4  80 kW for storage ring, 40 kW for booster synchrotron
B. Schriefer
Power per module limited by RF transistors
Increasing with modern semiconductor devices
Amplifier modules
80 kW unit
Combiner

## Slide 60
1.6 MW at cavity input
Example: SPS
200 MHz solid state amplifiers: 2  1.6 MW peak power, 2  16 towers per amplifier
E. Montesinos
80 modules per tower, 1280 modules with 5120 transistors per amplifier
Presently the largest RF installation in a particle accelerator
From LLRF
1/16 splitter

## Slide 61
RF power amplifier
E. Jensen
Power capability of commercially available amplifier types

## Slide 62
How to choose the right RF amplifier?
Prefer tube amplifier, when | Prefer solid-state amplifier, when
Amplifier must be installed in the accelerator tunnel Expecting important spikes from beam induced voltage Large output power of a single device is required, without combiners Not much space is available High peak power in pulsed mode Amplifier must be compact and/or close to cavity | Amplifier can be located in non-radioactive environment Circulator can be installed to protect the amplifier Delay due to unavoidable combiner stages is little issue Sufficient space can be made available Continuous operation Amplifier can be separate from the cavity
Mostly no hard criteria  decide on case by case basis

## Slide 63
Summary
RF system parameters
  Choose frequency and voltage wisely
Parameters of RF cavities
  R, R/Q
  No ‘one-size fits’ all
Power amplifier
  Ideal amplifier does not (yet) exist
  Tube or solid-state based
Feedbacks and longitudinal beam control
  Make the beam feel comfortable in bucket
  Beam phase, radial and synchronization loops

## Slide 64: RF Systems II
H. Damerau
CERN
4 October 2021
Introduction to Accelerator Physics

## Slide 65
The author consents to the photographic, audio and video recording of this lecture at the CERN Accelerator School. The term “lecture” includes any material incorporated therein including but not limited to text, images and references.
The author hereby grants CERN a royalty-free license to use his image and name as well as the recordings mentioned above, in order to post them on the CAS website.
The author hereby confirms that to his best knowledge the content of the lecture does not infringe the copyright, intellectual property or privacy rights of any third party. The author has cited and credited any third-party contribution in accordance with applicable professional standards and legislation in matters of attribution. Nevertheless the material represent entirely standard teaching material known for more than ten years. Naturally some figures will look alike those produced by other teachers.
Copyright statement and speaker’s release for video publishing

## Slide 66
Introduction
Choice of parameters
  Frequency and voltage
RF cavity parameters
  Shunt impedance, beam loading, power coupling
Power amplifiers
  Tube or solid state
  Local feedbacks
Longitudinal beam control system
  Building blocks: RF source and receiver
  Phase, radial and synchronization loops
Summary
Outline

## Slide 67
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 68
Local feedbacks

## Slide 69
Energy transfer from cavity to beam, but from beam to cavity
Both, RF generator and beam can induced voltage in cavity
Reduce beam induced voltage by reducing R, but not efficient
  Obviously needs more power  $$$
Feedback to decrease the apparent impedance for the beam
  Use amplifier to counteract beam induced voltage
C
Reduction of cavity impedance
Drive
Beam
Final amp
R
L
IG
IB

## Slide 70
Energy transfer from cavity to beam, but from beam to cavity
Both, RF generator and beam can induced voltage in cavity
Compare drive signal (no beam) with gap (beam and generator)
Amplify inverted difference
Reduction of cavity impedance
Drive
Beam
Final amp
L
IG
IB
FB ret.
+
V
-
+
C
R

## Slide 71
Gain [dB]
Frequency [MHz]
Transfer function with and without feedback
~24 dB
Example: 10 MHz RF system in CERN PS
Feedback gain of 24 dB
Equivalent impedance, Zeq(w)reduced
Impedance for amplifier remains unchanged, Z(w)
Cavity, amplifier with feedback
Z(w)
Zeq(w)
Why not further reduction with more gain?
Subtraction of gap voltage and drive signal imperfect due to
  Delay of cables and amplifier
  Parasitic resonances of amplifier and cavity system
  Bandwidth   Achievable gain 

## Slide 72
- Fast wide-band feedback
around amplifier (internal)
 Gain limited by delay
  10 + 1 ferrite loaded cavities, tunable from 2.8…10 MHz
Drive
+
FB ret.
+
1-turn delay feedback
Beam
Final amp.
Example: 10 MHz RF system in CERN PS

## Slide 73
- Fast wide-band feedback
around amplifier (internal)
 Gain limited by delay
  10 + 1 ferrite loaded cavities, tunable from 2.8…10 MHz
Drive
+
FB ret.
- 1-turn delay feedback
 High gain at n  frev
+
1-turn delay feedback
Beam
Final amp.
Example: RF feedback with 1-turn delay

## Slide 74
Frequency
Frequency
Log. Amplitude [dB]
10 dB/div
10 dB/div
Feedback off
Feedback on
Open/closed loop transfer functions
Frequency [MHz]
Log. Amplitude [dB]
Reduce cavity impedance beyond stability limit of wide-band FB
Important additional impedance reduction
Clever usage of beam periodicity in circular accelerator
Frequency [MHz]
Spectrum at cavity gap return
hRF=8
hRF=8
D. Perrelet
Example: RF feedback with 1-turn delay

## Slide 75
RF system overview
Cavity
Power amplifier
Low-level RF
system
Beam
Beam
Convert RF power into longitudinal electric field
Amplify low-power signal from beam control to kW, MW or GW
Provide RF signals with correct frequency, amplitude and phase

## Slide 76
Global feedbacks
Low-level RF beam control

## Slide 77
Longitudinal beam control
Local feedbacks  Act on individual RF stations
Global feedbacks  Act on all RF stations simultaneously
Df
Df
Df
RF source
Time of flight compensation
From beam control
RF distribution to compensate time of flight between stations
Beam control drives all stations like a single one
t12
t23
1
2
3
t31

## Slide 78
Basic building blocks

## Slide 79
Two signals at different frequencies w1 and w2
Phase difference, Df, between both signals changes linearly
Ambiguity to distinguish between Df = -p, p, -3p, 3p,...
Saw-tooth in phase means constant frequency difference
Equivalence of frequency and phase
Measure phase differences


## Slide 80
Example: analogue 4 quadrant multiplier and low pass filter
Signals:
Mixer or multiplier

## Slide 81
Example: analogue 4 quadrant multiplier and low pass filter
Signals:
Mixer or multiplier
Remove ripple  Low-pass filter

## Slide 82
Example: analogue 4 quadrant multiplier and low pass filter
Signals:
Phase discriminator in approximately +/-90° range
Remove ripple  Low-pass filter
Relative: arbitrary shift by 90°
How to detect phase differences?

## Slide 83
RF sources

## Slide 84
What finally generates the RF signal to power amplifier and cavity?
Need an RF source!
Electron accelerators
  Off-the-shelf high-performance laboratory generators as reference: BESSY SR, CERN CTF3
  Dedicated commercial fixed-frequency sources with low phase noise: free electron lasers, CERN AWAKE
Proton accelerators
  Special sweeping RF sources, controlled by beam-based loops: mostly in-house developments
RF sources

## Slide 85
Degradation of signal quality due to noise
  Amplitude and/or phase jitter
What is the difference between a coherent signal and noise?
Amplitude of coherent, quasi monochromatic signal (at 200 MHz) is independent of observation bandwidth
Incoherent noise power (dominated by spectrum analyzer front-end amplifier/mixer) is proportional to bandwidth
Thermal noise power
Noisy RF signals
Noise
Noise

## Slide 86
Compare noise power with carrier power as reference
Analysis of phase noise
Ratio of carrier to noise: dBc
Df
Bandwidth Df = 1 Hz for normalization
Noise power density
Its integral is the phase jitter and using
the jitter in time becomes

## Slide 87
Measure phase noise of a synthesized lab generator
Typical phase noise plots
Frequency range | Dtrms [fs]
10…100 Hz | 12.4
100 Hz …1 kHz | 5.4
1…10 kHz | 5.4
10…100 kHz | 11.1
100 kHz…1 MHz | 13.0
Total | 31.0
Note: jitter values can be added as square root of quadratic sum
Convenient split to relevant ranges

## Slide 88
Variable frequency: direct digital synthesis
t
Frequency word
fclk
Phase accumu-lator
sin
cos
sin/cos
look-up
t
t
f
RF signal
Digital data
Generate (almost) any frequency starting from a given clock frequency, fclk
Digitally programmable in frequency
2n adder

## Slide 89
RF signal
Digital data
Generate (almost) any frequency starting from a given clock frequency, fclk
Digitally programmable in frequency and phase
t
Frequency word
fclk
Phase accumu-lator
sin
cos
CORDIC
t
t
f
Phase offset word
t
f
Two output signals with ideal 90° phase shift
Output signals are digital data streams
2n adder
Variable frequency: direct digital synthesis
COordinate Rotation DIgital Computer

## Slide 90
Receivers

## Slide 91
I/Q representation of signals
Any signal can be represented by amplitude A and phase f
In phase, I and quadrature, Q describe the same signal
Avoids phase discontinuities at 0, 2p, …
A
f
I
Q

## Slide 92
Signal receivers
Radio with listens to beam or cavity signals
Listens to amplitude and phase
With win ≈ wLO input signal is down-converted to base-band
Resulting I/Q vector rotates slowly with win - wLO
I
Q
I
Q

## Slide 93
Digital receivers
No conceptual difference between analogue and digital
Digitization can be performed at any level
Analog down-conversion of I and Q, then digital processing
High input frequencies beyond ADC sampling rates
I
Q
I
Q
ADC
ADC

## Slide 94
No conceptual difference between analogue and digital
Digitization can be performed at any level
Analogue mixers become digital multipliers
All digital receiver
Theoretically perfect I/Q symmetry
Digital receivers
I
Q
I
Q
ADC

## Slide 95
Vector modulator

## Slide 96
Convert I/Q data into modulated RF signal
Invers receiver: vector modulator
I
Q
DAC

## Slide 97
Convert I/Q data into modulated RF signal
Perfect I/Q symmetry difficult to achieve
Up-conversion of digital signal to a high RF frequency
Inverse receiver: vector modulator
I
Q
DAC
DAC

## Slide 98
Beam phase loop

## Slide 99
fin, fin
Df
Electronic phase-locked loop
Loop filter, H(w)
VCO
RF
Slow signal
Frequency re-generation and multiplication
Voltage controlled oscillator (VCO) locked in phase to input
fout, fout
fVCO
~fin - fVCO
1
n
Fixed phase relationship: fout/n – fin = const.
Optional divider: fout = n · fin

## Slide 100
Beam phase
Df
-
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
DDS
Digital synthesizer
RF
Slow signal
h frev (digital)
fRF
Loop filter
h · frev, from B, p
ferr ~Df

## Slide 101
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
DDS
Phase-locked loop with beam phase as reference for RF system
Digital synthesizer
fout = fin ± Df
fRF
Loop filter
h · frev, from B, p
Precision VCO
RF
Slow signal
h frev (digital)
ferr ~Df

## Slide 102
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
DDS
Fast control of RF frequency to cavities, but no slow corrections
Digital synthesizer
fout = fin ± Df
Precision VCO
fRF
Loop filter
h · frev, from B, p
RF
Slow signal
h frev (digital)
ferr ~Df
Move the wave!

## Slide 103
Effect of beam phase loop at injection
Example: Injection of a bunch from PS Booster into PS
Essential in hadron accelerators to keep RF locked to beam
How does this look like in longitudinal phase space?
90° error, phase loop off
90° error, phase loop on

## Slide 104
Effect of beam phase loop at injection
Bunch in rigid bucket, no loop
Injection with phase loop
Essential in hadron accelerators to keep RF locked to beam
Even large transients (injection, transition) are controlled
Only minor longitudinal perturbation

## Slide 105
Beam phase loop during acceleration
What happens with phase loop during acceleration?
During plateaus the phase between RF and beam is either 0° or 180°
Fast phase changes well handled, but need slow frequency correction
Radial or synchro-nization loop
1.48 s
Df
Injection
Acceleration to intermediate plateau
Intermediate
plateau
Restart acceleration
Transition
End of acceleration
Ejection

## Slide 106
Radial loop

## Slide 107
Radial loop
Hybrid
D
S
D/S
DR
Reference magnet
B+
B-
B
frev
Df
h·frev
DDS
Frequency program
RF
Slow signal
Digital signal
Beam
Slow correction of average RF frequency

## Slide 108
Radial loop
Slow correction of RF frequency to keep beam centred
Why needed at all with arbitrary precision synthesizers driving the RF system?
At transition energy
  Longer path of higher energy particle compensated by higher velocity
  No revolution frequency change for energy offset
Need beam-based frequency correction

## Slide 109
Synchro(nization) loop

## Slide 110
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Beam phase loop
+
DDS
Fast control of RF frequency to cavities, but no slow corrections
h · frev, from B, p
fout = fin ± Df
ferr ~Df
fRF
Loop filter
Digital synthesizer
Precision VCO
RF
Slow signal
h frev (digital)

## Slide 111
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
Synchronization loop, internal reference
+
DDS
fRF
Loop filter
Ref.
DDS
Df
fRF, ref.
Avoids noise from radial detection when not crossing transition
h · frev, from B, p
Loop filter
RF
Slow signal
h frev (digital)
ferr ~Df

## Slide 112
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Cavity phase
Power amplifier
Synchronization loop, external reference
+
DDS
fRF
Loop filter
Df
fRF, ref.
h · frev, from B, p
Loop filter
fRF, ref from another accelerator
Synchronize between accelerators for transfer
RF
Slow signal
h frev (digital)
ferr ~Df
Synchronous phase, fs

## Slide 113
Before synchronization
Target accelerator is master at transfer
Target accelerator is master at transfer
Simple test case of circumference ratio 2: C2 = 2C1
Synchronize both accelerator to force: frev,1 = 2frev,2

## Slide 114
After synchronization
Source or target accelerator is master at transfer
Simple test case of circumference ratio 2: C2 = 2C1
Revolution frequencies coupled: frev,1 = 2frev,2
Ready to extract during every turn of the target accelerator

## Slide 115
Summary
RF system parameters
Parameters of RF cavities
Power amplifier
Local feedbacks
  Direct and 1-turn delay feedback
Building blocks of low-level RF systems
  Phase comparison, RF sources and receivers
Basic global feedback loops
  Beam phase, radial and synchronization loops
Make the beam feel comfortable!

## Slide 116
A big Thank You
to all colleagues providing support, material and feedback
Maria-Elena Angoletta, Philippe Baudrenghien, Thomas Bohl, Giorgia Favia, Jörn Jacob, Erk Jensen, John Molendijk, Eric Montesinos, Gerry McMonagle, Mauro Paoluzzi, Damien Perrelet, Bernhard Schriefer, Lukas Stingelin, Fumihiko Tamura, Frank Tecker, Daniel Valuch and many more…

## Slide 117
Thank you very much for your attention!

## Slide 118
References
D. Boussard, Design of a Ring RF System, CERN SL/91-2 (RFS, rev.), 1991, http://cds.cern.ch/record/1023436/files/CM-P00065157.pdf
E. Montesinos, Accelerators for Medical Applications - Radio Frequency Powering, CERN-2017-004-SP, http://cds.cern.ch/record/2315172/files/1804.08535.pdf
R. Garoby, Low level rf building blocks, CERN-1992-003, 1991, http://cds.cern.ch/record/225609/files/CM-P00059483.pdf
J. W. Wang, G. A. Loew, Field Emission and RF Breakdown in High-Gradient Room-Temperature Linac Structures, SLAC-PUB-7684, 1997, http://www.slac.stanford.edu/cgi-wrap/getdoc/slac-pub-7684.pdf
W. D. Kilpatrick, Criterion for vacuum sparking designed to include both rf and dc, Rev. Sci. Instrum. 28 (1957), 1957, http://inspirehep.net/record/44645

## Slide 119
For a single harmonic RF system
with it becomes
using
this simplifies to
Normalized Hamiltonian representation

## Slide 120
Efficient implementation of low pass filter
Standard form with sampling rate decimation: fclk  fclk/d
Cascaded integrator-comb filter (CIC)
z-1
-
+
z-1
-
+
…
+
z-1
+
+
z-1
+
…
Comb stages
Integrator stages
#1
#n
#1
#n
fclk
Fclk/d
n: filter order
d: decimation ratio
Easy to implement in programmable logic: no multipliers
Only adders and shift registers

## Slide 121
Why particularly interesting for circular accelerators?
Choose clock frequency, fclk = 2m frev and decimation d = 2m
Notches at all multiples of frev except zero
Linear phase f(f)  filter behaves like a constant delay
Ideal low-pass filter in digital receivers
  Filter selected multiple of frev while suppressing all others
Cascaded integrator-comb filter (CIC)
Amplitude
Phase
Example:
fclk = 128frev,
d = 128,
n = 3

## Slide 122
Thermal drift of long coaxial cables or optical fibres
Thermal coefficient of delay:
Transmission of reference signals
RG223 coaxial cable
Example: 2 km long RG223 cable with ~10 ms delay
DT of only 1° C (room temperature) changes delay by ~0.5 ns
1.8° at 10 MHz (CERN PS), but 73° at 400 MHz (LHC)
Optical fibres are typically 10…100 times more stable
What to do if this is still not sufficient?
Lutes/Diener, NASA TDA Progress Report 42-99

## Slide 123
Simple synchronization process
Bunch should be here
Locked!
Df
Beam azimuth
(from phase loop)
Ref. azimuth (from master divider)
frev (h = 1)
Act on fRF of slave
Df
200 ms
Move beam to off-momentum (B const.):
  Well defined frequency difference between accelerators
Measure azimuth error, when beam at correct azimuth
  Close synchronization loop
  Moves beam to ref. momentum