## Slide 1: Present status and upgrade plan of the Positron source
2021/4/15
Y. Enomoto

## Slide 2: Outline
Requirement and issues
Present status
Short term (Near future) plans
Mid term plans
Long term plans (Beyond 4 nC / bunch)
Major upgrade was done in 2020
→ Most of the problems so far were solved
Now, it’s time to consider next steps

## Slide 3: SuperKEKB positron source
W target
BC (bridge coil)
FC(flux concentrator) head
LAS (large aperture S-band)
solenoid
FC head + BC + target = FC assembly

## Slide 4: Injection requirement
Life in ring | 360 s
Current | 3.6 A
Injection bunch charge | 4 nC
Injection rate | 25 Hz x 2 bunch
Injection efficiency | 50 %
Circulation frequency | 105
Life time in the ring determines how much positron is needed.
K. Furukawa

## Slide 5: Problems to be solved
Discharge of FC
  New material for FC
  Optimization of support structure (done before 2020)
  External circuit to reduce voltage (done before 2020)
  Longer pulse width (will be done after 2021)
Orbit correction in solenoid
  Steering coils
  BPMs

## Slide 6: Discharge of the FC
1 kV / turn @ 12 kA operation 6 us pulse width
Slit gap = 0.2 mm
6 us
FC current (kA)
FC current waveform measured by CT
5 MV/m

## Slide 7: Yield strength
Chart: Yield strength (Mpa)
| C1020 | SH-1 | SH-2 | NC50
before brazing | 322.3 | 293.6 | 348.2 | 551.8
after brazing | 12.9 | 57.9 | 40.8 | 109.7
brazing + aging | 513.1
x40
C1020 after brazing
NC50 after brazing
NC50
NC50 after aging
(precipitation hardening)
C1020
Yield strength (MPa)

## Slide 8: Assembly, base management (2021/1 ver.)
 | Phase 1 | Phase 2 | Phase 3 | 2019 Q4 | 2020 ab | 2020c | delivered | removed | present | Note
Assembly 1 |  |  |  |  |  |  | <2015 | 2017/3 | In tunnel | 
Assembly 2 |  |  |  |  |  |  | 2016/3 |  | In operation | 
Assembly 3 |  |  |  |  |  |  | 2017/11 |  | Test bench | 
FC base 1 |  |  |  |  |  |  | <2015 |  |  | Test
FC base 2 |  |  |  |  |  |  | <2015 |  |  | Test
FC base 3 |  |  |  |  |  |  | <2015 | 2017/3 | In tunnel | 
FC base 4 |  |  |  |  |  |  |  | 2018/9 | In tunnel | 
FC base 5 |  |  |  |  |  |  | 2016/7 | 2020/9 | In tunnel | 
FC base 6 |  |  |  |  |  |  | 2017/11 |  | Test bench | bad quality
FC base 7 |  |  |  |  |  |  | 2019/10 |  | Test bench (back up) | New material
FC base 8 |  |  |  |  |  |  | 2020/6 |  | In operation | Final version
FC base 9 |  |  |  |  |  |  | 2021/3 |  | Test bench | Saper for Final version
in operation
spare
test bench
Material test started in 2018/10

## Slide 9: Orbit deflection in solenoid section
Measured by T. Kamitani
1,Prepare ballistic beam between SP_15_T and SP_16_5
2,Energize a part of solenoid by
1/10* max. value step.
3, Monitor beam position at SP_16_5
Measurement of deflection amount of 3 GeV electron beam
by asymmetric field in solenoid section
SP : BPM
SL : solenoid
QF/QD : quad
PX/PY : pusled steering
BM : bend
SC : screen
AC : acc. structure

## Slide 10: Asymmetry of magnetic connection
Iron yoke to connect flux of solenoid
need space for waveguide and support
Bx
By
Inner diameter of solenoid changes

## Slide 11
target
BPM and 1st steering
There were no BPMs and steerings for 22 m after the target

## Slide 12: BPM and steering coils inside solenoid
K. Yokoyama and K. Kakihara
BPM
Steering coil
support

## Slide 13: Orbit deflection by yoke
Asymmetric shape of yoke and saturation of magnetic field generate Bx, By inside yoke.
Simulation explain experimental results well.
A Yoke to concentrate magnetic flux by the BC to the target
Transvers magnetic field on beam axis (center) is not proportional to BC current.
If permeability is infinite, Bx, By is zero inside the yoke even if the shape is not symmetric

## Slide 14: Upgrade the yoke
old
new
Shape was optimized
To increase Saturation magnetic flux density,
material was changed from
ordinary steel (SS400, 1.5 T) to
permendur (K_MP11, 2.2 T)

## Slide 15
BC=650A
Peak value
Integrated value
X0.024
X0.158
X1.16

## Slide 16: installation
During 2020 summer shutdown,
  A new FC
  Two fast BPMs
  Two ordinary BPMs
  One vertical steering coil
  Three horizontal steering coils
Remove old positron source
Install new positron source

## Slide 17: Positron yield vs FC current
Design (0.58)
Present
(Further tuning was done after this measurement. Now the yield almost reached design value. See next page)
Before upgrade
(To avoid discharge,
FC current was limited very low)

## Slide 18: Recent status (2021a)
 | design | 2020ab | 2020c | 2021a | 2021a (10 nC, 0.58)
Energy (e-) | 3.5 GeV | 3.5 GeV | 3.5 GeV | 3.5 GeV | 
primary charge (e-) | 10 nC | 8.4 nC | 8 nC | 9 nC | 
e+/e- | 0.58 | 0.24 | 0.51 | 0.58 | 
e+ @ first BPM after the target | 5.8 nC | 2.0 nC | 4.1 nC | 5.1 nC | 5.8 nC (assume)
e+ @ before DR | - | 1.6 nC | 2.5 nC | 3.2 nC | 4.2 nC
e+ @ after DR | - | 1.4 nC | 2.1 nC | 2.9 nC | 3.3 nC
e+ @ Linac end | 4 nC | 1.4 nC | 2.1 nC | 2.9 nC | 3.3 nC
Primary beam
  90% (9 nC / 10 nC)
Positron yield（e+/e-）
  100% (0.58 / 0.58)
transport
  Assuming 5.8 nC (design value) @ first BPM after the target and present transport efficiency, charge @ Linac end is expected to be 3.3 nC.
  There is still room for improvement
Primary electron
First BMP after target
Before DR
After DR
Linac end
e+/e- design
Further beam tuning
Hardware upgrade

## Slide 19: Gradient after the target
name | Design gradient (MV/m) | Operation gradient (MV/m) 2020/10/30 | Max gradient @ KLY power = 40 MW
AC_15_1 | 14.0 | 7.3 | 17.0
AC_15_2 | 14.0 | 7.3 | 17.0
AC_16_1 | 10.0 | 11.3 | 12.2
AC_16_2 | 10.0 | 11.3 | 12.2
AC_16_3 | 10.0 | 11.3 | 12.2
AC_16_4 | 10.0 | 11.3 | 12.2
Data from H. Ego
https://www.pasj.jp/web_publish/pasj2014/proceedings/PDF/SAP0/SAP045.pdf
https://doi.org/10.18429/JACoW-IPAC2014-THPRI047
Due to the load problem, gradient of the first and second acc. structure after the target is low.
This may cause poor bunching which can be one of the reason for large beam loss during transportation to the DR.

## Slide 20: Fast BPM to decompose e+/e- in solenoid
Steering coils
BPM
Fast BPM
electron
positron
175 ps
To monitor positron in solenoid section, very fast response BPM was developed by
Monitor group (T. Suwada, F. Miyahara, A. Rehman)
Simulation by F. Miyahara
Small antenna
e+/e- separation chicane

## Slide 21: Transport between Target and DR
AC_15_1
AC_15_2
AC_16_1
AC_16_2
AC_16_3
AC_16_4
FC
+
target
AC_17_1
AC_17_2
AC_17_3
AC_17_4
AC_18_1
AC_18_2
AC_18_3
AC_18_4
solenoid
solenoid
Q
Normal
LAS
Solenoid section (15 m)
Quad section (115 m)
Electron / positron separator
 | LAS | Normal S band
Acc. Gradient (MV/m) | 14/10 | 20
Aperture (mm) | 30 | 20

## Slide 22: Transport between Target and DR – increase pulsed steering
To dumping ring
1-5
1-6
1-7
1-8
Normal x 32
LAS x 10
10m
2-6
2-1
2-2
2-3
2-4
2-7
2-8
Target & FC
15m long solenoid
About 100 Quad magnet
1.1 GeV @ DR
There are only 8 pulsed steering magnets. Others are DC magnets.
→Increase 6 pulsed steering magnets in 2021 summer shutdown.

## Slide 23: Transport between Target and DR – replace DC Q with pulsed Q
Surrounding Acc. Structure = impossible to be pulsed
Between Acc. Structure = possible to be pulsed

## Slide 24: Transport between Target and DR – replace DC Q with pulsed Q
Replace several DC Q magnets with pulsed Q magnets (2022～).
Also important for preserving electron emittance.
Surrounding Acc. Structure = impossible to be pulsed
Between Acc. Structure = possible to be pulsed

## Slide 25: Short term plans（1～2 years）
Increase Acc. Gradient at 1-5 unit（H. Ego）
  New load for the Acc. structure（under development）
Install pulsed magnets between target and DR（T. Natsui、K. Yokoyama、Y. Okayasu、T. Kamitani、Y. Enomoto）
  Increase steering magnets（2021）
  Replace DC Q magnets with pulsed Q magnets（2022）
Fast BPM （T. Suwada、F. Miyahara、A. Rehman）
  Under test
Increase FC current（RF group）
  Thanks to new material, higher current operation may be possible.
    Stable operation has been confirmed up to13 kA at test bench.
  Upgrade of the power supply is necessary（2021～）
Increase primary electron charge（M. Yoshida）
  It’s not difficult to increase current by increasing heater current
  Dark current to the PF ring issue have to be solved
Major upgrade was done in 2020 summer shutdown
Increase positrons up to 4 nC by several minor improvements.
Now, it’s time to consider new strategy for long term goal.

## Slide 26: Mid term plan（2～3 years）
Optimization of FC shape
  (unofficial) collaboration with CERN
Moving target
Decrease distance between FC and the first acc. structure

## Slide 27: Optimization of FC shape
H. Bajas @ LCWS2021

## Slide 28: Optimization of FC shape
H. Bajas @ LCWS2021

## Slide 29: Optimization of FC shape
H. Bajas @ LCWS2021

## Slide 30: Magnetic field simulation
~ 2014
Now
Simulation using realistic model and measured current shape was established
Excitation current

## Slide 31: Pulse width dependence
Magnetic field shape is determined by skin depth
It is important to use realistic current waveform for simulation.
Pulse width | short | Long
Magnetic field | strong | weak
voltage | high | Low
For fixed current

## Slide 32: Conduction current distribution in FC
Jx : conduction current density in x direction
y
z
Plot Jx as a function of y

## Slide 33: Jx vs y - pulse width dependence

## Slide 34
Frequency (kHz) | Skin depth(mm)
5 | 1.21
40 | 0.96
83 | 0.77
1000 | 0.43

## Slide 35: Slit width dependence of magnetic field

## Slide 36: Magnetic field measurement
Pick up coil is mounted on FRP rod.
XYZ stage with motor drive
Rotary stage with motor drive
XYZ positions are monitored by linear gauge by 10um precision

## Slide 37: Looking from downstream side with the measurement system attached

## Slide 38: Comparison between simulation and measurement
Chart: z (mm)
| 100 | 94.999999999999901 | 89.999999999999901 | 84.999999999999901 | 79.999999999999901 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 5 | 4.7999999999999901 | 4.5999999999999899 | 4.4000000000000004 | 4.2 | 4 | 3.7999999999999901 | 3.5999999999999899 | 3.3999999999999901 | 3.2 | 3 | 2.7999999999999901 | 2.5999999999999899 | 2.3999999999999901 | 2.19999999999999 | 2 | 1.7999999999999901 | 1.5999999999999901 | 1.3999999999999899 | 1.19999999999999 | 1
exp x2 | 0.15497 | 0.1959 | 0.21521 | 0.24804 | 0.26996 | 0.29178 | 0.31555 | 0.32743 | 0.35086 | 0.36473 | 0.38128 | 0.452 | 0.47391 | 0.49298 | 0.51528 | 0.55739 | 0.58844 | 0.58884 | 0.59933 | 0.60532 | 0.61396 | 0.6219 | 0.62485 | 0.63785 | 0.65382 | 0.67115 | 0.71149 | 0.75099 | 0.77719 | 0.81174 | 0.88055 | 0.93879 | 0.97571 | 0.97477 | 0.98448 | 0.99453 | 0.99017 | 0.99451 | 0.99777 | 1 | 0.99334 | 0.98329 | 0.97316 | 0.95992 | 0.93789 | 0.91412 | 0.88005 | 0.83813 | 0.81469 | 0.76529 | 0.67364 | 0.62621 | 0.53194 | 0.46263

## Slide 39: Mid term plan（2～3 years）
Optimization of FC shape
  (unofficial) collaboration with CERN
Moving target
Decrease distance between FC and the first acc. structure

## Slide 40: Target detail
X = 0
looking from downstream side
Target material : W
Target size : Φ4 x 14
Inserted in the pule Cu block
Connected by HIP process
X = 0 hole for electron
X = 2 center of the FC
X = 3.5 center of the W target
Primary beam size ～ 1 mm

## Slide 41: Improvement of positron yield by bringing the target and the FC to the beamline axis
Present
configuration
Bring to
center
Simulation by M. Fukuda
Injection beam size

## Slide 42: Requirement for e+/e-
e+：center of the target and the FC should be coincide with the center of the beam line
e-：increase hole size for flexible beam tuning
To fulfill both requirements, moving target is needed
  Target is inserted to the beamline only when the beam mode is KBP
    Fast (< 20 ms) and flexible control is required not to restrict operation pattern.
  Rotating type：arrangement of cooling water is difficult
  Linear motion type： high acceleration → mechanical shock

## Slide 43: Moving target – an idea
Guide by cam＋variable lift mechanism
  Cam shaft rotate at constant speed
  Increase lift only when the mode is KBP
  Minimize part which moves at high acceleration
  50 Hz = 3000 rpm
    Not unrealistic speed but careful evaluation of durability is important
If you have any ideas, please share them!!
https://gifmagazine.net/post_images/662332

## Slide 44: Mid term plan（2～3 years）
Optimization of FC shape
  (unofficial) collaboration with CERN
Moving target
Decrease distance between FC and the first acc. structure

## Slide 45: Beam loss between FC and the first Acc. structure
Calculated by T. Kamitani
Most of the positrons are lost between the FC and the
first Acc. Strucure.
福田さんによるGEANTを使ったsimulation

## Slide 46: Beam loss between FC and the first Acc. structure
simulation by M. Fukuda
In this simulation, aperture of the duct is not taken into consideration,
which is the reason why the number of positron does not decrease around Z = 150 ~ 230

## Slide 47
Layout of the SLC
In the SLC, distance between the FC and the first acc. structure is quite short.
In the SuperKEKB, the distance was determined taking workability into account ten years ago.
Experiences, records, tools and jigs on work around the target are accumulated
→New design to minimize the distance is possible now.
→Further reduction of the distance is possible, if the standing wave acc. structure is used, since the input coupler is able to be moved to downstream side.
Input coupler
Deterioration of the Acc. Structure by radiation is one of concern.
→easy replacement mechanism is desired.

## Slide 48: Beyond 4 nC / bunch
Increase beam power of primary electron
  Increase energy
    Do not consider this time
  Increase bunch charge
    Electron gun at C sector (after the arc)
Increase capture efficiency
  Increase magnetic field (magnetic field ratio is also important)
    Superconducting magnet
  Increase aperture
    L band acc. structure
If the 4 nC / bunch restriction is removed,
how much impact does it have on the long term (after upgrade of the QCS) operation?

## Slide 49: Beyond 4 nC / bunch
Increase beam power of primary electron
  Increase energy
    Do not consider this time
  Increase bunch charge
    Electron gun at C sector (after the arc)
Increase capture efficiency
  Increase magnetic field (magnetic field ratio is also important)
    Superconducting magnet
  Increase aperture
    L band acc. structure
If the 4 nC / bunch restriction is removed,
how much impact does it have on the long term (after upgrade of the QCS) operation?

## Slide 50: Electron gun at C sector
target
New electron gun
☓ acc. distance between e gun and targe decrease → beam energy decrease
(half of present energy)
○ no arc section → energy spread is not important. Easy beam tuning
If it’s possible to deliver primary electron beam over 20 nC / bunch, total primary beam power increase
Concern about heat on target.
PEDD (Peak energy deposition density (J/g))
cooling power

## Slide 51: PEDD（10 nC / bunch x2）
Simulation by Y. Morikawa
Distribution of energy deposition per pulse
Max. energy deposition along beam
axis per pules

## Slide 52: PEDD（10 nC / bunch x2）
Empirical Criterion : PEDD < 35 J/g
If the value is larger than criterion, increase beam size on the target.
Simulation by Y. Morikawa

## Slide 53: Cooling power and target temperature
KBP 2bunch
(total 11 nC @ SP_15_T)
Assume beam energy on target as 3.2 GeV
900W @ 25Hz 2bunch (11 nC total)
→temperature rise is 30 deg
→dumped power to the cooling water was 150 W
At 50Hz 2 bunch (20 nC in total),
beam power is 3600W
→temperature rise is 120 deg
Cooling power calculated from
cooling water temperature and flow
5 Hz
12.5 Hz
25 Hz
0 Hz
Empirical Criterion : If the beam power is < 10 kW, water cooled fixed targe works fine.

## Slide 54: Beyond 4 nC / bunch
Increase beam power of primary electron
  Increase energy
    Do not consider this time
  Increase bunch charge
    Electron gun at C sector (after the arc)
Increase capture efficiency
  Increase magnetic field (magnetic field ratio is also important)
    Superconducting magnet
  Increase aperture
    L band acc. structure
If the 4 nC / bunch restriction is removed,
how much impact does it have on the long term (after upgrade of the QCS) operation?

## Slide 55: Superconducting magnet
Replace FC with superconducting solenoid
  Flexible magnetic field profile
    Field at the entrance of the first acc. structure can be chosen freely
    High magnetic field at the exit surface of the target
      In the case of FC, B ≒ 0 due to eddy current
Increase magnetic field in the capture solenoid
  superconducting？

## Slide 56: Principle of AMD
B2 < B1,
Angle and position can be adjusted
by the ratio of magnetic field.
B1
B２
Velocity : v1
r position : r1
Angle : φ1
Velocity : v2
r position : r2
Angle : φ2
OHO’19
AMD : adiabatic matching device. FC is one type of AMD.

## Slide 57: Effect of eddy current on target
I. Chaikovska, “Status of the FCC-ee positron source” LCWS2021
Max. magnetic field should be at the exit surface of the target.
However, distance between the FC and the target cannot be zero.
In addition, pulsed magnetic field induce eddy current on the targe surface which reduce magnetic field from the FC.
Positron from the target surface travels to some position non-adiabatically, then captured to the field line and moves adiabatically.
Effective max. magnetic field is the field where the positron is captured to the field line
exit surface of the target

## Slide 58: Simulation model With target
This taper is important to reduce eddy current on the target

## Slide 59: Simulation model with Cu plate
Plate material : OFC
Distance between plate and FC : 2 mm

## Slide 60: Target dependence
Eddy current on the target reduce magnetic field by FC

## Slide 61: Consideration about superconducting magnet
Eddy current issue is avoided using DC magnet
  Increase effective max. magnetic field.
Superconducting magnet is necessary for generating a few Tesla DC magnetic field
  Present FC generate about 3.7 T at peak.
There are many things to do to operate superconducting magnet
  No infrastructure for cryogenics in the linac

## Slide 62: Increase magnetic filed in Capture solenoid section
Positron yield peak out around FC current is about 12 kA.
Field ratio may limit the yield
Increase the field in the following section will affect the yield.
Detailed simulation is planed.
Simulation by M. Fukuda
0.4 - 0.5 T
Two types of solenoid coils are used
0 - 5 m : large inner diameter type
5 - 15 m : small inner diameter type

## Slide 63: Beyond 4 nC / bunch
Increase beam power of primary electron
  Increase energy
    Do not consider this time
  Increase bunch charge
    Electron gun at C sector (after the arc)
Increase capture efficiency
  Increase magnetic field (magnetic field ratio is also important)
    Superconducting magnet
  Increase aperture
    L band acc. structure
If the 4 nC / bunch restriction is removed,
how much impact does it have on the long term (after upgrade of the QCS) operation?

## Slide 64: Increase aperture and choice of frequency
S. Tantawi., et al, “Distributed Coupling Accelerator Structures: A New Paradigm for High Gradient Linacs”, arXiv:1811.09925
Increase aperture
→decrease shunt impedance
→decrease acc. Gradient
→decrease is slower for longer wavelength
Aperture of normal acc. structure is 20 mm
Aperture of LAS (used for 10 acc. structure after the target) is 30 mm
Both of them are S-band.
L-band is preferable for further increasing aperture.

## Slide 65: L-band acc. structure
Prototype (8 years ago) stored in the linac tunnel

## Slide 66: Summary
Major upgrade was done in 2020 summer
  Positron charge is increased to 2.9 nC / bunch.
  Increase positrons up to 4 nC by several minor improvements for the time being.
Summarize possible upgrade plans in short, mid and long term
  Is there demand beyond 4 nC?
In addition to members of the linac, collaboration with people from the future project are very important for discussion, simulation and compensation for lack of man power.
  ILC : M. Fukuda, Y. Morikawa (CASA, KEK)
  FCC-ee : I. Chaikovska (IJCLab)
  CLIC : H. Bajas (CERN)