## Slide 1: Progress on the development of key technologies for the 4th generation ECR ion source FECR
L. Sun, H. W. Zhao, J. W. Guo, W. Wu, B. M. Wu, X. J. Ou, E. M. Mei, S. J. Zheng,
X. Z. Zhang, L. Zhu, C. J. Xin, Y. Q. Chen
and the other FECR team members
Institute of Modern Physics, CAS, 730000, Lanzhou, China
ICIS’21, Sept. 20~24, 2021, TRIUMF, Canada
IMP
W. Lu

## Slide 2
Outline
High Intensity HCI Beam Needs
FECR: a 4th Generation ECRIS
Key Technologies Development for FECR
  FECR magnet progress
  Microwave system
  Plasma chamber cooling
Summary

## Slide 3
HIAF Layout
High Intensity heavy-ion Accelerator Facility (HIAF，2018-2025)
T1
SECR
HFRS
T2
T3
T4
T5
T6
BRing: Booster Ring
C: 569 m
Bρ: 34 Tm
SRing: Spectrometer ring
C: 278m
Bρ: 15Tm
iLinac: Superconducting linac
E: 17 MeV/u( 238U35+)
iLinac-2 (reserved)
E: 100 MeV/u U46+
Physics:
Low energy nuclear structure terminal
Multi-discipline terminal
High energy fragment separator HFRS
High precision spectrometer ring SRing
Radioactive isotope beam terminal
High energy density physics terminal
E: 14 keV/u (238U35+)

## Slide 4
HIAF Main Specifications
 | SECR | iLinac | BRing | HFRS | SRing
Length / circumference (m) | / | 114 | 569 | 192 | 277
Beam Species | H2+~Un+ | H2+~Un+ | H~U | / | /
Final energy of U (MeV/u) | 0.014 (U35+) | 17 (U35+) | 835 (U35+) | 800 (U92+) | 800 (U92+)
Max. magnetic rigidity (T.m) | / | / | 34 | 25 | 15
High Power Mode (pulsed) | 50 pμA (U35+) | 28 pμA (U35+) | 1011ppp (U35+) | / | 1010ppp (U92+)
High Energy Mode (CW) | >10 pμA (U46+) | >6 pμA (U46+) | / | / | /
Operation mode | DC | CW | / | / | /
 | Pulsed 0.2~2 ms/3 Hz | Pulsed 0.2~2 ms/3 Hz | fast ramping (12 T/s, 3 Hz) | Momentum-resolution 1100 | DC, deceleration
Emittance or Acceptance (H/V, ·mm·mrad, dp/p) | ≤0.2 | 5 / 5 | 200/100, 0.5% | 30mrad(H)/15 mrad(V), 2% | 40/40, 1.5% (normal mode)
The highest beam intensity requirement for highly charged heavy ions in the world

## Slide 5
High Intensity HCI Beam Needs: Production
2nd G ECRIS
3rd G ECRIS
4th G ECRIS
238U

## Slide 6
FECR: What is a 4th G ECRIS?
Electron Cyclotron Resonance Ion Source
Plasma
Magnet
Microwave
Higher B Field!
Higher Frequency!
Bigger Volume!
Higher rf power!

## Slide 7
State of the Art ECRIS: 3rd G Sources
VENUS@LBNL: 28+18 GHz
SCECRISs@RIKEN: 28+18 GHz
SuSI@MSU: 24+18 GHz
SECRAL, SECRAL-II@IMP: 28/24+18 GHz

## Slide 8
FECR: a 4th G ECRIS
Specs. | Unit | 3rd G ECRIS | 4th G ECRIS | FECR
frequency | GHz | 24-28 | 40~56 | 45
Operational RF Power | kW | 4~10 | 10~40 | 20
BECR | T | 0.86~1.0 | 1.4~2.0 | 1.6
Brad | T | 1.8~2.2 | 2.8~4.0 | ≥3.2
Binj | T | 3.4~4.0 | 5.6~8.0 | ≥6.4
Bmin | T | 0.5~0.7 | / | 0.5~1.1
Bext | T | 1.8~2.2 | 3.0~4.5 | ≥3.4
Plasma Chamber ID | mm | 100~150 | >100 | ≥140
Mirror Length | mm | 420~500 | ≥500 | 500
Cooling Capacity@4.2 K | W | 0~6.0 | >10.0 | ≥10.0

## Slide 9
FECR: Challenges
Specs. | Unit | FECR | Challenges
frequency | GHz | 45 | High frequency high power microwave coupling High power plasma chamber & components cooling
Operational RF Power | kW | 20 | 
BECR | T | 1.6 | Reliable High Field Magnet with min-B Field Configuration
Brad | T | ≥3.2 | 
Binj | T | ≥6.4 | 
Bmin | T | 0.5~1.1 | 
Bext | T | ≥3.4 | 
Plasma Chamber ID | mm | ≥140 | 
Mirror Length | mm | 500 | 
Cooling Capacity@4.2 K | W | ≥10.0 | Radiation degradation and dynamic heat load
U35+ | mA | >1.0 | Intense solid material beam production
Pulsed Beam Frequency | Hz | 0.5~3 | High afterglow yield and pulse duration
Afterglow pulse width | ms | >2.0 | 
See Lixuan Li’s Poster-41 on Sept. 23
Wang Lu, et al., Rev. Sci. Instrum. 92, 033302 (2021)

## Slide 10
FECR Progresses: towards the Challenges
  FECR magnet progress
    Coldmass and cryogenics
  Microwave system
    High power high frequency microwave transmission and coupling
  Plasma chamber & Components cooling

## Slide 11
FECR Progresses: Magnet
3rd G ECRIS
4th G ECRIS
500
1100
7.0
12
Courtesy of MagLab
Nb3Sn vs. NbTi:
Treatment sensitive
Stress sensitive

## Slide 12
FECR Progresses: Magnet
Coldmass Structure
1st Stage@50 K
2nd Stage@4.2 K
Vacuum iron shield
Copper shield
G10 Suspension
Coldmass
Warmbore
Radial Support Rods
Axial Support Rods
Magnet Structure

## Slide 13
FECR Progresses: Magnet
COIL-PACK
SUBASSEMBLY
COLLARS
SEXTUPOLE
COILS
AXIAL-LOAD
END PLATE
SUBASSEMBLYS
SOLENOID
STRUCTURE
SUBASSEMBLY
SHELL-YOKE
SUBASSEMBLY
(Shell is strain gauged)
MASTER-KEY PLATES
BLADDER
SUBASSEMBLY
LOAD-KEYS
YOKES
YOKE-SHELL
ALIGNMENT PINS
AXIAL RODS
(Strain Gauged)
COIL END
BLOCKS
The magnet mechanical structure was designed by
collaboration with ATAP magnet group at LBNL as of 2017
This Nb3Sn magnet is being built by a Chinese company without collaboration
with ATAP/LBNL. DOE did not approve such collaboration.
Bladder & Keys assembly

## Slide 14
FECR Progresses: Magnet
 | Nominal engineering current density Je (A/mm2) | Nominal wire current Ie (A) | Nominal peak field Bpeak-n (T) | Load factor (%)
Sext. | 320 | 709 | 11.3 | 75.9
Inj. | 365 | 663 | 11.8 | 78.2
Mid. | -200 | 372 | 5.0 | 36.5
Ext. | 330 | 600 | 9.7 | 67.3

## Slide 15
FECR Progresses: Magnet
Key technologies
Coils fabrication
Keys & Bladder
½ Prototype Coldmass
Quench protection
Full Sized Coldmass
Quality control of mass production
Quench protection
Quench protection
Know-how of Nb3Sn coil
Quality control and analysis
SG assisted mechanical assembly
Reliability
Reliability
System integration
FECR Magnet
System integration
Coldmass alignment
Reliable operation
From prototyping to operational machine
To demonstrate 80~85% of FECR coldmass performance
Operational FECR ion source
2016-2019
2019-2021
2021-2022
2022-

## Slide 16
FECR Progresses: Prototyping Coils
Test of prototyping solenoid
Solenoid energized to 90% operation current 600 A (safety issue)
No quench!
Field consistent with calculation

## Slide 17
FECR Progresses: Prototyping Coils
Development of prototyping ½ sized sextupole coil
Winding
Heat Treatment
Potting
Prepared Coil
Mechanical mapping
Detailed Q/A
537 mm length
2016-2019

## Slide 18
FECR Progresses: Prototyping Coils
Test of prototyping ½ sized sextupole coil
Al Shell
Upper yoke
Pad
Lower yoke
Key
Shim1+shim2
A Mirror Structure for sextupole cold test
Bladder
30 min
Highest field in superconductor: 10.4 T
LF : 80% of short sample
No Quench!
Pole field
Coil
Feb. 2019
800A

## Slide 19
FECR Progresses: 1/2 sized prototype assembly
½ prototype with Al dummy coil mockup
Bladder & Key
Al Coil
Bladder pressurized
Locked with loading key & shim
Axial pretension
Cool down to 77 K
Warm up
Piston pressurized
Axially locked
Cool down to 77 K
Warm up
Strain Gauge monitored
½ prototype assembly

## Slide 20
FECR Progresses: 1/2 sized prototype assembly
Sextupole pre-assembly
Sextupole in collars
Sextupole & solenoids
Load pad and wiring
Radial preload with bladder & keys
Axial preload with pistons
Instrumentation in Pizzabox
2019-2020

## Slide 21
FECR Progresses: 1/2 sized prototype test
Challenges:
Quench detection and protection (in 10 ms)
Reliable active quench protection power supply
High voltage issues (~2 kV in helium gas)
Flux jumps (FJ) and resultant problems
Aug.2020

## Slide 22
FECR Progresses: Flux Jump (FJ) Challenges
Detected voltage (V)
Time (ms)
Monitored FJ voltage in quench detection system
FJ comes in many wave forms and hard to distinguish from real quench signal
Stemmed from complicated magnetic field configuration in ECRIS magnet
B@10% currents
B@100% currents

## Slide 23
FECR Progresses: 1/2 sized prototype test
96% of operational current
Improper quench (>100 ms) protection interfered by FJ
Improper quench protection caused performance degradation in Coil-6
Unknown degradation in Coil-5 (to be replaced with spared)
Warm-up & cool-down
Warm-up & cool-down
Warm-up & cool-down
reassembly
91%
86%
96%
Feb.2021
Sep.2020
June.2021

## Slide 24
FECR Progresses: 1/2 sized prototype test
Round 2
Round 3
Round 4
Sext + Solenoid training
Systematic training quenches in Coil 6 as performance degradation after late quench protection
No indication of further degradation in Coil 6
~78% of operation current
Warm-up & cool-down
Warm-up & cool-down
reassembly
78%
77%
77%
Feb.2021
June.2021
Sep.2020

## Slide 25
FECR Progresses: Full-sized Sextupole Coil Test
Pole Field (T)
Current (A)
Test of full-sized sext. coil
85% of operation current
Tested full-sized mirror structure
Full-sized tested to 85% design current with no quench
Single coil performance demonstrated
85%
July.2021

## Slide 26
FECR Progresses: Full-sized Coldmass
Ready for final assembly
COIL-PACK
SUBASSEMBLY
SOLENOID
STRUCTURE
SUBASSEMBLY
SHELL-YOKE
SUBASSEMBLY
LOAD-KEYS
YOKES
AXIAL RODS
(Strain Gauged)
2021-2022

## Slide 27
FECR Progresses: Cryogenic System
Parameters | Value | Note
Operation Temp. (K) | 4.3 K | 
Magnet Cooling | LHe bathing and “0” boiling-off | 
Stored Energy (MJ) | ~1.6 | 100% currents
Required heat load (W) | ≥ 12 | ~2 W static at 100% currents
Warm Bore (mm) | Ø162 | 
LHe Volume (L) | ~330 | 
Cryocoolers | 6 two-stage + 1 single stage coolers | Cold service enabled
Dimension (mm) | L1456×Ø1200×H2690 | 
Total weight (ton) | ~6.1 | 
Key parameters of FECR Cryogenic System
Current leads
Cryocoolers
Quench valve
Upper He Vessel
Adjustable
Suspension
2021-2022

## Slide 28
FECR Progresses: Cryogenic System
CH-110
3 × KDE422
3 × RDE-418D4
High power GM Cooler:
10 months continuous stability and reliability checking-test
3×KDE422 coolers ~6.6 W@4.2 K cooling capacity
Sumitomo
Sumitomo
Nanjing KEDE

## Slide 29
FECR Progresses: Microwave System test with SECRAL-II
45 GHz Microwave System for FECR
45 GHz/20 kW microwave transmission system based on Quasi-optical design
First 45 GHz ECR plasma with SECRAL-II ion source
Efficient transmission and coupling demonstrated
J. W. Guo, et al., AIP Conference Proceedings 2011, 090001 (2018)
2017-2018

## Slide 30
FECR Progresses: Microwave System Design
Quasi Optical
Oversized
WG

## Slide 31
FECR Progresses: Plasma Chamber Cooling
Chamber burnt with SECRAL-II
Typically：>7 kW
Chamber burnt with VENUS
1 kW μW~1.25 MW/m2 heat sink
LCW pressure of 6 kg/cm2，water BP =150~160℃
T. Thuillier, et al., Rev. Sci. Instrum. 87, 02A736 (2016)

## Slide 32
FECR Progresses: Plasma Chamber Cooling
 | Prf (kW) | Tmax on Al wall | Tmax of water at the hottest point
1 | 10 ：averagely distributed | 174℃ | 88℃
2 | 10：Gaussian distributed | 159℃ | 78℃
3 | 15：Gaussian distributed | 229℃ | 107℃
4 | 20：Gaussian distributed | 299℃ | 137℃
Water flow rate: 7 L/min with micro-channel
Water temperature distribution at the chamber wall of weakest plasma confinement point
Micro-channel structure of 0.4 mm×20
J. W. Guo’s talk @ECRIS 2020

## Slide 33
FECR Progresses: Plasma Chamber Demo with SECRAL-II
Continuous operation of ~100 eμA Kr28+ for 13 days with 6.0 kW microwave power
Robust chamber cooling enables long-term reliable operation
See Liangting Sun’s talk on Monday, Sept. 20

## Slide 34
FECR Progresses: Plasma Chamber for FECR
Cross section
Chamber-wall
Water
Plasma
T max ：272 ℃
T max ：128 ℃
T max ：272 ℃
Maximum permissible operating power exceeds 25 kW
A
B
A
B
Chamber ID:140 mm, Microchannel:0.4 mm *20, Channel height:1.5 mm, Flow rate: 15 L/min

## Slide 35
FECR Progresses: Plasma Chamber for FECR
Key Parameters | FECR Chamber | SECRAL-II Chamber
Max. Microwave Power | 25 kW | 12 kW
Max. Localized Power Density | 20 MW/m2 | 10 MW/m2
Chamber ID | Ø140 mm | Ø125 mm
Chamber OD | Ø156 mm | Ø136 mm
Length | 1225 mm | 887 mm
Microchannel region | 15×15.6×1.5 mm3 | 15×15.6×1.0 mm3
Fins | 0.4 mm×19 | 0.4 mm×19
Channel | 0.4 mm×20 | 0.4 mm×20
Inside-wall thickness | 1.5 mm | 1.5 mm
Outside-wall thickness | 1.5 mm | 1.5 mm
Water pressure | 10 bar | 8.9 bar
Water flow per channel | ＞ 15 L/m | ＞ 4.0 L/m
Total water flow | ＞ 50 L/m | ＞ 13 L/m
FECR
Chamber
SECRAL-II
Chamber
1225 mm
887 mm

## Slide 36
FECR Progresses: Other Cooling Issues
Directly cooled Plasma Electrode
Directly cooled Injection Baffle
Directly cooled Biased Disk
Tmax~238℃
Tmax~140℃

## Slide 37
FECR Progresses: System Setup
Injection parts
Extraction Solenoid
Plasma Chamber
Extraction System

## Slide 38
FECR Progresses: Time Schedule
½ prototype coldmass success
2021.08
FECR coldmass readiness
2021.12
FECR on test bench
2022.04
FECR magnet completion
2022.02~03
FECR First beam
2022.05~06

## Slide 39
Summary
FECR will demonstrate the first 4th G ECRIS using high field Nb3Sn technology (expected in 2022)
Intense research towards the challenges of FECR find solutions to
  Reliable complicated configuration magnet with single-strand Nb3Sn wire
  High power high frequency microwave coupling to ECR ion source
  Effective plasma chamber cooling for >10 kW microwave ECR heating
  Cryogenic cooling capacity >10 W@4.2 K with commercial cryocoolers

## Slide 40
Acknowledgement
Xi’an Superconducting Magnet Technology Inc.
Coil fabrication
Cold mass fabrication and assembly
Bruker OST LLC.
Nb3Sn Wire
Western Superconducting Tech Co., Ltd.
Nb3Sn Wire
Wire braiding
Lanzhou Kejin Taiji New Technology Co., Ltd.
Mirror structure
Mechanical mapping
Shanghai Chenguang Medical Technologies Co., Ltd.
Cryogenic system fabrication and integration
GyCOM Co., Ltd.
Gyrotron microwave generator and microwave transmission solutions
Lawrence Berkeley National Laboratory
Coldmass structure design
RIKEN
High temperature oven
Fruitful discussions and suggestions:
D. Xie, C. Lyneis, D. Hitz, T. Thuiller, T. Nakagawa
O. Tarvainen, E. Ravaioli, X. J. Liu, W. Kasparek
Welcome collaborations and Postdoc research !!