## Slide 1: A cold electron-impact ion source driven by laser-induced electron emission New opportunities for radioactive molecular beams?
Jochen Ballof, Mia Au, Katerina Chrysalidis, Christoph Düllmann, Valentine Fedosseev, Eduardo Granados, Reinhard Heinke, David Leimbach, Bruce Marsh, João Pedro Ramos, Annie Ringvall Moberg, Sebastian Rothe, Thierry Stora, Shane Wilkins, Alexander Yakushev

## Slide 2: ISOLDE and available beams

## Slide 3: (Un)available beams at ISOLDE
Available beams
  more than 1000 radioisotopes
  74 chemical elements
  lightest element: Helium
  heaviest element: Uranium
  half-lives down to ~ ms
Unavailable beams
  Many refractory elements
Plot proposed by S. Rothe
Boron
Silicon
4d refractories
Zr - Pd
5d refractories
Ta - Pd
Actinides

## Slide 4: ISOLDE target and ion source unit
2 cm
Principle design
Part of the
target station

## Slide 5: Ion sources at ISOLDE
Ion source requirements
  1. Compact and radiation hard
    Integrated in the target unit
    handling by robot required
  2. Withstand pulsed gas loads
    pulsed primary beam
  3. Efficient
  production of radio isotopes is limited
  4. Rapid
  low residence and ionization times
  decay of radio isotopes
  5. Chemical selectivity (desired)
  No (or less efficient) ionization of radiogenic impurities
VADIS
electron impact ionization
thermionic electron emission
hot cavity ionizer (with RILIS)
surface or resonant laser ionization
graphics by Y. Martinez-Palenzuela
Frequently used ion sources (1+)
LIST ion source:
Hot cavity, repeller, RFQ ion guide

## Slide 6: Molecular beams

## Slide 7: Molecular ISOL beams
Beam purification
  Shift the mass region to a higher mass to avoid
  isobaric contaminants. e.g. 66GeS, 133SnS, 70SeCO
Beam extraction by In-situ volatilization
  Elements with very low volatility are not released
  Reactive elements can be chemically trapped
  e.g. 8BF2, 15CO
To study the radioactive molecules
  Fundamental properties, e.g. 223RaF
+ CO
Target material
SeCO
https://web.mit.edu/radiomolecules/

## Slide 8: Molecule formation in RFQ structures
Ion traps for molecular formation/dissociation
  Development for gas injection into RFQ for in-trap chemistry
  Development of mass spectrometer and ToF detection for identification after RFQ
In-source laser ionization of molecules
M. Fan et al, Optical mass spectrometry of cold RaOH+ and RaOCH3+, PRL 126, 23002 (2021)
A. Ringvall Moberg et al, Time-of-Flight study of molecular beams extracted from the ISOLDE RFQ cooler and buncher NIMB 463, 522 (2020)
Mia Au
DREEBIT Wien filter
Offline 2 RFQ

## Slide 9: Volatile carrier molecules
Element not available
as beam at ISOLDE
G. Herrmann, Ark. Fys. 36, 111 (1967)
Volatile carriers known for all reactive elements
Many are not compatible with high-temperature conditions
U. Köster, (Im-)possible ISOL beams,
Eur. Phys. J. Special Topics 150, 285 (2007)
Volatile carrier compounds

## Slide 10: Do we have to operate at the highest temperatures?
Cold targets?
Cold ion sources?
Nano-sctructured target material (CaO) operated at ambient temperature
  fast diffusion in nano-materials and possible release by recoil effect
Foil target at ambient temperature, thermalizing recoils in gas atmosphere
  no diffusion required
J.P. Ramos et al, NIMB 376, 81 (2016)
J. Ballof et al., preprint, https://arxiv.org/abs/2108.01745
Cold RF-heated plasma ion sources at ISOLDE:
  COMIC / Helicon
  For delicate molecules: favour breakup over ionization
Ionization chamber of Helicon plasma source
after operation with Mo(CO)6
Ion source development required
A. Kronenberg et al, NIMB 266, 19 (2008)

## Slide 11: The photo-cathode electron-impact source
Decoupling electron-emission and temperature

## Slide 12: Proof-of-principle setup 1: Ta cathode
Laser | 
Pulse length | 265 fs
Power | ~ 4.5 W
Wavelength | 343 nm
Rep. Rate | 50 kHz
Beam diameter | ~ 6 mm
Beam spot on cathode | 1.5 mm
Cathode | 
Material | tantalum
Anode-cathode gap | 1.5 mm

## Slide 13: Proof-of-principle setup 1: Ta cathode
Target assembly
Before operation / during assembly
2 mm
Laser-induced craters
on the cathode surface
during focusing attempts
Ta-cathode
Anode assembly
After operation
Extraction side
Traces from laser-alignment on the extraction side

## Slide 14: Proof-of-principle setup 1: Ta cathode
Fragile carrier compound Mo(CO)6
FBDE: 1.7 eV
IP : 8.3 eV
Vapour pressure:
25 Pa (ambient temp.)
Measured efficiencies
Measured mass spectrum

## Slide 15: Proof-of-principle setup 1: Ta cathode
Results from first operation
  Fragile compound Mo(CO)6 could be ionized in the setup
  Efficiency of Mo(CO)6 is in the same order of magnitude as Kr
  Mechanism of electron production unclear: Photo-electric effect or thermionic emission?
  Efficiency is very likely limited by electron current:
  ~ 100 nA instead of ~ 100 mA with a hot VADIS
Further focusing attempts
  focusing the beam diameter from ~ 6 mm to below 1.5 mm caused cathode damage

## Slide 16: Proof-of-principle setup 2: Cu cathode
Setup optimized for photo-electric effect
Laser | 
Pulse length | 50 ns
Power | ~ 0.01 W
Wavelength | 215 nm
Rep. Rate | 10 kHz
Beam diameter | ~ 1.5 mm
Cathode | 
Material | copper
Anode-cathode gap | ~ 3 mm

## Slide 17: Proof-of-principle setup 2: Cu cathode
Target assembly
Photo-cathode after operation
2 mm
Cap made of oxygen free copper foil (OFHC)
PEEK insulator
No visible difference before and after operation
No polishing, nor special cleaning or bake out

## Slide 18: Proof-of-principle setup 2: Cu cathode
Results from Cu-cathode operation
  Source operated for 6 days (24/7)
  Kr and CO2 can be ionized with a photo-cathode electron-impact ion source
  No electron emission with 440 mW of blue light (430 nm) confirms photo-electric effect
  Source magnet increased efficiency by factor ~8
  Estimated quantum efficiency: 3 x 10-4
  Decomposition of CO2 degrades the photo-cathode.
    Estimated decrease of 65% in 66 hours, pressure ca. 1 x 10-4 mbar
    Typical hot VADIS: 1 x 10-6 mbar (injected gas)
Injected gas | Ionization efficiency
Kr | 4 x 10-5
CO2 | 2 x 10-5
200 V

## Slide 19: How to increase the efficiency?
e ∝ ne x s x f
Ionization efficiency
L. Penescu et al, RSI 81, 02A906
electron density
ionization cross section
ion extraction
electron focusing
other effects
Parameter | VADIS Thermionic emission | Photo-cathode prototype
Electron current | ~ 100 mA | ~ 0.1 to 1 µA
Ionization efficiency Kr | 30 % | 0.004 %
Diameter electron emitter | 1.2 cm | 0.15 cm
Increase of electron current required
First approximation: ionization efficiency increases proportionally with electron current

## Slide 20: Next Prototype?
Proposal for a future prototype:
perpendicular illumination
  Resolves space charge limitations
  Beam path developed for the PI-LIST ion source
Efficiency estimate by scaling of space-charge limited electron currents
R. Heinke et al, Hyperfine Interactions 238, (2017)
Parameter | Next prototype | Tested prototype
Electron emitter diameter | 12 mm | 1.5 mm
Anode-cathode distance | 3 mm | 1.5 mm
Repetition rate | 2 MHz | 50 kHz
Wavelength | 257 nm | 343 nm
Power | 3.7 W | 4.5 W
Mean electron current | 90 µA | 90 nA
Ionization efficiency Mo(CO)6 | 1% | 0.001%
Estimated parameters to reach 1% ionization efficiency:
J. Ballof et al., preprint, https://arxiv.org/abs/2108.01745

## Slide 21: Conclusion
Electron-impact ion source can be driven by a photo-cathode
Photo-cathode can cope with typical ISOL conditions and gas-loads (~ 10-6 mbar)
Ionization efficiency (proof-of-concept experiment) 0.001% for Mo(CO)6
Upgrading laser-system and source geometry could yield efficiencies of at least 1%
Impact on molecular beams
Decoupling of electron production from ion source temperature
First ISOL ion source for delicate molecules
Could facilitate refractory beam extraction and extract molecules for fundamental physics research

## Slide 22
Thank you for
your attention!

## Slide 25: The ISOL process
  Analyzing magnet m/z ratio
  Mass separated beams
  Target and ion source unit
  Proton beam of 1.4 GeV
  penetrates whole target
Isotope Separation On-Line
  Simultaneous production and separation of radioisotopes
  First applied in 1967 at CERN

## Slide 26: The ISOL process
  Thick target container 20 cm x 2 cm ø
  Proton
  Molecule formation
  Diffusion through solid (slowest step)
Molecular beam extraction
taking the example of 8BF2
  Multiwalled carbon nanotubes
  Production of nuclide
  Fragmentation of 12C 8B
  SF6
  Ionization
  8BF3 8BFx+
  8B 8BF3
SF6
  Effusion
Yield =
N0
erelease (T1/2)
eion eother
eform
Boron is refractory and reactive
Can‘t be extracted as atom -> more volatile molecule needed

## Slide 27: Extracted molecular beams
J. Ballof, PhD thesis (2021)

## Slide 28: Extracted molecular beams

## Slide 29: Proof-of-principle experiment 2: Cu cathode
Laser setup
2 mm
Estimation of transmission onto the cathode (ca. 35%)
532 nm
Ti:Sa
861 nm
IC
BIBO
430 nm
BBO
215 nm
Ion source
Nd:YAG
IC doubled

## Slide 30: Proof-of-principle experiment 2: Cu cathode
Time structure
by photodiode, blue light
Magnetof detector
No significant broadening of electron bunch in comparison to laser pulse
Single ion bunch, in contrast to laser ionization in a VAD(L)IS
Offset between laser pulse and electron release not measured

## Slide 31: How to increase the electron density?
Geometry required in which electron current is not space-charge limited
Laser system required that can produce the required currents
For short-pulse lasers
(i.e., electron flight time >> laser pulse length)
maximum mean electron current without virtual cathode formation
Anode-Cathode gap length
electron emitter radius
Anode voltage
laser pulse repetition rate
A. Valfells et al, Phys. Plasmas 9, 2377 (2002)

## Slide 32: Proof-of-principle experiment 2: Cu cathode

## Slide 33: Proof-of-principle experiment 2: Cu cathode