## Slide 1: Harmonic based beam position measurement
M. Bozzolan
CERN SY/BI technical board
6th May 2021
Thanks for the useful discussions to F.Caspers, M.Gasior, J.Tan and M.Wendt

## Slide 2: Linac 4 to PSB transfer line overview
LINAC 4
160MeV
Debuncher cavity
PS Booster
0
L4T
30
LT
LTB
BI
60
90
140
Distance (z) [m]
BI.BPM20
110
End
130
BSM2
22
Different H- beams at 160MeV (β=0.5) are produced by changing the debuncher setting
13 stripline BPM locations
No issue with “normal” energy spread beam (<400keV)
ISSUE: Trajectory of high energy spread beam (450keV) is noisy in BI line

## Slide 3: Remarks
Perfectly collimated beam and straight transport line  no magnets
Monochromatic beam from LINAC4  no initial energy spread
Gaussian longitudinal distribution
Zero transit time in the debuncher cavity
Only transverse field generated by the beam (as from relativistic beam)
Constant energy spread along the line
Generals
Technicals
This work comes from an issue observed by operation this year for the first time
A general approach is used, not specific to the installed system

## Slide 4: Shorted Stripline BPM
L4 and L4PSB line use the same BPM
Good sensitivity and immunity to electrode charging due to beam loss and stray charges
but … RF bunched beam is required
Beam current
Output signal in time domain
Output signal in frequency domain
Pick up
No low frequency component : H1 (352.2MHz) used
H1
H2
H3
SPICE model

## Slide 5: Trajectory fluctuation
-3mm
-2mm
V plane trajectory of several LHC25A injections in PSB
0
140m
-1mm
-0mm
BI.BPM20 & BI.BPM30 have the highest position fluctuation
Fluctuation decrease upstream and downstream
Low energy spread beams is OK
Same problem fot the H plane
L4T
LT
LTB
BI

## Slide 6: BPM sum signal (intensity but not current)
Chart: 352.2MHz component [dB]
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5 | 24 | 24.5 | 25 | 25.5 | 26 | 26.5 | 27 | 27.5 | 28 | 28.5 | 29 | 29.5 | 30 | 30.5 | 31 | 31.5 | 32 | 32.5 | 33 | 33.5 | 34 | 34.5 | 35 | 35.5 | 36 | 36.5 | 37 | 37.5 | 38 | 38.5 | 39 | 39.5 | 40 | 40.5 | 41 | 41.5 | 42 | 42.5 | 43 | 43.5 | 44 | 44.5 | 45 | 45.5 | 46 | 46.5 | 47 | 47.5 | 48 | 48.5 | 49 | 49.5 | 50 | 50.5 | 51 | 51.5 | 52 | 52.5 | 53 | 53.5 | 54 | 54.5 | 55 | 55.5 | 56 | 56.5 | 57 | 57.5 | 58 | 58.5 | 59 | 59.5 | 60 | 60.5 | 61 | 61.5 | 62 | 62.5 | 63 | 63.5 | 64 | 64.5 | 65 | 65.5 | 66 | 66.5 | 67 | 67.5 | 68 | 68.5 | 69 | 69.5 | 70 | 70.5 | 71 | 71.5 | 72 | 72.5 | 73 | 73.5 | 74 | 74.5 | 75 | 75.5 | 76 | 76.5 | 77 | 77.5 | 78 | 78.5 | 79 | 79.5 | 80 | 80.5 | 81 | 81.5 | 82 | 82.5 | 83 | 83.5 | 84 | 84.5 | 85 | 85.5 | 86 | 86.5 | 87 | 87.5 | 88 | 88.5 | 89 | 89.5 | 90 | 90.5 | 91 | 91.5 | 92 | 92.5 | 93 | 93.5 | 94 | 94.5 | 95 | 95.5 | 96 | 96.5 | 97 | 97.5 | 98 | 98.5 | 99 | 99.5 | 100 | 100.5 | 101 | 101.5 | 102 | 102.5 | 103 | 103.5 | 104 | 104.5 | 105 | 105.5 | 106 | 106.5 | 107 | 107.5 | 108 | 108.5 | 109 | 109.5 | 110 | 110.5 | 111 | 111.5 | 112 | 112.5 | 113 | 113.5 | 114 | 114.5 | 115 | 115.5 | 116 | 116.5 | 117 | 117.5 | 118 | 118.5 | 119 | 119.5 | 120 | 120.5 | 121 | 121.5 | 122 | 122.5 | 123 | 123.5 | 124 | 124.5 | 125 | 125.5 | 126 | 126.5 | 127 | 127.5 | 128 | 128.5 | 129 | 129.5
BPM measurements | -0.49442 | -1.2944 | -5.2944 | -11.2944 | -28.4944 | -37.8944 | -29.8944
L4T
LT
LTB
BI
[m]
Good transmission along the line (measured by BCTs)  same current in all the line
Cable loss contribution removed
Intensity (Σ) depends on the beam current AND on the bunch shape
At location around BI.BPM20 a notch of the intensity signal is present
S/N ≥ 40dB
Measured BPM signal for LHC25A beam

## Slide 7: Simplified debuncher model
Chart: RF signal phase[deg]
time
No net energy change
Head of the bunch accelerated
Tail of the bunch decelerated
Debunching phase working point
acceleration
deceleration
BEAM and RF VOLTAGE in debuncher cavity
travelling beam

## Slide 8: (my) Beam transport simulation
Sampling rate 0.1 ⁰
Two simulation modes: Single bunch for bunch length measurement Train of bunches for BPM response
Three initial conditions: average kinetic energy, energy spread and bunch length
Single bunch transport for pulse length calculation
Bunch train transport for BPM signal strength calculation
352.2MHz component
Distance from debuncher
Beam amplitude [a.u.]

## Slide 9: Benchmarking my beam transport
Chart: Distance [m]
Bunch length simulation
BPM signal amplitude simulation
σ=17⁰ @ debuncher (z=0)
Energy spread = 450keV
352.2MHz component [dB]
Distance [m]
“my simulation” single bunch fits BE/ABP results 
BPM signal amplitude decrease monotonically along the line (but real measurements don’t) 
“Nominal” value from BE/ABP
Reference level at debuncher (Z=0)
Measured value by SY/RF in PSB
BSM2

## Slide 10: But the BSM2
https://logbook.cern.ch/elogbook-server/GET/showEventInLogbook/3190762
From L4 elogbook on March 13th
σ≈50⁰ @ Z=22m
σ≈31⁰ @ Z=0, not 17⁰
… doesn’t fit with the “nominal” bunch length

## Slide 11: Bunch transport again
Chart: Distance from debuncher [m]
σ=31⁰ @ debuncher (z=0) and σ=50⁰ @ BSM2 (z=22)
Energy spread = 450keV
“Modified” bunch length
Chart: Distance from debuncher [m]
BPM measurements | -0.49442 | -0.64 | -2 | -2.15 | -5.5 | -10.8 | -13.8 | -20.7 | -33.5 | -43.1 | -37.8944 | -35.6 | -31
The notch of the harmonic component fit the measurements
Notch location depends on energy spread (debuncher setting) and initial bunch length (LINAC)

## Slide 12: Time domain waveforms
Single bunch @ 80m
Train of bunches @ 12m
Train of bunches @ 100m
Transported bunches progressively lose the gaussian shape because of the sinusoidal energy spread  Be careful with beam simulation (e.g. CST)
At around 100m the beam is almost completely debunched.
Harmonic components barely visible in time domain, but well measured with narrow band filtering
RF period
RF period
RF period

## Slide 13: Intuitive frequency response
time
Assuming the bunch shape is rectangular
At bunch length multiple of the RF period the beam current is flat
time
time
i(t)
Distance: Z=0
Distance: Z1>0
Distance: Z2>Z1
f
I(f)
f
f
i(t)
i(t)
I(f)
I(f)
1/t0
1/t0
1/t0
t0
2t0
t0
2t0
t0
2t0

## Slide 14: Bunch transverse distribution
Chart: RF signal phase[deg]
Train of bunches are assumed to have linear position slope at z=0
Average position is 0 and it should stay 0 since the beam is assumed to be perfectly collimated
Simulated beam position calculated as BPM
Bunch transverse position and amplitude @ Z=0
The 352.2MHz component is dominated by the relation between transverse and longitudinal distributions
Position depends on the bunch transverse distribution
Expected position
Region of bunch distribution dependance
In the highly debunched region:

## Slide 15: Transverse distribution effect on the same BPM
Simulation
Low energy spread (bunched beam)
Very close signals with minimal difference in amplitude & phase
Relevant amplitude and phase difference
Plus and minus electrode signals for high and low energy spread beam
Measurement
High energy spread (debunched beam)
Simulation
Measurement

## Slide 16: Summary of harmonic based position
Harmonic based position measurement (e.g. stripline BPM) is in general a good choice for LINAC
For sake of uniformity transfer line can be equipped with the LINAC BPM type
Depending on the LINAC configuration, BPMs may work well also in the transfer line, nevertheless beam simulations must be carefully done (bunch not gaussian)
In the region of the harmonic component notch beam position depends on the initial bunch transverse distribution

## Slide 17: H2 (704MHz) not an option
[mm]
/
[dB]
Position [mm]
H2 level @ electrodes [dB]

## Slide 18: Possible workaround
M.Gasior @ DIPAC 2005
“A CURRENT MODE INDUCTIVE PICK-UP FOR BEAM POSITION AND CURRENT MEASUREMENT”
One inductive PU was built and installed in L2 transfer line ~ 2005 then removed during LS1
(now in 150/R-007)
Acquisition electronics and software to be developed
No dedicated cables
$$ relative expensive device to produce (coated ceramic chamber+big custom ferrite)