## Slide 1: XLS Linac Performance
Andrea Latina (CERN)

## Slide 2: Contents
Two configurations at 100 Hz
  E = 2.7 GeV
  E = 5.5 GeV
PLACET Simulations of BBA performance
  Setup:
  All elements (Quadrupoles, Structures, BPMs)
    Position alignment error = 100 um rms
    Angle alignment error = 100 urad rms
  BPM resolution = 5 um
  100 random seeds of misalignment
  Each quadrupole equipped with 1 corrector and 1 Bpms

## Slide 3: Recap of the operating modes and of the parameters

## Slide 4: Beam-based alignment procedure
Orbit correction
  The correctors are used to send the beam through the center of the BPMs (that unfortunately are misaligned)
Dispersion-Free Steering
  The dispersion is measured by slightly off-setting the RF phase of LINAC0 and LINAC1
  The correctors are used to cancel the effects of unwanted dispersion
Wake-field free steering
  The effects of wakefield on the orbit is measured by slightly changing the bunch charge (-10%)
  The correctors are used to cancel the effects of the transverse wakefields

## Slide 5
Low energy = 2.35 GeV - design

## Slide 6
Low energy = 2.35 GeV - BBA

## Slide 7
Low energy = 5.5 GeV - design

## Slide 8
Low energy = 5.5 GeV - BBA

## Slide 9
The effects of misalignment for E = 2.35 GeV and E = 5.5 GeV are very well corrected using BBA
We still need to study the challenging case of E = 0.97 GeV at the end of Linac 3
Conclusions