## Slide 1: DESIGN STUDY FOR THE LHC UPGRADE WP3: MAGNETS
E. Todesco
CERN, Geneva, Switzerland
Thanks to O. Bruning, G. De Rijk, J. M. Rifflet,
L. Rossi, R. V. Weelderen
CERN, 8th September 2010
High Luminosity LHC Design study

## Slide 2: TENTATIVE TASK LIST
  Communication and management
  Nb3Sn quadrupoles
  Separation dipoles
  Radiation hardness
  Cooling
  SC link and powering
  Miscellaneous
First guess on tasks, to be discussed

## Slide 3: TASK 2 – Nb3Sn quadrupoles
The 120 mm aperture HQ is the technology demonstrator (US-LARP is the main actor)
  Issues:
    Radiation hardness
    Field quality
    Choose the length of the demonstrator
    Explore larger apertures
Activities
  Finalize the specification for a Nb3Sn magnet to be in the LHC
  Field quality
    Follow up the construction of instruments to measure field quality
    Compare with targets
    Explore the possibility of magnetic shimming

## Slide 4: TASK 2 – Nb3Sn quadrupoles
Activities (continued)
  Length issue
    Estimate the minimal distance one can have between two cold masses to evaluate the losses in performance for the scenario with two coils in the same cryostat (i.e. two 4-m-long instead of one 8-m-long)
    Test on two TQ?
  Cryostat
    Design of an horizontal cryostat for the LARP quads
    Test on HQ?
  Explore the design of a larger aperture
    Input from WP2 (140 mm? 160 mm?)
    Make a conceptual design to see if there are bottlenecks (stress, mechanical structure)
  Use components that are radiation resistant as soon as possible

## Slide 5: TASK 3 – SEPARATION DIPOLES
Separation dipoles for IR1 and IR5
  Input from WP2: strength and aperture needed
  Design of a Nb3Al separation dipole
  Follow up of model construction
  Conceptual design of a plan B Nb-Ti version
Plan B for the crab cavities: a dogleg if the compact option is not viable
  Input from WP4: strength needed for a dogleg for crab cavities
  Design of a dogleg for crab cavities

## Slide 6: TASK 4 – RADIATION HARDNESS
Input from WP2: a tentative layout with Nb3Sn
  Phase I could be used, or a 120 mm aperture with shorter magnets
Activities
  First estimate of the heat loads and radiation
  Estimate of which materials used in HQ today do not satisfy this limit
  Experiments if needed
  Explore how to replace these materials
  Test on TQ or HQ?
  Check of the radiation hardness of the other elements of the LHC

## Slide 7: TASK 5 – Cooling
Main issue: choose the operational temperature
Have a comparison between different options for Nb3Sn
  Supercritical (~4.5-5 K) versus superfluid (~1.9 K) operation
    4.5 K implies a loss of performance (10% in magnet length) and higher costs (10% more sc), but the related cryogenic costs should be estimated
  Superfluid - what is the best temperature ? 1.8 K ? 2.0 K?
Evaluate again the heat loads for the Nb-Ti option
  New luminosity: 51034 instead of 2.51034 cm-2 s-1

## Slide 8: TASK 6 – SC link
Superconducting link for the powering of the IR magnets
  Synergy with Eucard HFM
  Input from WP2 and magnet design, powering scheme: operational currents
  Design of sc link
  Check the consistency of Phase I scenario

## Slide 9: TASK 7 – MISCELLANEOUS
Review the phase I lay-out to validate the design for the new scenario
  Follow-up the advancement of the MQXC
  In particular the validation of the new insulation scheme
Conceptual design of larger aperture Q4
  Two-in-one Nb-Ti magnet, 194 mm separation, what is the largest possible aperture?
Conceptual design of quadrupoles for IR3 IR7
  To replace the resistive ones if not resistant to radiation

## Slide 10: PARTNERS (TENTATIVE LIST)
EU:
  CEA Saclay (Fr) – magnet design
  CEA Grenoble (Fr) – supercritical cooling system
  LASA INFN Milano (It) – magnet protection
  Wroclaw (Pl) – radiation hardness
World
  LARP: FNAL, BNL, LBL (Us) – Nb3Sn quadrupoles
  KEK (Jp) – Separation dipoles