## Slide 1
Antonio Gilardi
Measurements of wakefields and bunch length with beam in linear electron accelerators: a case study at the CLEAR facility.
Antonio Gilardi
Acknowledgment: Roberto Corsini – Kyrre Sjobak – Wilfrid Farabolini – Andrea Latina – Pasquale Arpaia
Notes: Hello to everyone.
I'm Antonio Gilardi and today I’m going to present the wakefield measurements in CLEAR.
Before to start I would like to acknowled: …..for the constant support and help

## Slide 2
Outline
CLEAR (CERN Linear Electron Accelerator for Research)
Wakefields study
  Background
  Problem
  Proposal
  Results
Bunch length study
  Background
  Problem
  Proposal
  Results
Conclusions
Antonio Gilardi
Notes: This is my outline, I will firstly give a brief introduction of CLEAR, the accelerator where I performed the whole activities.
Following; I will talk of the wakefield measurements carried our; about this topic I will briefly introduce a background then present the problem, the proposal and finally the results.
From the well-known picture on the side representing the overview of the CERN complex, you can already spot the CLEAR accelerator. It has the unique pecularity of being an indipendent LINAC.

## Slide 3
Outline
CLEAR (CERN Linear Electron Accelerator for Research)
Wakefields study
  Background
  Problem
  Proposal
  Results
Bunch length study
  Background
  Problem
  Proposal
  Results
Conclusions
Antonio Gilardi
Notes: This is my outline, I will firstly give a brief introduction of CLEAR, the accelerator where I performed the whole activities.
Following; I will talk of the wakefield measurements carried our; about this topic I will briefly introduce a background then present the problem, the proposal and finally the results.
From the well-known picture on the side representing the overview of the CERN complex, you can already spot the CLEAR accelerator. It has the unique pecularity of being an indipendent LINAC.

## Slide 4
CERN Linear Electron Accelerator for Research (CLEAR)
CLEAR is a user facility at CERN, running parallel with the main CERN accelerator complex, with the primary goal of general R&D for future accelerators.
The CLEAR beamline is 41 m long.
Web site http://clear.web.cern.ch
https://clear.web.cern.ch/sites/clear.web.cern.ch/files/documents/CLEAR_proposal.pdf
Antonio Gilardi
Notes: This is the CLEAR layout, CLEAR is a user facility with the primary goal of general R&D for future accelerators.

## Slide 5
Antonio Gilardi
Notes: This is the CLEAR layout, CLEAR is a user facility with the primary goal of general R&D for future accelerators.

## Slide 6
Outline
CLEAR (CERN Linear Electron Accelerator for Research)
Wakefields study
  Background
  Problem
  Proposal
  Results
Bunch length study
  Background
  Problem
  Proposal
  Results
Conclusions & Future development
Antonio Gilardi
Notes: This is my outline, I will firstly give a brief introduction of CLEAR, the accelerator where I performed the whole activities.
Following; I will talk of the wakefield measurements carried our; about this topic I will briefly introduce a background then present the problem, the proposal and finally the results.
From the well-known picture on the side representing the overview of the CERN complex, you can already spot the CLEAR accelerator. It has the unique pecularity of being an indipendent LINAC.

## Slide 7: Wakefields study – Background
Antonio Gilardi
Notes: This is an overview of the wakefield effects, you see a bunch that is passing from left to right in time from bottom to top left beyond a parasite field that can than remain trapped into the cavity and resonate.

## Slide 8
Ideal trajectory
Real trajectory
Bunch
Wakefields study – Background
Antonio Gilardi
Notes: Another view of this effects of a bunch passing trougth a series of cavity like can be an accelerating strcutrue.
This effect can modify the beam trajectory and even a modification of few degrees in a long accelerator may cause the loss of the beam.
This is way the wakefield are one of the big concerns for the novel accelerators.

## Slide 9: Wakefields study – Background
Ideal trajectory
Real trajectory
Bunch
Short-range  Intra bunch
Long-range  Between bunches
Antonio Gilardi
Notes: We can distinguish between two type of wakefield....

## Slide 10
Wakefields study – Problem
100 MV/m – Compact LInear Collider (CLIC)
25 MV/m – CLEAR accelerating structure
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 11
100 MV/m – Compact LInear Collider (CLIC)
25 MV/m – CLEAR accelerating structure
CLIC accelerating structure
YAG screen
OTR screen
Chromox screen
Radiation monitors
WFM
H/V Corrector magnets
iBPM
Girder
CLIC
BPM
Real trajectory
Ideal trajectory
Wakefields study – Problem
Antonio Gilardi
Notes: This is a simplified view of the experimental layout where we can see, two....

## Slide 12
CLIC accelerating structure
YAG screen
OTR screen
Chromox screen
Radiation monitors
WFM
H/V Corrector magnets
iBPM
Girder
CLIC
BPM
Real trajectory
Ideal trajectory
Wakefields study – Problem
Antonio Gilardi
Notes: The potential distructive effect that the wakefield can have was of course already well known during the design and installation times.
For this reason, two different devices were designed and installed for trying to estimate such effect and if needed to correct the trajectory.

## Slide 13
CLIC Beam Position Monitor (BPM)
Wake Field Monitor (WFM)
CLIC accelerating structure
YAG screen
OTR screen
Chromox screen
Radiation monitors
WFM
H/V Corrector magnets
iBPM
Girder
CLIC
BPM
Real trajectory
Ideal trajectory
Wakefields study – Problem
Antonio Gilardi
Notes: I’m talking about the CLIC BPM and the WFM.
The WFM are antennas installed on an extended cell in the middle of the suprestrucutre while the CLIC BPM are a particulary performing cavity BPM with a design resolutions in the nanometare range.
Unfortunatly both this device are not yet operational and thus can not be used. Several studies are ongoing on this components.

## Slide 14
Wakefields study – Proposal
Antonio Gilardi
Notes: The idea beyond the measurement methods is to study the effects of the wakefield estimating the different transverse kick that the beam recive while inducing a different displacement between the structure and the beam itself.
To do that, the beam centroid evolution while varyng the displacement is studied

## Slide 15
Before the accelerating structure
After the accelerating structure
Wakefields study – Proposal
Antonio Gilardi
Notes: In this animations you see the same beam before and after the structure, thus you see the impact of the wakefield after the beam has passed trougth the accelerating structure.
From this, it is clear how much wakefield are impacting the the beam distribution and as a consequence, the beam centroids.

## Slide 16
Under the assumption of:
Dominant dipolar component
(i.e., linear dependence with the displacement in the structure)
Linear dependence of the charge
Before the accelerating structure
After the accelerating structure
Wakefields study – Proposal
Antonio Gilardi
Notes: Using the assumption of a linear response with the displacement and with the charge, it is possible to write the equations that describe the transverse voltage that affect the beam

## Slide 17
Slope on the 2nd screen
Beam energy [MeV]
Beam charge [C]
Form factor (from simulation)
Under the assumption of:
Dominant dipolar component
(i.e., linear dependence with the displacement in the structure)
Linear dependence of the charge
Before the accelerating structure
After the accelerating structure
Wakefields study – Proposal
Antonio Gilardi
Notes: Where the first terms is the .....

## Slide 18
CLIC accelerating structure
Girder
Beam screen
Ideal trajectory
Real trajectory
Beam
Move the structure
CLIC accelerating structure
Girder
Beam screen
Beam
Ideal trajectory
Real trajectory
Move the beam
Beam screen
H/V Corrector magnets
Wakefields study – Proposal
Antonio Gilardi
Notes: In order to change the displacement between the beam and the structure two possible strategies are available.
The first involve the movement of the accelerating structure around the beam, using a movable girder.
The second one uses correctors to scan around the position of the beam.
For practical reason, we have decided to use the second.

## Slide 19
Wakefields study – Results
Between the wakefields simulations (Karl Bane’s formula) and from the measured data a discrepancy of an order of magnitude was found.
Antonio Gilardi
Notes: And early results obtained comparing the simulations and the experimental data, a discrepancy of about a factor 10 was found.

## Slide 20
Thanks to a first comparison with simulation a wrong calibration of the ICT in the CLEAR beam line was discovered.
This was corrected in spring 2019
Between the wakefields simulations (Karl Bane’s formula) and from the measured data a discrepancy of an order of magnitude was found.
10 bunches
1 bunch
16 bunch
Wakefields study – Results
Antonio Gilardi
Notes: In addition from those measuraments an indication of having a linear trend with the charge per bunch was obtained, this was already pointing of a dominance from the short range wakefield.

## Slide 21
- Single bunch
- Constant bunch length (4 ps)
Wakefields study – Results
Antonio Gilardi
Notes: Following experimental campaign were carried our with single bunch with constant bunch length.

## Slide 22
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Slope =1
- Single bunch
- Constant bunch length (4 ps)
Wakefields study – Results
Antonio Gilardi
Notes: From the centroid variations versus the imposed position, it can be seen that firstly, there is a wakefield impact, indeed we see that the slope is larger then one.
In addition, it can be seen that there is a linear trend in the centroid assessment.

## Slide 23
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Slope =1
Dominant dipolar component
- Single bunch
- Constant bunch length (4 ps)
Wakefields study – Results
Antonio Gilardi
Notes: So, it is clear the domination of the dipolar component.

## Slide 24
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Slope =1
Dominant dipolar component
- Single bunch
- Constant bunch length (4 ps)
Wakefields study – Results
Antonio Gilardi
Notes: Repeating the study for several charge per bunch, it is possible to obtain this results.
In this case it is clear the linear dependence with the charge.
Thus

## Slide 25
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Slope =1
Dominant dipolar component
- Single bunch
- Constant bunch length (4 ps)
Wakefields study – Results
Antonio Gilardi
Notes: Also the second assumption use to write the formula that describe the transverse field was verified.

## Slide 26
Mixed number of bunches
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Slope =1
Dominant dipolar component
- Single bunch
- Constant bunch length (4 ps)
Linear dependence of the charge
Wakefields study – Results
Antonio Gilardi
Notes: As a last comparison, to understand the type of wakefield; experimental campaigns with mixed number of bunches were performed.

## Slide 27
Slope =1
Dominant dipolar component
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Mixed number of bunches
- Single bunch
- Constant bunch length (4 ps)
Linear dependence of the charge
Wakefields study – Results
Antonio Gilardi
Notes: Plotting the results versus the charge per pulse and the charge per bunch; it is evident that there is a linear correlation with the charge per bunch.
This is clear indications that

## Slide 28
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Dominated by short range wakefield
Slope =1
Dominant dipolar component
Mixed number of bunches
- Single bunch
- Constant bunch length (4 ps)
Linear dependence of the charge
Wakefields study – Results
Antonio Gilardi
Notes: we are dominated by the short range wakefield.

## Slide 29
Outline
CLEAR (CERN Linear Electron Accelerator for Research)
Wakefields study
  Background
  Problem
  Proposal
  Results
Bunch length study
  Background
  Problem
  Proposal
  Results
Conclusions
Antonio Gilardi
Notes: This is my outline, I will firstly give a brief introduction of CLEAR, the accelerator where I performed the whole activities.
Following; I will talk of the wakefield measurements carried our; about this topic I will briefly introduce a background then present the problem, the proposal and finally the results.
From the well-known picture on the side representing the overview of the CERN complex, you can already spot the CLEAR accelerator. It has the unique pecularity of being an indipendent LINAC.

## Slide 30: Bunch length study – Background
Antonio Gilardi

## Slide 31: Bunch length study – Background
Antonio Gilardi

## Slide 32: Bunch length study – Background
Antonio Gilardi

## Slide 33: Bunch length study – Background
Antonio Gilardi

## Slide 34: Bunch length study – Background
Spot size at the RFD center
Divergence at the RFD center
Correlations between spot size and.
divergence at the RFD center
Antonio Gilardi

## Slide 35: Bunch length study – Background
Antonio Gilardi

## Slide 36: Bunch length study – Background
Bunch length
Calibration factors related with RFD characteristics
Correlation between longitudinal and transverse particle position at the RFD center
  Correlation between transverse divergence and longitudinal position at the RFD center
Neglecting the energy spread and energy chirp (correlations between energy and time) contributions.
Antonio Gilardi

## Slide 37: Bunch length study – Background
, and are the RFD frequency, and phase respectively
beam centroid ad the screen
The measurement is self-calibrated
Main properties
1.
Antonio Gilardi

## Slide 38: Bunch length study – Background
, and are the RFD frequency, and phase respectively
beam centroid ad the screen
The measurement is self-calibrated
Main properties
1.
Cancel the correlations between longitudinal position and transverse position/divergence
2.
RFD
ON
SCREEN
Antonio Gilardi

## Slide 39: Bunch length study – Background
, and are the RFD frequency, and phase respectively
beam centroid ad the screen
The measurement is self-calibrated
Main properties
1.
SCREEN
Cancel the correlations between longitudinal position and transverse position/divergence
2.
RFD
ON
Antonio Gilardi

## Slide 40: Bunch length study – Background
, and are the RFD frequency, and phase respectively
beam centroid ad the screen
The measurement is self-calibrated
Main properties
1.
SCREEN
Cancel the correlations between longitudinal position and transverse position/divergence
2.
RFD
ON
Antonio Gilardi

## Slide 41
Bunch length study – Problem
1. Energy spread and Energy chirp
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 42
2. Correlations between longitudinal position and transverse position/divergence
Bunch length study – Problem
1. Energy spread and Energy chirp
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 43
3. Elements between the RFD and the screen
Conventional
Non-conventional
1. Energy spread and Energy chirp
2. Correlations between longitudinal position and transverse position/divergence
RFD
QUADRUPOLES
SCREEN
Bunch length study – Problem
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 44
Bunch length study – Results 1
1. Energy spread and Energy chirp
Developed an analytical model to include these effects
Antonio Gilardi
Notes: Regarding the energy chirp and spread, I developed a new model for performing the measurements including this effects and measuring them using a polynomial fit.
This approach was tested in simulations using FEL and Plasma beam like parameters obtaining a good agreement.

## Slide 45
Bunch length study – Results 1
1. Energy spread and Energy chirp
FEL
PLASMA
Developed an analytical model to include these effects
Antonio Gilardi
Notes: Regarding the energy chirp and spread, I developed a new model for performing the measurements including this effects and measuring them using a polynomial fit.
This approach was tested in simulations using FEL and Plasma beam like parameters obtaining a good agreement.

## Slide 46
Bunch length study – Results 1
1. Energy spread and Energy chirp
FEL
PLASMA
Developed an analytical model to include these effects
Simulation results
Antonio Gilardi
Notes: Regarding the energy chirp and spread, I developed a new model for performing the measurements including this effects and measuring them using a polynomial fit.
This approach was tested in simulations using FEL and Plasma beam like parameters obtaining a good agreement.

## Slide 47
Bunch length study – Results 2
2. Correlations between longitudinal position and transverse position/divergence
FEL
PLASMA
Developed an analytical model to include these effects
Antonio Gilardi
Notes: Similarly for the correlations, I developed a new measurement model that allows to retrieve information on this numbers.
Also this was tested using tracking simulations but this time we used realistic start to end simulation of the GBS LINAC operational at the the ELI-NP .
Also in this case really good results were obtained.

## Slide 48
Bunch length study – Results 2
2. Correlations between longitudinal position and transverse position/divergence
FEL
PLASMA
Developed an analytical model to include these effects
Start2End simulations of a Compton source
Antonio Gilardi
Notes: Similarly for the correlations, I developed a new measurement model that allows to retrieve information on this numbers.
Also this was tested using tracking simulations but this time we used realistic start to end simulation of the GBS LINAC operational at the the ELI-NP .
Also in this case really good results were obtained.

## Slide 49
Bunch length study – Results 2
2. Correlations between longitudinal position and transverse position/divergence
FEL
PLASMA
Developed an analytical model to include these effects
Start2End simulations of a Compton source
Simulation results
Antonio Gilardi
Notes: Similarly for the correlations, I developed a new measurement model that allows to retrieve information on this numbers.
Also this was tested using tracking simulations but this time we used realistic start to end simulation of the GBS LINAC operational at the the ELI-NP .
Also in this case really good results were obtained.

## Slide 50
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 51
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 52
Bunch length study – Results 3
Good agreement between simulations with tracking code (ELEGANT) and theoretical derivation.
3. Elements between the RFD and the screen
The feature of self-calibration is preserved
Possibility of removing the correlations between longitudinal position and transverse position/divergence
Same procedure for assessing the bunch length
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 53
Bunch length study – Results 3
3. Elements between the RFD and the screen
The feature of self-calibration is preserved
Possibility of removing the correlations between longitudinal position and transverse position/divergence
Same procedure for assessing the bunch length
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
The simulation results were verified versus actual measurement campaigns.
Good agreement between simulations with tracking code (ELEGANT) and theoretical derivation.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 54
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 55
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Where is the so-called acquisition system resolution, determined by the imaging methodology (i.e., the screen technology, the camera used, and the measurement setup).
The smallest value of , by definition, can be
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 56
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Where is the so-called acquisition system resolution, determined by the imaging methodology (i.e., the screen technology, the camera used, and the measurement setup).
The smallest value of , by definition, can be
RFD OFF
RFD ON
1mm
Horizontal axis [mm]
Vertical axis [mm]
Simulations
Measurements
Measurements
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 57
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 58
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Using the uncertainty propagation on the bunch length formula, defining the G-factor as
The relative uncertainty on the bunch length can be written as:
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 59
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Without additional focusing element
With focusing element
Using the uncertainty propagation on the bunch length formula, defining the G-factor as
The relative uncertainty on the bunch length can be written as:
The results were validated using tracking code simulations (ELEGANT) -- good agreement.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 60
Bunch length study – Results 3
3. Elements between the RFD and the screen
I. Measurement validity assessment. II. Resolution performance. III. Uncertainty performance.
Without additional focusing element
With focusing element
Using the uncertainty propagation on the bunch length formula, defining the G-factor as
The relative uncertainty on the bunch length can be written as:
The results were validated using tracking code simulations (ELEGANT) -- good agreement.
Antonio Gilardi
Notes: The whole wakefield study is carried out on the latest baseline prototype of accelerating structure for the future compact linear collider.
This structure presents several challenging parameters, starting from the accelerating gradient, that is 100MV/m and just to give a number to compare with, it is about 4 times the gradient of the accelerating structure currently installed in CLEAR.
In addition, the pipe aperture goes down to a 2mm.

## Slide 61
Outline
CLEAR (CERN Linear Electron Accelerator for Research)
Wakefields measurements
  Background
  Problem
  Proposal
  Results
Bunch length study
  Background
  Problem
  Proposal
  Results
Conclusions
Antonio Gilardi
Notes: This is my outline, I will firstly give a brief introduction of CLEAR, the accelerator where I performed the whole activities.
Following; I will talk of the wakefield measurements carried our; about this topic I will briefly introduce a background then present the problem, the proposal and finally the results.
From the well-known picture on the side representing the overview of the CERN complex, you can already spot the CLEAR accelerator. It has the unique pecularity of being an indipendent LINAC.

## Slide 62
Conclusions
Wakefield
  The proposed measurement method, which uses a beam screen, was validated; in both single bunch and multi bunch operation.
  The assumption of the dominant dipolar component was demonstrated.
  The assumption of linear dependence with the charge was demonstrated.
  The wakefields affecting the CLIC structure were characterized and assessed. The results are consistent with what is expected from the analytical formulas.
Bunch length
  A novel measurement procedure for investigating the correlations between longitudinal position and transverse position/divergence was developed.
  A novel measurement procedure for investigating Energy spread and Energy chirp was developed.
  The novel layout's validity, including the focusing element to perform the bunch length measurement, was assessed.
  Really promising resolution and uncertainty enhancements were studied.
Antonio Gilardi
Notes: This bring me to the conclusions:…..

## Slide 63
Thanks for your attention
Antonio Gilardi

## Slide 64
Backup slides

## Slide 65
Wakefields - Simulations
Notes: Following experimental campaign were carried our with single bunch with constant bunch length.

## Slide 66
Wakefields - Results
Offset = 1 mm
Bunch Length = 4 ps
Charge = 500 pC
Offset = 1 mm
Bunch Length = 4 ps
Charge = 1nC
Notes: Following experimental campaign were carried our with single bunch with constant bunch length.

## Slide 67
Wakefields - Results
Notes: Following experimental campaign were carried our with single bunch with constant bunch length.

## Slide 68
Wakefields - Results
Notes: we are dominated by the short range wakefield.

## Slide 69
Screen before the accelerating structure
Horizontal
Vertical
Screen after the accelerating structure
4 lines
Projection of the integrated beam image over 10 acquisitions.
Projection of the beam image computed shot by shot and then averaged.
Gaussian fit of the integrated beam image over 10 acquisitions.
Gaussian fit of the beam image computed shot by shot and then averaged.
Wakefields - Results
CLIC accelerating structure
Girder
Beam screen
Beam
Ideal trajectory
Real trajectory
Beam screen
H/V Corrector magnets
Calibration of bump accuracy about 1%
Notes: the presence of 4 lines that indeicate the 4 different ways used for assessing the centroids.
The four different strageies are used in order to take into account the possibilities of non-gaussian beam and at the same time to have additional information on the reproducibility.
The results show a good accuracy and reproducibility in both plane.

## Slide 70
Innovative concept of two different beam
Probe beam:
Feed RF power in the ACcelerating Structure (ACS)
Test beam:
To carry out experiment!

## Slide 71
First beam – June 2003
Last beam – December 2016
CTF3 has addressed and solved the vast majority of CLIC issues related to drive beam generation, power production and two-beam acceleration.
A new machine is needed (CLEAR) to maintain local testing capability at CERN for CLIC instrumentation and high-gradient structure testing with beam (alongside with other non-CLIC activities).

## Slide 72
Wakefields study - WFM
Previous research experience – Antonio Gilardi
WakeFieldMonitor operating principle
WakeFieldMonitor setup
Log detector signals
Preliminary results performed at different charge to assess the electric center of the structure.
Notes: In collaboration with the University of Oslo, I also developed further the WFM. Just as an introduction, the operating principle is straight forward. In the first accelerating cell of the second structure of the superstructure there are 8 sensing antennas to pick a TM and TE like modes that then are transferred into dome hybrids and after a filtering and a limiters stage are acquired from a log detector.
On this topic, firstly I realize that there was an issues with length matching cabling. So firstly I spent a bit of time to refurbish the experimental setup then a full characterization of the transfer line was developed and and this allows us to calibrate the response of the log detector.
Recent results are showing that this device is starting to be operational and there are we are confident that in the future it can be used for absolute electrical center identification

## Slide 73
N = 10 M = 15

## Slide 74
Mechanical constraints impose a correlation while moving.
CLIC accelerating structure
GIRDER
Beam screen
Ideal trajectory
Real trajectory
BEAM
Move the structure
BEAM
H-Mover
1
CLIC STRUCTURE
H-Mover
2
V-Left-Mover
2
V-Right-Mover
2
V-Left-Mover
1
V-Right-Mover
1
GIRDER
CLIC ACCELERATING STRUCTURE
Notes: The first one relies on the movimentation of the whole accelerating structure that is positioned on a movable girder.
Unfortunately, during an experimental campaign to verify the system, it was found that while imposing a vertical movement the structure after a certain region was moving with an angle also in horizontal.
As a consequence this method was not used.

## Slide 75
- Single bunch
- Constant bunch length (4 ps)
Linear dependence of the charge
Dominant dipolar component
Linear dependence of the charge
Dominant dipolar component
- Multi bunch (20 bunches)
- Different bunch length
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Notes: For this reason, several simulations campaign were carried out in order to compensate the impact of the different bunch length.
The result, correcting for the bunch length shows a better linearity.

## Slide 76
- Single bunch
- Constant bunch length (4 ps)
Linear dependence of the charge
Dominant dipolar component
Linear dependence of the charge
Dominant dipolar component
- Multi bunch (20 bunches)
- Different bunch length
Under the assumption of:
Dominant dipolar component
Linear dependence of the charge
Linear dependence of the charge
Notes: For this reason, several simulations campaign were carried out in order to compensate the impact of the different bunch length.
The result, correcting for the bunch length shows a better linearity.