## Slide 1: Novel Muon Tomography Detector for the Pyramids Muography 2021 November 24-26, 2021
Some of this work was sponsored by the U.S. Department of Energy Office of Fossil Energy
PNNL-SA-166923
Richard Kouzes1, Alain Bonneville1,2, Azaree Lintereur3, Ayman Mahrous4, Isar Mostafanezhad5, Ben Rotter5, Ryan Pang5, Farjana Snigdha5, Michael Tytgat6, Yasser Assran7, Shereen Aly8, Basma ElMahdy9
1Pacific Northwest National Laboratory (Richland, WA), 2Oregon State University (Corvallis, OR), 3Penn State University (State College, PA), 4Egypt-Japan University of Science and Technology (Alexandria, Egypt), 5Nalu Scientific (Honolulu, HW), 6Ghent University (Ghent, Belgium), 7The British University in Egypt (Cairo, Egypt), 8Helwan University and Canadian International College (Cairo, Egypt), 9Helwan University and The British University in Egypt
Notes: 20 minutes Abstract— Cosmic-ray muons, which impinge upon the Earth at a rate of approximately 160 muons·m-2·s-1, can be used to image the density of geological and man-made materials located above a muon detector. The detectors used for these measurements must be capable of determining both the muon rate and angle of incidence. Applications of this capability include geological carbon storage, natural gas storage, enhanced oil recovery, compressed air storage, oil and gas production, tunnel detection, and detection of hidden rooms in man-made structures, such as the pyramids. For these applications the detector must be small, rugged, safe and have operational characteristics which enable use in remote locations, such as low power requirements. A new muon detector design has been constructed to make measurements on the Khafre pyramid to look for unknown voids that might exist in the structure. The new detector design uses plates of scintillator with fiber optic readout to obtain position information. This design will meet the operational requirements, while also providing a geometry which can be modified for different measurement conditions. 15-minute presentation

## Slide 2: Cosmic Ray Muons
Fundamental particle (lepton) t1/2=1.56 ms
Similar to electrons: 207 times an electron mass, or 105.7 MeV/c2
Created when high energy cosmic rays hit the atmosphere
160 muons/m2/s at sea level
Average energy is ~6 GeV
Muons lose about 2 MeV/g/cm2
Muons deposit ~2 MeV in 1 cm of plastic

## Slide 3: Muon Distributions
Muons span a wide energy range (MeV to TeV+)
Follow ~cos2 distribution
Flux is impacted by the weather and solar activity
Sea level energy plot from CRY (Hagmann UCRL-TM-229452 )
Sea level angular plot from (Shukla 2018)

## Slide 4: Muon Detection Applications
Muon detection has a wide range of applications
Background rejection for low-background experiments
  Neutrino detection
  Dark matter experiments
  Neutrinoless double beta decay
High energy physics basic research
Tomography using muons
  Volcanoes
  Pyramids (Khufu already imaged)
  Tunnel detection
  Underground storage
  Spent fuel storage
  Vehicle imaging for homeland security
From https://decisionsciences.com/our-product/#technology
Pyramids
Spent Fuel
Safeguards
Vehicle Inspection

## Slide 5: Muon Detection
Muons create ionization in the detector medium.
Coincidence removes background from gamma rays
Example of two polyvinyl toluene (PVT) panels
PVT scintillators
PMTs

## Slide 6: Muon Tomography Trajectory
  To determine the muon direction, the x and y muon interaction positions must be detected for at least two points separated vertically in space
  Angular resolution is determined by x and y resolution and spacing between detection planes
muon
z
x
y
spacing
(x1,y1)
(x2,y2)

## Slide 7: Previous Project: Borehole Detector
Develop muon detector capable of fitting in boreholes to perform density tomography of geological structures.
Create an efficient inversion method that incorporates muon trajectories and data generated by seismic and gravity techniques.
Chain of detectors to monitor muon flux over decades
Simple and rugged
Withstand severe environmental conditions
Example of deployment of muon detectors in a deep well to monitor density variations in a geological formation used to store CO2.

## Slide 8: Detector Design: The Size Challenge
From a lab size detector….
…to a borehole detector.
3.3 ft. long (~1 m)
5 to 8”
(13 to 20 cm)
LANL Gas Tube Mini Muon Tracker (MMT)

## Slide 9: Borehole Detector Design
Miniaturization of the detector elements and electronics
Goal: detect 1% change in CO2 density per year
Must fit in a borehole (~6 inches ~16 cm)
Must survive temperature > 45℃ & pressure > 10 MPa
Detector components
Polystyrene plastic scintillator rods
Optical fibers (Saint-Gobain BCF-922)
SiPM readout

## Slide 10: Prototype Underground Lab Test Data
Above ground
Below ground
Detector underground next to stairwell.
Polystyrene rods
Active area ~15x30 cm

## Slide 11: Tests of Muon Detectors at LANL Tunnel Facility
Mini Muon Tracker
Borehole Muon Detector
Mini Muon Tracker
Notes: LANL Participants:
C. Rowe
E. Guardincerri
M. Durham
UNM collaborators
M. Roy
M. Dichter

## Slide 12: New Project: Pyramid Tomography
Detector design (inspired by borehole design) requirements:
  Assembly must be less than 1 meter cubed in size
  Light enough to be easily hand transported
  No toxic, flammable or asphyxiating gases
Pyramid of Khafre
  215.3 m base
  136.5 m high
From http://guardians.net/egypt/pyramids/Khafre/KhafrePyramid.htm

## Slide 13: Muon Pyramid Detector Design
Detector specifications
  Polyvinyl toluene (PVT) scintillator with fiber readout
  SiPM readout (only low voltage required)
  Position resolution of better than 5 mm
  61 cm by 61 cm square active area in two panels
  Variable angular resolution by changing panel spacing between 20 cm and 100 cm
Components
  PVT scintillator with orthogonal fiber optics on opposite sides (from Eljen Technology)
  Custom PC boards (by Nalu Scientific) to mount SiPMs (from Hamamatsu) at one end of each fiber
  Commercial digitizer electronics (from CAEN)
  Controlled by a laptop with custom software
  Mounted in cases and support frame

## Slide 14: Muon Detector Concept
PVT slab: 61 cm x 61 cm x 2 cm
Wavelength shifting optical fibers (2 mm) spaced at 1 cm embedded in both faces in orthogonal directions
PVT
fibers

## Slide 15: Muon Detector Concept
Muon deposits about 4 MeV in the 2-cm thick PVT slab producing scintillation light
PVT
muon
fibers
scintillation

## Slide 16: Muon Detector Concept
Small amount of scintillation light is transported to the fibers
Black coating reduces reflections to improve localization
PVT
muon
fibers
scintillation

## Slide 17: Muon Detector Concept
Fibers wavelength shift the light and transport it to the SiPMs
SiPMs generate electrical pulses proportional to light collected
PVT
muon
fibers
scintillation
Muon position is extrapolated based on signal size on all hit fibers

## Slide 18: Muon Detector Construction
Orders for components made
PVT, SiPMs and electronics sent to Nalu
Nalu made a custom PC board to mount SiPMs
Vendors to ship components to Egypt for final assembly

## Slide 19: Muon Detector Scintillator
Scintillator fabricated and delivered
Fibers spaced at 1 cm
Interpolation should give < 5mm position information

## Slide 20: Muon Detector SiPM Board
Printed circuit boards delivered
All SiPMs functional

## Slide 21: Muon Detector Electronics
CAEN electronics delivered
  DT5550W motherboard
  A55PETx piggy board
  SCI-5550W readout software
Electronics testing underway
Detector being assembled

## Slide 22: Simulations
Simulations are being made of the muon detector for tomography in the Khafre pyramid

## Slide 23: Results and Next Steps
Components for the detector are in hand
Detector assembly and testing done at Nalu Scientific
Components in transit to Egypt
Final assembly and testing will be performed at EJUST in Egypt
The detector should be fully operational early in calendar year 2022
Pyramid measurements to be made in 2022

## Slide 24: Pacific Northwest National Laboratory
Questions
Project Collaborators: Alain Bonnevillea,i, Richard T. Kouzesa, Jared Yamaokaa, Charlotte Roweb, Elena Guardincerrib, J. Matthew Durhamb, Christopher L. Morrisb, Daniel C. Poulsonb, Kenie Plaud-Ramosb, Deborah J. Morleyb, Jeffrey D. Baconb, James Bynesc, Julien Cercillieuxc, Chris Ketterc, Khanh Lec, Isar Mostafanezhadc j, Gary Varnerc, Joshua Flygared, Azaree T. Lintereurd, Ayman Mahrouse, Bjorn Paulssonf, Nedra Bonalg, Robert Mellorsh, George Chaplineh, Ben Rotter j, Ryan Pang j, Farjana Snigdha j, Michael Tytgatk, Yasser Assranl, Shereen Alym, Basma ElMahdyn
a Pacific Northwest National Laboratory, Richland WA h Lawrence Livermore National Laboratory, Livermore, CA
b Los Alamos National Laboratory, Los Alamos, NM i Oregon State University, Corvallis, OR c University of Hawaii at Manoa, Honolulu, HI j Nalu Scientific d Pennsylvania State University, State College, PA k Ghent University, Ghent, Belgium
e EJUST, Cairo, Egypt l The British University in Egypt, Cairo, Egypt
f Paulsson Inc. m Helwan University and Canadian International College, Cairo, Egypt
g Sandia National Laboratory, Albuquerque, NM n Helwan University and The British University in Egypt