## Slide 1
LHCb ECAL Upgrade 2 – prototypes to be studied
Several ECAL prototypes, built with different technologies.
Ways to improve the intrinsic time resolution:
Two longitudinal sections (split at ~7X0), double sided readout
PMTs with best time characteristics
The ECAL prototypes
W-GAGG:Ce SPACAL: for the very central area. GAGG:Ce is an extremely radiation hard scintillator, with a very high light yield
Pb-PS:PTF:POPOP SPACAL: for intermediate areas. The scintillator can be a polystyrene-based one (PTF and POPOP dopants)
  tests with polysiloxane-based scintillators are foreseen
Modified Shashlik, with improved time resolution: for periphery
  With faster WLS fibers (R&D with KURARAY)
  Two modes of double sided readout: split and continuous WLS fibers
LAPPD (only MCP part) can be (optionally) used as a timing layer in between the longitudinal sections (LAPPD Gen II received in Bologna for tests)
Purpose: study of different options considered for the LHCb U2 (Lumi of 1..2∙1034 cm-2s-1, doses up to 1 MGy for 300 fb-1).
To be measured: energy resolution, intrinsic time resolution.
timing layer

## Slide 2
Beam requirements:
e±:
  Wide range of energies: (10?)-20-150 GeV
  Good purity (>50%)
  Rate: > 1 kHz during the spill (for most of the energies)
μ
  high energy, 50-150 GeV
Beam requirements
Up to now, we tested the prototypes in DESY, at 1-5 GeV electrons. At LHCb, ECAL will work at higher energies!
We absolutely need to study the performance till as high energies as possible in NA (at least 100-150 GeV).

## Slide 3
prototype under study
beam
The setup is:
Scintillators for the beam trigger (CMS)
SciFi hodoscope (CMS)
Two MCP-PMT-based Cerenkov counters (plex radiator) for the time reference (provided by us)
Required infrastructure:
Rack for electronics (present at PPE164)
XY moving table (present at PPE164)
The idea is to use as much as possible the CMS infrastructure which is present in the area
Infrastructure requirements – option 1 (PPE164)

## Slide 4
prototype under study
beam
Infrastructure requirements – option 2 (outside of PPE164)
The setup is:
Scintillators for the beam trigger
Two MCP-PMT-based Cerenkov counters (plex radiator) for the time reference
Three XY DWC for coordinate measurements
Required infrastructure:
Rack for electronics
XY moving table (provided by us)
Gas (Ar/CO2) for DWC (provided by us) Need a place to install the bottle
Mostly a standalone / portable setup
@H8, 2018

## Slide 5
note on planning
More prototypes are expected after / will arrive late for our July-August tests.
We would need some more time in October (3 days?).
Can be any beam line, not necessarily H4
Can be night shifts only.