## Slide 1: Some brainstorming ideas for the design of Linac4-RFQ3
Hermann Pommerenke (SY-RF-MKS)
6 May 2021

## Slide 2: Recent RFQs developed at CERN
…
Linac4-RFQ 352 MHz 3 m
HF-RFQ 750 MHz 2 m
PIXE-RFQ 750 MHz 1 m
Carbon-RFQ 750 MHz 4.8 m
commissioned 2018 (now with AVO ADAM)
operational,
work in progress on spare and upgrade
RF measurements & tuning completed in 2020
Beam dynamics & RF design completed early 2020, now mechanical design by CIEMAT
C. Rossi et al., „Commissioning and operational experience gained with the Linac4-RFQ at CERN”, Proc. Linac14, 2014

## Slide 3: Trapezoidal electrodes/vanes
standard vane
trapezoidal vane
concentrate more electric field in the gap (equivalent to reducing gap length in DTL)
what can we gain? (Example: Carbon-RFQ)
standard vanes
trapezoidal vanes
Φ (a.u.)

## Slide 4: The trapezoidal vane - details
many degrees of freedom:
m : modulation
L : length r0: mid-cell aperture
g : accelerating gap length [not in standard vanes] ρt : transverse vane tip radius
maximum steepness
purely sinusoidal

## Slide 5: Standard vs. sinusoidal vs. trapezoidal RFQ
a – minimum aperture, m – modulation factor, g – accelerating gap length, Ws - synchronous energy, Фs – synchronous phase, A1,0 – acceleration efficiency, B – focusing strength, ρl – longitudinal radius of curvature, Es,max – max. surface electric field, σ0 transverse phase advance per focusing period (zero-current)

## Slide 6: Profile of trapezoidal vanes

## Slide 7: Sixteen-term potential function
RFQ electric fields commonly described by multipole expansion (typically 8 terms)
for trapezoidal vanes we need more terms!
precomputed in lookup tables (COMSOL)
quadrupole
acceleration

## Slide 8
b = (c+19mm)/sqrt(2)
c
ideal cavity dimension
capacitance
Capacitance with trapezoidal vanes

## Slide 9: Some other ideas
non-uniform voltage
  voltage becomes additional tapered parameter
  can be advantageous for beam dynamics and maximum surface fields
  RF design more challenging, more difficult to tune
  Examples: LEDA-RFQ, IFMIF RFQs, FETS RFQ, J-PARC RFQs, XiPAF RFQ
equipartioned RFQ design (R. A. Jameson)
  natural balance of transv./long. forces to minimize emittance growth from space charge
  Examples: IFMIF RFQ, J-PARC epRFQ
Y. Kondo, T. Morishita, R. A. Jameson, „Development of a radio frequency quadrupole linac implemented with the equipartitioning beam dynamics scheme”, Phys. Rev. Accel. Beams 22, 120101 (2019)

## Slide 10: Example: J-PARC epRFQ
Y. Kondo, T. Morishita, R. A. Jameson, „Development of a radio frequency quadrupole linac implemented with the equipartitioning beam dynamics scheme”, Phys. Rev. Accel. Beams 22, 120101 (2019)

## Slide 11: RFQs worldwide – Kilpatrick criterion
Kilpatrick criterion is used for most RFQ developments (common design choices CW-RFQ: <=1.8 Kp, pulsed RFQ: <=2.0 Kp)
but: during commissioning: more can often be achieved:
experiment
design

## Slide 12: „Gap scaling“ and other quantities for RFQs
d = V/Emax (not too far from RFQ r0)
where
V = max. measured inter-vane voltage Emax = max. measured surface field
VDC = 7747 V, dDC = 100 µm from DC experiment (I. Profatilova https://indico.cern.ch/event/925403/contributions/3889048/attachments/2050505/3436872/20200604_WP_RFQ3_design_Introduction.pdf)

## Slide 13: What about Sc and RF pulsed heating?
Example: proton HF-RFQ: tpls = 20 us, f0 = 750 MHz
Emax on vane tip (2.0 Kilpatrick)
small hotspot on inter-module gap
(2.2 Kilpatrick)
Hmax on vane undercut edge resulting pulsed heating:
ΔT = 1.8 K (critical: 40…100 K)
Sc maximum is not on vane, i.e. not in location of breakdowns
E & H are well-separated in RFQ
Sc maximum is located on undercut edge next to dipole rod
not critical either, scaled threshold at 20 us: 860 mW/um²

## Slide 14: Dipole-mode detuning by length adjustment
maximum spectral margin from operating mode (TE210) to dipole modes is crucial for field stability
„classic“ techniques: dipole stabilization rods (DSR, used in L4-, HF-, PIXE-RFQ), vane coupling rings, coupling windows …
Carbon-RFQ detuned using length adjustment only, no DSRs necessary
would not need these