## Slide 1: Short-term DAQ/SC development plan to support detector prototypes
G. Lehmann Miotto CERN

## Slide 2: Introduction
Focus on the short term plans up to the VD coldbox test
The VD ProtoDUNE II run is seen in the long-term plan context, since we would like to use the quasi-final DAQ and SC interfaces and components for it
Slow Control
Continuity with NP04/NP02
DAQ
Introduction of the new SW design,
Support for legacy electronics as needed,
Possibly ad-hoc solutions (e.g. timing)

## Slide 3: Slow Control
Work kept to absolute minimum necessary
Same WinCC OA server, different project
Data archiving to oracle
Control and monitoring in control rooms and via cerntsice for experts
Monitoring over web (if we find someone to work on this)
Coldbox on detector ground
Transformer and impedence monitor from NP02
SC racks installed close to the coldbox on an insulating support
Relying on infrastructure designed and setup for NP02/NP04
De facto very few people working part time on it

## Slide 4: Slow Control
Inventory of equipment ongoing
Interaction with cryogenics defined
To a large extend re-deployment of power supplies and instrumentation used in NP02/NP04
Need to understand what is needed for the photon detectors in terms of control and monitoring
Safety matrix to be discussed and agreed upon with other consortia and NP technical coordination

## Slide 5: DAQ
Development organised around release cycles
  Dunedaq-v2.0.0 ThanksGiving (26 Nov 2020)
    Basic application framework: queues, modules, logging, commands reception & execution
  Dunedaq-v2.2.0 MinidaqArising (23 Jan 2021)
    Single DAQ application implementing readout, trigger, event builder, data writer modules
  Dunedaq-v2.4.0 SleeplessNights (22 Mar 2021)
    Distributed DAQ applications supporting data flow functionality; FELIX support; first implementation of simple run control and operational monitoring
  Dunedaq-v2.6.0 ItsVaccinated (4 June 2021)
    Introduction of trigger logic, timing application and timestamping of external hardware signals; support for readout of WIB1, WIB2 and DAPHNE

## Slide 6: DAQ Today

## Slide 7: Dunedaq-v2.8.0
Trigger primitives based data selection;
Trigger primitives storage;
First implementation of readout interface for ND;
Data quality monitoring prototype.

## Slide 8: Supporting VD specific activities
In order to support the VD developments there are two areas that require immediate work:
  Ethernet based readout for the top electronics
  Check of the compatibility of the two existing timing distribution systems and establishment of the mechanism for having a unique sample counter in all front-end systems, used by the DAQ to identify the data

## Slide 9: Support for 40G Ethernet FE
As a first implementation, usable for the coldbox, data will be received over 40/100G NICs
  Use of standard NW stack or DPDK
  No hit finding
  Getting familiar with data formats, initialisation sequences, etc
The longer term goal of implementing a system symmetric to the FELIX readout will be described later

## Slide 10: Dunedaq-v2.10.0
Multi-host event building;
Support of ethernet readout for VD top electronics;
Extended control, configuration, monitoring.
What will the VD PDS electronics interface look like?

## Slide 11: Timing compatibility – Test 0
The experts consider that the two timing distribution systems can inter-operate without problems (more details in next talk)
A first test setup will be prepared to start validating the relative stablity of the two systems and measure the differences in the timestamps produced by the two systems

## Slide 12
EHN1 surface (NP02)
VD coldbox pit racks