## Slide 1: DAQ/SC Conceptual Design Review for FD2
G. Lehmann Miotto / CERN

## Slide 2: Agenda

## Slide 3: Preface
The DAQ/SC consortium is developing solutions for all DUNE detectors, far and near
Interfaces to all detector components are defined uniformly, in order to make this possible
Wherever specific needs require custom interfaces or behaviors, this results in additional effort

## Slide 4: DAQ/SC Consortium organization
Facility & Integration WG
FD Upstream DAQ WG
Dataflow WG
FD Data Selection WG
Control Configuration Monitoring WG
Data Monitoring WG
DUNE/LBNF management
Slow Control WG
ND Upstream DAQ WG
ND Trigger WG
DAQ/SC management board
DAQ/SC institutes board
Consortium lead
FD technical lead
ND technical lead
Resources coordinator
G. Lehmann Miotto
F. Filthaut
D. Newbold
A. Thea
A. Kaboth
J. Brooke, R. Sipos
J. Klein, P. Rodrigues
K. Biery
P. J. Dunne
P. Mendez Lorenzo
A. Habig, B. King
J. Hays
A. Tapper
🇨🇦🇳🇱🇬🇧🇺🇸

## Slide 5: DAQ overview and requirements
G. Lehmann Miotto / CERN

## Slide 6: Outline
VD DAQ requirements
Detectors
Physics
Offline
DAQ interfaces
DAQ overview
Subsystems
Components

## Slide 7: DAQ Requirements
Distribute clock and unique timestamping to all detectors
  Common clock (62.5 or 125 MHz)
  1 us synchronization across FDs
  ~10 ns synchronization within one FD
Configure, control and monitor the data taking process
  Provide sw tools for detector experts to implement their specific functions within the DAQ framework
  The DAQ shall introduce negligible downtime, compared to the experiment requirements
Receive timestamped data over optical links from all detectors
  Charge readout: data sampled at ~2 MHz
  Photon detectors: 5 us waveforms of tiles that pass an internal trigger threshold

## Slide 8: DAQ Requirements
Buffer, select, aggregate and store detector data
  Select data with > 100 MeV of visible ionization energy with very high efficiency (>90%)
  Select data with < 100 MeV and > 10 MeV of neutrino visible energy with a good efficiency
  Generate a SNB trigger candidate if there are more than 60 neutrino interactions wih Eν>10 MeV within 10 seconds with an efficiency > 95%
  Store all data for 30s corresponding to a SNB trigger (goal to reach 100 s)
Transfer the recorded data to FNAL over a dedicated WAN connection
  Cap of 30 PB/year for all far detectors raw data set by offline long-term storage capacity; more data may be transferred to FNAL, but not for permanent storage
  In addition, condition, configuration and monitoring data will be transferred to FNAL
See talk by J. Klein

## Slide 9: DAQ VD Specifications
Readout 1040 WIB links (10G), 400 uTCA links (40G), few hundred PDS links (?)
  While internal data organisation differs, all packets coming from the electronics shall have a 64b timestamp and a field fully specifying the origin
    WIB frame has a header with the required info and 1 ADC value for 256 channels,
    PDS data expected to have a header with the required info and 375 (750?) consecutive ADC values for 1 channel,
    Data from uTCA boards will have the required info and N consecutive ADC values for 64 channels
  It is a responsibility of the electronics experts to provide data decoders for their data
Reduce data volume from ~2 TB/s to ~0.5 10-3 TB/s -> reduction factor 4000
  Achieved through selection in time and geographic regions of activity based on the data themselves and through lossless data compression at the end of the chain
See talk by R. Sipos

## Slide 10: DAQ Physical Interfaces

## Slide 11: DAQ Interfaces
Protocols ↔ detector electronics
Trigger strategy ↔ Physics groups
Data formats, conditions ↔ offline computing
Data taking procedures ↔ detector electronics, calibration devices

## Slide 12: DAQ – Detectors communication
Besides the interfaces mentioned earlier, there are also finer grained aspects that need to be discussed and agreed upon
Example: mapping of detector channels can complicate our lives

## Slide 13: DAQ Hardware
Largely based on commercial components
Distributed on underground cryo-mezzanine and surface MCR
DAQ VD M&S of ~4.2 M$
VD procurement 2023 - 2027
System scale:
~200 servers, redundant network with aggregate bandwidth of ~600 Gb/s
125 kW in each DAQ barrack on top of the cryogenic mezzanines; Short term UPS
50 kW in a common counting room;

## Slide 14: DAQ Subsystems
While timing, readout, trigger and data filter implement specific application-level functions of the DAQ system, the CCM, DQM and Dataflow are a mixture of application-level software and services/libraries used by all other components. As an example, the Dataflow implements the event building application logic, but also provides the DAQ network communication libraries.
See talk by K. Biery
See talk by A. Thea

## Slide 15: DAQ overview
Only fiber connections to DAQ for electrical decoupling

## Slide 16: DAQ overview

## Slide 17: VD DAQ/SC CDR Review
In this review we will focus on some of the DAQ and SC aspects that are relevant to address the CDR charge:
1. Are the requirements documented? Are they reasonable?
2. Is the scope understood? Is there a team in place? Which institutions are interested?
3. Is there a reasonable plan for R&D and prototyping?
4. Is the design concept reasonable and feasible? Have appropriate mechanical and electrical calculations been performed?

## Slide 18: Agenda