## Slide 1: Summary
G. Lehmann Miotto

## Slide 2: Charge Questions
1. Are the requirements documented? Are they reasonable?
2. Is the scope understood? Is there a team in place? Which institutions are interested?
3. Is there a reasonable plan for R&D and prototyping?
4. Is the design concept reasonable and feasible? Have appropriate mechanical and electrical calculations been performed?

## Slide 3: Are the requirements documented and reasonable?
The requirements for the VD far detector are understood and documented
  Overall far detector requirements (TDR)
  The VD CDR will re-state and highlight the requirements: no changes expected for DAQ/SC
The requirements are reasonable and achievable
  The requirement of 30 s of continuous storage for a SNB candidate is reasonable; is the goal of 100 s of continuous storage needed? This does not have design implications, but cost.
  The requirement of reducing the data volume to 30 PB/y for the full far detector is reasonable; the push to extend the physics reach to lower energies wrt the DUNE goal, requires careful tuning of the trigger/filter and data compression

## Slide 4: Is the scope understood? Is there a team in place? Which institutions are interested?
The scope of DAQ and SC for VD is understood
  Interface documents need to be revised/completed with all VD consortia (PDS, CALCI in particular)
  The 3D configuration produces more data than HD, but at manageable level
A team is in place but not complete
  The DAQ team can carry out the development, support, installation & commissioning programme, with careful planning
  The SC team is insufficient; SC for coldbox and ProtoDUNE-II relies on expertise at CERN
DAQ Institutions: Canada, CERN, Netherlands, UK, US

## Slide 5: Is the design concept reasonable and feasible? Have appropriate mechanical and electrical calculations been performed?
We believe that the design concepts for DAQ and SC are reasonable
  More work is needed for the layout of the timing system, but the relevant experts are actively working on this
The feasibility is linked to the pledged resources becoming available timely
  SC is not covered sufficiently from an effort point of view
  DAQ is covered but may be stretched on the M&S
    Staging scenarios are possible and will not put the VD at risk
Mechanical and electrical requirements have been discussed and agreed upon with the technical coordination and I&I
  Room, racks, power & cooling for DAQ/SC underground is sufficient ; power & cooling for DAQ/SC on surface is scarse , but sufficient
  The DAQ is electrically decoupled from the VD, in order to avoid any noise injection
  The SC equipment is partially on detector ground; any connection to equipment on building ground is electrically decoupled