## Slide 1: ATLAS VCSEL based links
Ph. Farthouat, CERN

## Slide 2: Purpose of this meeting
We are (have been) experiencing VCSELs failures in ATLAS
  Pixel/SCT, Lar, RPC
LHCb is also reporting some failures
This meeting is an attempt to:
  Give a complete picture of the use of VCSELs in ATLAS
  Share information about failures in different sub-systems and the on-going analysis
  Prepare coordinated actions/work in view of understanding and solving the problems

## Slide 3: VCSELs in ATLAS
Detector | VCSEL type | Manufacturer | Package | Number | Failures
Pixel on-det. | Oxide 8-way Array | True-Light | Custom Ac. Sinica | 312 | None
SCT on-det. | Proton implant | True-Light | Custom Ac. Sinica | ~8200 | Very few see report
SCT/Pixel off-det. | Oxide 12-way Array | True-Ligh | Custom Ac. Sinica | ~650 272+376 | ~20/week see report
TRT | Oxide | AOC (Finisar) | LC | 768 | None
LAr | Oxide | True-Light | Custom Ac. Sinica | ~1600 | ~1-2/month see report
Tiles | Proton implant | True-Light | Custom Ac. Sinica | 512 | None
MDT | Oxide | AOC (Finisar) | LC | ~1200 | None
RPC | Oxide | Avago | MT-RJ | ~512 | ~1/month see report
TGC | Oxide | Infineon | LC | ~200 | None
CSC | Oxide | Stratos | SC | ~160 | None
S-Link | Oxide | Infineon | SFP | ~1600 | ≤6 since 2006

## Slide 4: Remarks
On-detector VCSELs of SCT and Pixel send light only when there are transmitting data
  “on time” is a function of trigger rate and occupancy
All other VCSELs are on half of the time
  TTC transmission (SCT/Pixel off detect.)
  Gbit links using 8b10b (or similar) encoding for all the others
Detailed reports this afternoon for those failing and the on-detector SCT and Pixel

## Slide 5: Agenda
Introduction and VCSELs in ATLAS
VCSELs in LHCb
VCSELs in the RPC
VCSELs in the Lar
On-detector SCT VCSELs
Off-detector SCT/Pixel VCSELs
On-detector Pixel VCSELs
On-going analysis for the on-detector Pixel VCSELs
Work in Taiwan and interactions with True-Light
Discussion