## Slide 1: The Beam Interlock System User Interface (CIBU) Overview and Radiation Tests Results
Raffaello Secondo on behalf of TE-MPE-MI
8th June 2021

## Slide 2: Beam Interlock System (BIS) Concept
∑(USER PERMITS = TRUE)  BEAM PERMIT = TRUE
BIC: main controller, acts as concentrator collecting USER PERMITS, generating BEAM PERMIT
Beam
Interlock
Controller
User Interface (CIBU)
User Systems
TARGET SYSTEM (BEAM DUMP)
14
14
1
<4m
Current Loops
USER PERMITS
<1200 m
RS-485
OR >1200 m
Fiber Optics
BEAM PERMITS
Single-Mode
Optical Fibers
SOFTWARE PERMIT (SIS)

## Slide 3: Beam Interlock System (BIS) User Interface (CIBU)
LHC : ~150 CIBUs
SPS and Injectors: ~350
User Permit A
Beam Interlock Controller
USER SYSTEMS
(PIC, FMCM, BLM etc..)
Front
Rear
User Interface (CIBU)
BEAM PERMIT
User Permit B
User Permit A
User Permit B

## Slide 4: CIBU Positions - LHC
CCR
Point1
  L1: RR13, US151, SR1,
  R1: RR17, USA151, USA152, US15, US153
Point 2:
  L2: UA23, SR2
  R2: UA23, UA27, CR4
Point 3:
  U3: UJ33
  S3: SR3
Point 4:
  R4: UA47, US451, UX45
  L4: UA43, SX4, SR4
Point 5:
  R5: USC55, RR57
  L5: RR53, USC55, SR5
Point 6:
  R6: UA67, SR6, US65, UA67
  L6: UA63, SR6, US651
Point 7:
  U7: RR73, RR77, TZ76
  S7: SR7
Point 8:
  R8: UA87, UX85, UX85 (platform)
  L8: UA83, US851, SR8
2x CIBU in the RR  12 total

## Slide 5: Target Radiation Levels
HL-LHC Radiation Level Specification:
https://edms.cern.ch/document/LHC-N-ES-0001/1.0
Hi-Lumi, RR (L1) ultimate scenario: 4000 fb-1
TID = ~280 Gy
Max. HEH fluence/year = ~ 1.4x1010 cm-2
HEH total fluence = ~1.6 x1011 cm-2 total
1MeVn-eq fluence = ~ 8 x1011 cm-2

## Slide 6: Planning and Strategy
BIS v2: first installation planned during LS3
CIBU spares BISv1 running low
  CIBUv1 components hard to find
  Priority: CIBU preliminary design to be compatible with BIS v1
Evaluate and Test Components
CHARM
First BISv2 Installation
LHC
schedule
Focus on ONE design:
  COTS from available databases
  BE-CEM-EPR: Purchase components + hold the Lot purchased + Radiation Test and report
Aiming at a full system validation at CHARM

## Slide 7: Choice of Components
User Permit A
Beam Interlock Controller
USER SYSTEMS
(PIC, FMCM, BLM etc..)
Front
Rear
User Interface (CIBU)
BEAM PERMIT
User Permit B
User Permit A
User Permit B
CRITICAL
MONITORING:
2x Power supply monitoring
On board voltages
User Input Current

## Slide 8: COTS selection - Critical
USER INPUT
RS-485
OUTPUT
CIBU v2 schematic
CRITICAL |  | 
Component | Function | Second choice
FOD060L (AlGaAS) | High speed optocoupler 3.3V | Broadcom/Avago HCPL-060L (GaAsP)
MAX3430 | RS485 Transceiver | MAX13448E
BC847B and PZT2222A | NPN transistors | -
74LVT14D | Schmitt Trigger | -

## Slide 9: Radiation Tests Results
  RS485 driver MAX3430
  Report: EDMS #2417502
  No errors on RX side. Fail-safe feature tested.
  Reached TID 500 Gy and HEH fluence 8.5x1011 cm-2.
  SETs observed in data transmission, average device cross-section
  σ = ~ 1x10-11 cm2 in worst case conditions
Tests carried out at PSI by BE-CEM-EPR
Schmitt Trigger 74LVT14D
Report: EDMS #2417025
TID 500 Gy, HEH fluence 8.5x1011 cm-2
No large variation/degradation of all
quantities
74LVT14D Test Board
BJT Transistors: BC847B and PZT2222AT1G
Report: EDMS #2454604
TID 500 Gy, HEH fluence 8.5x1011 cm-2
Worst case degradation of 40%, within the manufacturer specifications
Courtesy of BE-CEM-EPR

## Slide 10: Radiation Tests Results - Optocoupler
BA6-Extraction
TRUEFALSE CRITICAL
FALSE  TRUE
Courtesy of BE-CEM-EPR
  FOD060: ~ 128 SET in 2x1011 cm-2
  HCLP-060L: ~ 7 SET in 2x1011 cm-2
  No variation of shape and pulse duration
Present CIBU optocoupler σ_SEE = 8.3 x 10-10 cm2
Report: EDMS #2416544
DDEF:
  FOD060L: ~ 9x1012 cm-2 1MeV neq (AlGaAs)
  HCPL-060L: ~ 5x1012 cm-2 1MeV neq (GaAsP)
Strong response to TID and DD.
Neutrons test foreseen.

## Slide 11: Radiation Tests Results – Full CIBU critical Chain
@500 Gy and HEH 8.5x1011 cm-2:
38 SETs
19 SETs
0 SETs
Report: EDMS #2415099
Total cross-section σ < 4.4 x 10-12 cm-2 (95% confidence)
Steps of 100 Gy and 1.7E11 p/cm2 fluence
Reached 500 Gy and HEH 8.5 x1011 cm-2
Hi-Lumi ultimate target: TID 280 Gy, HEH 1.4x1010 cm-2 max. annual
Courtesy of BE-CEM-EPR

## Slide 12: COTS selection – Non critical
MONITORING |  | 
Component | Function | Comments
INA240 | Current Sense Amplifier | Tested
AD7291 | 12-bit ADC + I2C | Tested
TPS3808G12DBVT TPS3808G33DBVT | FPGA supervisory circuit | Scheduled for Test
M2GL005-TQ144 | IGLOO2 FPGA | Tested (purchase new Lot)
POWER |  | 
Component | Function | Comments
LT3083 | LDO Voltage Regulator | Tested (purchase new Lot)
FSV1060V | Schottky Diode | Scheduled for Test
TPP40-105 | AC/DC Power Supply | Test foreseen

## Slide 13: Monitoring components results
INA240
EDMS #2588515
Reached 500 Gy and HEH 8.61 x1011 cm-2
High SEL cross-section
AD7291
EDMS #2591354
Reached 500 Gy and HEH 8.61 x1011 cm-2
No SEL, SEU, SEFI observed
No increase in current consumption
USER INPUT
MONITORING | 
Component | Function
INA240 | Current Sense Amplifier
AD7291 | 12-bit ADC + I2C
TPS3808G12DBVT TPS3808G33DBVT | FPGA supervisory circuit
Igloo2 | FPGA
Courtesy of BE-CEM-EPR

## Slide 14: Conclusions and Plans
  CIBU v2:
    Highly critical generic interface with users connected to the BIS.
    Foreseen deployment in the RRs during Hi-Lumi.
  Strategy:
    Focus on one unique design
    BE-CEM-EPR procurement and tests at component level at PSI
    Full critical circuit qualified
  Planned Activities
  Test Monitoring
    on-board ADC qualified
    INA240: high SEL cross-section
    FPGA supervisory circuit to be tested
  Power Supply Unit: Radiation tests to be planned
  Neutron Test on optocouplers.
  System level test at CHARM in 2021/2022 to validate the system