## Slide 1: ERL Prospects for High Energy Colliders
Introduction: Luminosity limitations in ‘conventional’ Colliders
The Energy Recovery concept
LHeC; FCCeh, FCC-ee und ERLC (ILC) as show case applications of the ERL concept in HEP:
Push-Pull; Recirculating Linac and Circular ERL configurations
Key aspects that need to be validated and demonstrated

## Slide 2: Circular Collider: Peak Luminosity
Luminosity recipe (round beams):
  1) maximize bunch intensities
  2) minimize the beam emittance
3) minimize beam size @ IP (constant beam power);
4) maximize number of bunches;
5) Optimize and potentially compensate for geometric form factor‘F’; Hourglass, X-ing etc
6) Improve machine ‘Efficiency’
Limited by beam-beam interaction
Injector complex / Synchrotron radiation
Optics & beam stability @ IP
Beam Power & Synchrotron Radiation
Assumptions for a HEP collider:
Equal number of bunches and matched beam sizes
in the 2 colliding beams
L

## Slide 3: Performance limitation of circular colliders
Beam-Beam Interaction:
Imposes a limit to the maximum acceptable bunch intensity
Limits the luminosity reach of a circular collider
Circular machine  Synchrotron Radiation in arcs:
Beam size increases in horizontal and shrinks in vertical plane  flat beams!
 minimize by* and increase N until xx reaches the beam-beam limit

and

## Slide 4: Performance limitation of circular colliders
Synchrotron Radiation in arcs:
Beam size increases in hor and shrinks in vert
LHeC CDR; arXiv:1206.2913
Reduced performance reach for higher beam energies
@ fixed power footprint  limits total beam current!
If bunch intensity is limited by beam-beam, then
SR limits the number of bunches
Power Scales with E4 and r-1
Circular lepton collide performance is limited by:
Beam-beam  bunch intensity
Synchrotron Radiation power  total beam current

## Slide 5
CM Energy spread
Linac Luminosity
Linac Beam Power
Beam Quality
L Spectrum
Bunches are squeezed for
Maximum Luminosity
Strong E-M Fields @ IP
Particles follow curved trajectory through IP
They emit photons [Synchrotron Radiation] @ the IP
[beamstrahlung]
Luminosity reach is directly proportional to beam power, and hence power consumption!
Independent of the underlying linac technology!!!!! What matters is Wall plug Efficiency!!
D. Schulte @ 9th International School for Linear Colliders
Markus Roth TU Darmstadt; Accelerators for Medical Applications 2015; Vösendorf, Austria
A linear Collider overcomes the beam-beam limit of a circular collider
[as the beam does not need to remain to be stable over many passages]
and even utilizes it for performance enhancement [pinch factor]
and minimizes the power losses through Synchrotron Radiation [no bends]
But it does so at the price of power requirements for luminosity production
and that the particles have only once the chance to collide!!!
Luminosity proportional to beam power [Beam Current x Energy]
And e+ production might be challenging!

## Slide 6
Energy Recovery
Recuperate the energy [and e+] from the spend beam after the interaction point
before the beam is dumped
non-linearity of the
beam-beam interaction can
not lead to instabilities and
beam losses if the circulation
of the particles in the machine
is short after the interaction

## Slide 7: The Best of both Worlds
Energy Recovery Linac concept: First proposal 50 years ago
M. Tigner: “A Possible Apparatus for Electron Clashing-Beam Experiments”,
Il Nuovo Cimento Series 10, Vol. 37, issue 3, pp 1228-1231,1 Giugno 1965
First Tests: Done at SCA @ Stanford in 1986
Interesting concept for FELs and Compton photon light sources,
and high current electron cooler concepts and colliders!!!
https://images.app.goo.gl/fJPy8BFcnWnzByRY8
Truly Revolutionary Accelerator design Concept!!!!
With the potential of changing the collider landscape!!!

## Slide 8: Energy Recovery Linac Configurations
Push-Pull Configuration:
2 SC linacs facing each other
Allows only pulsed linac operation
But allows Energy Recovery
Coupled Linac Configuration:
4 SC linacs facing each other
Allows CW linac operation
Allows Energy Recovery
Allows Positron recovery!
Costly implementation as 2 x SRF and SRF is the main cost driver for the ERL

## Slide 9
Valery Telnov BINP
In his proposal the machine is still pulsed and the cycle duration [seconds] is determined by the refrigeration system
Projects peak luminosity of ca 1036 cm-2s-1 @ 200MW wall plug power [wiggler 5MW; HOMs 45MW; cryo 110MW]
Luminosity independent of beam energy due to Energy Recovery! But Cryo sclaes with Linac length and HOM with I!
250GeV machine with 0.16A @ 1/3rd duty cycle  > 10GW beam power!!!
 https://indico.cern.ch/event/995633/contributions/4275159/attachments/2208757/3755756/telnov-lcws21.pdf
4 Linac ERL Collider Concept:

## Slide 10
Valery Telnov BINP
4 Linac ERL Collider Concept:
SRF taken from LCLS-II:
Q0 = 3 1010 @ 1.8K with E = 20MeV/m  heat of about 1kW/GeV
1/3rd duty factor with 3m bunch spacing  L = 0.5 1036 cm-2s-1 @ 160MW
and N= 1010, d = 3m, I = 0.16A and 250GeV CME

## Slide 11: Energy Recovery Linac Configurations
Recirculating Linac Configuration:
SC linac(s) that are connected through return arcs
Still implies some synchrotron radiation (depending on design ca. ½ of ring)
More cost efficient installation as the SC linac is passed more than once
Allows true CW SRF operation [beam loading only as transients during ramp-up]
Still avoids limits through beam-beam interaction!!!
Implies some beam size blow-up through arcs  return-arcs lattice design!
Multiple passes of beams with different energies through same SC linac implies
high beam current in SRF cavities
Effective ERL applications require
SRF technology with Q0 > 1010 and
Cost effectiveness requires peak fields of
V > 15MV/m

## Slide 12: LHeC / FCC-eh Racetrack ERL Collider configuration:
Example LHeC: 3-turn Recirculating SRF Linac and ERL operation
2 1km long SRF linacs
3 separate return arcs at each end of the linac,
matched for the beam energies
Each beam passes 6 times through the SRF:
3 passes with acceleration and 3 with passes deceleration  6 times Ie in SRF!
Operation in parallel with LHC/HE-LHC/FCC-hh
TeV scale collisions ➔ 50-60 GeV e-beam energy
power consumption < 100 MW
* LHeC CDR, arXiv:2007.14491
Arc 1
Arc 3
Arc 5

## Slide 13: LHeC / FCC-eh ERL Configuration: Layout Options & Scaling
Configurations:
FCC-he considers Point ‘L’ since FCC Week in Berlin
LHeC
arXIV:2007.14491

## Slide 14: LHeC: Recirculating Linac with ERL Operation as Baseline
Performance with 100MW Wall Plug Power limit:
1034 cm-2 s-1 Luminosity reach | PROTONS | ELECTRONS
Beam Energy [GeV] | 7000 | 60
Luminosity [1033cm-2s-1] | 16 | 16
Normalized emittance gex,y [mm] | 2.5 | 20
Beta Function b*x,y [m] | 0.05 | 0.10
rms Beam size s*x,y [mm] | 4 | 4
rms Beam divergence s’*x,y [mrad] | 80 | 40
Beam Current @ IP[mA] | 1112 | 15
Bunch Spacing [ns] | 25 | 25
Bunch Population | 2.2*1011 | 2.3*109
Bunch charge [nC] | 35 | 0.64
25 
 1034cm-2s-1 Luminosity can be reached in ep at HL-LHC [and FCC-pp]
arXIV:2007.14491

## Slide 15
Maximum Power of 300MW per beam @ 120 GeV and 2.47mA
V. Litvinenko BNL and Stony Brook University; T. Roser BNL; C. Llatas BNL
Two 11 to 90 GeV SRF linacs in 4 pass configuration
1/3rd of power consumption as compared to circular collider
CM Energy reach of 600GeV in 100km circumference tunnel
https://arxiv.org/abs/1909.04437
Physics Letters B, 804 (2020) 135394
Circular Energy Recovery Collider Concept: CERC proposal

## Slide 16
Vladimir Litvinenko; BNL and Stony Brook University
Circular ER Collider Concept:
10MW RF power
30MW RF power
100MW RF power

## Slide 17: ERL: SRF Challenge
Q0 versus accelerating voltage:
 Q0 directly linked to required cryogenics power!!
Hasan Padamse: ‘50 years of success for SRF accelerators’
Superconducting Sci. Technol. 30 (2017) 053003
 impressive progress over the last 10 years!!!
A(t) = * e-t/t ; Q0 = wt / 2
See talk by Bob Rimmer at this Symposium for more details!

## Slide 18: Performance Optimization for ERL Configurations
Synchrotron Radiation Power:
Can not be avoided for the racetrack configuration  requires scaling of the
return arcs with beam energy! But can reduce SRP by about 50% wrt ring
Beam-Beam interaction:
Not a limit - similar to linear colliders  can increase Ibunch
Beam size defined by source [like in a LC] and thus can be optimized
But beam size can not be pushed as extreme as in LC as the beam still needs
to pass through the SRF without losses during the deceleration phase
 Can recuperate positrons after collisions
Lattice and Optics design of return arcs:
Novel lattice design requirements for return-arcs!!! Optics and FFAGs.
Need to demonstrate total beam intensity limit for stability in SRF
 how many re-circulations and beam currents are possible?!
and need to demonstrate
Limits for beam perturbation with beam-beam interaction and SR in ERL configuration
What level of non-linearity and beam size are acceptable!!!
Acceptance of deceleration path!

## Slide 19
ERL2015, Stony Brook University, June 9, 2015
D. Pellegrini (EPFL/CERN) @ ERL’15
The momentum acceptance of the beam dump channel defines in the end the injection energy for the ERL [and thus the ERL efficiency]!!!

## Slide 20
ERL2015, Stony Brook University, June 9, 2015
D. Pellegrini (EPFL/CERN) @ ERL’15

## Slide 21
ERL
Facilities
Overview:
e.g.
ERL2017 workshop
@ CERN and
Updated 2019 & 2021
Legacy ERLs no longer in operation
Operational & upcoming ERLs
Planned ERL facilities
Normal Conducting ERLs
HEP ERL based studies

## Slide 22
ERL Evolution:
First Idea:
M. Tigner 1965
1960
1970
1980
1990
2000
2010
2020
2030
2040
First Demonstration
SLAC SCA / FEL 1987
JLab First MW beam power operation
FEL Demo [1999] & Upgrade [2000]
Multi-turn Operation
BINP FEL 2004 [NC]
HEP / NP ERL application
LHeC/FCC-eh; FCC-ee; ILC;
Multi-turn SRF, multi-MW
PERLE@Orsay 2025
ALICE
JEARI ERL
Multi-MW Operation
bERLin-Pro 2020
Multi-turn SRF
C-Beta 2019-2020
PERLE can validate the next 10-fold step in beam power
and provide the remaining demonstrations
[multi-turn ERL efficiency at high beam power]

HEP is ready for implementing a truly green accelerator concept!

## Slide 23
End

## Slide 24: Variations in the ERL Configuration:
Super Conducting 3-turn Recirculating Linac with Energy Recovery operation
CDR option with
9.3km [1/3rd of LHC];
60 GeV
Smaller version with
5km [1/5th of LHC];
50 GeV
Operation in parallel with
LHC/HE-LHC/FCC-hh
TeV scale collision energy
➔ 50-60 GeV electron beam energy
power consumption < 100 MW
O. Brüning, M. Klein and LHeC and PERLE Collaboration
Topical Review Exploring the energy frontier with deep inelastic scattering at the LHC
Journal of Physics G: Nuclear and Particle Physics, Volume 46 #2; November 2019

## Slide 25: ERL Validation Needs and Experience
Chart: SRF ERL Virtual Beam Power [MW]
| 2003 | 1997 | 2001 | 2018 | 2013 | 2016 | 2018 | 2008 | 2016 | 2019 | 2017 | 2017 | 2019 | 2014 | 2025 | 2017 | 2030 | 2020 | 2019
Virtual Beam Power | 0.03675 | 0.24 | 1.53 | 0.7079 | 0.0002 | 0.02 | 8 | 2.7e-05 | 0.0001755 | 5 | 6 | 0.001368 | 1.05 | 2.4e-05 | 684 | 0.0088 | 900 | 8 | 0.65
Operational experience up to 1MW virtual beam power:
bERLpro [1]
C-Beta [4]
PERLE [3]
MESA [2]
ERL@CBAF [5]
EUV KEK [1]
ARIEL TRIUMF [1]
CeC@RHIC [1]
sDALINAC [2]
eRHIC [6]
LHeC [3]
cERL @KEK [1]
ALICE [1]
Test ERL@BNL [1]
CBAF-ER [1]
IR-ERL JLab [1]
ERL demo [1]
JLab pioneering
ERL Collider Projects
ERL Test Facilities
ERL Applications
1.5MW Highest
demonstrated
Virtual beam
power
Proposed Collider Projects [e.g. LHeC / FCC-eh and FCC-ee and ILC-ERL] extrapolate demonstrated virtual beam power far beyond the achieved 1.5MW operation!!!
Demonstration of multi-turn, multi MW ERL
Operation is on its way!!!
C-Beta and PERLE

## Slide 26: Arc Optics: Emittance preserving FMC cells
52.3599
0
500
0
0.5
-0.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
52.3599
0
500
0
0.5
-0.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
52.3599
0
500
0
0.5
-0.5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
total emittance increase in Arc 1- 5: DexN = 4.9 mm rad
Arc 1 , Arc 2
TME-like Optics
DBA-like Optics
Imaginary gt Optics
Arc 3, Arc 4
Arc 5, Arc 6
factor of 20 smaller than FODO
Emittance dilution due to
quantum excitations:
Bogacz (JLab) @ ERL2015, Stony Brook University, June 9, 2015 and LHeC at HL-LHC", to be published
[Double Bend Achromat]
[Theoretical Minimum Emittance]
[Flexible Momentum Compaction]
Scaling with beam energy and radius of curvature!