## Slide 1: Conceptual layout of the MUC Test Facility 2nd Muon Community Meeting, 12-14 July 2021
by Rui FRANQUEIRA XIMENES*
CERN – Systems Department
Sources Targets Interaction (STI)
Targets Collimators Dumps (TCD)
rui.franqueira.ximenes@cern.ch

## Slide 2: TT10 line option (recap)
First ideas proposed by Marco C. in the 1st Community meeting. TT10 line option seen as most attractive (Roberto L. presentation).
  O(80kW) should be easily feasible by going sufficiently underground.
  4 MW does not appear to be a showstopper in this layout, but detailed studies will have to be performed.
  Future upgrades towards a collider and HP-SPL should be compatible with this layout.
  Experience with other facilities available
  Important to collect all requirements at this stage in order to be able to provide a first cost estimate by end of 2021 as requested by the study

## Slide 3: Layout
Layout components of the Demonstrator:
Target & Horn (first stage) and potentially superconducting solenoid at a later stage
Momentum selection chicane
Collimation & diagnostics area
Muon Cooling area
Downstream diagnostics area
++
Service areas (Cooling & ventilation, cryogenics, power, transport, etc…)
Radioactive storage
Branch to other experiments ?
… other??
Services (Cryogenics, cooling & ventilation, power, transport, etc)
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
*Indicative dimensions by C. Rogers

## Slide 4: Layout ideas
Target + Horn (and/or superconducting solenoid)
Target + Horn length (O) 5 m. (What volume with solenoid?)
Cooling (Target + Horn) and power (Horn) supplies required
High activation / radiation levels (specially for 4 MW case):
Service rooms for power & Cooling Ventilation
Shielding (& space for it)
Vessel
Handling solutions.
Radioactive storage in the surrounding area
Access from surface
All of these set requirements for the layout
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 5: Layout ideas
Target + Horn (and/or superconducting solenoid) - NuMI @ FNAL
Underground hall
Vertical Handling
Equipment by modules
Module is a suspended frame w/ equipment + shielding + utilities connections
Yun He, NuMI Neutrino Beam Operations and Megawatt Upgrade, NUFACT2019
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 6: Layout ideas
Target + Horn (and/or superconducting solenoid) - NuMI @ FNAL
Utilities room on a separate gallery parallel to the beamline
Shielding between beam line access shaft
Yun He, NuMI Neutrino Beam Operations and Megawatt Upgrade, NUFACT2019
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 7: Layout ideas
Target + Horn (and/or superconducting solenoid) - T2K @ J-PARC
Vertical Handling
Equipment by modules
Module is a suspended frame w/ equipment + shielding + utilities connections
Installation by steps
Placed inside a He vessel
https://t2k.org/docs/photos/beamline
https://doi.org/10.1016/j.nima.2011.06.067
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 8: Layout ideas
Target + Horn (and/or superconducting solenoid) - CN2PY - LBNO
Wide transversal tunnel offset from target & Horn leading to a bunker area.
Vertical Handling along the beam line & access tunnel
Equipment is supported on the ground (shielding blocks) & contained in a vessel.
Multiple shielding blocks
Placed inside a He vessel
Utilities room on a separate gallery parallel to the beamline
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
I. Efthymiopoulos, Design Study For A Future Laguna-LBNO Long-baseline
Neutrino Facility At Cern, THPFI056, IPAC2013

## Slide 9: Layout ideas
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Target + Horn (and/or superconducting solenoid) - CENF
Beam line located in a deep trench with handling made from the surface building
Trench with fixed shielding
Equipment on modules with integrated shielding, contained in a vessel.
Utilities connected on top of the module to the services rooms on the side
R.Steerenberg, Design Study for a CERN Short Base-Line Neutrino Facility, TUPEA052, IPAC2013

## Slide 10: Layout ideas
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Target + Horn (and/or superconducting solenoid) - CNGS
Vertical handling with longitudinal rail system
Target sits on a alignment table controlled laterally from the outside of the shielding.
Shielding with fins for cooling
M.Calviani, Design, maintenance and operational aspects of the CNGS target, 4th HPTW,

## Slide 11: Layout ideas
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Target + Horn (and/or superconducting solenoid) - BDF
https://doi.org/10.23731/CYRM-2020-002
Very detailed study thought from installation to decommissioning of the target
Target enclosed in a shielding bunker inside a helium vessel.
Target handled vertically with the building crane.
Services chimneys for electrical and cooling connections of the target and proximity shielding.
Target exchange via a shielded vessel.
Crane++ concept
Crane concept

## Slide 12: Layout ideas
Momentum selection chicane
Chicane (“dogleg”) for momentum selection
  What would be the momentum of the selected muons?
  And what would be the aperture of the magnets and beam line components?
Can also serve as extraction to other experiments (nuSTORM / ENUBET ?)
Set of Collimator, bending magnets, quadrupole magnets and a dump.
Highly radioactive
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 13: Layout ideas
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Momentum selection chicane – AD-Target Area @CERN
Receives 26 GeV/c p+ beam from PS.
AD-T Chicane (“dogleg”) for 3.57 GeV/c momentum selection.
How will it be for the MUC ?
https://cds.cern.ch/record/2773294?ln=en
BTV downstream AD-T area

## Slide 14: Layout ideas
Muon Cooling Area
Collimation & upstream diagnostics + Muon Cooling area + Downstream diagnostics area
Collimation w/ ~5 x cryostats (Ø 2x4 m)
Cooling w/ ~10 x cryostats (Ø 2x4 m)
Needs a klystron area & other utilities
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 15: Layout ideas
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Muon Cooling Area - FCC e+e- Crymodules tunnel & klystrons gallery
Jean-Pierre Corso, Integration of the FCC, FCC Week 2021

## Slide 16: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
CERN TT10 branch

## Slide 17: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
62 m
120 m
40 m
CERN TT10 branch
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Indicative dimensions. Model is very flexible at this stage

## Slide 18: Conceptual layout
Service Gallery
Collimation + Cooling area
Branch to nuSTORM / ENUBET
Extraction TT10
Space for radioactive storage
Utilities room
Target + Horn + dogleg
Vertical shaft
Vertical shaft
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10

## Slide 19: Conceptual layout
Service Gallery
Collimation + Cooling area
Branch to nuSTORM / ENUBET
Extraction TT10
Space for radioactive storage
Utilities room
Target + Horn + dogleg
Vertical shaft
Vertical shaft
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
81 m
38.5 m
Ø12 m
59.5 m
11 m
5.5 m
5.5 m
30 m
5.5 m
10.5 m
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Indicative dimensions. Model is very flexible at this stage

## Slide 20: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Target + Horn + chicane hall
Cooling tunnel
Services Gallery

## Slide 21: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
7 m
11 m
11 m
6.5 m
5 m
6.5 m
5.5 m
5.5 m
10.5 m
5.2 m
5.2 m
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Target + Horn + chicane hall
Cooling tunnel
Services Gallery
Indicative dimensions. Model is very flexible at this stage

## Slide 22: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
TIDVG5 (450 GeV/c)
AD-T 3.57 GeV/c momentum chicane
CENF Shielding, target & horn
**Representative elements only**
Target trench like system with beam line below tunnel floor level → robust solution for radio protection
Vertical handling with beam equipment in modules, placed in a vessel (N2) container
Close-by radioactive storage
Utilities in parallel gallery
Clear separation from downstream cooling area
Possibility to branch to other experiments
Flexible facility with space accounted for future upgrades. At an early stage (80 kW), shielding may be reduced for cost optimization and could start with a simple target & horn. Flexibility to introduce more complex target systems depending on the progresses of the studies for the final Muon collider .

## Slide 23: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
The Facility is flexible enough to accommodate other experiments.
nuSTORM and potentially ENUBET could be branched from the MUC Demonstrator Facility.
The same target complex would be used profiting from its shielding and general target systems infrastructure, utilities, and accesses.
The double deflection of the beamline could reduce radiation streaming towards the nuSTORM ring.
Synergies between experiments would reduce costs on both sides.
Is the 26 GeV/c beam from the PS appropriate for these two experiments?

## Slide 24: Conceptual layout
MUC Demonstrator VERY Conceptual layout → To be taken with a “grain of salt”
Target + horn (1st phase) / superconducting solenoid (2nd phase)
Momentum selection chicane 10x 4 m
Collimation and upstream diagnostics area: 10x4 m
Cooling area: 50x4 m
Downstream diagnostics area: 5x4 m
Injection from TT10
Muon Cooling section can be extended if needed
Experimental cavern (e.g. for low energy muons) can be foreseen downstream muon cooling tunnel

## Slide 25: Conclusions
Supported on existing facilities and previous studies, a first MUC Demonstrator facility “concept” layout is show.
The facility shall be flexible enough & compatible with future upgrades.
3D facility modelling, even if with limited degree of detail is key for costing. Important to collect all requirements at this stage in order to be able to provide a first cost estimate by end of 2021, as requested by the study
Further inputs are needed, and early discussions with Civil engineering, RP, Transport, Cooling & ventilation, power, etc are of major importance
Comments and feedback are welcome! e.g. sizes of components in the collimator and muon cooling part, etc
by Rui FRANQUEIRA XIMENES* (on behalf of many other)
CERN – Systems Department
Sources Targets Interaction (STI)
Targets Collimators Dumps (TCD)
rui.franqueira.ximenes@cern.ch

## Slide 26
Thank you very much for your support and for your attention