## Slide 1: Study Horn-based Target System for Muon Collider
Katsuya Yonehara
Fermilab

## Slide 2: Motivation
Challenge to make Multi-Mega-Watt Target System
  Heat and radiation treatment
    For NuMI, 1/3 of total beam power is deposited in Target hall, 1/3 in Decay Pipe, and 1/3 in Hadron Absorber
    For NuMI, C-graphite target was activated 75 Rad/hr on contact after servicing 2yrs with 1e21 POT
  Phase space manipulation for cooling channels
    Achromatic pion capture optics
Investigate horn based systems
  Sub-MW target system exist
  Make a conceptual model
  Run numerical simulation to validate a new horn concept
I introduced a solenoid-based target system which is shown in my previous presentation
https://indico.cern.ch/event/1049225/

## Slide 3: Horn-based target system
Van der Meer’s original sketch of
magnetic horn in 1961
Lorentz force () makes focusing
  Assume path length inside horn field is parabolic
Widely used for neutrino experiments
  T2K: 515 kW (2020)
  NuMI: 843 kW (2021)
  Both use C graphite
  Horn survives more than 107 beam pulses

## Slide 4: Neutrino target system
LBNF: State of the art target system
  1.5-m-long C graphite cantilever target
  He gas cooling
  Accept 1.2-MW beam
    Proton beam momentum 120 GeV/c
    Proton bunch length 5 ns
    Beam repetition rate 1.2 second

## Slide 5: Apply Horn-based target system for Muon collider
Technology exists
  A big confidence to operate > 1-MW beam
Focus single charge (?)
Complex beam optics (?)
Low energy pion will be lost at inner conductor and cooling water
  30 % pion lost reported in the past study (?)
No quantitative study made in the past
(or at least I cannot find any citation)
Horizontal proton beam position at NuMI target
NuMI target scan
Linear focusing by NuMI Horns
Pros Cons

## Slide 6: Conceptual design of Horn (I)
B. Zwaska (2021)

## Slide 7: Numerical study of forward and backward pions/muons
8 GeV protons
G4beamline
Green circle: virtual detector
Blue: positive charged particle
Red: negative charged particle
Green: neutral particle
1-m-long Carbon
graphite target
(invisible in this plot)
P. Snopok, N. Muldrow (2021)

## Slide 8: Preliminary simulation result (I) Note: Proton momentum 1 to 10 GeV/c
1e6 POT

## Slide 9: Preliminary simulation result (II) Momentum cut MeV/c
1e6 POT
Ratio of forward and backward = 9:1

## Slide 10: Conceptual design of Horn (II)
Horn is axisymmetric, no x-y asymmetry like quad
Focusing mode in horn depends on a direction of horn current vs beam current
f
f
I
I
f
f
I
I
Attractive
Repulsive

## Slide 11: Toy model (I)
Target
Horn
D
f
r
q
d
Q
Horn focusing force
Cross-sectional shape of horn
Focusing geometry can be fixed from known dimensions with a simplified model
Dashed line: actual particle track
Solid line: simplified ray trace

## Slide 12: Toy model (II)
D
f
r
q
d
Q
Geometry constraint
Focusing force
If we know , all focusing geometries are fixed
is a good approximation for neutrino target
Will find a correlation from slide 9
is horn current (kA)
is (mm)
is longitudinal momentum (GeV/c)

## Slide 13: Summary
Study a conceptually new horn-based target system
  Capture both charges