## Slide 2: PRELIMINARY STUDY If we extend the LHC or SPS straight insertion where would the neutrinos come out to the surface of the earth?
Patrimony and Site Information
EDMS: 2065924

## Slide 3
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?
Problem:
« If we extend the LHC straight insertions where would the neutrinos come out the surface of the earth?”
EDMS: 2065924
Hypothesis:
The LHC straight insertions directions are given by the lines built from the middle of Beam 1 and Beam 2 DFBA elements on each side of the Insertion Point.

## Slide 4
PRELIMINARY STUDY If we extend the SPS straight sections where would the neutrinos come out to the surface of the earth?
Problem:
« If we extend the SPS straight sections where would the neutrinos come out the surface of the earth?”
EDMS: 2353912
Hypothesis:
The SPS straight sections directions are given by the lines built on dipole MBA X1590 beam exit points on one side and MBA X2030 beam entrance point on the other side. (X for the SPS point)

## Slide 5
Data:
Coordinates of DFBA beam points
  from Geode Survey database
  in CCS (XYZ) coordinate system
EDMS: 2065924
EU-DEM v1.1 : Digital Surface model for Europe
  The spatial reference system is geographic, lat/lon with horizontal datum ETRS89, ellipsoid GRS80 and vertical datum EVRS2000 with geoid EGG08.
  https://opendem.info/opendemeu_meta_eudem.html
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?

## Slide 6
Methodology:
LHC straight insertions lines are extended in CCS coordinate system
One point is created every 200 m along these lines (CCS coordinate system) – (Discretisation of the Beam lines)
EDMS: 2065924
3) XYZ Coordinates of each point are converted to WGS84 Geodetic Coordinates System
  The results is geographic coordinates (lat, long) with ellipsoidal heights (He) of each point.
4) The EU-DEM is converted to WG84
  The Geoid heights (Hg) are unchanged as the ellipsoids WGS84 and GRS80 are slightly equivalent).
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?

## Slide 7
Methodology:
SPS straight sections lines are extended in CCS coordinate system
One point is created every 200 m along these lines (CCS coordinate system) – (Discretisation of the Beam lines)
EDMS: 2353912
3) XYZ Coordinates of each point are converted to WGS84 Geodetic Coordinates System
  The results is geographic coordinates (lat, long) with ellipsoidal heights (He) of each point.
4) The EU-DEM is converted to WG84
  The Geoid heights (Hg) are unchanged as the ellipsoids WGS84 and GRS80 are slightly equivalent).
PRELIMINARY STUDY If we extend the SPS straight sections where would the neutrinos come out to the surface of the earth?

## Slide 8
Methodology:
5) The Geoidal ellipsoidal heights (He) of the beam points are converted to Geoidal Heights (H) :
  N is the ondulation of geoid in the studied area estimated to 50 m. In reality it varies from + 47 m to + 54 m.
6) The difference between the heights (H) of each point and their projection to the DEM (Hgprj) is calculated.
  If the Delta > 0, the point is at the surface of the earth
  If Delta is < 0 the point is underground.
EDMS: 2065924
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?
H = hellipsoid - Ngeoid
Extended Insertion line
Delta
N
H
He
DEM Topography
Ellipsoid
Geoid
Hgprj
H = He – N
Delta = H – Hgprj

## Slide 9
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?
Results:
Point | Side | First exit to the surface of the earth (Distance from IP in Km)
1 | L | 263
1 | R | 40
2 | L | 258
2 | R | 25
3 | L | 17
3 | R | 74
4 | L | 37
4 | R | 30
5 | L | 26
5 | R | 237
6 | L | 35
6 | R | 255
7 | L | 76
7 | R | 161
8 | L | 145
8 | R | 35
 | Min | 17 km
 | Max | 263 km

## Slide 10
PRELIMINARY STUDY If we extend the SPS straight insertion where would the neutrinos come out to the surface of the earth?
Results:
Point | Side | First exit to the surface of the earth (Distance from SPS point in Km)
1 | L | 64
1 | R | 7
2 | L | 28
2 | R | 35
3 | L | 44
3 | R | 10
4 | L | 80
4 | R | 6
5 | L | 10
5 | R | 21
6 | L | 51
6 | R | 10
 | Min | 6 km
 | Max | 80 km
EDMS: 2065924

## Slide 11
Tolerance and accuracy:
Heights
  EU-DEM: Accuracy : +/- 7.0 m RMSE
  EU-DEM is a DEM, and not a DTM (Digital terrain Model).
  An error of + 20.0 m is estimated
  The assumption for the Geoid undulation is +/- 3.0 m
= > The accuracy of the DTM is roughly evaluated to +/- 30 m
LHC straight insertions directions:
The error is estimated to max 0.1 degree in both horizontal and vertical directions. This corresponds to 20cm /100 m
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?
=> To simulate the uncertainty of the results, the calculations are made for the worst possible cases
30 m
0.1deg
Uncertainty
=> To get rid of the influence of any parameter that would not have been taken into account in this preliminary study a buffer of 1000 m is added

## Slide 12
PRELIMINARY STUDY If we extend the LHC straight insertion where would the neutrinos come out to the surface of the earth?
3D View

## Slide 13
Conclusions:
The presented maps are a very quick and preliminary study of the question. But the geographic tools and the data are available.
For LHC the longest distance is on the other side of the alps. For SPS, it is on the other side of the Jura
The depth of the SPS and its “horizontality” bring some uncertainty on the exact locations. The beam is grazing the surface of the earth
For a more precise study, some more investigations have to be performed
We now have Gil a technical Student to automatise the production of such maps according to the collider position
EDMS: 2065924
PRELIMINARY STUDY If we extend the SPS straight sections where would the neutrinos come out to the surface of the earth?