## Slide 1
WP3 update
Positron Source: Target and Capture System
Iryna Chaikovska
on behalf of the WP3 team
17 June 2021

## Slide 2: General updates
FCC-ee injector review (April 19th) => Positron source advantages/disadvantages of single bunch vs multi-bunch operation.
IJCLab: Salim OGUR has started to work at IJCLab from 1st June 2021. A new PhD will start this Autumn 2021 (the potential candidate is identified).
PSI: A new PhD will start in summer 2021 (the candidate is identified).
The detailed plan for 2 PhD to be discussed between IJCLab and PSI.
A new MoU between CNRS/IN2P3 and CERN is under the preparation.

## Slide 3: Some highlights
@ILC
FC: 5 T -> 0.5 T + L band 1.3GHz, 2a=60 mm
Target: W26Re, 16mm
Nb. bunches: 66 in ~0.5 us and 1320 in 63 ms
e+ yield: 1.25-1.28
The dedicated/systematic studies on the target thermal load/target design, beam losses on the structures (FC/SC solenoid, DC solenoid, acc. sections…), radiation environment, etc. will be done in Tasks 3.5/3.6

## Slide 4: Some highlights (work ongoing)
Discussions/iterations between CERN and PSI on the conceptual design of the SC solenoid and target integration have been started.
CERN/STI group performed the FLUKA power deposition studies for the first solenoid design as proposed by PSI.
Based on these results, the PSI colleagues redesigned the solenoid and sent a the new design to the CERN/STI group this week (the design is also a bit more realistic than the old one since it includes for example the cryostats).
Implementation of this new design in FLUKA is ongoing to perform a power deposition analysis, and study the long-term radiation damage based on the operational parameters.
Task 3.5 Design and integration of positron target area
Task 3.6 Design of target mechanical system
Courtesy of A. Lechner
SC solenoid studies

## Slide 5: Annual number of hits on the target
The CDR injector was supposed to hit the target with electrons at 200 Hz with 2 bunches:
400 Hits/s * 3600 s *24 h* 185 days * 0.804 = 5.1E9 Hits/year
The first fill from scratch (daily few times). The required positron charge during top up may vary between 0 to 100% of the nominal charge.
Roughly, we expect <10% of the nominal positron charge to be top-upped. Therefore, we expect after first fill in 17 mins, the injectors carries ~2E9 e+/e-.
The linac is OFF when the synchrotrons are filled, therefore the linac duty cycle is 80.4%
The new injector option may hit the target with electrons at 100 Hz with 20 bunches (number of bunches is not fixed yet):
2000 Hits/s * 3600 s *24 h* 185 days * 0.50 = ~1.6E10 Hits/year
The first fill from scratch (daily few times), the required positron charge during top up may vary between 0 to 100% of the nominal charge.
Roughly, we expect <5% of the nominal positron charge to be top-upped. Therefore, we expect after first fill in 5 mins, the injectors carries ~1E9 e+/e-.
The linac is OFF when the synchrotrons are filled, therefore the linac duty cycle is 50%
Courtesy of S. Ogur
Assumption: the collider will work 185 days per year (Z-operation).
SLC (rotating target, 365 days):
~4E9 Hits/year
1 hit = 1 bunch
Notes: It is essential for estimating the annual dose in the solenoid.