## Slide 2: EP R&D Project on Noble Liquid Calorimetry High Density Feedthrough Design
Maria Barba, Michel Chalifour, Johan Bremer, Martin Aleksa
Meeting on FCC Noble Liquid Calorimetry
June 17th, 2021
WP3: Calorimetry and Light-based detectors

## Slide 3: Collaboration WP3 & WP4
87 K
WP3 : Calorimetry and Light-based Detectors
WP4 : R&D on Light-weight Cryostats
Goal : Development of high-density signal feedthroughs for future LAr calorimeters
Goal : Decrease thickness and material budget of the next generation of cryostats for HEP
High-density flange made of different material candidates:
3D-printed plastics
Araldite resins
Fiberglass with epoxy resins
Development and testing of carbon fiber cryostats

## Slide 4: Collaboration WP3 & WP4
WP4 : R&D on Light-weight Cryostats
Prototypes to test:
Prototype 1
Prototype 2
Prototype 3
SS flange
Carbon fiber cylinder
10 cm

## Slide 5: Collaboration WP3 & WP4
WP3 : Calorimetry and Light-based Detectors
Samples to test:
Accura 25
Flange
MY750
G10
SS compression
plate
Indium seal
Sample 1:
MY750

## Slide 6: Collaboration WP3 & WP4
Type of tests:
Pressure (3.5 bar) and leak test at 300 K
Pressure (3.5 bar) and leak test at 80 K
To verify:
Resistance to low temperature
Resistance to high-pressure
Leak-tightness
Same “adaptable” experimental setup to test the feedthrough samples and the carbon fibre prototypes
Test schedule  one sample per week
Feedthroughs samples
LN2
LN2
GHe
Pumping and leak detector
DAQ
Cryostat
Thermal shield (GN2)
Sample

## Slide 7: Collaboration WP3 & WP4
Carbon fiber prototypes
LN2
LN2
GHe
Pumping and leak detector
DAQ
Cryostat
Thermal shield (LN2)
Prototype (cooled by radiation from thermal shield)
Type of tests:
Pressure (3.5 bar) and leak test at 300 K
Pressure (3.5 bar) and leak test at 80 K
To verify:
Resistance to low temperature
Resistance to high-pressure
Leak-tightness
Same “adaptable” experimental setup to test the feedthrough samples and the carbon fibre prototypes
Test schedule  one sample per week

## Slide 8: Collaboration WP3 & WP4
WP3 : Calorimetry and Light-based Detectors
WP4 : R&D on Light-weight Cryostats

## Slide 9: WP3 : Calorimetry and Light-based Detectors
CTE and thermal conductivity measurements at low temperature ongoing…
CTE of Accura25 between 300 and 77 K (11 mm/m)
CTE of MY750 between 300 and 77 K (10 mm/m)
CTE of Accura25 between 77 and 4.2 K
CTE of MY750 between 77 and 4.2 K
λ of Accura25 between 300 and 77 K
λ of MY750 between 300 and 77 K
λ of Accura25 between 77 and 4.2 K
λ of MY750 between 77 and 4.2 K

## Slide 10
Thank you for your attention!
Questions?