## Slide 1: LSSO Presentation of the new safety mandate
Stéphane Détraz (EP LSO)
EXSO 31 MARCH 2022

## Slide 2: LSSO mandate defined in the General Safety Instruction GSI-SO-14
  This new safety instruction was published in May 2021 and can be found on EDMS:
  https://edms.cern.ch/ui/file/2476308/LAST_RELEASED/GSI-SO-14_E.pdf
  LSSO stands for LASER SAFETY SUPPORT OFFICER
  This safety role has been created in the larger context of updating the current CERN safety rules related to Non-ionizing radiation (NIR).
  This GSI concerns the field of LASER optical radiations with wavelengths between 100nm and 1mm.
  The current rule (IS22) dates from 1994! HSE and the LSOC are working on editing new GSI and SSI to comply with the current international safety standards (IEC-60825) and clarify the LASER risk management at CERN.
EXSO 31 March 2022
S. Détraz | LSSO mandate
2

## Slide 3: Where and Why we need LSSOs
  A LSSO is linked to a defined DLA.
  → DLA: Designated Laser Area. It’s an area inside which you can operate class 3B and 4 lasers with exposed beams.
  → You are not allowed to have class 3B or 4 exposed beams outside a DLA.
  Any experiment using class 3B or 4 lasers shall appoint a LSSO.
  The department Laser Safety Officer (LSO) is a laser safety expert who has an advisory and support role to the DSO and people using lasers within the department.
  The LSSO is also a laser safety expert. But in addition, she/he shall be very familiar with the laser system installed inside the DLA. And she/he is responsible for ensuring Laser Safety, in compliance with the relevant safety rules, within the DLA.
  Previously this role was known as Laser supervisor/Laser safety expert but it was not official. This mandate involves responsibility and an extra load of work that shall be recognized by the CERN/Institute hierarchy.
  The mandate gives also authority to the LSSO. She/he can grant access to the DLA and forbid laser operation if all safety measures are not in place.
EXSO 31 March 2022
S. Détraz | LSSO mandate
3

## Slide 4: Highlights of some LSSO duties (1)
  Register any class 3R, 3B or 4 lasers into the CERN NIRREG database.
    For this purpose, she/he shall fill up the Laser ISI registration form and send it to the LSO or his deputy. During the current year, a short training on the new NIRREG database (using EAMlight) will be provided to every LSSO. Following this training they will be able to add new DLA and laser information directly into the database.
  Carry out a risk analysis of the activities inside the DLA. The LSSO could ask the help of the LSO or any other SO. She/he could also use the checklist tables inside the “Laser safety visit” document.
  Take the necessary measures to suppress or mitigate the risks inside the DLA and check that we have no foreseeable risk outside the DLA linked to the laser activity. The LSSO shall receive from the laser owner the necessary information and resources to carry out this task.
    Bringing a laser to CERN implies bringing the resources needed to implement the safety measures determined by the LSSO of the DLA where the laser will be installed.
EXSO 31 March 2022
S. Détraz | LSSO mandate
4

## Slide 5: Highlights of some LSSO duties (2)
  Create or update the safety documentation. The documents shall be uploaded into the experiment EDMS safety folder. The LSO shall be informed of any major modification.
    HSE is currently re-writing the Non-Ionising Radiation (inc. lasers) rules. New procedures and documents should be published in the coming months. In the meantime, LSSO shall fill-up the “Laser safety visit” document with the Laser installation description, the risk assessment and all the necessary procedures (operation, alignment, maintenance…). It is important to have a complete and up to date documentation. The LSSO’s supervisor shall give her/him the necessary time not only to implement the safety measures for the DLA but also to write the safety documentation.
    This documentation is submitted to the LSO or his deputy.
  Carry out regular safety check on her/his installation (e.g., interlocks, shutters, safety glasses, beam dump…).
  Ensure that users of the DLA are trained and informed: general safety training but also on-job training. Keep an updated list of authorized DLA users and list of procedures they are authorized to perform.
EXSO 31 March 2022
S. Détraz | LSSO mandate
5

## Slide 6: LSSO appointment
  The LSSO shall have a sufficient knowledge of the laser systems used within the DLA to understand the potential safety issues.
  The LSSO shall be trained in Laser safety. HSE is working on the creation of a LSSO training. In the meantime, she/he could follow an external training (to be discussed with the LSO).
  For DLA under the responsibility of a department, the LSSO shall be appointed by the group leader responsible for the DLA, amongst employed members of the personnel.
  For DLA under the responsibility of a large experiment, the LSSO shall be appointed by the technical coordinator responsible for the DLA, amongst members of the personnel.
  This appointment is approved by the LSO and DSO or LEXGLIMOS.
  During laser operation in the DLA and specially during critical phases (installation, laser alignment and maintenance, special operations) the LSSO shall be present at CERN to supervise the tasks. The LSSO (or her/his deputy) should be reachable in case of emergency.
EXSO 31 March 2022
S. Détraz | LSSO mandate
6